## Slide 1
Verify This!
An introduction to UVM
Day 1 Day 2 Day 3 Day 4 Day 5 Day 6 Day 7 Day 8
github.com/leandrotozzi/verifythis · SystemVerilog · Verilator · UVM 2020.3.1

## Slide 2
How to use this course
Especially if you are taking it on your own
What you need to know first: Verilog or VHDL, and having simulated something. Object-oriented programming is not required — day 2 is exactly that. The only thing the course takes for granted is SystemVerilog: if you come from VHDL or Verilog-2001, half an hour with docs/systemverilog-para-el-que-viene-de-vhdl.md (in Spanish) before starting
It is seven days of class, of 4 to 5 and a quarter hours — ≈ 31 h, and each agenda carries its own. Plus an optional day 8, after the wrap-up. On your own, count double: half of it goes into running the examples, and that is the half that teaches
s opens the presenter notes in another window · n shows them down here, without leaving the page. That is where what the instructor would say out loud lives: the classic trap, the reason behind the number, the mistake everybody makes the first time. Do not skip them
Every day closes with a review of clickable options and with a self-checking exercise: cd code/ejercicios/d1 && bash run.sh. The names of the other eighteen are in code/ejercicios/README.md
Notes: If you are teaching the course, these two slides are skipped with the 1 key. They are here because most people who open this will not have an instructor alongside, and without the presenter notes half the material gets lost — and that half is also the hardest one to reconstruct by reading the code.

## Slide 3
How to use this course
Running it, moving around it, and where to look when something breaks
Run the examples: make u4/tests runs one, make u4 the whole unit. A verification course that is only read is worth nothing. A UVM example takes a minute and a half the first time and fifteen seconds the second, if you have ccache installed — and if you do not have Linux, the short road is GitHub Codespaces, which already ships with it
0–8 jump to the cover and to each day · i opens the index · Esc shows the whole deck · and the corner ribbon unfolds the cheat sheet of the day
If you are on your own, read the book: en/libro/day1.html is this same course straight through, with the notes already inside the text. Keep the deck alongside for the reviews
When something does not work, go to the end: the appendices The debug toolbox —what to look at for each symptom— and The 21 silent traps —everything that compiles, runs and lies—. Those are the two slides to print
Notes: The last two are the ones that pay off most for someone studying alone, and the ones nobody reads until they are already stuck: the book carries these same notes inside the text, and the appendices are written as a table of symptoms, to look things up in rather than to read straight through.

## Slide 4
Agenda
Day 1 · ≈ 4 h · units 1 and 2
Unit 1 · Why we verify
Trends
What UVM is
The VTALU spec
The verification plan
Unit 2 · The testbench without UVM
The conventional testbench
Functional coverage
Interfaces and BFM · the clocking block
Two exercises, and the second one is solved with the wave viewer
And closing the day, going back to the first slide
By the end of the day you can:
Write a five-column verification plan for a DUT you have not seen before
Prove that your scoreboard checks something: put a bug into the DUT on purpose and watch it fail
Read the number a covergroup gives, say which row of the plan is missing, and what to look at first when it reads 0 %
Explain which race a clocking block avoids — and why they are optional anyway
Notes: The four verbs below are the contract of the day, and it is worth reading them out loud before starting: on video they are the ten seconds in which someone decides whether this is the one they were looking for. Three are rows 2, 4 and 5 of the closing self-assessment, brought to the front; the one about the bug on purpose is the practice that runs through the whole course, from make mutante today to +BUG=1 in the capstone. Whoever can answer them at the end of the day does not need to watch anything else. And an honest warning for whoever comes from VHDL or from Verilog-2001, which is the declared audience: day 2 levels the OOP, but nobody levels SystemVerilog, and today interface, logic, enum, package, covergroup, clocking and an assert property all show up. It is all on one page in docs/systemverilog-para-el-que-viene-de-vhdl.md (in Spanish): half an hour before starting, and day 1 stops having two steps at once.

## Slide 5
Six out of seven
And the bug that reached silicon passed a green regression
How IC/ASIC projects end in 2024: 14 % get first silicon right and 75 % run late

## Slide 6
14 % of projects get first silicon right. Six out of seven go back to the fab, and it is the worst figure in twenty years of the survey
Every functional bug that reached silicon went through a testbench first. That testbench ran, finished, and said everything was fine
Nobody tapes out with a FAILED in the log. You tape out with a PASS
Today has a single question: how do you know you verified? And “I ran a lot of tests” is not an answer
Notes: It is the first content slide of the course on purpose: before explaining what UVM is and before any other chart, a question the student cannot answer yet. The number is from the Wilson Research Group 2024 survey and it is not an impression: only 14 % come out right on first silicon, so six out of seven need at least one respin, and it is the worst figure in twenty years of the survey. Asking who has done a tape-out and how it went hooks better than the chart. If they ask where the data comes from: res/trends/data.json, and the figures are regenerated with make figs. The honesty worth saying out loud: not every respin is functional —there are timing ones, analog ones, a spec that changed late—. But the one that is went through a regression that said PASS, because had it said FAILED it would not have been fabricated. That is the enemy of the day, and it is not the verification engineer nor their testbench: it is a PASS nobody knew the meaning of. The question in the last bullet is thrown to the group and not answered. The answers that will come are “100 % coverage”, “I ran a thousand operations” and “nothing failed”, and all three come back today: the first is the coverage section, the second is the plan, and the third is the one that hurts most, because nothing failed is exactly what the respin’s regression said. The short answer arrives in the conventional testbench, when we put a bug into the DUT on purpose; the long one is the whole day, and the last slide of the day comes back to this question with what the student wrote.

## Slide 7
Trends
Why they come back: what is inside a chip today
What is inside 2024 IC/ASICs: asynchronous clocks, embedded processor, security, AI, RISC-V and safety

## Slide 8
Notes: It is the first half of the answer to why they come back: inside there are two asynchronous clocks in almost all of them, a processor in five out of six and an AI accelerator in more than half. It is not that verification is done worse than twenty years ago; it is that there is much more to verify, and the question on the first slide is harder to answer than ever.

## Slide 9: Trends
Verification is not a stage, it is half the work
49 % of the designer’s time goes to verification; 47 % of the verification engineer’s time goes to debug

## Slide 10
Notes: Here is the argument for why this course exists: the verification effort has already caught up with design. Verifying is not the final step before tape-out: it is half the project, with its own team and its own language. The lower 47 % is planted today and collected twice: in the second exercise this afternoon, when the log says FAILED and nothing else, and in the reporting section on day 3, which is where the log learns to say why.

## Slide 11: Trends
And it is verified, mostly, with UVM
What verification uses in 2024: UVM at 80 % in IC/ASIC and 50 % in FPGA

## Slide 12
Notes: This one answers with what: eight out of ten ASIC projects verify with UVM, and half of the FPGA ones. What follows —the COBOL joke and the introduction— is what that UVM is and why it is not scary. And one thing worth leaving said now: UVM does not answer the question on the first slide. The testbench does; UVM is the way to write it so that the person next to you recognizes it.

## Slide 13: Is SystemVerilog the COBOL of electronics?
Language | Reserved Keywords
ANSI COBOL 85 | 357
SystemVerilog | 248
VHDL 2008 | 115
Verilog 95 | 102
C# | 102
C++ 20 | 92
Python 3 | 35
“* No academic computer scientists participated in the design of COBOL; all of those on the committee came from commerce or government” Sound familiar?
Notes: It is a joke with a moral: SystemVerilog has 248 keywords —the ones in Annex B of IEEE 1800-2017— and nobody uses them all. In this course we are going to use about thirty. The same thing happens with UVM: the library is enormous and with six or seven classes you put together a complete testbench. It is useful for lowering the anxiety of whoever arrives scared by the size of UVM. And it is the bridge to the next section: eight out of ten verify with UVM, UVM is written in this language, and on days 1 and 2 everything UVM will later hand you ready-made gets written by hand. Thirty keywords are enough.

## Slide 14
Introduction
What is UVM?
Universal Verification Methodology: a class library written in SystemVerilog, plus a pile of conventions on how to use it
It is not a language and it is not a simulator. Everything we are going to see in the course can be written by hand — and on days 1 and 2 we are going to write it by hand
It is made by Accellera, the same consortium that standardized SystemVerilog, and it is IEEE 1800.2. The course uses the reference implementation, uvm-core 2020.3.1
It comes from OVM (Cadence + Mentor), with ideas from VMM (Synopsys) and from eRM (Verisity): the methodologies of four vendors that competed, until the industry got tired of translating testbenches between tools
And there is the goal, and it is a single one: that the testbench of the person next to you looks like yours
Notes: The link with what came before is one line: eight out of ten projects verify with this. And the clarification that keeps UVM from looking like the answer to the question of the day: it is not. The answer is a testbench with a plan, a check and a measure; UVM is the way to write it so it scales and so someone else recognizes it. The sentence that orders the section is the one in the second bullet, and it is worth saying it loudly because it lowers the anxiety of whoever arrives scared: UVM does nothing you could not do yourself. There is no magic inside. There is a factory, some ports, some phases and a lot of agreement about names. If somebody asks why bother then: because of the last bullet. A verification engineer who changes project —or company— opens the testbench and recognizes the structure on day one. That is what you are buying. It is not simulation speed and it is not fewer lines: it is that the structure is the same everywhere. The historical note is useful for whoever comes from the industry: until 2011 every vendor had its own, and porting a testbench from VMM to OVM meant rewriting it. UVM exists because that was unsustainable, not because somebody had a better idea. And one clarification that avoids a classic misunderstanding: Open Source here means that the library is free (Apache 2.0). The simulator that runs it almost always is not — except in this course, which is what all of this is about.

## Slide 15: Introduction
Where it comes from
From eRM, VMM, AVM and OVM to UVM

## Slide 16
Notes: The diagram in one sentence: six acronyms from four vendors that converge. eRM was Verisity’s (the e language), RVM and later VMM Synopsys’, AVM Mentor’s and URM Cadence’s; OVM merged AVM with URM, and it is the base UVM came out of. What has to be pointed out is the date at the bottom and the jump it means: UVM 1.0 is from 2011, which means this is young. Somebody with fifteen years of career today started before it existed. And the moral that gets used for the rest of the course: when they find code with ovm_component instead of uvm_component, it is not a typo — it is a testbench from before 2011 that nobody migrated. It happens more than it seems.

## Slide 17: Introduction
A SystemVerilog testbench, from the inside
Anatomy of a SystemVerilog testbench

## Slide 18
Notes: This is the testbench we are going to write, by hand, on days 1 and 2. It is worth saying it like that: the boxes in this diagram are not theory, they are the files that are going to be open between today and day 4. Point at the tester, the driver, the monitor and the scoreboard, and make the point that none of those names is UVM’s: they are the names anybody gives to the pieces of a testbench, in any language. UVM did not invent them; it standardized them.

## Slide 19: Introduction
The same testbench, with UVM structure
The same testbench with UVM structure

## Slide 20
Notes: It is worth staying here a while: this diagram is the map of the rest of the course. Point at driver, monitor, scoreboard and sequencer, and say that each one is going to be a section. By the end of day 5 the student is going to have everything except the agent and the sequencer, which are day 6. The comparison worth making live is against the previous diagram: they are the same boxes. What UVM adds is the tree that contains them, the ports they talk through and the phases that build them in order. Nothing else, and that is not little.

## Slide 21: Introduction
The class tree
The UVM base class hierarchy

## Slide 22
Notes: This diagram is scary and that is why it is worth defusing it right away: out of all of this we are going to extend ten: uvm_component, uvm_test, uvm_env, uvm_agent, uvm_driver, uvm_monitor, uvm_subscriber, uvm_sequence_item, uvm_sequence and uvm_callback. They are the amber ones in the drawing minus the scoreboard —which in the course is a uvm_subscriber—, plus the sequence and the callback. What does have to be marked is the split at the top, because it explains half the course: hanging off uvm_object is the data —the transactions, the sequences, the configs— and hanging off uvm_component is the structure —everything that lives in the tree and has phases—. An object is created and thrown away; a component is built once and lasts the whole simulation. The colours say what you do with each one: the amber ones you extend yourself, the grey ones are never touched —they are only there for the others to inherit from— and uvm_sequencer is the only green one because it is the only one instantiated without extending it, with a parameterized typedef. That comes on day 6; the only time the course extends it is for the virtual sequencer on day 7. The question to throw at the group when we get to agents: is a uvm_sequence an object or a component? An object. And that is why it does not show up in print_topology(). It is the same tree that is in the printed cheat sheet, top left, as text, to look at again when needed.

## Slide 23: Introduction
Run more tests writing less code
That is the promise, and it has one condition: the env and the components barely change from one test to another. What changes is the stimulus
For that to work, the testbench has to leave hooks: virtual methods, the factory and callbacks. A test hooks in there and does not touch the structure
A new test is then one of these three things, and none of them touches the env:
  adding constraints to reach a corner case
  doing a factory override to swap one class for another
  injecting errors or delays with callbacks
And on top of all that, the lever that pays off the most: the same test with hundreds of different seeds
Notes: This is the slide you have to be able to repeat at the end of the course, because it is the whole thesis. And it is worth being honest: “run more tests, write less code” is a vendor slogan, but the verifiable part is true and you can point at it with your finger on day 6 — the add_test of the sequences is two lines, and it changes the whole stimulus without touching a single class of the env. The order of the three hooks is not accidental, it goes from smallest to largest: a constraint changes values, an override changes a class, a callback changes behaviour at one point of the class that already exists. All three are a section of the course —Constrained random on day 5, The factory pattern on day 2 and Callbacks on day 6—, so this slide can be put up three more times. And the last line is the most underestimated one. A test with a thousand seeds is not “the same test a thousand times”: it is a thousand different scenarios for the price of writing one. It is literally the d7-semillas exercise, the one day 7 starts with. And the close that leads to the DUT: nothing on this slide answers how do you know you verified? yet. Answering it is what comes next —the spec, the plan and a testbench that can be put to the test—, and only with that written by hand does what UVM adds become visible.

## Slide 24
The VTALU spec
VTALU protocol: start and operands stable until done

## Slide 25
start has to stay at 1 and the operands stable until the operation finishes
done goes up when the operation finishes: on the multiplication it is a one-cycle pulse; on add/sub/and/xor it is a level, and it stays up while start stays up
reset_n is asynchronous and active low; the diagram starts with the DUT already out of reset
ovf comes out together with done, and it is the borrow of the subtraction: it is 1 when A < B. For the other operations it is always 0
Notes: The protocol is everything you have to respect: start up and operands stable until done. Careful with the fine print: done is a pulse on the multiplication (it turns itself off) and a level on add/sub/and/xor, where it is start && (op != no_op). It is the kind of detail that only shows up when the testbench hangs and nobody knows why.

## Slide 26: The VTALU spec
Operation | Opcode | Cycles | ovf
no_op | 3’b000 | — | 0
add_op | 3’b001 | 1 | 0
sub_op | 3’b010 | 1 | A < B
and_op | 3’b011 | 1 | 0
xor_op | 3’b100 | 1 | 0
mul_op | 3’b101 | 4 | 0
free | 3’b110 | 1 | 0
rst_op | 3’b111 | — | —
Cycles counts clk edges with start up, up to and including the one that raises done: one on the single-cycle ops, four on the multiplication. The plan and the day 7 assertions count the same way
rst_op is not decoded by the RTL — the DUT sees it as unused. It is the testbench convention for pulsing reset_n, and that is why it is in the operation_t of the testbench
3'b110 is free on purpose: it is today’s exercise
Notes: rst_op belongs to the testbench, not to the RTL: the DUT sees 3’b111 as unused. It is in the enum because the tester asks for the reset as if it were one more operation, and that way the reset enters the functional coverage. A good moment to preview that the coverage plan includes “any operation after a reset”. The ovf column is the one that gets the most discussion, and that is good: with 8-bit operands and a 16-bit result, neither the addition nor the multiplication can overflow — the subtraction can, and only when A < B. Which means there is an output of the DUT that for five of the six operations is always 0. Ask out loud: how do you verify a signal that almost never moves? The answer is today’s, in functional coverage, and it is a bin. And the free opcode: 3’b110 is not there by chance and not by oversight. It is this afternoon’s exercise, and it is worth saying now so that nobody reads it as a design slip.

## Slide 27: The VTALU spec
Single Cycle: Add - Sub - AND - XOR
// The two resets are deliberately different: the one on the result is // SYNCHRONOUS and the one on done is ASYNCHRONOUS. Not an oversight: the spec. always_ff @(posedge clk) begin if (!reset_n) begin result_1c <= 16'h0000; ovf_1c <= 1'b0; end else if (start) begin ovf_1c <= (op == 3'b010) && (A < B); case (op) 3'b001: result_1c <= {8'h00, A} + {8'h00, B}; 3'b010: result_1c <= {8'h00, A} - {8'h00, B}; 3'b011: result_1c <= {8'h00, A} & {8'h00, B}; 3'b100: result_1c <= {8'h00, A} ^ {8'h00, B}; default: ; // 3'b110 is free: it is the day 1 exercise endcase end end // done goes high on the edge if start is high and the op is not no_op always_ff @(posedge clk or negedge reset_n) begin if (!reset_n) done_1c <= 1'b0; else done_1c <= start && (op != 3'b000); end
Two always_ff and nothing else: one registers A op B, the other raises done
The resets are not the same: the one on the result is synchronous —only clk in the sensitivity list—, the one on done is asynchronous
done <= start && (op != no_op): that is why on these four operations done is a level and stays up while start is
Notes: The asymmetry of the two resets is not an oversight: it comes from the original VHDL and is copied as is on purpose. It is exactly the kind of detail a testbench has to expose, and that is why the DUT was not “cleaned up” when it was translated. Say it out loud: this contradicts the bare asynchronous of the spec bullet, and no row of the plan looks at what the reset leaves on the outputs: the reset row looks at the operation that comes after. It is a gap in the plan, and for now it stays that way. That done is a level here and a pulse on the multiplication is the fine print that is going to hang the first testbench of the course. It is worth going back to the waveform of the first slide and pointing at it again. The default: ; of the case is what makes no_op and the unused opcodes not change the result: the ALU keeps whatever it computed last.

## Slide 28: The VTALU spec
Multi Cycle: Multiplication
// Four register stages. done is pipelined alongside the data, and each // stage clears itself with (& ~done_mult): that is what makes done a // one-cycle pulse instead of staying high for as long as start does. It is // subtle -- it is copied straight from the VHDL. always_ff @(posedge clk or negedge reset_n) begin if (!reset_n) begin done_mult <= 1'b0; done3 <= 1'b0; done2 <= 1'b0; done1 <= 1'b0; a_int <= 8'h00; b_int <= 8'h00; mult1 <= 16'h0000; mult2 <= 16'h0000; result_mult <= 16'h0000; end else begin a_int <= A; b_int <= B; mult1 <= a_int * b_int; mult2 <= mult1; result_mult <= mult2; done3 <= start & ~done_mult; done2 <= done3 & ~done_mult; done1 <= done2 & ~done_mult; done_mult <= done1 & ~done_mult; end end
It is a pipeline: the operands get registered, they get multiplied, and the product goes through two more registers before coming out on result_mult: four edges
The done travels down the same chain —done3, done2, done1— so it arrives exactly with the data and not before
The & ~done_mult of each stage is what turns the chain off on its own: that is why here done is a one-cycle pulse, even if start stays up
Notes: The four-edge latency is on purpose, and it is the reason the conventional testbench exists: it forces the testbench to wait for done instead of reading the result on the next cycle. A combinational DUT would teach nothing. The & ~done_mult is subtle and worth reading slowly: without it, while start was up the chain would reload itself and done would stay at 1. It is copied from the original VHDL as is. The question that orders the slide: what happens if the testbench sends a multiplication and reads the result on the next cycle? It reads the previous result, and the scoreboard reports an error that is not in the DUT.

## Slide 29: The VTALU spec
Top Level
assign es_mult = (op == 3'b101); assign start_1c = es_mult ? 1'b0 : start; assign start_mult = es_mult ? start : 1'b0; assign result_mux = es_mult ? result_mult : result_1c; assign done = es_mult ? done_mult : done_1c;
The top computes nothing: it instantiates the two blocks and decodes the opcode
es_mult = (op == mul_op). The start is routed to only one of them, and result_mux and done come out of the same side. ovf follows the same pattern right below the excerpt —assign ovf = es_mult ? 1'b0 : ovf_1c;— and result_mux only comes out through result after the +VTALU_BUG XOR
That is why the bus protocol is a single one even though inside there are two different latencies: what the testbench sees is start → done
Notes: That both blocks share A, B and clk and only split on the start is what makes the DUT have a single interface. Worth pointing out because it is the shape the vtalu_bfm of interfaces and BFM is going to have. The complete file, with both instances and their connections, is in code/vtalu_dut/vtalu.sv. Here there are only the decode and the four lines that decide. Worth pointing out why it is a decode and not a loose bit: with an op[2] the opcodes would have to sit in tidy halves of the space, and the design would lose the freedom to assign them as convenient. A decode costs one gate and does not tie the spec down. And along the way, the free opcode 3’b110 falls on the single-cycle side without anybody having to do anything. The DUT does not validate the opcode; the one that has to catch it is the verification plan.

## Slide 30: The VTALU spec
How to run it
The DUT lives in code/vtalu_dut/, in SystemVerilog
The simulator of the course is Verilator (free, no licence):
make u4/tests # one UVM example: ~1 min 30 the first time make u4/tests # the second, with ccache: ~15 seconds make # the 38 examples
The ones that use UVM compile the whole library the first time. Install ccache before starting: the course detects it on its own and does not recompile twice
Every example has its run.sh; the common flags are in code/verilator/common.sh
Notes: Here it is worth leaving the deck and running it live. The numbers on the slide are measured on a 12-core laptop. On a 2-core machine —a free Codespaces— the first one is 4 minutes; the second is still 15 seconds, because a ccache hit is copying a file and that does not depend on how many cores you have. Which means the expensive part is paid once. What has to be explained is where the difference between 1 min 30 and 15 seconds comes from, because it is not magic: Verilator compiles every simulation to a native binary, and for that it generates about 2300 C++ files —almost all of them from the UVM library—. ccache stores the result of each one; the second time it does not compile again, it copies. It is in the Dockerfile and in the devcontainer, and outside it is enough to have it installed. And the one to stress anyway: Verilator is free — the student takes it home and keeps practising without asking anybody for a licence.

## Slide 31: The VTALU spec
Looking at the real waves
The diagram on the first slide is drawn. The real one you generate yourself, and it is the tool 47 % of the work gets done with: debugging
cd code/u2/convencional VLT_TRACE=1 bash run.sh # compiles with --trace and dumps vtalu.vcd gtkwave vtalu.vcd # or surfer, or whatever viewer you use
VLT_TRACE=1 turns on two things at once: Verilator’s --trace and the top’s $dumpfile/$dumpvars, which without the flag would not compile
It costs nothing and it is free, same as the simulator. When the testbench hangs on while (done == 0), this is what is going to tell you why
Notes: It is worth opening it live once, even for thirty seconds: load op_set, start and done, and show the one-cycle pulse of the multiplication next to the level of the single-cycle ones. It is the fine print of the protocol of slide 1, but seen. And say it explicitly: whoever takes the course alone has their safety net here. When an exercise does not work out, the answer is almost always in the waves before it is in the code.

## Slide 32: The VTALU spec
Summary of the unit
The protocol is a single sentence, and it has to be respected: start at 1 and the operands stable until done goes up
The fine print that is going to hang the first testbench: done is a one-cycle pulse on the multiplication and a level on the single-cycle ones
Inside there are two blocks with different latencies —one and four cycles— and the top decodes the opcode. Outside, the bus is a single one
ovf is one more output, and it belongs to sub_op and to nobody else
rst_op does not exist for the RTL: it is a testbench convention for pulsing reset_n, and that is why it enters the coverage
The DUT does not validate the opcode: the free one raises done all the same, with the result of the previous operation. Catching it is the verification plan’s job, not the design’s
And the tool used 47 % of the time is already installed: VLT_TRACE=1 and GTKWave
Notes: Closing of the section that looks like RTL and is really about verification. The question to close with: which of these seven facts is the most expensive one to forget? The one about done, and it will show today, in the waves exercise. Worth saying why the DUT was not “cleaned up” when it was translated from VHDL: the asymmetry of the resets and the unvalidated opcode are exactly the kind of thing a testbench has to expose. A tidy DUT teaches nothing.

## Slide 33
The verification plan
The most professional deliverable of the discipline, and the cheapest
It is a table. It gets written before the testbench — if it gets written after, it describes what the testbench already does instead of what the spec asks for
It comes out of the spec you have just read, not out of the testbench that does not exist yet
And it is what gets delivered: the day 7 capstone is handed in with the plan filled, which is exactly what gets handed in on a project
Notes: This is the slide that orders the whole course, and that is why it comes before the first line of testbench. Everything that comes after —the stimulus, the scoreboard, the covergroups, the assertions— are columns of this table. It is worth saying it head on: the plan is not bureaucracy. It is the only serious answer to “are you done verifying yet?”, and it is the first thing a technical lead asks for when they ask how the block is going. The empty template is in docs/en/verification-plan.md, and it gets used twice in the course: here to read it, and on day 7 to fill it from scratch.

## Slide 34: The verification plan
The five columns
Column | The question it answers | What does not go in
Feature | which part of the spec does this row come from? | the name of a testbench file
Scenario | which concrete situation has to be provoked? | “test the ALU”
Stimulus | who provokes it: the random or a directed case? | “by hand”
Check | who says it went right? | “you look at the wave”
Measure | which bin gets filled when it happens? | “you see it in the log”
One row per scenario, not per feature: a feature with three corner cases is three rows, and they get closed one at a time
Notes: It is worth reading the right-hand column out loud: they are the five mistakes people make the first time, and all five sound reasonable when you write them. The hardest column is the measure one, because it forces you to decide beforehand what you are going to count. It is the one that on day 1 still cannot be filled —the bins do not exist until the next unit— and that is why the plan gets filled as the testbench grows.

## Slide 35: The verification plan
Two rules that come out of the columns
If the check column says “by eye”, the scenario is not verified. It is simulated, which is another thing
If the measure column is empty, nobody is going to find out that the scenario never happened. A case the random never touched and that has no bin is indistinguishable from one that happened a thousand times
And one distinction that orders the check column: the scoreboard checks what the DUT computes; the assertions check how it is talked to
Notes: The difference between verified and simulated is who finds out when it fails at three in the morning in the regression. If the check is a pair of eyes, nobody finds out: the regression passes green with the bug inside. The third bullet is a promise the course keeps on day 7: until then every check is a scoreboard check, and half the protocol goes unchecked. Worth saying now so that day 7 does not look like an add-on. A serious plan has both columns, and the VTALU table —which is seen whole in the next unit, already with the bins— has eight scoreboard rows and four assertion ones.

## Slide 36
The conventional testbench
The VTALU plan, with three columns to fill
Feature | Scenario | Stimulus | Check | Measure
ALU | the six operations |  |  | 
ALU | operands at 00 and at FF |  |  | 
reset | operate after a reset |  |  | 
mult | a mult after a single-cycle one |  |  | 
ALU | the same operation twice in a row |  |  | 
sub | subtract too much: A < B, and ovf goes up |  |  | 
Six rows that come out of the spec, and none of the right-hand columns yet. This section fills two: the stimulus provokes them and the scoreboard says whether the result was right
The third one —which bin gets filled when it happens— is the next section
The testbench has three parts because the plan has three columns to fill
Notes: The order matters and it is the one from the previous unit: the plan first, the testbench after. If you write the testbench first, you end up measuring what the testbench does instead of what the spec asks for. Worth reading the six rows one at a time and asking which one is missing. The answer that usually comes up —“test intermediate values”— is good for discussing why it is not there: 256 × 256 × 5 combinations do not get simulated, and that is where random comes in. The last one is the one that brings today’s topic: the DUT has TWO outputs, and a row of the plan that only closes by looking at both. A scoreboard that compares result and nothing else passes green with ovf stuck at zero. The table comes back twice: in functional coverage with the measure column filled in, row by row, and at the end of that whole section, with the twelve rows and the three columns. Worth announcing now so nobody reads it as decoration: it is the same table, filling up.

## Slide 37: The conventional testbench
The stimulus: a thousand operations, and the protocol by hand
repeat (1000) begin @(negedge clk); op_set = get_op(); A = get_data(); B = get_data(); start = 1'b1; case (op_set) // handle the start signal no_op: begin @(posedge clk); start = 1'b0; end rst_op: begin reset_n = 1'b0; start = 1'b0; @(negedge clk); reset_n = 1'b1; end default: begin // Wait for an EDGE with done up, not for done itself: on the // one-cycle ops done is a level still up from the previous op, // and a plain wait(done) drops this one without a sound. enviadas++; do @(negedge clk); while (done == 0); start = 1'b0; end endcase // case (op_set) end $finish;
A thousand rounds: pick the operation, pick the operands, raise start, wait for an edge with done up, lower start
The case is there because of the fine print of the spec: no_op does not raise done, rst_op pulses reset_n, and the rest wait
get_op() and get_data() bias the random towards the edges —00 and FF— to reach the cases the plan asks for. It is constrained random written by hand
enviadas gets counted here and chequeadas in the scoreboard, and a final demands they match: it is the testbench checking itself
Notice who knows about the protocol here: the tester. In interfaces and BFM that moves to the BFM and in the body of the repeat shrinks to one line
Notes: This is the “before” slide of the whole course: the stimulus and the protocol mixed in the same loop. Worth pointing at it, because the next five units are successive separations of these thirty lines. The do … while (done == 0) of the default is the one that hangs if the DUT does not answer, and it is the place the student is going to end up in the first time they break something. The safety net is VLT_TRACE=1 and the waves. And why it is not a wait(done), which is the first thing anybody writes: on the one-cycle operations done is a level, and on the negedge where the tester loads the next operation it is still up from the previous one. The wait(done) does not block, start drops at the same instant and the DUT never sees that operation. There is no error: the scoreboard does not fire, and the coverage —which samples op_set— counts it anyway. This testbench had it, and it dropped four in ten one-cycle operations with the report in green: on d1, 77 shifts checked against 130 with the fix. What catches it is the sent-versus- checked counter, and it is the cheapest silent trap to guard against. The bias of get_data() —a quarter at 00, a quarter at FF, half in the middle— is exactly what the transactions are going to write in one line with dist and :/. Worth naming it now so that the saving is visible later.

## Slide 38: The conventional testbench
The self-checking: predict and compare
// Sent by the tester, compared by the scoreboard: the final block below // demands that the two match. int enviadas, chequeadas; // Scoreboard loop: checks that everything came out right always @(posedge done) begin : scoreboard shortint predicted_result; bit predicted_ovf; #1; case (op_set) add_op: predicted_result = A + B; sub_op: predicted_result = A - B; and_op: predicted_result = A & B; xor_op: predicted_result = A ^ B; mul_op: predicted_result = A * B; endcase // case (op_set) // ovf belongs to sub and to nobody else: with 8-bit inputs and a 16-bit // output, neither the addition nor the multiplication can overflow. predicted_ovf = (op_set == sub_op) && (A < B); if ((op_set != no_op) && (op_set != rst_op)) begin chequeadas++; if (predicted_result != result || predicted_ovf != ovf) $error ("FAILED: A: %0h B: %0h op: %s result: %0h ovf: %0b", A, B, op_set.name(), result, ovf); end end : scoreboard
An always @(posedge done): every time the DUT says it finished, the scoreboard predicts the result and compares it
The #1 is not decoration: without it the signals get read at the same instant done goes up and a delta race can be swallowed
no_op and rst_op do not raise done, so this block should not run with them. The if is defensive —with no prediction for those two it would compare garbage— and inside goes chequeadas++, the other half of the counter
The covergroup —the third leg— is the section that follows
Notes: The reference model is four lines of case because the DUT is an ALU. On a real project it can be a model in C or the RTL of the previous generation, but the shape is always this one: predict with something that is not the DUT, and compare. That the scoreboard reads A, B and op_set off the wire at the moment of the result works only because the protocol forces them to stay stable. It is fragile, and in the analysis ports it will be replaced by a queue of commands the monitor sends. And the $error here is going to be a `uvm_error from reporting on: same concept, with a counter and a severity policy behind it.

## Slide 39: The conventional testbench
How do you know the scoreboard checks anything?
FAILED: A: 15 B: ce op: xor_op result: da ovf: 0
A thousand operations and not one error. Now the same testbench with the DUT broken on purpose: VTALU_BUG=1 bash run.sh flips bit 0 of the result
It fails on the first comparison. That —and not the earlier PASS— is what proves the scoreboard looks at the result
A scoreboard that never saw an error is not proven: it may have compared against itself, or compared nothing at all
make mutante does this with the three testbenches of days 1 and 2, and fails if any of them does not fail. It is the first answer to the question of the day
Notes: Run it live, it takes seconds because there is no UVM: first bash run.sh —a thousand operations, silence, and the coverage summary—, then VTALU_BUG=1 bash run.sh, which ends in the line on the slide and a $stop. What has to be said in so many words is what that line proves and what it does not. It proves the scoreboard compares the bit the bug touched. It does not prove it compares ovf: a bug that only touched ovf is another run, and that is why the plan has a row for each output. This is the short answer to the first slide of the day: the regression that said PASS and sent the bug to the fab had never seen a FAILED. It did not know whether it was checking. A PASS says nothing until you know what FAILED would have said. And it is not a day-1 trick: it is the practice that runs through the course. +BUG=1 in the day 7 capstone and +GOLDEN_BUG in the day 8 reference model are this very thing, and the exercise checkers demand it.

## Slide 40: The conventional testbench
Unit summary
The testbench has three parts because the plan has three columns to fill: stimulus, self-checking and measure. Today they are loose in one file
The stimulus biases the random towards the edges —00 and FF— because uniform randomness almost never visits them
The #1 before reading the signals is not decoration: without it you read in the very instant the DUT writes, and the result is undefined
A PASS proves nothing until you have seen the FAILED: VTALU_BUG=1 is the way to see it, and make mutante the way not to forget
And what to look at for interfaces and BFM: the tester knows the protocol. It moves start and waits for done by hand
Notes: The last bullet is the one that orders the rest of the day: this testbench works, it is proven, and it is badly divided. The tester knows how start is wiggled and the scoreboard knows when to read done: the protocol lives in two places of the same file, and the day it changes both have to be touched. That is the whole motivation for interfaces and BFM, and it is worth leaving as an open question instead of answering it here. Before that, the next section fills in the third column.

## Slide 41
Functional coverage
When are you done verifying?
Code coverage —lines, branches, toggle— the simulator gives you for free. It says which RTL got executed
Functional coverage you write yourself. It says which scenarios of the spec went through the DUT
They are not the same thing, and the first one misleads: a test that always sends add_op with A=B=8'h01 executes almost every line of the adder and verified nothing
Functional coverage is the contract between the spec and the testbench: if a case of the spec has no bin, nobody is going to find out it is missing
Notes: The question on the slide is the one a verification engineer gets asked in the tape-out meeting, and it is not answered with “I ran a lot of tests”. If somebody asks why code coverage is not enough: because it measures the DUT, not the spec. A DUT that is missing a whole feature can give 100 % of lines — the lines nobody wrote do not show up in the report.

## Slide 42: Functional coverage
From the verification plan to the covergroup
The six rows of the plan from the previous section, translated:
From the plan | How it gets measured
the six operations | coverpoint op_set with one bin per operation
operands at 00 and at FF | cross of A, B and the operation
operate after a reset | transition bin rst_op => op
a mult after a single-cycle one | transition bin
the same operation twice in a row | repetition bin [* 2]
subtract too much: A < B, and ovf goes up | coverpoint borrow with the hubo_borrow bin
The six rows stop being good intentions: each one is a line of code, and the simulator tells you which ones have not happened yet
Notes: It is worth going back to the plan of the previous section and reading it out loud before showing this table: the point is that there is not one item of the plan left untranslated. The order matters — the plan first, the covergroup after. The other way round you end up measuring what the testbench does, not what the spec asks for.

## Slide 43: Functional coverage
Anatomy: it is three steps, not one
covergroup op_cov; // 1. WHAT gets measured coverpoint op_set; endgroup op_cov oc; // 2. it gets INSTANTIATED: it is a type, like a class initial oc = new(); always @(posedge clk) oc.sample(); // 3. WHEN it gets counted
A covergroup is a type: declaring it measures nothing, it has to be new()ed
sample() is the one that counts. Without sample() the report reads 0 % and the code compiles just the same
Where to sample is a design decision. Here, the edge the DUT reads on, never the same one the tester writes on; when the TB has monitors it will be “every time the monitor sees a command”
Notes: Everybody’s first-time mistake is declaring the covergroup and forgetting the new() or the sample(). There is no warning: the report simply says 0 % and you spend half an hour looking for the bug in the bins. The third point is the one that holds for the rest of the course: the moment of the sample defines what you are measuring. Sampling on the clock counts cycles; sampling on transactions counts operations. In the analysis ports the coverage becomes a subscriber and samples when a command arrives — which is the right thing. And the edge is not a whim: sampling on the same negedge the tester writes op_set on is a race the LRM does not define —Verilator always resolves it the same way; another simulator may not—. It is the same rule as the day 7 assertions: you read on the opposite edge to the one that writes.

## Slide 44: Functional coverage
bins: the buckets that have to be filled
coverpoint op_set; // automatic bins: one per value of the enum coverpoint op_set { bins single_cycle[] = {[add_op : xor_op], rst_op, no_op}; // [] -> one per value bins multi_cycle = {mul_op}; // no [] -> a single one }
Without { }, SystemVerilog creates one bin per value. That works for an enum; for an int the tool chops the range into 64 buckets —auto_bin_max— that correspond to no row of the plan
The brackets [] hand out: one bucket per value of the range. Without them, every value falls into the same bucket
A coverpoint is covered when all of its bins have at least one hit. A bin that cannot be filled pins your number down forever
Notes: The brackets are the detail most often copied wrong, and it is worth showing it with both cases side by side: bins x[] = {[0:3]} is four buckets, and bins x = {[0:3]} is a single one that gets filled by any of the four values landing. The syntax differs by two characters and the number the tool reports changes completely. The practical consequence has to be said loudly because it is a silent trap: a bin without [] over a large range always gives 100 %. You covered one value out of a thousand and the tool tells you it is done. Nobody warns you. And the last bullet is the warning that orders what comes next: a bin that cannot be filled is not a tool problem, it is a decision somebody did not write down. The way to write it down is called ignore_bins, and it has its own slide in this section.

## Slide 45: Functional coverage
The VTALU covergroup
//op_cov: make sure every operation, and every interaction between them, is covered covergroup op_cov; coverpoint op_set { bins single_cycle[] = {[add_op : xor_op], rst_op,no_op}; bins multi_cycle = {mul_op}; // => are transitional coverage. From => To // Transition bins. Verilator 5.052 does NOT implement them yet: any form // with "=>" or "[* n]" aborts with an Internal Error. Minimal repro in // code/verilator/repro-cg-transition.sv. They stay because they are part // of the topic; when Verilator supports them, drop the ifndef, nothing else. `ifndef VERILATOR bins opn_rst[] = ([add_op:mul_op] => rst_op); bins rst_opn[] = (rst_op => [add_op:mul_op]); bins sngl_mul[] = ([add_op:xor_op],no_op => mul_op); bins mul_sngl[] = (mul_op => [add_op:xor_op], no_op); bins twoops[] = ([add_op:mul_op] [* 2]); bins manymult = (mul_op [* 3:5]); `endif } endgroup
single_cycle[] generates six bins —one per operation—, multi_cycle a single one
What is inside `ifndef VERILATOR are the transition bins, which come further on in this same section
Notes: This is the first real covergroup of the course, and it is worth reading it top to bottom answering the three questions of the previous slide: what gets measured (the coverpoints), into which buckets (the bins) and when it gets counted (the sample(), which is further down in the same file). That multi_cycle is a single bin and single_cycle[] is six is not broken symmetry: it is the verification plan. The six that are not the multiplication matter one by one; the multiplication matters as a separate case because it is the only one that takes more than one cycle. The shape of the covergroup is the table of the plan, and that is why the plan gets written first. The `ifndef VERILATOR is worth naming now and not hiding: those bins are a topic of the course, they are written, and today Verilator does not compile them. It is in docs/en/verilator.md with the version and the date. A course that covers up what its tool does not do is a course that lies.

## Slide 46: Functional coverage
ignore_bins: saying out loud what does not get covered
// Check the corners where the inputs are all 0s or all 1s all_ops : coverpoint op_set { ignore_bins null_ops = {rst_op, no_op};} a_leg: coverpoint A { bins zeros = {8'h00}; bins others= {[8'h01:8'hFE]}; bins ones = {8'hFF}; } b_leg: coverpoint B { bins zeros = {8'h00}; bins others= {[8'h01:8'hFE]}; bins ones = {8'hFF}; } // VTALU rev2: the borrow of the subtraction, the row of the plan that the // scoreboard can only close by looking at TWO outputs. Without this bin, a // subtraction that never went negative looks exactly like one that did. borrow: coverpoint ((op_set == sub_op) && (A < B)) { bins hubo_borrow = {1}; ignore_bins resto = {0}; }
all_ops ignores rst_op and no_op: it makes no sense to ask for “an addition with the operands at 0x00” when the operation is a reset
a_leg and b_leg bring 256 values down to the three buckets that matter: all zeros, the middle, all ones
An impossible bin you leave in place keeps your coverage pinned below 100 % and nobody knows why. ignore_bins turns it into a written decision
Notes: There is a relative worth naming: illegal_bins. ignore_bins takes the bin out of the count; illegal_bins takes it out of the count and also reports an error if it ever happens. It is for the cases the spec forbids — a reserved opcode, an illegal handshake. The rule of thumb: if it cannot be covered, ignore_bins; if it must not happen, illegal_bins; if it simply has not happened yet, leave it and write the test.

## Slide 47: Functional coverage
cross: the combinations, and how not to drown
op_00_FF : cross a_leg, b_leg, all_ops; // 3 x 3 x 5 = 45 bins, almost all meaningless
A cross is the cartesian product of its coverpoints: it grows fast and most of the combinations are in nobody’s spec
binsof(x) intersect {v} reads as “the bins of x that contain v”
They combine with && and ||, and what is left over gets thrown away with ignore_bins
That way the 45 bins come down to the 11 the plan actually asked for
Notes: The arithmetic in the comment is what has to be done out loud, because the number is scary and it has to be: three bins of A by three of B by five operations is 45, and out of those 45 the plan asked for eleven. The other 34 are not wrong — they are surplus, and a surplus bin is as expensive as a missing one: it pins your coverage below 100 % and nobody knows whether it is a real hole. binsof(x) intersect {v} is worth reading in plain words before writing it, because the syntax does not help: “the bins of x that contain v”. Then they combine with && and || like any condition. The scale mistake to anticipate: on a real DUT a cross of three coverpoints with automatic bins is thousands of buckets, and a regression never fills them. When somebody says “the coverage is not going up”, half the time the problem is an unfiltered cross, not a missing test. And the number to keep at hand for the “Reading the number” slide: the 45 are the LRM count, one bin per enum member. Verilator measures 54, because it hands out the automatic bins by the base type (bit [2:0], 8 values minus the 2 of ignore_bins, that is 3 x 3 x 6). The 9 extra are the 3'b110 crossed, and they are exactly the 9 that stay at zero.

## Slide 48: Functional coverage
The VTALU cross
bins mul_00 = binsof (all_ops) intersect {mul_op} && (binsof (a_leg.zeros) || binsof (b_leg.zeros)); bins mul_FF = binsof (all_ops) intersect {mul_op} && (binsof (a_leg.ones) || binsof (b_leg.ones)); bins mul_max = binsof (all_ops) intersect {mul_op} && (binsof (a_leg.ones) && binsof (b_leg.ones)); ignore_bins others_only = binsof(a_leg.others) && binsof(b_leg.others);
mul_00 reads straight through: a multiplication where A or B is 0x00. The other eight bins of the cross are these two lines with another op
mul_max is the only one with &&: it asks for both legs at 0xFF: the maximum product, FF × FF = FE01. It does not overflow — 8 bits by 8 fit in 16
Verilator 5.052 ignores binsof / intersect (%Warning-COVERIGN) and measures the whole cross: that is why the number is not a commercial tool’s
Notes: Worth reading mul_00 and mul_max in plain words, one after the other, because the difference between || and && is the one that gets copied wrong, and here both bins belong to the same operation: “a multiplication where A or B is 0x00” against “a multiplication with A and B at 0xFF”. The first is two cases, the second is a single one — the maximum product, the top corner of the input space. And here it is worth killing the misunderstanding that comes on its own, because it is expensive: FF × FF does not overflow anything. It gives FE01, which fits exactly in the 16 bits of result —8 bits by 8 never go past 16— and that is why the DUT forces ovf to 0 in every multiplication: assign ovf = es_mult ? 1'b0 : ovf_1c;. The bin is called mul_max and not mul_ovf for precisely that reason: the case is worth something for being the maximum of the input space, not for overflowing. The only operation that overflows is the subtraction, and only when A < B. The honesty of this slide is part of the course, so it is worth saying and not rushing past: the 86.8 % the example reports is not the number Questa would give. Verilator ignores the filter and measures the whole cross, and on top it adds a value the enum does not have: where the LRM counts 45, Verilator counts 54 (the 9 extra are the 3'b110 crossed, and they are the 9 that stay at zero). That is why the percentage comes out lower, and for a reason that is not the testbench’s. It is written, dated and with a version in docs/en/verilator.md. The useful question for the classroom: does that invalidate the exercise? No. What gets learned —writing the cross, filtering it, and knowing which bin belongs to which row of the plan— is identical. The only thing that cannot be done with this tool is signing off on coverage closure, and that is not the goal of the course.

## Slide 49: Functional coverage
Transition bins: when the order matters
bins opn_rst[] = ([add_op:mul_op] => rst_op); // A and then B bins sngl_mul[] = ([add_op:xor_op], no_op => mul_op); bins twoops[] = ([add_op:mul_op] [* 2]); // twice in a row bins manymult = (mul_op [* 3:5]); // between 3 and 5 times in a row
Three rows of the plan are not values, they are sequences: “after a reset”, “a mult after a single-cycle one”
Verilator 5.052 still does not compile them (Internal Error). In the code they are inside `ifndef VERILATOR: they are part of the topic and read just the same
Minimal repro in code/verilator/repro-cg-transition.sv. The day Verilator supports them, the ifndef gets deleted and nothing else
Notes: It is the only place in the course where the free tool falls short, and it is worth saying head on instead of hiding it: the concept belongs to the language, not to the simulator, and on Questa or VCS these bins run. There are two more cousins worth naming: [-> n] (goto, n times not necessarily in a row) and [= n] (non-consecutive). They are in coverage.svh of the analysis ports.

## Slide 50: Functional coverage
The knobs: when a bin counts as covered
coverpoint op_set { option.at_least = 10; // a bin only counts at 10 hits bins single[] = {[add_op:xor_op]}; } coverpoint A { option.auto_bin_max = 8; } // 8 automatic buckets, not 64
option.at_least is the one that matters most: by default it is 1, so a bin that happened once already shows up as covered. The corner case that came up once in a thousand runs is not verified, and the 100 % says it is
option.auto_bin_max bounds the automatic bins. Without { } and without this knob, an 8-bit coverpoint does not give 256 buckets: it gives 64, handed out by the tool and not by the spec
option.weight changes how much a coverpoint weighs in the total, and type_option.merge_instances adds every instance into a single number instead of reporting them separately
Verilator 5.052 honours auto_bin_max, and at_least only written in the coverpoint: in the covergroup it ignores it without warning. It is in docs/en/verilator.md
Notes: This is the slide that puts an asterisk on every percentage of the unit, and that is why it only arrives now: at_least = 1 means the tool tells you covered with a single hit. For a bin that represents a value of an enum that is perfect —either it happened or it did not—. For the bin that represents the maximum product of the multiplier, one hit is an anecdote, not a verification. The field rule, and it is worth giving because the question comes on its own: at_least high on the bins that represent a rare case, default on the ones that represent a value. Raising it for the whole covergroup is not rigour, it is a regression that never closes and a number nobody looks at. auto_bin_max is the flip side of the bracket trap, the one on the bins slide. There the problem was a surplus bin; here it is the other way round: if the coverpoint is an int and you write it no bins, the tool invents 64 ranges that do not correspond to any row of the plan. The number that comes out is real and means nothing. And the usual honesty: the four knobs are the LRM’s, not Verilator’s. What this tool does with each one is measured, dated and with a repro in code/verilator/repro-cg-options.sv. The at_least one is the worst of the four because it is silent: in the covergroup you write it, it compiles, and it does nothing.

## Slide 51: Functional coverage
Reading the number
$ make u2/convencional Coverage Summary: covergroup : 86.8% (66/76)
66 of 76 bins filled, with 1000 randomizations and 615 operations on the bus —no_op and rst_op get drawn and never sent, and the testbench prints that right before the Verilator report—. The other rows come out 0/0: --coverage-user leaves code coverage out
The 10 that are missing are a single value: all_ops.auto_5 and its nine crosses. It is 3'b110, which the enum does not have — Verilator hands out the automatic bins by the base type, bit [2:0], and not by enum member
Which means no row of the plan was left uncovered, and on Questa this gives 100 %. The number is not the goal: the question that helps is which bin is missing, and only the per-bin report says that, obj_dir/top/coverage.dat
Run → look at what is missing → write the directed test → run again. That is called coverage closure, and it is what a verification engineer spends the day on
Notes: This is where it is worth running it live and opening the coverage.dat: the student has to see that the ten zeros have the same name, and that the name is not in the operation_t. The lesson is to read the report and not the number: the number says 86.8 % and the report says “nothing is missing, the tool invented a bucket”. On a commercial tool the automatic bin of an enum is one per member (IEEE 1800, 19.5) and this gives 100 % from the start; it is noted in docs/en/verilator.md. And the punchline: the exercise of the day uses precisely 3'b110 for the shift, so the new operation fills the phantom bucket and the coverage goes from 86.8 % to 100 % — 77 out of 77, with the shift’s own bin added. The one who raises it is the same one who wrote the test, and the checker counts bins and not the percentage, because we have just seen the percentage cannot read.

## Slide 52: Functional coverage
The verification plan, whole and in one table
# | Feature | Scenario | Stimulus | Check | Measure
1 | ALU | the six operations | random | scoreboard | coverpoint op_set
2 | ALU | operands at 00 and at FF | dist biased to the edges | scoreboard | cross op_00_FF
3 | mult | maximum product: FF × FF | directed case | scoreboard, 16 bits | bin mul_max
4 | reset | operate after a reset | rst_op interleaved | scoreboard | bin rst_op => op
5 | mult | a mult after a single-cycle one | random | scoreboard | transition bin
6 | ALU | the same operation twice in a row | random | scoreboard | bin [* 2]
7 | sub | subtract too much: A < B, and ovf goes up | random | scoreboard, two outputs | bin hubo_borrow
8 | sub | A == B: the result is 0 and ovf does not go up | random | scoreboard, two outputs | bin sub_00/sub_FF
9 | ovf | ovf does not go up for any other operation | random | assertion | c_ovf
10 | protocol | the operands are not touched with start up | random | assertion | cover property
11 | protocol | done arrives, and before 5 cycles | random | assertion | cover property
12 | protocol | no_op is the only one that does not answer | random | assertion | cover property
The three right-hand columns are the three parts of the testbench of this section. What ties them together is the plan, and until now you had not seen it whole
The two subtraction rows are the ones that force the scoreboard to look at two outputs: if it only compares result, it passes green with ovf stuck at zero
The last four are checked by no scoreboard: they are ovf and protocol rules, and get checked where they happen —the assertions
The twelve rows are numbered the same as in docs/en/verification-plan.md, which also says which file each one lives in and carries the capstone template
Notes: This is the slide that answers “and what is this for?” for the rest of day 1, and it is worth saying head on why it only arrives now: the three right-hand columns are stimulus, self-checking and coverage — the three parts the previous unit showed loose. The plan is the table that makes them one thing. The row that gets the most discussion is the maximum-product one, and that is good: FF × FF is the case a short test does not fill, and that is why its stimulus column says directed case: the plan is decided before knowing how long the random will run. There you see that the plan does not only measure, it also decides which test has to be written. It is the d5c exercise, the last one of the day 5 afternoon, with this same row. The three protocol rows are worth naming and moving on: they are the half the course does not touch until day 7, and they serve to plant the idea that a scoreboard does not check everything. A serious verification plan has both columns. And what the student takes home: docs/en/verification-plan.md is the same table as an artifact, with an empty template. The day 7 capstone is handed in with the plan filled — which is exactly what gets handed in on a project.

## Slide 53: Functional coverage
Summary of the unit
Code coverage ≠ functional coverage. The first one measures which RTL got executed; the second, which scenarios of the spec happened
A covergroup is a type: it has to be instantiated with new() and somebody has to call sample(). Without that the report reads 0 % without a warning
The bins are the buckets. [] hands out one per value; without brackets, the whole range goes into a single one
ignore_bins is executable documentation: it says out loud what does not get covered and why. An impossible bin you leave in place pins your number down
A cross is the cartesian product and grows extremely fast: without bounding it, the coverage never closes
option.at_least is 1 by default: a bin that happened once already shows up as covered, and a rare case with one hit is not verified
The number is not the goal. The goal is the plan; the coverage only says how much of the plan was met
Notes: Closing of the most misunderstood concept of the course. The sentence to take home: coverage does not tell you the design is right, it tells you that you tested it. A DUT that is missing a whole feature gives 100 % of code coverage and 0 % of the functional coverage nobody wrote. And the operational mistake that repeats the most, to leave it burned in: the missing sample(). It compiles, it runs, and the report reads zero.

## Slide 54
Interfaces and BFM
First: the signals stop being loose
interface vtalu_bfm; // brings in operation_t. e.g. (no_op = 3'b000) import vtalu_pkg::*; byte unsigned A; byte unsigned B; bit clk; bit reset_n; wire [ 2:0] op; bit start; wire done; wire [15:0] result; wire ovf; operation_t op_set; assign op = op_set; // The BFM is a first step towards modularity // It takes care of driving every low-level signal // and keeps the protocol in one single place // DUT clock initial begin clk = 0; forever begin #10; clk = ~clk; end end
An interface is a bundle of signals with a name of its own. Nine wires that used to be declared in the top now live together
The clock gets generated inside: the interface is not a wire, it is a model of the bus
Connecting the DUT becomes .A(bfm.A), .clk(bfm.clk)… and a new signal gets declared once: the modules that use it see it appear without touching their ports
What is not needed here and you will see in somebody else’s RTL: the modport, which is the same interface with the directions set for one side of the wire
Notes: First step towards UVM and it does not have a single line of UVM. The immediate gain is a maintenance one and it is worth measuring: with loose signals, splitting the testbench into modules forces every one of them through every port list, and a new signal gets wired in all of them. Here it gets declared in the interface, and the only port that changes is the DUT’s. One detail of types that costs you: op is a wire [2:0] and op_set is the operation_t. The assign op = op_set is the bridge between the testbench enum and the DUT wires. It is the only place in the course where the seam between the two worlds is visible. And the modport, which does not show up in the rest of the course and does in anybody else’s RTL: it is a view of the interface with the directions declared —modport dut (input A, input B, output result)—, and the module asks for it in its port list (vtalu_bfm.dut bus). It is good for two things, and both are worth it: it lets the compiler stop the DUT if it writes a signal that was an input as far as it is concerned, and it lets whoever reads the interface know who drives what without opening the RTL. It is not here because the BFM belongs to the testbench and drives everything; at work the interface almost always comes with two or three modports and what you need to know is which one to ask for.

## Slide 55: Interfaces and BFM
Then: the protocol hides inside a task
// The protocol handling can now be changed in one single place. // Fix it here once, and the fix propagates through the rest of the code task send_op(input byte iA, input byte iB, input operation_t iop, output shortint alu_result); op_set = iop; if (iop == rst_op) begin @(posedge clk); reset_n = 1'b0; start = 1'b0; @(posedge clk); #1; reset_n = 1'b1; end else begin @(negedge clk); A = iA; B = iB; start = 1'b1; if (iop == no_op) begin @(posedge clk); #1; start = 1'b0; end else begin do @(negedge clk); while (done == 0); start = 1'b0; end end endtask : send_op
send_op(A, B, op, result) translates “do an addition” into the signal wiggling the DUT expects. That is a Bus Functional Model
Inside it is all the fine print of the spec: the reset_n pulse, the no_op that does not wait for done, and the do ... while (done == 0) of the rest
From here on nobody moves bfm.start by hand. Whoever wants an operation asks for it
Notes: The sentence that orders the section: the protocol gets written once. If tomorrow the DUT asks for two cycles of start, this task gets touched and nothing else. The #1 after the @(posedge clk) is the same precaution as the scoreboard of the conventional testbench: moving the signals one delta after the edge, not on the edge. And the hook for day 4: the driver of the put and get ports is exactly this task, but inside a class and fed by a port. The operation —hiding the wire— is the same; what changes is where the data comes from.

## Slide 56: Interfaces and BFM
The top, with the BFM in the middle
The testbench is still split into the same three pieces —tester, scoreboard and coverage—, and not one of them changed its name
What changed is how they connect to the DUT: there are no loose signals travelling any more, there is a single interface the three of them share
module top; vtalu_bfm bfm (); // Tester: generates the stimulus tester tester_i (bfm); // Coverage: provides functional coverage coverage coverage_i (bfm); // ScoreBoard: checks the results scoreboard scoreboard_i (bfm); vtalu DUT ( .A(bfm.A), .B(bfm.B), .op(bfm.op), .clk(bfm.clk), .reset_n(bfm.reset_n), .start(bfm.start), .done(bfm.done), .ovf(bfm.ovf), .result(bfm.result) ); endmodule : top
Notes: It is worth reading this top.sv next to the previous section’s, because the diff is the whole section: where there was a list of logic declared in the top and wired by hand to the DUT, now there is one line that instantiates the BFM and one that plugs it in. What has to be pointed out, because it is what repeats for the rest of the course: the DUT connects to bfm.A, bfm.B, bfm.op… The interface is not an abstract object, it is the same old wires grouped under a name. Nothing became slower or stranger — it became harder to connect wrong. And the detail that pays for itself the day the DUT grows: adding a signal to the protocol means touching the interface, and everyone who uses it sees it appear. In the previous version you had to remember to wire it in every instance.

## Slide 57: Interfaces and BFM
Scoreboard: the same check, now talking to the BFM
module scoreboard ( vtalu_bfm bfm ); import vtalu_pkg::*; always @(posedge bfm.done) begin shortint predicted_result; bit predicted_ovf; #1; case (bfm.op_set) add_op: predicted_result = bfm.A + bfm.B; sub_op: predicted_result = bfm.A - bfm.B; and_op: predicted_result = bfm.A & bfm.B; xor_op: predicted_result = bfm.A ^ bfm.B; mul_op: predicted_result = bfm.A * bfm.B; endcase // case (op_set) // ovf belongs to sub and to nobody else: with 8-bit inputs and a 16-bit // output, neither the addition nor the multiplication can overflow. predicted_ovf = (bfm.op_set == sub_op) && (bfm.A < bfm.B); if ((bfm.op_set != no_op) && (bfm.op_set != rst_op)) if (predicted_result != bfm.result || predicted_ovf != bfm.ovf) $error( "FAILED: A: %0h B: %0h op: %s result: %0h ovf: %0b", bfm.A, bfm.B, bfm.op_set.name(), bfm.result, bfm.ovf ); end endmodule : scoreboard
It is the conventional testbench’s scoreboard: it predicts and compares with the same logic
The only thing that changed is where it gets the signals from: they used to be variables of the same module, now they are bfm.A, bfm.B, bfm.op_set
And that is why it is a separate module now: it can live in its own file because it shares nothing with the tester except the interface
Notes: What has to be pointed out is what did not change. The verification logic is identical; what got modularized is the wiring. That is the whole section. The bfm. in front of every signal is the first time the student sees an interface hierarchy, and it is worth writing it on the board: top.bfm.A. In the tests that same reference is going to arrive through the config_db into a class, and there the prefix will be a handle instead of an instance name. The debt that stays open: the scoreboard still watches the signals directly. Only in the analysis ports is it going to receive transactions from a monitor and stop knowing that a clk exists.

## Slide 58: Interfaces and BFM
Tester: it asks for operations, it does not move wires
initial begin byte unsigned iA; byte unsigned iB; operation_t op_set; shortint result; bfm.reset_alu(); repeat (1000) begin : random_loop op_set = get_op(); iA = get_data(); iB = get_data(); bfm.send_op(iA, iB, op_set, result); end : random_loop $finish; end // initial begin
The tester no longer touches start or waits for done: it calls bfm.send_op(...) and forgets about the protocol
The handshake ended up written once, inside the BFM. If tomorrow the DUT asks for two cycles of start, one file gets touched
That is the definition of Bus Functional Model: the task translates “do an addition” into the signal wiggling the DUT expects
Notes: The comparison with the conventional testbench is the slide: over there the tester raised start, waited for done and lowered start, mixed in with the stimulus generation. Here it only generates stimulus. Worth counting how many places of the conventional testbench knew about the protocol —the tester and the scoreboard— and how many move start now: one, the send_op. The scoreboard still waits for done on its own; that debt gets paid by the monitor of the analysis ports. And the hook for day 4: in the put and get ports this same tester is going to be a class with a put_port, and the BFM is going to end up on the other side of a driver. The operation is the same one we did here —hiding the wire— repeated one level up.

## Slide 59: Interfaces and BFM
The protocol rule, written in the simulator’s language
// IMMEDIATE: a statement. It checks the present, where the thread goes by. assert (op_set != no_op || done == 0) else $error("no_op should not raise done"); // CONCURRENT: a declaration with a clock. It plugs itself in once and // checks EVERY edge of the simulation, on its own, forever. a_operandos_estables : assert property (@(negedge clk) start |=> $stable(A) && $stable(B));
The rule —while start is up, the operands are not touched— is already written twice: in prose in the spec, and wrapped inside send_op() here
An assertion is that same sentence a third time, but executable: it does not merely comply with the rule, it checks it
And it checks it where it happens —in the interface, on the exact edge— and not at the end, comparing results
Notes: This is a hook, not the section: the syntax must not be explained here, and least of all the |=> or the edge. The only thing that has to stick is that the protocol rule can be written in a form the simulator understands. Worth pointing out the asymmetry that opens up: the BFM complies with the protocol, and that is enough while all the stimulus goes through the BFM. As soon as a legacy module, a VIP from another team or a driver written in a hurry shows up, complying stops being the same as checking. If somebody asks why one says negedge and the other does not, the short answer is “because the BFM writes on the negedge, and that is only fully visible in the assertions”. That is the question we want to plant.

## Slide 60: Interfaces and BFM
Where each thing gets checked
The conventional testbench’s scoreboard checks the result: A op B against what the DUT returned. It is the half this course develops to the end
An assertion checks the protocol: who moves, when, and for how many cycles. It is the other half
A DUT that returns result correctly but drops done one cycle early passes every test of the next six days. Nobody is watching it
It is seen whole in the assertions section, with the same VTALU and the same run.sh
Notes: The sentence worth leaving on the board for the whole course: the scoreboard checks what the DUT computes; the assertions, how it is talked to. What is left of day 1 and the six days that follow are the first half; the second arrives at the end, and it arrives on this same example. There is no need to promise more than that. The assertions come back with the property of this slide, write it for real, and show why the edge chosen is not a detail.

## Slide 61: Interfaces and BFM
The hole the BFM leaves: the timing
// 1. Sample AT the edge. The DUT always_ff updates d_out with a // nonblocking assignment, which lands after this initial already ran: // you read the OLD value. @(posedge clk); en_el_flanco = d_out; // 2. The same edge, one delta later. The nonblocking assignment landed // already and you read the NEW value. That "#1" is visible nowhere and // changes the result. @(posedge clk); #1; un_delta_despues = d_out; // 3. The opposite edge: the trick the whole course BFM uses. It works, // but it asks whoever reads it to know why. @(negedge clk); en_el_flanco_opuesto = d_out;
The BFM wrapped the protocol. What it did not wrap is when it drives and when it samples: that is still decided task by task
Three ways of reading the same data: 0, 11 and 11. Two values, but three mechanisms, and the middle one depends on a #1 that is visible nowhere
The @(negedge clk) of our BFM is the third one. It works — and it asks whoever reads it to know why
Notes: Run this live, it takes two seconds: make u2/clocking. The three lines it prints are the whole slide. The first one is the surprising one and it is worth explaining slowly: sampling on the posedge gives the old value, because the DUT’s always_ff updates with a nonblocking assignment and that one lands after this initial already ran. It is not a Verilator bug and not an oddity: it is the LRM region order, and it is the same on Questa. The second one is the worst of the three, and it is the one to mark as a silent trap: it works, and it works by accident. The #1 does not say which problem it solves, it is not documented, and the day somebody deletes it because “it did nothing” the testbench keeps compiling and starts lying. It is the same #1 as the scoreboard of the conventional testbench, and the difference is a single one: there the slide says which race it avoids. An explained #1 is a patch that knows it is a patch; a loose #1 is the trap. And the third is ours. Worth being honest with the group: the course drives on negedge and samples on posedge because it is the trick you can understand without having seen clocking blocks, not because it is what gets written on a project.

## Slide 62: Interfaces and BFM
Why the edge alone is not enough: the regions
The regions of an edge: Preponed, Active and NBA, and the three samples that give different values

## Slide 63
An edge is not an indivisible instant: inside it there are regions, in a fixed order
The <= of the always_ff lands in NBA: whoever reads in Active reads the old value
The #1 crosses the NBA, the opposite edge crosses it with room to spare, and SVA needs neither of the two: it samples in preponed, before everything
Notes: This figure is the one to leave on screen while reading the three samples of the previous slide. Without it the explanation is “the old value”, which sounds like a quirk of the simulator; with it, it is a consequence of the order, and the order is in the LRM. The scheduler has more regions than the four in the drawing —docs/clocking-blocks.md (in Spanish) lists them all— but these are enough to explain the three cases, and adding the others changes no answer. The question worth asking the group before showing the answer: if the DUT writes in NBA and your initial wakes up in Active, which one runs first? That is where it shows on its own why sampling on the edge gives the value from before. And the hook with day 7: the amber bar on the left is the region where SVA samples. It is the same figure that explains why an assertion does not check what happened but what it saw, and why the @() you give it changes the result.

## Slide 64: Interfaces and BFM
The clocking block: the edge and the delta, declared once
interface reg_bfm (input bit clk); byte unsigned d_in, d_out; // The only two timing lines in the testbench: // input #1step samples the STABLE value right before the edge, which is // what the hardware sees. Never what the nonblocking // assignment just wrote on that same edge. // output #0 drives ON the edge, in the nonblocking region, so the DUT // does not see it until the next edge. clocking cb @(posedge clk); default input #1step output #0; output d_in; input d_out; endclocking modport tb (clocking cb); endinterface : reg_bfm
input #1step — sample the value stable just before the edge, which is the one the hardware sees. Never the one the nonblocking assignment just wrote
output #0 — drive on the edge, with the nonblocking assignments, so the DUT does not see it until the next edge
Driving becomes cb.d_in <= value; sampling, reading cb.d_out; waiting, @(cb). No #1 in any task
And the value read is the same at any point of the cycle: the race got closed by declaration, not by habit
Notes: This is the slide you have to be able to repeat in an interview, because clocking block is one of the first things people get asked and the good answer is not “it synchronizes”: it is it declares the sampling and driving instant once, in the interface, so that no task picks it again. The detail that confuses and is worth previewing: in the example you need three @(cb) to see the 11, and not two. One for the output #0 to put the data, another for the DUT to take it, and the third because the input #1step samples what is stable before the edge. The arithmetic is in plain sight in the code and does not depend on the simulator — which is exactly the difference with the #1. If somebody asks why the course does not use it from day 1: because to understand which problem it solves you have to have had the problem. Only now, with the BFM written and the three lines running, does the question make sense. Verilator supports it since 5.x and the example ends in $fatal if the sampling stops giving 11: it is the safety net that warns if a release changes the semantics.

## Slide 65: Interfaces and BFM
Are they mandatory? No — and it is worth knowing why
The question | The answer
Can a correct TB be written without clocking blocks? | Yes. With NBA in the driver and scheduler discipline, there is no race
What should a team use? | Use them on synchronous interfaces — it is what the lowRISC/OpenTitan style guide says
They are not UVM’s: they are SystemVerilog’s. UVM neither asks for them nor knows them
Dave Rich —the reference at Verification Academy— has held since 2014 that they are optional: what avoids the race is understanding the scheduler, not the clocking block
The two positions answer different questions: one is language correctness, the other is team policy. Both are right
Notes: This slide is the one that keeps the course from lying by simplifying, and it is worth spelling out: “always use clocking blocks” is a style rule, not a theorem. Whoever repeats it as if it were the latter is in for an uncomfortable argument with the first senior they run into. Dave Rich’s sentence that orders the topic —and it is worth quoting verbatim— is from 2014: “If you are already familiar with Verilog testbenches, then you probably don’t need them.” He held it in 2022 and in 2024. It does not say they are wrong: it says they are not a necessary condition. And on the other side is lowRISC, which in OpenTitan’s DV Coding Style Guide makes them mandatory for synchronous signals. They do not contradict each other: Dave answers “can I?” and lowRISC answers “what do we all do here?”. It is exactly the difference between well-used malloc/free and a style guide that mandates smart pointers — an expert being able to manage memory by hand does not make RAII useless. Where they really move the needle, and this is what to retain: reusable agents and VIP —whoever writes them is far from whoever uses them—, gate-level with SDF, and protocols where the spec defines setup/hold. There they stop being style. The long material, with the sources, is in docs/clocking-blocks.md (in Spanish).

## Slide 66: Interfaces and BFM
The price: two names for the same wire
// The two reads, at the SAME instant, on the SAME wire. por_cb = bfm.cb.d_out; crudo = bfm.d_out; $display("at the same instant, on the same wire:"); $display(" bfm.cb.d_out (what the clocking block sampled) : %0d", por_cb); $display(" bfm.d_out (the live wire) : %0d", crudo); $display(""); $display("They differ by one cycle, and no warning says so. A monitor that"); $display("reads through the clocking block and a scoreboard that reads the"); $display("raw wire do not fail every time: they fail when the data changes.");
With the signal inside a clocking block there are two ways of reading it: bfm.d_out is the live wire, bfm.cb.d_out is what got sampled #1step before the edge
On a signal that changes every cycle they differ by one cycle: the example prints 3 and 4, at the same instant and on the same wire
Nobody warns you. It compiles, it runs, and the scoreboard fails only when the data changes
The rule: if a signal went into the clocking block, the whole protocol reads it through there — and you wait on @(bfm.cb), not on @(posedge bfm.clk)
Notes: This is the flip side of the previous slide and the reason the course does not use them in its BFM: used badly they are worse than not using them, because the failure mode is intermittent and the waveform looks fine. The real mistake, the one that shows up in the forums, has two shapes and it is worth naming both. One is mixing the event: @(posedge vif.clk) and then reading vif.cb.foo. The other is mixing the access: the monitor reads vif.cb.data and the scoreboard —or an assertion, or a debug $display— reads vif.data. Both end the same way: two temporal views of the same wire, and a mismatch that shows up once every twenty runs. Worth running the example and leaving the number in plain sight: 3 and 4. Nobody argues with a 3 and a 4 on the same wire. And the moral that hooks into the silent traps appendix, where this one is written down: in verification the expensive error is not the one that breaks, it is the one that lies. A half-done clocking block lies.

## Slide 67: Interfaces and BFM
Summary of the unit
An interface is a bundle of named signals: adding a wire stops being touching six port lists
A BFM is the interface plus the protocol: send_op(A, B, op, result) translates “do an addition” into the signal wiggling
All the fine print of the spec —the reset pulse, waiting for done, the no_op that does not answer— ends up written once
From here on nobody moves bfm.start by hand. Whoever wants an operation asks for it
The tester, the scoreboard and the coverage become separate modules, each one in its file, connected by the BFM
And this does not get abandoned: the agent’s driver keeps calling this same task
The rule the BFM complies with can also be checked, with an assertion that lives in this same interface. That is the assertions section
And the clocking block closes the last hole: the edge and the delta stop being decided task by task and get declared once
Notes: This is the most important section of day 1 and the one that looks least like it. Everything that comes after —classes, factory, agents, sequences— rearranges pieces above this line. The line itself never gets touched again. The short way to say it: from here on the testbench stops talking in wires and starts talking in operations. That is the first step towards UVM, and it is already taken, without having written a single class. If the group comes from RTL, the analogy closes on its own: the BFM is to the testbench what a device driver is to the operating system.

## Slide 68
Review · Day 1
1 of 7 · The question of the day
A thousand random operations, the scoreboard reported no error and the log ends in PASS. What are you missing to say the DUT is verified?
☐ Nothing: a thousand operations without an error is a verified DUT
☐ Running more seeds until code coverage reaches 100 %
☒ Knowing what the log would have said with a bug inside: run it with the mutated DUT
☐ Replacing the scoreboard with assertions, which check the protocol on the exact edge and not at the end
Watch it fail — the PASS of a scoreboard that never saw an error says nothing: it may not have compared. VTALU_BUG=1 flips one bit of the result and the testbench has to fail; make mutante demands it for the three testbenches of days 1 and 2.

## Slide 69
Review · Day 1
2 of 7 · The ALU spec
While the VTALU is running an operation, what do start and the operands have to do?
☐ start drops right away: it is a start pulse, and the DUT already latched everything
☐ It makes no difference: the DUT registers them on the first edge
☐ The operands have to change on every cycle
☒ start at 1 and the operands still until done goes up
Stable until done — it is the DUT protocol, and it is exactly the reason the BFM exists: to wrap that rule in a single place so that no test forgets it. The first distractor describes a real protocol —pulse start, latched operands— that this DUT does not have.

## Slide 70
Review · Day 1
3 of 7 · Functional coverage
The test runs 1000 random operations and the code coverage reads 100 %. What does that tell you about the verification?
☐ That the DUT is verified and the verification plan can be closed
☐ That the testbench has no bugs
☐ That few scenarios are missing: 100 % already walked the whole design
☒ Very little: it measures the RTL that ran, not the spec
Very little — code coverage measures the DUT; functional coverage measures the spec. A feature the designer never wrote gives 100 % of lines and 0 % of what matters, and the report is not going to tell you.

## Slide 71
Review · Day 1
4 of 7 · covergroup
You declare a covergroup, you new() it, you run a thousand operations and the report reads 0 %. What is the first thing to look at?
☒ That nobody is calling sample()
☐ That the bins are badly defined and match no value at all
☐ That the DUT is not answering
☐ That ignore_bins are missing
The sample() — a covergroup does not sample itself: somebody has to call it, on the edge or when a transaction arrives. Without that call the code compiles, runs, and the report reads 0 without a single warning.

## Slide 72
Review · Day 1
5 of 7 · Interfaces and BFM
What does the testbench gain when the protocol moves into a BFM?
☒ It stops talking in signals and starts talking in operations
☐ It simulates faster: one BFM task costs the simulator less than moving wires
☐ The testbench becomes synthesizable
☐ You save having to declare a clk
It stops talking in signals — the BFM translates one operation into a handshake of signals. The tester never touches a wire again; the scoreboard and the coverage keep reading them, through the interface, until a monitor sends them transactions. It is the first step towards UVM.

## Slide 73
Review · Day 1
6 of 7 · The verification plan
In the verification plan, what goes in the Measure column?
☐ How long the scenario takes to run, so the regression can be estimated
☐ The name of the testbench file that covers that row
☒ Which bin gets filled when the scenario happens
☐ How many times the test has to be run to call it covered
Which bin gets filled — the five columns are Feature, Scenario, Stimulus, Check and Measure, and this is the one that costs the most: it forces you to decide beforehand what is going to be counted. If it is left empty, nobody is going to find out that the scenario never happened — a case the random never touched and that has no bin is indistinguishable from one that happened a thousand times.

## Slide 74
Review · Day 1
7 of 7 · clocking block
Are clocking blocks needed to write a UVM testbench without races?
☐ Yes: without a clocking block, driver and DUT always compete on the same edge
☐ Yes, and they are also part of the UVM library
☒ No: NBA in the driver plus scheduler discipline is enough
☐ No: the uvm_driver replaces them, since it already samples in the right region
They are not needed, and they are worth using anyway — they belong to SystemVerilog, not to UVM, and no uvm_driver samples for you. What avoids the race is understanding the scheduler: a driver that drives with <= against a DUT that registers with <= is already deterministic. The clocking block does not replace that understanding, it wraps it — and that is where it pays off: reusable agents, VIP, gate-level and protocols with setup/hold in the spec.

## Slide 75
Exercise · Day 1 · 1 of 2
A new operation, end to end
cd code/ejercicios/d1 && bash run.sh
The VTALU has a free opcode, 3'b110. Teach it to shift, and teach the TB that it has to verify it too
It gets touched in three places: the RTL, the stimulus with its check, and the measure — the bin that does not exist today
The run.sh fails until it prints EXERCISE OK and the report closes with 77 covered bins; the solution is right next to it
Notes: Half an hour, and it is worth leaving them alone: the statement and the README are enough. The guaranteed stumble is the width: the hardware shifts by B[2:0], not by the whole B, so with B = 8'h20 it shifts zero places and not thirty-two. The scoreboard model has to do the same or the TB they wrote themselves is going to accuse them. It is warned about in the README, and it still happens. The third step is the most skipped one and the only one that fails silently: bins single_cycle[] covers the range [add_op : xor_op], which reaches up to 3'b100. shr_op falls outside every bin, the simulation passes green and — here is the worst part — the report still says 100 %: 76 out of 76. The missing bin does not lower the percentage because it never made it into the denominator. There is the lesson that holds for the rest of the course: an opcode nobody measures is an opcode nobody verified, and the percentage is precisely the metric that cannot see it. With the solution it is 77 out of 77, starting from 86.8 % (66 out of 76). The ten that were missing were a single one: the bucket Verilator invents for 3'b110, the value the enum did not have — and the shift is precisely 3'b110, so it fills it along the way. Worth showing both numbers and not only the percentage: that is why the run.sh demands, on top of the 100 %, that single_cycle has one more bin: a half-done job reaches the 100 % too.

## Slide 76
Exercise · Day 1 · 2 of 2
The waves: when the log is not enough
cd code/ejercicios/d1b && bash run.sh
The run aborts with a single line: FAILED: A: e5 B: 0 op: mul_op result: fe01 ovf: 0. e5 * 00 is 0, not fe01. The scoreboard is right, and so is the DUT: what got it wrong is the BFM’s handshake
That is where what the log gives you ends. The run.sh leaves ondas.vcd next to it: gtkwave ondas.vcd
Stage 1: two times that only exist in the viewer, in respuesta.txt. Stage 2: the line of the BFM that explains them
It is the only exercise of the course that is not solved by reading the log
Notes: Half an hour, and it is the exercise that justifies the debug appendix: there it says that the waves are the tool 47 % of the work gets done with, and up to here the course had not made them use one even once. The bug is a protocol one and it is the same one that comes back in the capstone: send_op counts edges instead of waiting for the handshake. For single-cycle operations it makes no difference; the multiplication takes four, so send_op returns too early, the next stimulus overwrites A and B, and when done finally goes up the scoreboard compares the new operands against the old result. That is why the two times stage 1 asks for are not bureaucracy: the second is the done of the first multiplication, and whoever looks for it in the viewer sees that A and B have already changed. That is the answer to the why, and there is no way to read it in the log. The question to throw at the group when they finish: if the multiplier went from four edges to five, which of the two versions of send_op finds out? Neither counts right; only the one that waits for done keeps working. It is literally the clue of the APB wait state of day 7. And this is the 47 % from the trends slide, seen up close: the log says failed and for the why you have to go somewhere else. Today that somewhere else is the waves; on day 3, in reporting, it is the log that learns to say it.

## Slide 77
Six out of seven, again
Closing the day
The regression that sent the bug to the fab said PASS. Today you have three ways of knowing whether that PASS was worth anything, and all three are columns of one table
What had to be tested? A plan: one row per scenario, written before the testbench, from the spec
Who said it was right? A scoreboard that predicts and compares — and that you watched fail with a bug inside
How much of the plan passed? A covergroup with one bin per row, and the per-bin report, not the percentage
The tester already asks for operations instead of moving wires: that was the BFM. What you still cannot do is change the stimulus without editing the file. Tomorrow is that
Notes: Thirty seconds, and they are the ones that close the arc of the day: the first slide asked a question and this one answers it with what the student wrote, not with theory. If the group is tired, put the 14 % slide back up for a second before this one: the question was “how do you know you verified?”, and the short answer is “I have the plan, I watched it fail and I know which bin is missing”. What not to over-promise: this does not prevent the respin. What it prevents is sending to the fab a PASS nobody knew the meaning of. The last bullet is the one day 2 opens with “Yesterday we left…”: a tester that only multiplies is copying the file and deleting five lines. That is the problem classes solve, and it is worth leaving as a problem and not as a promise.

## Slide 78
Yesterday we left…
Where the testbench stands
A testbench that works: it sends stimulus, checks the result and measures functional coverage. The verification plan says which row each thing closes
The BFM took the signals inside an interface, and the testbench went on to call send_op() instead of moving wires
And one problem was left open: changing the stimulus means editing the file. A tester that only multiplies is copying the one that is there and deleting five lines
Notes: Thirty seconds, and they are not filler: day 2 is the most abstract of the course and it starts without touching the VTALU all morning. The student has to walk in knowing this is the answer to something that already happened to them yesterday. The bullet to underline is the third one, because it is the problem the whole unit solves. If the group comes from a previous class, it is enough to ask “how did you make a tester that only multiplies yesterday?” and wait for the answer —copy and delete— before moving on to the agenda. If it is taught on video, this is the slide that replaces the week of distance between one chapter and the next.

## Slide 79
Agenda
Day 2 · ≈ 4 h · unit 3 · the OOP UVM takes for granted
Classes and extensions
Polymorphism
Static variables and methods
Parameterized classes
The factory pattern
A testbench without a single module
By the end of the day you can:
Extend a class and change its behaviour without copying it, and say what super does
Change the class a testbench uses without touching the code that uses it, with a factory
Write the day 1 testbench without a single module
Notes: Day 2 is the only one that does not touch the VTALU all morning, and that is why it is worth putting the three verbs up front: they are the answer to “what is this for?”, which is the question that shows up half an hour in. The third one is the one that closes the day and the one practised in the exercise. The first two are rows 6 and 7 of the closing self-assessment.

## Slide 80
Classes and extensions
Why OOP in a testbench?
The conventional testbench is a module: it gets elaborated once, it exists from time 0 until the $finish, and it is always the same one
A stimulus looks nothing like that: it shows up, it travels through the testbench, it gets compared and it gets thrown away. That is not a module, it is an object
Modules = structure, they get elaborated. Classes = data and behaviour, they get created and destroyed while the simulation runs
And it is not optional: UVM is a class library. uvm_test, uvm_component, uvm_object. Without this, the rest of the course cannot be read
Notes: Here is the real wall of the course, and it is not UVM: it is OOP. Whoever arrives from RTL has never written a class, and from the tests on everything is classes. If the group comes from software, this unit goes fast and you gain time for day 3. If it comes from RTL, it is the unit where you spend whatever time is left over, even if you have to take it from somewhere else. The question that orders everything: does this exist all the time or does it show up and leave? The first is a module; the second, an object.

## Slide 81: Classes and extensions
What a struct cannot do
typedef struct { int length; int width; } rectangle_struct; typedef struct {int side;} square_struct; module top_struct; rectangle_struct rectangle_s; square_struct square_s; initial begin rectangle_s.length = 50; rectangle_s.width = 20; $display("rectangle area: %0d", rectangle_s.length * rectangle_s.width); square_s.side = 50; $display("square area: %0d", square_s.side ** 2); end endmodule
The struct holds data and nothing else: the area calculation has to be written outside, and again in every place where it is needed
square_struct has no relationship at all with rectangle_struct, even though a square is a particular case of a rectangle
It does not randomize itself, it does not compare itself, it does not print itself
Notes: It is worth starting by asking what is wrong with the struct, because the spontaneous answer is “nothing” — and they are right: for holding three fields it works perfectly. The course is not here to say the struct is wrong, it is here to say where it falls short. The three bullets are three different things and it is worth separating them. The first one is cohesion: the data is here and the operation on the data is in another file, so nothing forces them to agree. The second is inheritance: a square is a rectangle and the language has no way of saying so, so it gets copied and pasted. The third is the one you pay for on day 5: a command_s does not know how to randomize itself or compare itself against itself, and all of that has to be written outside, once for every place that uses it. The honest punchline, so that nobody leaves with a religious idea: the command_s of the conventional testbench is a struct, it works, and it was fine while the testbench was a module. What changes is the scale.

## Slide 82: Classes and extensions
The first class: data, methods and constructor
class rectangle; int length; int width; function new(int l, int w); length = l; width = w; endfunction function int area; return length * width; endfunction endclass : rectangle module top_rectangle; rectangle rectangle_h; initial begin rectangle_h = new(.l(50), .w(20)); $display("rectangle area: %0d", rectangle_h.area()); end endmodule : top_rectangle
The class puts the data (length, width) together with what gets done with it (area()). The area gets computed in a single place
new() is the constructor: it runs once, when the object gets created
.l(50) is argument passing by name. UVM uses it all the time
Notes: The comparison with the previous slide is the whole class: the same two fields, plus a function that used to live loose. Worth pointing at area() and saying that that is the entire difference — the data and what gets done with the data travel together. new() is worth presenting without mystery: it is an ordinary function, with a reserved name, that the simulator calls on its own when the object gets created. It returns the handle. It does nothing magic and there is no destructor on the other side. Passing by name looks cosmetic and it is not: when the constructor has five arguments —and uvm_component’s has two that are always the same— .l(50) is what makes the call readable without going to look up the signature. The whole of code/ in the course is written that way. And the question to leave hanging, the one the next slide answers: if I declare rectangle r; and I never call new(), how many objects are there?

## Slide 83: Classes and extensions
A handle and an object are not the same thing
rectangle rectangle_h; // 1. a HANDLE. No object yet: it is null rectangle_h = new(.l(50), .w(20)); // 2. new() creates the OBJECT and returns its handle
Declaring a handle creates nothing. Until the new() it is null, and using it there blows up at simulation time, not at compile time
The handle looks like a pointer, but it takes no arithmetic: there is no h + 1
The memory of a struct the simulator reserves the moment it sees it; that of an object, only at the new()
And there is no free(): when no handle is left pointing at it, the object gets collected on its own
Notes: The null pointer is THE mistake of the first week, and Verilator’s message does not help: it tells you that you dereferenced null, not where the new() was missing. It is worth writing the two lines on the board and asking how many objects there are after each one. The answer is zero and one. This comes back twice more in the course: in the class hierarchies, when obj1_h = obj2_h copies the handle and not the object; and in the tests, when the virtual interface that was not read from the config_db is left at null.

## Slide 84: Classes and extensions
Extending: extends and super
class rectangle; // Data members int length; int width; function new(int l, int w); length = l; width = w; endfunction function int area(); return length * width; endfunction endclass // Extending classes! class square extends rectangle; // Override Constructor function new(int side); // super: the call to the parent method super.new(.l(side), .w(side)); endfunction endclass
square extends rectangle inherits length, width and area() without copying a single line. A square is a rectangle with a constraint, and the code says it that way
The child’s constructor calls super.new(): the top part of the object also has to be built, and it goes first
Extending is not copying: if tomorrow area() changes, it changes for both
Notes: The constructor order is the first thing to nail down, because it is mandatory and it fails badly: super.new() goes before anything else of the child. The reason is physical — the object is a single one, and the part the base class contributes has to be built before touching anything. If you forget it, SystemVerilog calls it on its own when the base constructor takes no arguments, and it does not compile when it does take them. On day 3, uvm_component’s takes them. The last bullet is the whole argument of the unit and it is worth saying with an example: if area() changes tomorrow, in the struct version you have to remember both places; here it changes in one and the other finds out on its own. That “finds out on its own” is what inheritance buys you, and it is the same promise the env makes to the tests on day 3. And the warning about where this is heading, so that the word does not turn up cold on the next slide: inheriting lets the child use what belongs to the parent. What still cannot be done is for the parent to call the child’s version — that is polymorphism, and it is the section that follows.

## Slide 85: Classes and extensions
Where all of this comes back
What you have just seen | What it is called in UVM
class with data and methods | uvm_object — the transactions of day 5
class that also lives in the TB tree | uvm_component — driver, monitor, scoreboard
new() | the constructor, with name (and parent if it is a component)
extends | every test, every tester, every agent of the course
super.new() | the mandatory first line of every UVM constructor
One piece is missing: storing a square object in a rectangle variable. That is the unit that follows
Notes: Close with the table and not with the example: the student has to leave knowing that this was not a programming detour, it was the vocabulary of the rest of the course. The last bullet leaves the door open to polymorphism, which is the only thing missing before a factory can be read. And one single thing more before moving on: declaring a handle creates nothing. Until the new() it is null, and using it there is the mistake that repeats the most in the whole week. It comes back three times —here, in the tests with the virtual interface that was not read from the config_db, and in the hierarchies when obj1_h = obj2_h copies the handle and not the object— so it is worth naming it all three.

## Slide 86
Polymorphism
A trago variable, a fernet object: which servir() runs?
trago, fernet and mojito: which servir() lives in which class

## Slide 87
A fernet is a trago, so storing it in a trago variable compiles and is legal
The question is the other one: when you call the method through that variable, does SystemVerilog look at the type of the variable or at the type of the object?
The default answer is the one you do not want, and the word that changes it is a single one
Notes: It is the concept that holds up everything that comes: the factory, the overrides, the transactions. Whoever gets lost here loses the rest of the course, so it is not worth moving on until everybody sees why the variable can be of the base class. It is worth taking a vote before showing the code: “what does it print?”. Half the room says “Fernet”, and seeing that they are wrong is what fixes the concept. And warn about it before they ask: in SystemVerilog virtual is overloaded — virtual method, virtual class and virtual interface are three different things. Here it is the first one.

## Slide 88: Polymorphism
The three classes: a trago that does not know how to serve itself
class trago; int hielos = -1; function new(int a); hielos = a; endfunction : new function void servir(); $fatal(1, "A generic trago cannot be served: order a real one."); endfunction : servir endclass : trago class fernet extends trago; function new(int hielos); super.new(hielos); endfunction : new function void servir(); $display("Fernet: 70/30, and the coke last"); endfunction : servir endclass : fernet
trago defines servir() with a $fatal: the base class does not know what it gets served with, and it says so loudly
fernet and mojito extend trago and redefine servir(), each one with its own
mojito —which does not fit on the screen— is the same as fernet, with another $display
Notes: The $fatal in the base class is a pattern you see a lot and that in this same section we are going to replace with something better: if the method cannot be implemented here, the right thing is not to explode in simulation, it is not to let it compile. That the three classes have a method with the same name and the same signature is what makes everything that follows possible. Now it remains to decide which one runs, and that is not yet said anywhere in the code. The whole file is in code/u3/polimorfismo/01-sin-virtual/not_virtual.sv.

## Slide 89: Polymorphism
Without virtual the variable rules, and that breaks
fernet_h = new(15); fernet_h.servir(); $display("The fernet has %0d ice cubes", fernet_h.hielos); mojito_h = new(1); mojito_h.servir(); $display("The mojito has %0d ice cubes", mojito_h.hielos); // The variable is trago, the object is fernet. trago_h = fernet_h; trago_h.servir(); // ** Fatal: A generic trago cannot be served $display("The trago has %0d ice cubes", trago_h.hielos); trago_h = mojito_h; trago_h.servir(); $display("The trago has %0d ice cubes", trago_h.hielos);
The first two calls work: the variable fernet_h is of type fernet and so is the object
The third one explodes. trago_h points at a fernet, but since the method is not virtual, SystemVerilog resolves at compile time by the type of the variable, and calls trago’s servir()
It is called static binding: the decision of which code to run is already taken before the object exists
Notes: This is worth running: bash code/u3/polimorfismo/01-sin-virtual/run.sh. The example ends in $fatal on purpose, and the run.sh gives PASS precisely when that message shows up. The question that always comes: “and why does hielos come out right?”. Because fields are never virtual: the variable sees the fields of its own type, and hielos is in trago. Methods are the only thing that can be resolved by object, and only if you ask for it.

## Slide 90: Polymorphism
Virtual methods: one word, and now the object rules
virtual function void servir(); $fatal(1, "A generic trago cannot be served: order a real one."); endfunction : servir
It is the only difference between 01-sin-virtual and 02-virtual: the keyword virtual on the method of the base class
With that the call gets resolved at simulation time, looking at the object inside the variable — dynamic binding
trago_h.servir() now serves a fernet or a mojito, without whoever wrote that line knowing which one they are going to get
That is the whole idea: whoever uses the object stops being the one who picks the type
Notes: Worth running the two examples one after the other and showing the diff: one word. A detail that always gets asked: fernet and mojito do not write virtual on their servir(), and they are virtual all the same. Once the method is virtual in the base, it is virtual for all of its descendants. Writing it anyway does no harm and plenty of people do it out of tidiness. The rule of thumb for the rest of the course: in verification, every method you might want to redefine goes virtual. UVM does it that way — build_phase, run_phase, do_copy, do_compare are all virtual, and that is why the override of the env works. The cost exists and it is real —a method table and an indirect jump— but in a testbench you are never going to measure it. In synthesizable RTL there are no classes, so the discussion does not apply.

## Slide 91: Polymorphism
Abstract classes: moving the error to compile time
The $fatal of trago finds out late: it compiles, it runs, and it explodes in the middle of the simulation. In an overnight regression that is a lost run
SystemVerilog allows declaring an abstract class —virtual class—: it only serves as a base, it cannot be instantiated
Inside it can declare pure virtual methods: methods with no body
Extending the class forces you to redefine them. If not, it is a compile error
The error did not go away: it moved to a moment where it comes out cheap
Notes: This is the slide to leave clear, because the criterion repeats through the whole course: the sooner it fails, the better. Compile time better than simulation, simulation better than silicon. In verification a compile error is good news: the overnight regression does not get lost, and whoever broke something finds out in a minute. Where it is going to show up again: uvm_object and uvm_component are declared virtual class in the library, so they are abstract by right. What `uvm_component_utils does not do is force you to implement anything: the other way round, it provides get_type_name() and the registry’s type_id. The real pure virtual in UVM is uvm_subscriber::write(), which you are going to have to write no matter what on day 4. And in the day 3 exercise, the virtual class base_tester.

## Slide 92: Polymorphism
pure virtual: the same example, with no $fatal possible
// Abstract class: it only works as a base, it cannot be instantiated. virtual class trago; int hielos = -1; function new(int a); hielos = a; endfunction : new // pure virtual: no body. Extending it forces you to redefine it. pure virtual function void servir(); endclass : trago
virtual class trago no longer has a servir() that explodes: it has no body, and that is why there is nothing that can run wrong
The commented-out line of the top —trago_h = new(3)— does not compile: an abstract class does not get instantiated
If you delete mojito’s override, the compiler says “Class ‘mojito’ extends ‘trago’ but is missing implementation for ‘servir’” and that is the end of it
Notes: The point is not the $fatal, it is when you find out: without an abstract class it explodes in the middle of the simulation, with pure virtual it does not compile. Worth doing live: comment out mojito’s servir() and compile. The compiler message is the one that teaches. And the hook forward: the factory uses this to create, and the env for the overrides. What today is a fernet and a mojito, tomorrow is going to be a base_tester and the testers that extend it — same mechanics, another vocabulary.

## Slide 93: Polymorphism
Summary of the unit
Without virtual the variable rules, and it is decided at compile time. With virtual the object rules, and it gets resolved during simulation. One word, and it changes everything
The underlying idea, the one that comes back in every section that follows: whoever uses the object stops being the one who picks the type
In SystemVerilog virtual is overloaded: virtual method, virtual class and virtual interface are three different things — and in UVM you are going to write all three
Notes: It is the unit that unlocks the next half of the course, and it is worth saying so: without polymorphism there is no factory, there is no uvm_component that can serve as a base, and there is no override. Everything else is plumbing. Forgetting virtual is also the trap of the day 2 exercise —get_op() is declared without virtual on purpose—, so if somebody asks about it here, do not give it away: it is understood much better by suffering it.

## Slide 94
Static variables
The global variable you can actually defend
In a testbench there is always something there is only one of: the error counter, the list of in-flight transactions, the handle to the configuration
The easy answer is a global variable, and it is the one nobody can debug afterwards: you do not know who wrote it, or from where, or when
static is the same idea, but with a last name attached. The variable lives in the class, not in the object, and to touch it you have to name the class: bandeja_de_fernet::vasos
That :: is the whole argument. The day the value looks odd, a grep tells you exactly who put it there
And it is not a loose OOP topic: the factory and the uvm_config_db are the two most important static variables of a UVM testbench
Notes: The question that orders the unit: what is there only one of in a testbench? The factory, the configuration database, the error counter. All of that in UVM is static, and that is why you write uvm_config_db#(T)::set(...) with a double colon and without instantiating anything. And the second half, which is the one you take to work: static solves the “where it lives”, not the “who touches it”. That one is solved by protected plus access methods, which is the third slide. A public static is a global variable with a longer prefix.

## Slide 95: Static variables
bandeja_de_fernet has no methods and no constructor: it is a class that exists only to be the place where the queue lives
Nobody instantiates it. It gets named with the :: operator, which tells the compiler “look this variable up in the namespace of that class”
And there is the advantage over the global: bandeja_de_fernet::vasos says where it is declared. A loose vasos does not
class bandeja_de_fernet; // Static queue static fernet vasos[$]; endclass : bandeja_de_fernet module top; initial begin fernet fernet_h; fernet_h = new(2, "the one at table 7"); // :: operator //---------------- // The variable in the bandeja_de_fernet class is reached by // naming the class and putting the :: operator before the name // That tells the compiler we want a static variable inside // the namespace of the class bandeja_de_fernet::vasos.push_back(fernet_h); fernet_h = new(3, "the one at table 4"); bandeja_de_fernet::vasos.push_back(fernet_h); fernet_h = new(15, "the one at the bar"); // class::static_variable. You know right away where it is declared bandeja_de_fernet::vasos.push_back(fernet_h); $display("Fernets on the tray:"); foreach (bandeja_de_fernet::vasos[i]) $display(bandeja_de_fernet::vasos[i].get_name()); end endmodule : top
Notes: Put plainly: static is the global variable you can actually defend in a code review. It lives in the class, not in the object. The second slide shows why it has to be encapsulated with static methods: if you leave it public, the day you swap the queue for another structure you have to touch the whole testbench.

## Slide 96: Static variables
There is a single copy in memory, no matter how many objects get instantiated
And it exists even if none gets instantiated: the static does not wait for the new()
class pepe; static int cant; int val = -1; function new(int a); // Static Variable cant++; val = a; endfunction : new endclass : pepe //---------------------------------------- module top_pepes; initial begin pepe pepe1_h, pepe2_h; pepe1_h = new(10); pepe2_h = new(254654); $display("PEPE1 VAL = %0d", pepe1_h.val); $display("PEPE2 VAL = %0d", pepe2_h.val); // There is only one copy of a static variable in memory, // no matter how many instances of the class exist $display("NUMBER OF PEPES = %0d", pepe::cant); end endmodule : top_pepes
And what about encapsulation?
Notes: pepe::cant counts how many objects got created, and the detail to point out is that the counter exists even if there is not one object. A static does not wait for the new(): it is there from the moment the simulation starts. That is why it works for counting instances, and that is why it cannot be initialized with anything that depends on an object. A good question to throw out: if cant gets incremented in the constructor, what happens if somebody extends pepe and forgets the super.new()? It does not count. It is the same topic as classes and extensions seen from another side. The question on the slide is on purpose: cant is public, and anybody in the testbench can write it. Leaving that discomfort hanging in the air for a while is what makes the next slide make sense.

## Slide 97: Static variables
Static methods
In the two previous examples the queue was out in the open, so the day it gets swapped for another structure you have to go and fix the whole testbench
The version that survives a code review is two words: the variable protected, and static access methods that are the only door
It is the same thing UVM does with the factory: nobody touches the type dictionary, you ask it with type_id::create()
class bandeja_de_fernet; protected static fernet vasos[$]; static function void bandeja_fernet(fernet l); vasos.push_back(l); endfunction : bandeja_fernet static function void lista_fernets(); $display("Fernets on the tray:"); foreach (vasos[i]) $display(vasos[i].get_name()); endfunction : lista_fernets endclass : bandeja_de_fernet module top; initial begin fernet fernet_h; fernet_h = new(2, "the one at table 7"); bandeja_de_fernet::bandeja_fernet(fernet_h); fernet_h = new(3, "the one at table 4"); bandeja_de_fernet::bandeja_fernet(fernet_h); fernet_h = new(15, "the one at the bar"); bandeja_de_fernet::bandeja_fernet(fernet_h); bandeja_de_fernet::lista_fernets(); end endmodule : top
Notes: The difference between the two versions is two words —protected in front of the queue and static function on the accessors— and it changes who can break what. In the first one, any line of the testbench can push_back onto the queue; in this one, only bandeja_fernet(). The argument is not purism: it is that now vasos can be swapped for an associative array, for a uvm_tlm_fifo or for whatever, without going out to fix the whole testbench. Encapsulating is being able to change your mind later. A syntax detail that confuses: a static method cannot touch instance variables, only static ones. It makes sense —it gets called without an object, so there is no this—, but the simulator’s error message does not put it that way. And the hook: UVM’s type_id::create(), which they are going to write a hundred times from the env on, is exactly this — a static access method to a static structure.

## Slide 98: Static variables
Summary of the unit
A single copy no matter how many objects you instantiate, it exists even if you instantiate none, and to touch it you have to name the class with ::
That :: is the whole argument: the day the value looks odd, a grep tells you who put it there. But static solves where it lives, not who touches it — that one is protected plus static access methods
Where it comes back: uvm_config_db#(T)::set(...) and type_id::create(), the two most important static variables of a UVM testbench
Notes: The hook worth leaving served: uvm_config_db#(T)::set(...) gets written with a double colon and without instantiating anything, and now they know why. Same for type_id::create(), which they are going to write a hundred times from the env on — it is exactly a static access method to a static structure. The question that orders the unit and works as a review: what is there only one of in a testbench? The factory, the configuration database, the error counter. All of that is static, and not by accident.

## Slide 99
Parameterized classes
It is not a class: it is a mould
The bandeja_de_fernet of the previous section works for fernets. For mojitos you have to write another one just like it, with one word changed
You already solved that in RTL and you do not call it OOP: a FIFO does not get copied for every data width, it gets parameterized. #(.awidth(8), .dwidth(16))
A parameterized class is the same thing, with types instead of numbers: bandeja #(fernet) and bandeja #(mojito)
And there is a consequence that surprises: every different #(...) is a different class, generated at compile time. They share nothing, not even the static
Why it matters: every #(...) you see in the rest of the course is this. uvm_analysis_port #(T), uvm_subscriber #(T), uvm_sequence #(T)
Notes: Starting from Verilog’s parameter is deliberate: the RTL student already knows how to parameterize, only with widths. Here the parameter is a type, and the rest is the same. What has to be left crystal clear before moving on is the third bullet, because it is question 6 of the review and because it is the base of all of UVM: bandeja#(fernet) and bandeja#(mojito) are not the same class with a different field. SystemVerilog generates a whole class for every combination of parameters, at compile time. That is why each one has its own static queue. The short way of saying it: the parameterized class is not a class, it is the recipe for manufacturing classes. The class appears when you write the #(...). And a limit worth naming now so that it does not surprise them: since it gets resolved at compile time, the type has to be known there. You cannot pick the parameter at runtime. Picking at runtime is what the factory solves, which is the unit that follows.

## Slide 100: Parameterized classes
Before the new syntax, the parameter you already know: a RAM that does not get copied for every width, it gets instantiated with #(.awidth(8), .dwidth(16))
Every instantiation with different parameters produces different hardware, and nobody argues about it
Parameterized class definitions are that same thing on the software side, with one difference: the parameter can be a type
module RAM #( awidth, dwidth ) ( input wire [awidth-1:0] address, inout wire [dwidth-1:0] data, input we ); initial $display("awidth: %0d dwidth %0d", awidth, dwidth); // code to implement RAM //... endmodule // RAM module top; wire [ 7:0] address; wire [15:0] data; wire write_enable; RAM #( .awidth(8), .dwidth(16) ) my_ram ( address, data, write_enable ); endmodule // top
Notes: It is worth saying what we are going to use them for, otherwise it looks like a loose OOP topic: uvm_analysis_port#(T), uvm_subscriber#(T), uvm_tlm_fifo#(T). Every #(...) that shows up in the rest of the course is this.

## Slide 101: Parameterized classes
Version with static methods: the tray does not get instantiated, you ask it with ::
The queue is static and even so there are two: bandeja#(fernet) and bandeja#(mojito) are two different classes, each one with its own
// Parameterized class // the T (type) parameter is what says which // kind of queue this is. class bandeja #( type T ); protected static T vasos[$]; static function void bandeja_trago(T l); vasos.push_back(l); endfunction : bandeja_trago static function void lista_tragos(); $display("Drinks on the tray:"); foreach (vasos[i]) $display(vasos[i].get_name()); endfunction : lista_tragos endclass : bandeja module top; initial begin fernet fernet_h; mojito mojito_h; fernet_h = new(15, "the one at the bar"); bandeja#(fernet)::bandeja_trago(fernet_h); fernet_h = new(15, "the one at table 4"); bandeja#(fernet)::bandeja_trago(fernet_h); mojito_h = new(1, "the one at table 7"); bandeja#(mojito)::bandeja_trago(mojito_h); mojito_h = new(1, "the one at the counter"); bandeja#(mojito)::bandeja_trago(mojito_h); $display("-- Fernets --"); bandeja#(fernet)::lista_tragos(); $display("-- Mojitos --"); bandeja#(mojito)::lista_tragos(); end endmodule : top
Notes: This is the slide where the mould thing gets demonstrated, and it is worth doing it by running the example: two fernets and two mojitos go in, and each lista_tragos() prints only its own. The queue is static and even so there are two. The question for the board: how many queues are there in memory? Two. And how many would there be with three drinks? Three. Every bandeja#(X) the compiler sees in the code generates its class, with its own static. The ones nobody uses do not exist. A detail that always gets asked: T is not declared anywhere as “trago or derivatives”. SystemVerilog has no such constraint — the check is by use. If you put in a type that has no get_name(), the error shows up when compiling the specialization, not when declaring the class, and the message points inside bandeja. It is confusing the first time.

## Slide 102: Parameterized classes
Variables with parameters
Here the tray gets instantiated like any object and you have to have the handle to use it — it stops being visible from the whole testbench
It does exactly the same thing as the previous version. What changes is the scope, and that is the decision: static when there really is only one, instantiated when there can be more than one
module top; // Since bandeja is not static, it has to be instantiated // the parameter is a variable type // Using a type that does not have the get_name() // method is a syntax error fernet fernet_h; mojito mojito_h; bandeja #(fernet) bandeja_de_fernet; bandeja #(mojito) bandeja_de_mojito; initial begin bandeja_de_fernet = new(); fernet_h = new(15, "the one at the bar"); bandeja_de_fernet.bandeja_trago(fernet_h); fernet_h = new(15, "the one at table 4"); bandeja_de_fernet.bandeja_trago(fernet_h); bandeja_de_mojito = new(); mojito_h = new(1, "the one at table 7"); bandeja_de_mojito.bandeja_trago(mojito_h); mojito_h = new(1, "the one on the sidewalk"); bandeja_de_mojito.bandeja_trago(mojito_h); $display("-- Fernets --"); bandeja_de_fernet.lista_tragos(); $display("-- Mojitos --"); bandeja_de_mojito.lista_tragos(); end endmodule : top
Notes: The two versions do exactly the same thing and the difference is one of design, not of syntax: in the previous one the tray is global —anybody in the testbench sees it—; in this one you have to have the handle to be able to use it. The rule you take to work: static when there really is only one in the whole testbench, instantiated when there can be more than one. And when in doubt, instantiated: it is easier to add a second object than to take the static off something half the testbench already uses. With that in hand, place UVM: the uvm_config_db is static because there is only one. A uvm_analysis_port#(command_transaction) is instantiated because each monitor has its own. The student already has the criterion to read both.

## Slide 103: Parameterized classes
Summary of the unit
A parameterized class is not a class: it is the recipe. And every different #(...) is a different class, which shares nothing with the others — not even the static
The limit: it gets resolved at compile time, so the type has to be known there. Picking at runtime is the section that follows
Where it comes back: uvm_analysis_port #(T), uvm_subscriber #(T), uvm_sequence #(T) — every #(...) in the rest of the course is this
Notes: The bullet about the different classes is the one to leave nailed down, because it is the review question and because it is the base of all of UVM. bandeja#(fernet) and bandeja#(mojito) are not the same class with a different field: they are two whole classes, each one with its own static. And the last bullet places the section: the uvm_config_db is static because there is only one; a uvm_analysis_port#(command_transaction) is instantiated because each monitor has its own. With that they can already read both.

## Slide 104
The factory pattern
Who decides the type?
Every new() you write is a hardcoded decision: that line is always going to build that class, and to change it you have to edit it and recompile
In a testbench that does not scale. You want the same env sending additions today and multiplications tomorrow, picked from the command line
The parameterized classes of the previous unit are not enough either: the #(...) gets resolved at compile time, and here the decision has to happen at runtime
The factory is the answer: instead of building it yourself, you ask for the object from somebody who knows which type to hand over
It is the most visible pattern of UVM, and with it you understand type_id::create() and set_type_override(), which are going to be in every file of the rest of the course
Notes: The sentence that orders the unit: whoever uses the object stops being the one who picks the type. Everything else is implementation detail. It is worth saying up front where this ends, because otherwise it looks like a programming detour: the +UVM_TESTNAME=add_test of the tests, tomorrow, is going to be a factory — UVM reads a string from the command line and builds the class that corresponds. Here you see the mechanism from the inside. And for whoever comes from software: yes, it is the GoF Factory Method, and we invented nothing. The Python version that closes the section is there precisely for that.

## Slide 105: The factory pattern
A design pattern, not a language feature: a class whose only job is to build objects for you
You ask it for an object by describing which one you want —a string, an enum— and it hands it back already built, of whichever subtype corresponds
Before the solution, the problem. Look at what happens when the new() is written in the place where the object gets used:
// ILLUSTRATION -- not compiled. In the previous example, new() gets called every // time an object is needed: building a new set of drinks means editing the source. bandeja_de_fernet = new(); fernet_h = new(15, "the one at the bar"); bandeja_de_fernet.bandeja_trago(fernet_h); fernet_h = new(15, "the one at table 4"); bandeja_de_fernet.bandeja_trago(fernet_h); bandeja_de_mojito = new(); mojito_h = new(1, "the one at table 7"); bandeja_de_mojito.bandeja_trago(mojito_h); mojito_h = new(1, "the one on the sidewalk"); bandeja_de_mojito.bandeja_trago(mojito_h); // Consider the case where a set of random drinks has to be read from a file // dynamically. // --> Doing that with NON hardcoded code is impossible // You would need a script that generates the source, recompile it...
The idea is to create data of random types without changing the code.
Notes: The problem first, the pattern after: I want to change the type of object that gets created without touching the code that creates it. With that in your head, UVM’s factory —the env— is the same idea wrapped in macros. The Python version is next to it on purpose: it shows whoever comes from software that we invented nothing.

## Slide 106: The factory pattern
cantina builds fernet and mojito, and returns a trago handle

## Slide 107
The factory is the method at the top: it takes an argument and returns an object of the type that argument asks for
Polymorphism is what makes it possible: fernet and mojito extend trago, so both fit in a trago variable
Without the second there is nowhere to put what the first returns. They are the two halves of the same tool
Notes: The factory does not work without polymorphism, and it is worth saying it that way: if hacer_trago() could not return a fernet stored in a trago variable, there would be nothing to manufacture. They are the two halves of the same thing. The useful question about the diagram: what type is the thing hacer_trago() returns? trago, always. What changes is which object comes inside. The caller never finds out, and that is exactly the point. And the limit you see right away: if the caller needs something only fernet has —the sin_hielo of the example— the comfort is over and you have to cast. That is the next slide, and it is the reason UVM’s factory is better than this one.

## Slide 108: The factory pattern
virtual is enough as long as you use methods the base class already declares. But fernet adds a field of its own —sin_hielo— that trago knows nothing about
To reach it you have to bring the handle down to its real type, and that is $cast: it converts the variable of the second argument to the class of the first
It checks at runtime and returns 0 if it does not work, so it never goes alone: always inside an if with its $fatal
//********************************************************************* // Part of the factory Class! //********************************************************************* class cantina; // Static method that builds the drinks static function trago hacer_trago(string pedido, int hielos, string name); mojito nuevo_mojito; fernet nuevo_fernet; case (pedido) "fernet": begin nuevo_fernet = new(hielos, name); return nuevo_fernet; end "mojito": begin nuevo_mojito = new(hielos, name); return nuevo_mojito; end default: begin $fatal(1, {"No such drink: ", pedido}); return null; end endcase // case (pedido) endfunction : hacer_trago endclass : cantina
And $cast in use, in the top: the factory always returns a trago, and to reach sin_hielo you have to bring it down to fernet
// Using the factory! trago_h = cantina::hacer_trago("fernet", 15, "the one at the bar"); trago_h.servir(); // Reaching a member of fernet (derived from trago) through a trago variable // requires casting it to fernet. if (!$cast(fernet_h, trago_h)) $fatal(1, "Could not cast trago_h to fernet_h"); if (fernet_h.sin_hielo) $display("And on top of that it comes warm!"); bandeja#(fernet)::bandeja_trago(fernet_h); if (!$cast(fernet_h, cantina::hacer_trago("fernet", 2, "the one at table 4"))) $fatal(1, "Could not cast the cantina drink to fernet_h");
Notes: Two things about this code, and both come back in UVM. The first: $cast checks at runtime and returns 0, it does not abort. That is why in the example every call goes inside an if (!$cast(...)) $fatal(...). A $cast without a check is the assert(randomize()) of the transactions in another disguise: if it fails, you carry on with a handle at null and the error shows up three lines later, in another place. The second: look at the case (pedido) of hacer_trago(). To add a new drink you have to edit the factory. In other words we took the hardcoding out of whoever uses it and put it in a single place — better, but it is still there. There is what UVM solves, and it is worth saying so: `uvm_component_utils registers the class on its own, so UVM’s factory has no case to maintain, and type_id::create() returns the right type without anybody casting. Both annoyances of this slide disappear in the env.

## Slide 109: The factory pattern
Python Style
class Trago: """Factory class that builds a Trago.""" @staticmethod def factory(kind): """Factory Method.""" if kind == "CubaLibre": return CubaLibre() if kind == "Fernet": return Fernet() if kind == "Mojito": return Mojito() if kind == "Whiscola": return Whiscola() raise ValueError("No such trago: " + kind)
The same factory, in a language that has nothing to do with hardware: a static method with an if per type and a raise for what does not exist
And the same annoyance: adding a drink forces you to edit the factory
The whole file is in code/u3/factory/factory.py and it runs with python3: it generates twenty drinks at random and serves them all the same way
Notes: It is there on purpose and the moral is short: this is not a verification oddity, it is a design pattern from 1994 that in Python takes ten lines. The bottom part of the file is worth opening if there is time left: Trago.__subclasses__() asks the language which classes inherit from Trago, and with that the generator no longer needs a hand-written list. It is exactly what UVM’s factory registration does with `uvm_component_utils, but from the top down instead of each class signing itself up. The punchline: the final loop treats the twenty drinks the same, without asking what type they are. That is polymorphism, and it is what makes a factory worth anything. The slide works for two opposite audiences. For whoever comes from software it lowers the suspicion —“ah, it is the same old factory”—. For whoever comes from RTL it shows that what they are learning is not “weird SystemVerilog stuff”: it is programming, and you can go and read about it outside the EDA world.

## Slide 110: The factory pattern
Summary of the unit
Every new() is a hardcoded decision. The factory moves it to runtime: instead of building, you ask for the object from somebody who knows which type to hand over
It does not work without polymorphism —somebody who manufactures and a base variable to store it in are both needed— and the $cast returns 0 instead of aborting, so it never goes alone: always inside an if with its $fatal
Where it comes back: `uvm_component_utils registers the class on its own —the case you have just written by hand— and +UVM_TESTNAME picks it from the command line
Notes: Closing of the most abstract section of day 2, and it is worth landing it with what is coming: the +UVM_TESTNAME=add_test of the tests is a factory — UVM reads a string from the command line and builds the class that corresponds. Here they saw the mechanism from the inside, a day early. The sentence that sums up the whole section: whoever uses the object stops being the one who picks the type. Everything else is implementation detail. And for whoever comes from software: it is the GoF Factory Method, from 1994, and in Python it takes ten lines. We invented nothing, and that is good news.

## Slide 111
A testbench without a single module
The same testbench, without a single module
This section adds no functionality: it verifies the same as the interfaces and BFM testbench
What changes is what it is made of. The three modules —tester, scoreboard, coverage— become three classes, and the initial becomes a method
The piece that binds them appears: a testbench class that instantiates the others, hands them the BFM and launches their threads. Nobody instantiates it for you
It is the last version without UVM, and that is why it is worth looking at closely: everything this class does by hand, from the tests on the library is going to do
The question to walk out of the section with: which part replaces which?
Notes: The real goal of the section is not to teach anything new, it is to leave a point of comparison. If the student can look at testbench.svh and say “this is the env, this is the build_phase, this is the run_phase”, day 3 starts downhill. It is worth writing the table on the board before showing the code, and coming back to it at the end of day 3:
Here, by hand | From the tests on | testbench.execute() that does new() on the three | build_phase of the env | passing the BFM through the constructor | uvm_config_db | fork ... join_none | UVM runs one run_phase per component | $finish inside the tester | objections |
And say out loud what can be seen on its own: there is not a single module in the classes of the testbench. The modules were left for the DUT, the clock and the interface — which is precisely what gets synthesized.

## Slide 112: A testbench without a single module
A testbench of modules works until it has to be reused: to change the stimulus you have to edit the module, and to have two versions you have to copy it
With classes, changing the stimulus is extending a class, and the two versions live side by side. That is all OOP buys you here
The VTALU TB, piece by piece
top: Instantiates the testbench class
testbench: Top-Level Class
tester: Generates the stimulus
scoreboard: Checks that the VTALU is working
coverage: Captures the functional coverage information
The object tree of the testbench without modules: top elaborates, and inside live the testbench class and its three pieces

## Slide 113
Notes: It is the same testbench as interfaces and BFM, but in objects: what changes is the shape, not what it does. If possible, show them side by side. The drawing is the one to be able to redraw from memory at the end of the day, and the line that splits it in half is the one that matters: above, what gets elaborated —the module, the DUT, the interface—; below, what somebody has to create. An object nobody creates is a null handle, and that is the mistake of the first afternoon. It is the last version without UVM. From the tests on the same thing gets assembled by UVM, and the student has to be able to say which part replaces which.

## Slide 114: A testbench without a single module
The top: the only thing that is still a module
The top is still a module, and it is going to stay that way until the end of the course: classes do not get elaborated, somebody has to exist before time 0
It imports the package with the classes, instantiates the DUT and the BFM, and declares the handle to the testbench
Inside the initial, two lines: new(bfm) and execute()
module top; // Class definitions and shared resources are kept in a package import vtalu_pkg::*; // The macros are defined in common too. UVM does this as well `include "vtalu_macros.svh" // The DUT and the BFM get instantiated vtalu DUT ( .A(bfm.A), .B(bfm.B), .op(bfm.op_set), .clk(bfm.clk), .reset_n(bfm.reset_n), .start(bfm.start), .done(bfm.done), .ovf(bfm.ovf), .result(bfm.result) ); vtalu_bfm bfm (); // A variable to hold our TB testbench testbench_h; initial begin // The testbench object gets built and launched testbench_h = new(bfm); testbench_h.execute(); end endmodule : top
Notes: The top is still a module and it is going to stay that way until the end of the course, even with UVM. The reason is that classes do not get elaborated: somebody has to exist before time 0 to instantiate the DUT, the interface and the clock. The detail to point a finger at is how the BFM gets passed: here it gets handed to the constructor, new(bfm), and it works because the top knows the class. In UVM that line is not going to exist — the test gets created by the factory and nobody can pass it arguments. That is why the uvm_config_db shows up in the tests. A good question to leave hanging: why is the package import before everything else? Because the classes live in a package and the module has to see them. It is the first time the compilation order matters, and it will not be the last.

## Slide 115: A testbench without a single module
The testbench class: the one that assembles and starts
There is one object above everything else that instantiates the others, hands them what they need and launches their threads. Every OOP testbench has one
Here we write it by hand: three new() and a fork ... join_none
From the env on that class is going to be called uvm_env, the new() are going to be type_id::create() in the build_phase, and the fork UVM is going to do on its own
class testbench; // virtual: the object-world equivalent of a module's port list. It tells // the compiler that this variable is going to receive a handle to an // interface at some point in the future. See the slide in the TB-in-objects section. virtual vtalu_bfm bfm; tester tester_h; coverage coverage_h; scoreboard scoreboard_h; function new(virtual vtalu_bfm b); bfm = b; endfunction : new task execute(); tester_h = new(bfm); coverage_h = new(bfm); scoreboard_h = new(bfm); // One thread per object. join_none: execute() returns and the three go on. fork tester_h.execute(); coverage_h.execute(); scoreboard_h.execute(); join_none endtask : execute endclass : testbench
Notes: This is the class UVM is going to replace, so it is worth reading it line by line: new() on the three objects, fork ... join_none to start them, and that is it. That is an env written by hand. Two things to flag. The first is the virtual vtalu_bfm bfm: the word virtual here has nothing to do with the virtual methods of polymorphism. A virtual interface is a handle to an interface that is going to be assigned later on — it is the equivalent, in the world of objects, of the port list of a module. It is the third meaning of virtual in SystemVerilog and that is why it is worth naming it out loud. The second is the join_none: the three objects run in separate threads and execute() returns right away. If it were join, the testbench would wait for the three to finish and the scoreboard never finishes. It is the same decision UVM takes on its own when it runs a run_phase per component. And one that always gets asked: who ends the simulation? The tester’s $finish, inside execute(). It is ugly and it shows: one object decides for everybody. In the tests that becomes an objection, which is the tidy form of the same thing.

## Slide 116: A testbench without a single module
The tester class: the stimulus, with no wires
It sends a thousand random operations, with the same bias to the edges as the conventional testbench: the goal is still to fill the bins of the covergroup
Against the modular version two things change and nothing else:
  the BFM arrives through a variable —a virtual interface— instead of through a port list
  the initial is now a method, execute(), that somebody has to call
// The initial block is replaced by an execute() task task execute(); byte unsigned iA; byte unsigned iB; shortint unsigned result; operation_t op_set; bfm.reset_alu(); op_set = rst_op; iA = get_data(); iB = get_data(); bfm.send_op(iA, iB, op_set, result); op_set = mul_op; bfm.send_op(iA, iB, op_set, result); bfm.send_op(iA, iB, op_set, result); op_set = rst_op; bfm.send_op(iA, iB, op_set, result); repeat (1000) begin : random_loop op_set = get_op(); iA = get_data(); iB = get_data(); bfm.send_op(iA, iB, op_set, result); $display("%2h %6s %2h = %4h", iA, op_set.name(), iB, result); end : random_loop $finish; endtask : execute
Notes: There is a trap here put in on purpose and it is worth not giving it away now: look at the declaration of get_op(). It says protected function, not protected virtual function. Without virtual, execute() is always going to call this class’s one, even if the object is of a derived class — which is exactly what they saw in polymorphism with servir(). That is the day 2 exercise, and it is good that they walk into it: inheritance does not show until somebody writes virtual, and that is understood much better by suffering it than by reading it. The other thing to point out is what is not in this class: the protocol. reset_alu() and send_op() still live in the BFM, the same as in interfaces and BFM, and the tester calls them with bfm.send_op(...). That is the whole point of the BFM and that is why it holds without changes until the end of the course: the class above asks for an operation, and it does not even know a done exists. And the detail you see at the start of execute(): the four directed operations before the repeat (1000) are not decoration. They are the reset, the multiplication after the reset and the repeated mult — that is, three rows of the verification plan of the conventional testbench that the random should not be left to wait for.

## Slide 117: A testbench without a single module
The scoreboard: the always became a task
A sensitivity list does not exist in a class. What replaces it is a forever with the wait inside — same semantics, written as sequential code
// The always @(posedge done) of the modular version, as a forever loop: an // object has no sensitivity list, it has a task that blocks. task execute(); shortint predicted_result; bit predicted_ovf; forever begin : self_checker @(posedge bfm.done) #1; case (bfm.op_set) add_op: predicted_result = bfm.A + bfm.B; sub_op: predicted_result = bfm.A - bfm.B; and_op: predicted_result = bfm.A & bfm.B; xor_op: predicted_result = bfm.A ^ bfm.B; mul_op: predicted_result = bfm.A * bfm.B; endcase // case (op_set) // ovf belongs to sub and to nobody else: with 8-bit inputs and a 16-bit // output, neither the addition nor the multiplication can overflow. predicted_ovf = (bfm.op_set == sub_op) && (bfm.A < bfm.B); if ((bfm.op_set != no_op) && (bfm.op_set != rst_op)) if (predicted_result != bfm.result || predicted_ovf != bfm.ovf) $error( "FAILED: A: %0h B: %0h op: %s result: %0h ovf: %0b", bfm.A, bfm.B, bfm.op_set.name(), bfm.result, bfm.ovf ); end : self_checker endtask : execute
Notes: The translation to point out: the always @(posedge done) of the modular testbench is a forever begin @(posedge bfm.done) ... end here. It is the same wait, written as sequential code inside a method. An object has no sensitivity list; it has a task that blocks. The #1 of the first line is one of those details that get paid for dearly: without it, the scoreboard reads the signals at the very instant done goes up and can eat a delta race. With it, it reads when everything has settled. It is the reason verification samples on the edge the design does not use. And what this scoreboard still does wrong, to leave it hanging: it reads the operation off the wire (bfm.op_set) at the moment of the result. It works because the protocol forces the operands to stay stable, but it is fragile — the day the DUT has several operations in flight, it breaks. In the analysis ports the scoreboard is going to compare against a queue of commands the monitor sends it, and that does scale.

## Slide 118: A testbench without a single module
The coverage class: the covergroup inside an object
// In a class, we don't need to declare variables to hold the covergroups, but we do need // to call a constructor to create them. function new (virtual vtalu_bfm b); op_cov = new(); zeros_or_ones_on_ops = new(); bfm = b; endfunction : new task execute(); forever begin : sampling_block @(negedge bfm.clk); A = bfm.A; B = bfm.B; op_set = bfm.op_set; op_cov.sample(); zeros_or_ones_on_ops.sample(); end : sampling_block endtask : execute
The covergroup is the same as the conventional testbench’s, line by line. What changed is where it lives
In a module, declaring the covergroup was enough. In a class it has to be built: the class’s new() does op_cov = new()
The execute() is the always @(negedge clk) from before, written as a forever: it copies the BFM signals and calls sample()
Notes: The op_cov = new() inside the constructor is the trap of the slide: in a module the covergroup gets instantiated on its own, in a class it does not. If you forget it, the code compiles, it runs, and the report says 0 %. It is the same silent trap as the conventional testbench’s, with one more turn of the screw. The transition bins are still inside `ifndef VERILATOR, the same as in the conventional testbench, and for the same reason: Verilator 5.052 still does not compile them. What has to be said before the analysis ports: here the sampling happens on the clock edge, that is, cycles get counted. When the coverage is a subscriber it is going to sample when a command arrives, and there operations get counted — which is what the verification plan asked for from the conventional testbench on.

## Slide 119: A testbench without a single module
The map of day 3: what replaces what
Here, by hand | From the tests on
testbench.execute() with three new() | the build_phase of the env
passing the BFM through the constructor | uvm_config_db
fork ... join_none | UVM runs one run_phase per component
$finish inside the tester | objections
picking the tester by editing the code | set_type_override of the factory
$display that gets put in and deleted | `uvm_info and the verbosity ceiling
This is the complete testbench, without UVM and with nothing missing. It works
Everything that comes on day 3 replaces one row of this table, and nothing else
We come back to this slide at the close of the day, to cross them out
Notes: This is the slide worth writing down, because it is the whole map of day 3. The strong claim has to be made explicit: UVM adds no functionality here. The testbench of this unit does everything the env’s is going to do. What it adds is convention — that the left-hand column is solved the same way in every testbench in the world. And the honest question that is going to come up: “so what for?”. So that whoever joins the project knows where to look without reading the whole testbench, and so that the new tester costs four lines instead of a class. Both benefits are of scale, and that is why in a hundred-line example UVM looks like too much — it has to be said that way, instead of selling smoke. At the close of day 3, with the env and the override already seen, you come back here and read the right-hand column straight through. That is where the day closes on its own.

## Slide 120: A testbench without a single module
Summary of the unit
The day 1 testbench without a single module: the same three pieces, plus the class that binds them —testbench—, which is the direct ancestor of the uvm_env
The top is still a module and it will be until the end, and the BFM arrives through a virtual interface: it is the only way a class has of touching signals
It is the last version without UVM. From here on, every piece we write by hand has a class of the library that replaces it — execute() is going to be the run_phase
Notes: The slide to close the whole of day 2 with, because it leaves the bridge built. The question to leave posed: which part replaces which? Day 3 answers it piece by piece, and it starts downhill if the student walks out of here able to draw the object tree on the board. And the argument for why the whole day was worth it: with modules, changing the stimulus is editing the file. With classes it is extending a class, and the two versions live side by side. That is the exercise that follows.

## Slide 121
Review · Day 2
1 of 8 · Handle and object
rectangle rectangle_h; — after that line, how many objects are there?
☒ None: rectangle_h is null until somebody calls new()
☐ One, with length and width at 0
☐ One half built: the fields exist but the constructor has not run
☐ It depends on whether the class has a constructor
None — declaring a handle reserves nothing. There is the difference with a struct, which the simulator reserves the moment it sees it. And using the handle before the new() does not fail at compile time: it blows up in the middle of the simulation.

## Slide 122
Review · Day 2
2 of 8 · Polymorphism
A variable of type trago holds a fernet object. If servir() is not virtual, what gets executed?
☐ fernet’s servir()
☐ A compile error
☒ trago’s servir()
☐ Both, the base class one first
trago’s — without virtual, SystemVerilog looks at the type of the variable, not at the object’s. It is literally what code/u3/polimorfismo/01-sin-virtual prints: “A generic trago cannot be served”.

## Slide 123
Review · Day 2
3 of 8 · Abstract classes
What do I gain by using an abstract class with pure virtual methods instead of a base class whose method does $fatal?
☐ Nothing, it is a matter of style
☒ That the error moves from simulation to the compiler
☐ That the base class can be instantiated
☐ That the simulator can pick the most specific override at run time
The error moves to the compiler — with $fatal you find out halfway through the simulation that an override was missing. With pure virtual it does not compile. Catching it earlier is always cheaper.

## Slide 124
Review · Day 2
4 of 8 · Static variables
I instantiate 10 objects of a class that has a static variable. How many copies are there in memory?
☐ 10, one per object
☐ 0 until somebody writes it: the memory is reserved on first access
☒ 1, shared by every instance
☐ It depends on the simulator
A single one — and it exists even if you instantiate no object at all. That is what makes it useful for global TB data, and what makes it dangerous if you leave it public.

## Slide 125
Review · Day 2
5 of 8 · Static methods
Why is it worth declaring the static variable protected and exposing it with static methods?
☒ To be able to change the data structure without touching whoever uses it
☐ Because a static without protected is reserved once per instance
☐ So that it takes up less memory
☐ Because UVM demands it
To be able to change it later — if the queue is out in the open, the day you swap it for another structure you have to go and fix every place that touched it. Encapsulating is being able to change your mind.

## Slide 126
Review · Day 2
6 of 8 · Parameterized classes
bandeja#(fernet) and bandeja#(mojito) have a static queue inside. Do they share the queue?
☐ Yes, static is a single one for everybody
☐ Yes: the parameter changes the type of the methods, not the static storage
☐ It depends on whether they get instantiated or not
☒ No: each specialization is a different class, with its own queue
They do not share it — SystemVerilog generates one class per combination of parameters. static is unique inside each one of those classes, not across all of them. UVM leans on this all the time.

## Slide 127
Review · Day 2
7 of 8 · The factory pattern
What problem does the factory pattern solve?
☐ Creating objects faster
☒ Deciding at run time which subtype to build
☐ Avoiding having to declare classes
☐ Centralizing the new()s in one class, to be able to count and free them
Deciding the subtype at runtime — without hardcoding the new: you ask the factory for an object and it decides which one. It is the piece that is later going to let you change the stimulus of a whole test without touching the code of the env.

## Slide 128
Review · Day 2
8 of 8 · $cast
When does a $cast(destination, source) succeed?
☐ Always: it converts any class into any other
☐ Only between classes with no inheritance
☐ When the two classes have the same fields, even if they are not related
☒ Only if the object in source is of the class of destination or of a derived one
Only if the object allows it — $cast checks at runtime and returns 0 if it does not work. That is why UVM’s factory is more comfortable than the cantina of the section: type_id::create() returns the right type and saves you the cast.

## Slide 129
Exercise · Day 2
A tester that only multiplies
cd code/ejercicios/d2 && bash run.sh
Extend tester, redefine get_op(), and have the testbench instantiate it
It is going to carry on sending random operations. That is where the exercise starts
Hint: polymorphism
Notes: The exercise is set up so that they fail: get_op() in the object-based testbench is not virtual, so execute() always calls the base class’s one even if the object is a mult_tester. Until they add virtual, inheritance does not show — and that is understood much better when you suffer it than when you read it. It is on purpose the same problem as the day 3 exercise: there they are going to solve it with the factory, and only then do you see what the factory is for.

## Slide 130
Yesterday we left…
Where the testbench stands
The day 1 testbench without a single module: three classes, one that binds them, and a top that only instantiates the DUT and the BFM
The BFM gets into the classes through a virtual interface, which is the only way a class has of touching signals
And the factory is already written by hand: a case that has to be edited every time a new type shows up. Today the one you do not edit shows up
Notes: Day 3 is where UVM walks in, so the recap has an extra job: making it clear that what is coming replaces pieces the student already wrote, and is not a pile of new pieces to learn from scratch. The whole unit can be read as “this thing you did by hand, the library brings it done”. The third bullet is the hook: the case of 060 is exactly what `uvm_component_utils does on its own, and saying it here stops the macro from being a magic formula.

## Slide 131
Agenda
Day 3 · ≈ 4 h 30 · unit 4 · UVM walks in
Tests
Components and phases
The env: structure and stimulus
Reporting: verbosity and actions
By the end of the day you can:
Explain why a UVM simulation ends at t=0 if nobody raises an objection
Say why build_phase runs top-down and connect_phase the other way round
Make a scoreboard that fails say something more than “it failed”
Notes: The third one is the one that pays off the most in the long run and the one most underestimated: it is row 10 of the closing self-assessment and the one aiming at the 47 % of day 1. A uvm_error that prints “FAIL” leaves whoever is debugging where they were; one that prints the transaction, the prediction and the time saves them half a morning. The first two are library mechanics and they are the ones most often answered with an “it rings a bell”. The second exercise of the day exists so that they stop ringing and start having been suffered.

## Slide 132
Tests
Compile once, pick the test from the command line
The object-based testbench has the stimulus inside: changing test means changing code and compiling again
A thousand tests at five minutes of compilation each are 5000 minutes: three and a half days of machine time to run nothing new
UVM turns the order around: the testbench gets compiled once, and the test that runs is picked when the simulation starts
$ ./obj_dir/top/sim +UVM_TESTNAME=random_test $ ./obj_dir/top/sim +UVM_TESTNAME=add_test # the same binary
That is what this unit buys, and what gets paid with the ceremony that comes: registration in the factory, a constructor with a fixed signature and phases
Notes: The arithmetic is UVM’s commercial argument, and it is worth saying it with the numbers in hand: it is not that the modular testbench is wrong, it is that it does not scale. If possible, live: compile once and run the two lines above. Let them see that the second one compiles nothing. What gets collected from the object-based testbench: the testbench is already split into tester, coverage and scoreboard, and that is why you can change the tester alone. What gets paid up front: in the components those three classes stop being loose objects that the test new()s and become components of the tree.

## Slide 133: Tests
The top: instantiate, publish the interface, start
initial begin // null and "*": from the root and visible to the whole tree. See the // uvm_config_db slide. uvm_config_db#(virtual vtalu_bfm)::set(null, "*", "bfm", bfm); // UVM reads +UVM_TESTNAME, and builds THAT test with the factory. run_test();
The top is still a module: it instantiates the BFM and the DUT the same as before. The only new thing is these two lines
run_test() with no argument means “whichever +UVM_TESTNAME says”. With an argument —run_test("random_test")— that one becomes the default, and +UVM_TESTNAME still overrides it from the command line
Before run_test() there is not a single UVM object alive: that is why the set goes here
Notes: The virtual interface gets passed through the config_db because classes do not see the signals of the module: bfm lives in top, and random_test is an object that gets created at simulation time. There is no way to hand it over through the constructor — uvm_component’s constructor only accepts name and parent. It is worth pointing at the order: first the set, then run_test(). The other way round the test gets built before the data is in the database and the get fails with the fatal. It is a mistake you rarely see because almost nobody writes the top the wrong way round, but it explains why the set cannot go in a separate initial. The slide that follows is the one to explain well: it is mistake number one of whoever starts with UVM.

## Slide 134: Tests
uvm_config_db: the testbench’s mailbox
A global and typed database: the #(...) is part of the key
Four arguments: scope (cntxt, inst_name), name and data
The scope is a hierarchical path, and that is where the whole point is
// ILLUSTRATION -- not compiled. The two halves of the config_db, side by side: // the set() lives in top.sv and the get() in tb_classes/driver.svh. // -- IN THE TOP -- top is a module, not a uvm_component --------------------- // cntxt = null : the scope starts at the UVM root // inst = "*" : visible to the whole component tree uvm_config_db #(virtual vtalu_bfm)::set(null, "*", "bfm", bfm); // -- IN A COMPONENT -- always inside build_phase ---------------------------- // cntxt = this : the scope is the hierarchical path of THIS component // inst = "" : with no suffix, the path is exactly the component's if (!uvm_config_db #(virtual vtalu_bfm)::get(this, "", "bfm", bfm)) `uvm_fatal("DRIVER", "Failed to get BFM") // The 3rd argument ("bfm") is the NAME of the datum inside the database. // If the string in the set and the one in the get are not identical, this still // compiles and blows up at run time with a null pointer.
Notes: The first two arguments are where, the third is what. In the set of the top it is null, "*" because top is a module, it is not in the UVM tree: the translation is “from the root, visible to everybody”. In the get it is this, "", that is, “me”. It is worth writing on the board the path that comes out: uvm_test_top.env_h.driver_h. And the shortcut to warn against from the start: get(null, "*", ...) also compiles and also works — it searches the whole tree and keeps the first thing it finds. With a single interface you never notice. The day the testbench has two, the driver of bus A can end up driving bus B, and it does not fail: it lies. It is one of those mistakes that get paid for three months later.

## Slide 135: Tests
A test in three parts: 1 · register it
class random_test extends uvm_test; `uvm_component_utils(random_test); virtual vtalu_bfm bfm;
random_test extends uvm_test, which extends uvm_component: it is a node of the tree, not a loose object
The `uvm_component_utils macro enrols it in the factory. Without that line, +UVM_TESTNAME=random_test finds nothing and UVM aborts
The handle to the virtual interface gets declared here and filled in in the build_phase: they are two different moments
Notes: It is the first time the factory shows up for real, and you still cannot see what it is for: here it only acts as a directory of names. The second half —creating by type and being able to substitute it from outside— arrives in the env with the overrides. The semicolon after the macro is redundant and UVM tolerates it. It is in the code of the book and we left it the same so that whoever compares does not get dizzy, but if somebody asks: it is not needed.

## Slide 136: Tests
2 · the constructor and the build_phase
function new(string name, uvm_component parent); super.new(name, parent); endfunction : new // The get goes in build_phase and not in the constructor: when the // constructor runs, the tree does not exist yet. function void build_phase(uvm_phase phase); if (!uvm_config_db#(virtual vtalu_bfm)::get(this, "", "bfm", bfm)) `uvm_fatal("RANDOM TEST", "Failed to get BFM") endfunction : build_phase
The constructor of a uvm_component has a fixed signature: name and parent, in that order, and super.new(name, parent) as the first line
The get of the config_db goes in build_phase, not in the constructor: when the constructor runs the tree is still being assembled
if (!get(...)) uvm_fatal: the get returns a bit. Ignoring it leaves the handle at null and the failure shows up a hundred lines later, in another file
Notes: The fixed signature is the first thing everybody breaks: a constructor with one argument too many and the factory cannot create it, because it always calls with (name, parent). build_phase is a phase, not a function you call yourself: UVM walks it top-down over the already assembled tree. In this test you cannot tell yet, because the tree is a single node; in the components, when the env builds its children, the top-down order is what makes the parent exist before the child. The fatal is not paranoia: without it, a typo in the name of the data —“bfm” against “BFM”— gives a simulation that runs, sends not one stimulus and finishes with 0 errors.

## Slide 137: Tests
3 · the run_phase: this is where the simulation happens
task run_phase(uvm_phase phase); random_tester random_tester_h; coverage coverage_h; scoreboard scoreboard_h; phase.raise_objection(this); random_tester_h = new(bfm); coverage_h = new(bfm); scoreboard_h = new(bfm); fork coverage_h.execute(); scoreboard_h.execute(); join_none random_tester_h.execute(); phase.drop_objection(this); endtask : run_phase
It is the same body as the execute() of the object-based testbench: tester, coverage and scoreboard, with the two observers in fork ... join_none
What changes is who calls it: before it was called by the top module, now it is called by UVM when the run phase’s turn comes
The two new lines are the raise and the drop of the objection, which are the ones that decide when everything ends
Notes: It is worth showing it next to the tb.execute() of the object-based testbench: the stimulus did not change by one line. The only thing we did was move it inside a class that UVM knows how to create and call. That is the whole job of this unit. join_none and not join: coverage and scoreboard are infinite loops that watch the signals. If we waited for them to finish, it never finishes. And the one people miss: the simulation does not last as long as the run_phase lasts, it lasts as long as the objections last. That is what comes now.

## Slide 138: Tests
Objections: who decides when it ends
task run_phase(uvm_phase phase); phase.raise_objection(this); // "I still have work" ... // the stimulus phase.drop_objection(this); // "done, as far as I am concerned it can end" endtask
Every run_phase runs in parallel: none of them can decide on its own when to finish. UVM counts, and the phase ends when the last objection drops
Without raise_objection the simulation ends at time 0, and the test passes with 0 errors without having sent a single stimulus
Without drop_objection it never ends: there is no error, the simulation just keeps running
Both symptoms are silent, and that is why two plusargs exist: +UVM_OBJECTION_TRACE says who raised it and who dropped it, and +UVM_TIMEOUT puts a ceiling on the run
Notes: It is the mechanism that decides how long the simulation lasts, and it is the one that produces the two classic hangs of the first week. Worth writing the two failures on the board, because the student is going to see them before any DUT bug. The rule of thumb: the objection gets raised by whoever has work, and dropped by the same one. In this course it is always the test. Never raise it in a component and drop it in another one — that is how a real testbench hangs. And a third participant is missing, which is the next slide: the objection knows when the test finished sending, not when the scoreboard finished comparing. That is the difference the drain_time pays for. And the day 6 hook: set_automatic_phase_objection(1) is this same thing, done by the sequencer instead of by the test.

## Slide 139: Tests
The end that is not the end: drain_time
The objection says “I finished sending”. It does not say “I finished comparing”: between the two there is a scoreboard with a FIFO inside and results the DUT has not answered yet
When the last objection drops the phase cuts at that instant: what was left in flight does not arrive, nobody compares it, and the summary says UVM_ERROR : 0
task run_phase(uvm_phase phase); phase.get_objection().set_drain_time(this, 200ns); // a cushion after the last drop phase.raise_objection(this); ... // the stimulus phase.drop_objection(this); endtask
The drain_time is a number picked by eye. The version with a criterion is phase_ready_to_end(): UVM calls it when the last objection dropped, and the component that still has work raises one more and the phase carries on
It is the bug of the second week, and it is silent: no error, no hang, and the last transactions were never compared
Notes: It is the flip side of the previous slide and it is worth saying it in those words: the objection measures the stimulus, not the analysis. The test knows when it finished sending; the scoreboard is the one that knows when it finished comparing, and nobody asked it. The drain_time is the cheap answer and it is enough for 90 % of the cases: a fixed cushion after the last drop_objection, in the order of what the DUT takes to answer. In this course it would be a couple of cycles; on a bus with latency, whatever the spec says. phase_ready_to_end() is the expensive answer and the one used in a serious testbench, because it is not a number: the scoreboard looks at its own FIFO, and if it has items left it raises one more objection. The shape is always the same —check phase.get_name() == "run", and raise only if something really is missing—, and the trap has to be said: if whoever implements it never drops it, they hung the phase. The third piece, for whoever wants to hook in at exactly that instant, is all_dropped: a callback of the objection object that fires when the count reaches zero. And the hook forward: the scoreboard with a FIFO of the analysis ports is exactly the case of this slide, and the capstone steps on it again.

## Slide 140: Tests
The timeline, end to end
Timeline of an objection: raise, stimulus, drop, drain_time and the end of the phase, with the transactions still in flight

## Slide 141
raise and drop mark the stimulus, and nothing but the stimulus
What is left in flight is not in that count: the three empty boxes of the drawing
The drain_time is the time given away so those answers arrive and get compared
Without raise nothing sits between the marks; without drop, the line never ends
Notes: The figure is there to be paused on, asking where the simulation ends. The answer almost everybody gives the first time —“when the test finished sending”— is exactly the one that produces the bug: that is where the last objection drops, and that is where the phase cuts if nobody asked for a cushion. It is worth pointing at the three empty boxes: they are transactions the DUT has not answered yet. They are not lost through anybody’s mistake, they are in flight, which is the normal state of any pipeline. What decides whether they get compared or not is how much longer the phase lives. The detail worth saying out loud: the drain_time is measured from the last drop, not from the beginning. If the test sends a thousand operations and the DUT takes two cycles to answer, the cushion is two cycles and not two thousand. And the version with a criterion —phase_ready_to_end()— is this same figure with one difference: the length of the cushion gets decided by the scoreboard looking at its FIFO, instead of being decided up front by whoever wrote the test.

## Slide 142: Tests
The second test: the same thing, with another tester
task run_phase(uvm_phase phase); add_tester add_tester_h; coverage coverage_h; scoreboard scoreboard_h; phase.raise_objection(this); add_tester_h = new(bfm); coverage_h = new(bfm); scoreboard_h = new(bfm); fork coverage_h.execute(); scoreboard_h.execute(); join_none add_tester_h.execute(); phase.drop_objection(this); endtask : run_phase
add_test is random_test with one different line: add_tester instead of random_tester. Everything else repeats exactly as it is
That repetition is real and it is ugly, and it is the debt the components pay: when the testbench is a tree of components, the test is going to build an env and it is not going to touch the stimulus
For now it is worth seeing it copied: it is the problem that motivates what follows
Notes: The duplication should not be apologized for, it should be pointed at. The student has to finish this slide with the feeling of “this cannot be right”, because that feeling is exactly the reason for the components and the env. If somebody jumps ahead and proposes a base class with the common run_phase and a virtual method to pick the tester: that is fine, and it is more or less what base_test does in the sequences. Tell them so and move on.

## Slide 143: Tests
How it gets run, and what it prints
set -e . "$(dirname "${BASH_SOURCE[0]}")/../../verilator/common.sh" vlt_uvm top --coverage-user -Wno-fatal -f dut.f -f tb.f run_sim +UVM_TESTNAME=random_test run_sim +UVM_TESTNAME=add_test cov_report
UVM_INFO @ 0: reporter [RNTST] Running test random_test... UVM_INFO $UVM_HOME/src/base/uvm_report_server.svh(1009) @ 46340: reporter [UVM/REPORT/SERVER] --- UVM Report Summary --- ** Report counts by severity UVM_INFO : 1 UVM_WARNING : 0 UVM_ERROR : 0 UVM_FATAL : 0 ** Report counts by id [RNTST] 1 - $UVM_HOME/src/base/uvm_root.svh:633: Verilog $finish - S i m u l a t i o n R e p o r t: Verilator 5.052 2026-09-05 - Verilator: $finish at 46ns
A single vlt_uvm, two run_sim: one compilation, two tests. That is all the unit promises, and here it is done
[RNTST] Running test random_test... is UVM saying what it found in the factory under the name you passed it
The Report Summary with UVM_ERROR : 0 is the verdict: reporting takes it apart and explains where each row comes from
Notes: Worth running it live and timing it: the compilation takes minutes, the two run_sim take seconds. That is the number that justifies all the ceremony of the unit. The $finish at 46ns at the bottom is from the first test; add_test ends at 41 ns. Both send the same number of operations, but the multiplication takes more cycles than the addition, so the time depends on what came out of the random. And a useful warning: UVM_ERROR : 0 means “nobody called uvm_error”, not “the DUT is fine”. Here the scoreboard does report with `uvm_error, so the count is worth something — but a scoreboard that never receives anything gives exactly the same zero. Reporting shows how to tell them apart.

## Slide 144: Tests
Summary of the unit
The testbench gets compiled once and the test gets picked from the command line: +UVM_TESTNAME=random_test. That is the whole business of the section
The arithmetic that justifies it: a thousand tests at five minutes of compilation each are three and a half days of waiting for it to compile
The top is still a module. It publishes the BFM in the uvm_config_db before run_test(), because before that line there is not a single UVM object alive
The uvm_config_db is a global and typed database: the #(...) is part of the key, and the scope is a hierarchical path
A test gets registered with `uvm_component_utils. Without that line, the factory does not find it and UVM aborts
The virtual interface gets declared in the class and filled in in the build_phase: they are two different moments, and confusing them leaves a null
The objection says when the test finished sending, not when the scoreboard finished comparing. That difference is paid for with drain_time, or else with phase_ready_to_end()
Notes: Closing of the first real UVM unit. It is worth acknowledging the discomfort out loud: today they put in a lot of ceremony to do the same thing they were already doing. What they bought is the first bullet, and it does not pay out until there are two tests — which is the env. The mistake they are going to walk into and it is worth anticipating: the get() that forgets to check the return value. It does not fail, it lies: it leaves the virtual interface at null and the testbench falls over three layers further down. That is why every get of the course goes inside an if with its uvm_fatal.

## Slide 145
Components and phases
A component is what is in the tree, and the tree is walked by UVM
A testbench has three different things: the structure —what parts there are and how they connect—, the sequences —which commands, in what order— and the data. This unit is the first one; the data is day 5 and the sequences day 6
In the tests the test did new() on three loose objects and called them itself. That is not a structure: it is a long function
A uvm_component is a node with a name and a parent. UVM assembles the whole tree and then walks all of it calling phases, in an order it guarantees
Turning a class into a component is four steps, always the same ones:
  extend uvm_component or one of its daughters
  register it with `uvm_component_utils()
  the minimum constructor: (string name, uvm_component parent)
  override the phases it needs
Notes: The sentence on the slide is the one that orders the unit: a component is what is in the tree. Everything else —the name, the parent, the phases, the print_topology of the agents— comes out of there. The practical consequence that has to be said out loud: if something is not a component, UVM does not see it. It does not build it, it does not call phases on it and it does not show up in the topology. Later on we are going to have objects that on purpose are not components —the transactions— and that is where the distinction buys you something. The three axes —structure, sequences, data— work as a map of the rest of the course: components and env are structure, transactions are data, sequences are sequences.

## Slide 146: Components and phases
Intro UVM phases
Every uvm component has these phase methods by inheritance
UVM creates the TB and goes calling these methods in order
The phases are methods: they get overridden like any other virtual method. Whether it is also worth calling super is the topic of the next slide
function void build_phase(uvm_phase phase): UVM creates the TB (top-down). UVM components get instantiated in this method. If you try to instantiate them anywhere else it is an error
function void connect_phase(uvm_phase phase): Connecting components
function void end_of_elaboration_phase(uvm_phase phase): UVM calls it once it has created and connected every component
task run_phase(uvm_phase phase): UVM runs this task in its own thread. Every run_phase runs simultaneously
function void report_phase(uvm_phase phase): It runs when the last objection of the test drops. It shows Results
Notes: Three things that have to be said no matter what: build_phase is top-down, connect_phase is bottom-up, and every run_phase runs in parallel, each one in its thread. And the classic mistake: creating components after build has ended. UVM does warn you, and well: ILLCRT tells you which component and under which parent.

## Slide 147: Components and phases
The tree, twice: one walk goes down and the other goes up
The tree walked twice: build_phase goes down and connect_phase goes up, and the real order in which a child gets built

## Slide 148
build_phase goes down because a parent has to exist to create its children
connect_phase goes up for the opposite reason: the other end has to be there
The child gets created inside the parent build; its own build runs later
That is why the config_db set() goes before the create() that builds it
Notes: The drawing answers two questions that in the table read like an arbitrary convention. The first one: why build_phase is top-down. Because a parent has to exist in order to create its children, and there is no other way to assemble a tree; the ones in the middle need the opposite, that the children are already there. The second one is the one asked under one’s breath: if the parent creates the child inside its own build_phase, when does the build_phase of the child run? Later, and that is the part that has to be said slowly: create() calls the constructor, not the phase. UVM walks the tree calling the phase on the components that showed up along the way, so the child gets built in two steps. The practical consequence is the one in the last bullet, and it is the one that buys you something: a uvm_config_db::set() written after the create() of the child arrives late, the child already read, and the field stays at its default without anybody warning. It is the same asymmetric failure mode as the next slide. If somebody asks about the code: uvm_topdown_phase::traverse runs the phase on the component and only then walks its children —get_first_child()—, which by then already exist.

## Slide 149: Components and phases
And what about super.build_phase()?
// uvm_component.svh:2385-2393 -- uvm-core 2020.3.1, with the return; elided function void uvm_component::build_phase(uvm_phase phase); build(); // -> apply_config_settings(): the automatic config endfunction function void uvm_component::connect_phase(uvm_phase phase); connect(); // -> return; it is empty, like all the others endfunction
build_phase is the only phase that does anything in uvm_component: it applies the fields registered with `uvm_field_*. The course does not use those macros
Careful, there are two different supers: that one, and the one of a base class of yours, which builds what you wrote. The second one the course does call
Out there: always put it in, unless you can name why in your case it is a no-op. Adding it costs nothing; skipping it when it mattered —a `uvm_field_*, or inheriting from uvm_agent— leaves the field at its default and nobody warns you
And the order matters: whatever has to be decided before the children get built goes before the super. The set_type_override of add_test is that
Notes: This slide exists because the student is going to see super.build_phase(phase) in every piece of material on the internet and in most of the course’s build_phase it is not there. The honest answer is not “they forgot”: it is that without the field macros the call to uvm_component’s does nothing. The numbers, so that nobody has to take our word for it: grep -rn 'super\.build_phase' code/ --include='*.sv' --include='*.svh' --exclude-dir=.uvm gives 15 real calls —plus 6 comments that talk about them— over 306 build_phase. Those 15 call the super of a base_test or a random_test of ours, which builds the env. None of them calls uvm_component’s, which is what the slide is about. The other underlying difference: there are two ways of configuring a component. The automatic one (`uvm_field_* + config_db, magic by macros) and the manual one (uvm_config_db::get() in the build_phase, which is the one the course uses). The manual one is more code and vastly easier to debug — the field macros generate hundreds of lines you are never going to read. Why the recommendation for out there is the opposite of what the course does: the failure mode is asymmetric. Putting it in for nothing has zero effect. Leaving it out when it was needed is silence: the field stays at its default and the simulation runs. This course can name why in its case it is a no-op —there is not a single `uvm_field_* macro in code/ outside the vendored library —there are 0, and the build counts them—; whoever walks into somebody else’s testbench cannot. uvm_agent is the counterexample we have at hand: besides uvm_component, it is implemented by uvm_agent —which reads is_active there— and by the two sequencer bases (seq/uvm_sequencer_base.svh:122, which reads wait_for_sequences_count from the config_db, and seq/uvm_sequencer_param_base.svh:236). It comes back on day 6. The same goes for the other phases, cheaper still: in uvm_component they are return;, but uvm_driver::end_of_elaboration_phase checks that the seq_item_port is connected, and that one we do extend.

## Slide 150: Components and phases
The full picture: there are nine, not five
Phase | What for | Order
build_phase | instantiate the components | top-down
connect_phase | connect the ports | bottom-up
end_of_elaboration_phase | hierarchy ready, before simulating | bottom-up
start_of_simulation_phase | last call before time 0 | bottom-up
run_phase | task: this is where the simulation happens | one thread each
extract_phase | gather the data from the run | bottom-up
check_phase | decide whether it passed | bottom-up
report_phase | print the verdict | bottom-up
final_phase | close files and exit | top-down
The course uses five. The other four exist, they are empty, and you are going to see them
Notes: The table is there so that nobody leaves believing UVM has five phases: it has nine common ones and twelve runtime ones. The course uses five because with a single agent that is enough, and that has to be said — it is not that the others do not matter. The three you are most likely to run into outside: start_of_simulation_phase is where people print the configuration banner of the test; check_phase is where a tidy scoreboard decides the verdict, instead of counting errors along the way; and report_phase is the one they have already seen. That extract / check / report are separate has a concrete reason: they are bottom-up, so a child scoreboard finishes extracting before the parent env decides. If you do the three things in report_phase, you lose that guarantee. The question that orders the table: why is build_phase top-down? Because a parent has to exist in order to create its children. The ones in the middle need the opposite — that the children are already there. The other top-down one is final_phase, which closes the tree in the same order it was built.

## Slide 151: Components and phases
And inside the run_phase, a schedule
The twelve runtime phases running in parallel with run_phase, and where the default_sequence hooks in

## Slide 152
The twelve are tasks, they run in parallel with run_phase, and they are there to coordinate components from different teams without hand-made flags
The course uses run_phase and nothing else — with a single agent there is nothing to coordinate. But the default_sequence of day 6 hooks into main_phase
Notes: This slide exists so that main_phase does not show up for the first time on day 6. The exact distinction, which confuses everybody: run_phase and the schedule reset → configure → main → shutdown run at the same time, not one inside the other. A component can implement either of the two paths; what is not advisable is mixing them in the same testbench, because then nobody knows what runs when. The honest question is “so which one do I use?”. For a testbench of a single block, run_phase, which is what the course does. The schedule earns its keep in integration: the agent of the configuration bus finishes its configure and only then does the data one start its main, without either of the two teams having had to write a uvm_event or a shared flag.

## Slide 153: Components and phases
The scoreboard, now as a component
// The scoreboard of the TB in objects, now as a uvm_component. The four steps // --extend, register, constructor, phases-- are in the slides of the components section. class scoreboard extends uvm_component; `uvm_component_utils(scoreboard); virtual vtalu_bfm bfm; function new(string name, uvm_component parent); super.new(name, parent); endfunction : new // Self-sufficient: the component asks the config_db for the BFM. Before, the // test passed it in through the constructor, and the test had to receive it // only to hand it out. function void build_phase(uvm_phase phase); if (!uvm_config_db#(virtual vtalu_bfm)::get(this, "", "bfm", bfm)) `uvm_fatal("SCOREBOARD", "Failed to get BFM") endfunction : build_phase
The four steps, in order: it extends uvm_component, it registers itself, constructor (name, parent), and an override of build_phase
The underlying change does not show in the diff: before, the test received the BFM and handed it to the scoreboard through the constructor. Now the scoreboard asks for it itself from the config_db
The run_phase is the execute() of the object-based testbench without touching a comma: the check did not change, what changed is who starts it
Notes: The point of the slide is self-sufficiency. A component that needs somebody to hand it its dependencies forces that somebody to know them, and the test ends up being a delivery service for handles it does not use. With the config_db, the test does not know that the scoreboard needs a BFM. That is exactly what makes the env able to exist: if every component configures itself, the parent only has to build it. The price has to be said too: the dependency stopped being in the constructor, where it could be seen, and moved into a string. A misspelt "bfm" compiles. That is why the if (!get(...)) uvm_fatal is not optional.

## Slide 154: Components and phases
The test builds the tree and steps aside
class random_test extends uvm_test; `uvm_component_utils(random_test); random_tester tester_h; coverage coverage_h; scoreboard scoreboard_h; // Components get instantiated in build_phase, never in the constructor. function void build_phase(uvm_phase phase); tester_h = new("tester_h", this); coverage_h = new("coverage_h", this); scoreboard_h = new("scoreboard_h", this); endfunction : build_phase function new(string name, uvm_component parent); super.new(name, parent); endfunction : new // No run_phase: the test's job ends once the tree is built. endclass
The three new("name", this) are what creates the tree: this is the parent, and the string is the name that is going to come out in print_topology and in every message
They go in build_phase and nowhere else. In the constructor there is no hierarchy yet; after build_phase, UVM has already moved on
random_test has no run_phase: its job finished when the tree was assembled. The three children have theirs, and they run in parallel
Notes: It is the change of mindset of the unit, and it is worth saying it in these words: the test stopped doing the test. Now it assembles it and steps aside. The objection also moved: it is no longer raised by the test, it is raised by the components that have work — or, in this example, by the tester. Worth showing random_tester.svh for a second so that it can be seen. And the trap that is going to show up on its own: new() works here because the type is written in the declaration. In the env that gets replaced by type_id::create(), and that is the change that enables the overrides. Not yet, but it is worth planting.

## Slide 155: Components and phases
The second test: it inherits, and it copies anyway
// add_test extends random_test, redeclares tester_h with another type and // REWRITES the whole build_phase. That duplication is the problem the env section solves // with the factory override. class add_test extends random_test; `uvm_component_utils(add_test); add_tester tester_h; function new(string name, uvm_component parent); super.new(name, parent); endfunction : new function void build_phase(uvm_phase phase); tester_h = new("tester_h", this); coverage_h = new("coverage_h", this); scoreboard_h = new("scoreboard_h", this); endfunction endclass
add_test extends random_test, so it inherits coverage_h and scoreboard_h. It only redeclares tester_h, with another type
But the build_phase is written out again in full, and the three lines are identical except for one. Inheriting the class was not enough to inherit the structure
And there is something worse hidden: add_tester tester_h; shadows the tester_h of the base class. They are two different variables with the same name
It is the same problem as the tests, in disguise. The env solves it for real: one structure, and the factory substitutes the piece that changes
Notes: This is the slide that has to be left uncomfortable. If the student walks out thinking “this is still wrong”, the env explains itself. The shadowing of the handle deserves a minute: in the base class there is a random_tester tester_h and here an add_tester tester_h. Any method inherited from random_test that uses tester_h is going to see the base one, which stayed at null. Here it does no harm because there is none, but it is a time bomb and it is exactly the kind of silent mistake the course goes after. The hook: in the env there are not two tests, there is one; and add_test becomes a line of set_type_override_by_type.

## Slide 156: Components and phases
Summary of the unit
A uvm_component is a node with a name and a parent. UVM assembles the tree with those two pieces of data and then walks it on its own
Turning a class into a component is four steps, always the same ones: extend, register with the macro, the two-argument constructor, and the phases
The phases are virtual methods that UVM calls in order: build_phase (top-down), connect_phase, end_of_elaboration_phase, run_phase, report_phase
Components get instantiated in the build_phase and nowhere else
Every run_phase runs in parallel, each one in its thread. None of them decides on its own when the simulation ends: that is the objections
There are two super.build_phase(): uvm_component’s and your base class’s. Always put it in, unless you can name why in your case it is a no-op
Notes: The unit that turns the testbench into something UVM can walk, and with that the tools that did not exist before show up: print_topology() shows the tree, and the uvm_config_db can use paths because now there are paths. The super.build_phase() deserves the pass we gave it because it is the most repeated question in the forums. What has to be said out loud is the asymmetry: not calling it switches off the automatic assignment of the fields registered with `uvm_field_*, and that does not give an error, it gives a default. This course does not use those macros and that is why it can skip it; the student who lands in somebody else’s testbench does not know whether they can, so they put it in. What is not valid is doing half of each.

## Slide 157
The env: structure and stimulus
Two things that change for different reasons
A testbench has structure —which components there are and how they connect— and stimulus —what gets sent to the DUT—
They change for different reasons and at different rates: the structure changes when the design changes; the stimulus, every time you write a test
Up to the components they are glued together: add_test is a copy of random_test with one line changed. Ten tests are ten copies, and one change in the structure is ten edits
This section splits them into two classes: the uvm_env keeps the structure, the uvm_test keeps the stimulus
And the piece that makes it possible is the factory: the env asks for a generic base_tester, and each test tells the factory which one to hand over
Notes: Hinge section of the course, and the sentence to leave behind is this one: what changes together goes together, what changes separately goes separately. Everything that comes afterwards —agents, sequences— is this same operation applied to something else. If the group is going slowly, this is the unit where it is worth spending whatever time is left over, even if it has to be taken from somewhere else. A student who does not understand why the env and the test are two classes is not going to be able to read any production testbench, because they are all built like this. The question to start with, before showing one line of code: if tomorrow the design adds a second interface, how many of your ten tests have to be touched? None, if the structure lives in a single place. All ten, if each test assembles it.

## Slide 158: The env: structure and stimulus
Intractable vs. adaptable
“Playing football is very simple, but playing simple football is the hardest thing there is.” — Johan Cruyff
The same move: tangled and simple

## Slide 159
Intractable is the code that comes out fast and afterwards will not let itself be touched. The criterion is not aesthetic: somebody else is going to modify it, and that somebody is going to be you a year from now, remembering nothing
Three rules to turn the VTALU TB around: one class, one thing; nothing hardcoded; program against the interface, not against the implementation
Notes: Swap football for testbench and Cruyff’s line is the whole unit. The three rules sound like an office poster until you measure them, so it is worth landing them on the testbench in front of them: One class, one thing — the random_test of the components does two: it assembles the structure and it picks the stimulus. That is why it has to be copied to make add_test. Nothing hardcoded — tester_h = new(...) nails the type into that line. The type_id::create() does not. Against the interface — the env is going to ask for a base_tester, which is an abstract class: it neither knows nor cares which one arrives. And an honest warning, because at work this gets abused: adaptable code does not mean code prepared for everything. Every point of flexibility is paid for in indirection, and the indirection is paid for at three in the morning. What gets separated is what has already been shown to change — and here it has been shown: there are two tests and there is already copy and paste.

## Slide 160: The env: structure and stimulus
The problem: two tests, the same build_phase() twice
random_test and add_test write the same build_phase()

## Slide 161
Today there are two tests: random_test builds a random_tester, add_test an add_tester. Everything else —coverage and scoreboard— they build the same way
add_test inherits from random_test and rewrites its whole build_phase(): the three new() calls are identical and written twice
The testers, on the other hand, duplicate nothing: add_tester extends random_tester and only overrides get_op(). The run_phase() is written once, in random_tester, and it is inherited
Which means: the inheritance ladder is already solved well below, in the testers, and solved badly above, in the tests. The next two slides show how it came out below; the rest of the section applies it above
Duplicating the build_phase is not ugly, it is expensive: ten tests are ten copies, and one change in the structure is ten edits
Notes: This is the problem slide, and it is worth not jumping ahead to the solution: let the duplication be seen first, and let it be seen where it is. It is not in the testers —those already inherit properly— but in the tests, which is where nobody looks for it. The question that orders the next two slides: which part of a tester is the test, and which part is infrastructure? The get_op() is the test —four lines—; all the rest is infrastructure that has nothing to do with what you want to prove. And the general criterion, which holds for any language: when two sibling classes share an identical method, the method is in the wrong place. It goes to the parent.

## Slide 162: The env: structure and stimulus
The way out: an abstract class, and the stimulus in the daughters
abstract base_tester with a shared run_phase() and pure virtual methods

## Slide 163
base_tester is an abstract class: it writes the run_phase() a single time —a thousand operations— and assembles it by calling get_op() and get_data()
Those two methods are pure virtual, so the class cannot be instantiated and every daughter is forced to define them. The one that forgets does not compile
But there is still repeated code: both testers randomize the operands the same way, and that is a sign that a step is missing in the hierarchy
Notes: This is where polymorphism gets collected: base_tester is an abstract class with pure virtual methods, that is, the run_phase() is written a single time and the daughters are forced to define get_op() and get_data(). If one forgets, it does not compile — which is the whole argument of that unit. And along the way the trap of the day 2 exercise gets fixed: here get_op() is virtual, because it is pure virtual. Worth going back two days and showing it. The bullet that matters is the last one, and it is the one that pushes into the next slide: the two testers still randomize the operands the same way. Two sisters sharing code is a sign that a step is missing in the hierarchy — and the step is that add_tester should not inherit from base_tester but from random_tester.

## Slide 164: The env: structure and stimulus
The result: the three-storey hierarchy
random_tester as the base and add_tester inheriting from it

## Slide 165
base_tester puts in the run_phase() and declares get_op() and get_data() as pure virtual. Nobody instantiates it
random_tester goes down one step and defines both: random operation, random operands
add_tester inherits from random_tester, not from base_tester: it keeps the random operands and only redefines get_op()
And the same step works for all the ones that come: xor_tester, mult_tester, maxmult_tester. Each one, one useful line
Notes: The jump to point out is the third arrow: add_tester does not inherit from the abstract one, it inherits from the concrete one. It is counter-intuitive the first time and it is the decision that makes a new test cost four lines. The rule, said in a way that sticks: you inherit from whoever has what you do not want to write again. Not from the one that “conceptually corresponds”. And the hook backwards: this is polymorphism used for real. pure virtual in the parent is what guarantees that no tester forgets to define get_op() — and if it forgets, it does not compile.

## Slide 166
The env: structure and stimulus
add_tester
The result is that add_tester is very simple: it inherits from random_tester and only redefines get_op()
class add_tester extends random_tester; `uvm_component_utils(add_tester) function operation_t get_op(); return add_op; endfunction : get_op function new(string name, uvm_component parent); super.new(name, parent); endfunction : new endclass : add_tester
Notes: This is the slide of the section worth leaving on screen for a while: a whole test of the VTALU is four useful lines. Everything else —sending a thousand operations, randomizing operands, talking to the BFM— is already written and does not get touched. The rule you take away: if adding a test costs four lines, you are going to write many. If it costs copying a class of sixty, you are going to write three and then invent excuses. The coverage of the project is decided here, not in the covergroup. And the question that orders the hierarchy: why does add_tester inherit from random_tester and not from base_tester? Because it wants the random operands and only changes the operation. Inheritance is not chosen by conceptual likeness, it is chosen by what you do not want to write again.

## Slide 167: The env: structure and stimulus
The other half: who instantiates whom
The testers are already well distributed. The other half is missing: who instantiates them
The obvious way out is a family of uvm_test, one per tester. And it is the bad one: look at the random_test below
It instantiates the three components and it picks the tester. Every new test copies that whole structure to change one line
class random_test extends uvm_test; `uvm_component_utils(random_test); random_tester tester_h; coverage coverage_h; scoreboard scoreboard_h; // Components get instantiated in build_phase, never in the constructor. function void build_phase(uvm_phase phase); tester_h = new("tester_h", this); coverage_h = new("coverage_h", this); scoreboard_h = new("scoreboard_h", this); endfunction : build_phase function new(string name, uvm_component parent); super.new(name, parent); endfunction : new // No run_phase: the test's job ends once the tree is built. endclass
The random_test does two things: it assembles the structure of the testbench and it picks which stimulus to send. They are two reasons to change in a single class
UVM splits that in two: the structure moves to a uvm_env, and the test is left only with picking the stimulus
A typical env defines two methods and nothing else: build_phase to instantiate and connect_phase to connect
Notes: It is worth doing the arithmetic out loud, because the problem is easier to see with numbers than with the design argument: if every test instantiates its three components, with ten tests there are ten build_phase saying the same thing. The day a fourth component is added to the testbench, that is ten edits — and the one you forget does not fail at compile time, it simply runs without that component. uvm_env is not magic and it does not bring new behaviour: it is a uvm_component with another name. What it contributes is convention: when somebody opens a testbench that is not theirs, they know the structure is in the env. That is half the value of UVM and it is worth saying it that bluntly — it is not the library, it is that everybody puts the things in the same place. Good question: why does the env almost never have a run_phase? Because it neither sends nor watches anything; it only builds and connects. If your env has a run_phase, it is a sign that test logic got inside the structure.

## Slide 168: The env: structure and stimulus
The map after splitting
The class diagram before and after splitting structure from stimulus with uvm_env

## Slide 169
Two parallel hierarchies, and that is the whole section: on the left the tests —the stimulus—, on the right the env and its components —the structure—
The env is a single one and it does not get touched. The tests are many and they change all the time
The only thing that binds them is the factory: the test says “when they ask for a base_tester, give them this one”
Notes: Worth leaving the diagram on screen and asking them to place where each class of the components ended up. The exercise makes it obvious what disappeared: there is no longer a build_phase per test instantiating three components. The control question: if tomorrow the testbench adds a fourth component, how many files get touched? One, the env. With the structure of the components it was as many as there were tests.

## Slide 170
The env: structure and stimulus
The env class: instantiate and connect, nothing else
The env defines the structure of the testbench: it instantiates the components and then connects them. It is a single one, and it does not change from one test to another
The tests, on the other hand, are many and they change all the time. That is the whole division
The build_phase() does not use new(): each component gets asked for with type_id::create(), which is the factory formula of the next slide
// The structure of the TB, and nothing else: it instantiates the components and // connects them. Which tester arrives is the test's call, with a factory override. class env extends uvm_env; `uvm_component_utils(env); base_tester tester_h; coverage coverage_h; scoreboard scoreboard_h; function void build_phase(uvm_phase phase); // base_tester is abstract and this works anyway: create() does not build // it, it asks the factory what to hand out when somebody asks for a base_tester. tester_h = base_tester::type_id::create("tester_h", this); coverage_h = coverage::type_id::create("coverage_h", this); scoreboard_h = scoreboard::type_id::create("scoreboard_h", this); endfunction : build_phase function new(string name, uvm_component parent); super.new(name, parent); endfunction : new endclass
Notes: Hinge section of the course: separating WHAT structure the testbench has (env) from WHAT stimulus gets sent (test). Everything that comes afterwards —agents, sequences— is this same idea taken further. If the group is going slowly, this is the slide where it is worth spending whatever time is left over.

## Slide 171: The env: structure and stimulus
UVM’s factory: the class signs itself up
The factory had two annoyances: the result had to be cast, and the case of the factory had to be edited to add a type
UVM’s has neither of the two. A class registers itself, with a macro on its first line:
  `uvm_component_utils() for what goes in the tree
  `uvm_object_utils() for what does not —the transactions—
And it returns an object of the right type, without casting: type_id is a different class for every registered class, so the type is put in by the compiler
Notes: The macro is what replaces the case of the hand-written factory: each class signs itself up in the dictionary, and adding a type does not force you to edit the factory. The difference between the two macros is the one that gets collected in the transactions, and it is worth planting now: uvm_component_utils is for what lives in the tree and receives phases; uvm_object_utils is for what travels —a piece of data— and receives none. Picking the wrong one compiles and gives strange errors later. Not having to cast is not cosmetic: the $cast of the factory could be forgotten, and forgetting it was a null pointer in simulation.

## Slide 172: The env: structure and stimulus
The formula, read from left to right
Anatomy of the line type::type_id::create(name, this)

## Slide 173
It is the static member/method pattern of the static variables, exactly as it is: type_id is a static member of the class, and create() a static method of that member
The two arguments are the usual ones: the name that is going to come out in the topology, and the parent that hangs it from the tree
The misspelt class and the one that does not exist show at compile time. The one that forgot the `uvm_component_utils only if no ancestor is registered: if it extends a registered one, the type_id is inherited and there is no error
Notes: Worth reading the formula out loud once, slowly, because it is going to be written fifty times in what is left of the course: “class, colon colon, type_id, colon colon, create, name, this”. The last bullet is the one that is not reassuring, and it should be said that way. If base_tester was not registered and nothing above it was either, base_tester::type_id does not exist and it does not compile: that is the good case. But in this very section’s hierarchy —the three of them registered— forgetting the macro in add_tester breaks nothing: the type_id and the get_type() are inherited from random_tester, the testbench compiles clean, and the set_type_override of add_test ends up registering random_tester. Measured: add_tester::get_type().get_type_name() returns random_tester, the env builds a random_tester, and the test runs with UVM_ERROR : 0. It belongs to the “does not break, lies” family of the silent-traps appendix: the only case where it does fail to compile is if the handle is declared of the derived type, and here the handle is base_tester tester_h;. The name of the first argument is not decorative: it is the path of the component, the one the config_db uses and the one print_topology prints. Giving it a name other than the handle’s is a cheap way of losing half an hour in the agents.

## Slide 174: The env: structure and stimulus
The objection that comes on its own: base_tester is abstract
Now the objection that comes on its own: tester_h is of type base_tester, which is an abstract class. And this compiles, runs and works. Why?
function void build_phase(uvm_phase phase); // base_tester is abstract and this works anyway: create() does not build // it, it asks the factory what to hand out when somebody asks for a base_tester. tester_h = base_tester::type_id::create("tester_h", this); coverage_h = coverage::type_id::create("coverage_h", this); scoreboard_h = scoreboard::type_id::create("scoreboard_h", this); endfunction : build_phase
Because base_tester here is not a mould: it is an order form. The env does not build a base_tester, it asks the factory for one
The factory returns an object of some derived class, and which one is decided by a set_type_override done before the build_phase runs
That override is done by the test, which is the one that instantiates the env. The structure never finds out which tester it got
Notes: The objection on the slide is correct and it has to be taken seriously, because otherwise it looks like a dirty trick: base_tester is abstract and that code does compile and run. The explanation in one line: type_id::create() does not build a base_tester; it asks the factory what to build when somebody asks for a base_tester, and returns that. The analogy that works: base_tester here is not a mould, it is an order form. Nobody instantiates the form. The corollary, which is the one paid for later: if no test did the override, the factory really does try to build the abstract class and there it really does explode — and the message does not say “you were missing the override”, it says something about an abstract class. Worth showing it once by commenting out the set_type_override of random_test.

## Slide 175: The env: structure and stimulus
The override: changing the part without touching the plan
In the components, add_test was random_test copied with one line changed. The copy was the problem, not the solution
An add_tester is a base_tester, so it works anywhere the code asks for a base_tester — that is polymorphism
So there is no need to touch the env: it is enough to tell the factory “when they ask you for a base_tester, hand over an add_tester”
That is the factory override, and it is the only thing a test has to do
Notes: The sentence that orders the slide: the override does not change the code, it changes what the factory returns. The env still says exactly the same thing. It is worth naming the two forms that exist, because both show up in code that is not yours: set_type_override changes every request for that type in the whole testbench; set_inst_override changes only the ones on one path — "uvm_test_top.env_h.tester_h", absolute—. The course uses the first because there is a single tester; with two agents, the second is the one that helps, and it has its slide two further on. And the hook forward: it is exactly the mechanism that in the transactions is going to replace a command_transaction with a maxmult_transaction. Same call, another type.

## Slide 176: The env: structure and stimulus
The factory override
Anatomy of the factory override with set_type_override()

## Slide 177
The static method set_type_override() tells the factory that when it sees a request for a base_class_name it should return an object of type new_class_name
This feature is the one that lets us separate the structure of the TB (uvm_env) from the type of stimulus generated (uvm_test)
Notes: The override is what makes the env never change: the test asks for a base_tester and the factory returns whichever one that test wants. When somebody asks whether this is not black magic: it is a dictionary of types, and that is why everything has to be registered with `uvm_component_utils. If you forget it, the factory does not find the class and the error message does not help at all.

## Slide 178: The env: structure and stimulus
The factory override, in the test
class random_test extends uvm_test; `uvm_component_utils(random_test); env env_h; function void build_phase(uvm_phase phase); base_tester::type_id::set_type_override(random_tester::get_type()); env_h = env::type_id::create("env_h", this); endfunction : build_phase function new(string name, uvm_component parent); super.new(name, parent); endfunction : new endclass
We can see that this version is more adaptable
Every test does an override of base_tester depending on the tester it needs for its stimulus
The env class creates the object; running it is UVM’s job
Now the test class does one thing well (generating stimulus) and the env class does another thing very well (creating the structure)
Notes: The whole test is two lines: the override and the create() of the env. Worth showing it next to the random_test of the components, which instantiated three components by hand. That is the result of the section, measured. And there is a detail of order that is paid for dearly and that is worth saying now, because it comes back as question 5 of the review: the set_type_override() goes before the create() of the env. The factory decides what to build at the moment of the create(), not before and not after. If the override arrives late, there is no error — the env has already built the base class and the test runs with the wrong stimulus. The same thing again: it does not break, it lies. With that the arc is said: the env never changes, the test always changes, and the only thing that binds them is a type string in the factory.

## Slide 179: The env: structure and stimulus
By instance, and the knob for seeing what got set
base_tester::type_id::set_type_override(add_tester::get_type()); // ALL of them base_tester::type_id::set_inst_override(mult_tester::get_type(), "uvm_test_top.env_h.t2_h"); // just one uvm_coreservice_t::get().get_factory().print(0); // which overrides are in place
Instance Overrides: Requested Type Override Path Override Type base_tester uvm_test_top.env_h.t2_h mult_tester base_tester env_h.t3_h mult_tester <- registered and did NOT apply Type Overrides: base_tester add_tester
set_inst_override changes one path, not a type. And where the two coincide, the instance one wins
The path is absolute and starts at uvm_test_top. Measured: "env_h.t3_h" gets registered all the same, gives no error, and t3_h comes out an add_tester
factory.print(0) is the counterpart of uvm_top.print_topology(): one says what you asked for, the other what came out. When they do not match, the bug is in between
With * it works: "*.env_h.t4_h" applies. It is the workaround when the test does not know where it is going to be instantiated
Notes: It is the second half of the override and the one that shows up as soon as there are two agents of the same type: you do not want to change both, you want to change one. The path trap has to be said with the measurement’s number, because it is exactly the way this mechanism fails: the override with the badly written path gets registered all the same. factory.print(0) shows it in the table, tidy, as if it were working. There is no warning, there is no error, and the component comes out of the base type. It is the same family as the late set_type_override of the traps appendix: the factory does not validate paths because it cannot — when the override is registered, the component does not exist yet. The practical rule: the path is the one uvm_top.print_topology() prints, without the <unnamed> at the top. If the tree says uvm_test_top.env_h.t2_h, that is what goes between quotes. And if you do not want to depend on where they instantiate you, *.env_h.t2_h, which is also measured and also applies. The pair of tools is what to take home: factory.print(0) says what the factory has written down, print_topology() says what actually got built. An override that shows up in the first and is not visible in the second is a badly written path or a create() that arrived first.

## Slide 180: The env: structure and stimulus
Summary of the unit
A testbench has structure —which components there are and how they connect— and stimulus —what gets sent—. They change for different reasons and at different rates
Up to the components they were glued together: add_test was a copy of random_test with one line changed. Duplicating the loop is not ugly, it is expensive
The uvm_env keeps the structure; the test only says which stimulus it wants. A new test stops touching the env
The piece that makes it possible is the factory: the env asks for a base_tester and the test decides which one arrives, with set_type_override
The abstract class base_tester has the run_phase written a single time; the only thing each tester redefines is get_op() and get_data()
The three rules for writing adaptable code: one class, one thing; no copying and pasting structure; and programming against the base class
Notes: It is the unit where all of day 2 gets collected. It is worth making it explicit by pointing at the add_test: it is two lines —the override and nothing else—, and it changes the whole stimulus without touching the env. That could not be done in the object-based testbench. The intractable / adaptable distinction is the one to leave as vocabulary, because it comes back with the agent and with the sequences. Intractable code is the one that comes out fast and afterwards will not let itself be touched: almost always it is duplicated structure.

## Slide 181
Reporting
47 % of the time goes here
The day-1 trends chart said that almost half of a verification engineer’s time goes into debug. This section is about that half
A scoreboard that only says FAIL leaves you right there: you know something is wrong and you do not know which component, at what moment, or with what data
The natural reaction is to fill the code with $display, and then delete them. And put them back next week
UVM solves it the other way round: the messages stay in and get filtered. Each one brings along the time, the hierarchical path of the component and the file
And there are two different knobs, which get confused all the time: verbosity filters `uvm_info; the actions control warnings, errors and fatals
Notes: It is worth going back to the day 1 chart before starting, because this section looks like plumbing and it is the one that returns the most hours. The argument is not “nice messages”: it is that a message that brings along the hierarchical path saves you the question “who said it?”, which is half of any debug. The second idea, which is the one that costs: debug messages do not get deleted. A `uvm_info at UVM_HIGH costs nothing when the ceiling is at UVM_MEDIUM, and the day you need it, it is there. That the day 5 exercise gets solved by raising the verbosity is no coincidence — it is set up so that they live it. And the distinction on the last line is worth writing on the board from the start, because it is question 6 of the review: verbosity and info on one side, actions and error/warning/fatal on the other. They never cross.

## Slide 182: Reporting
What $display cannot do
A thousand operations per test, dozens of tests per regression: one $display per transaction and the log stops being readable before the first coffee
And with $display the only way of lowering the noise is deleting lines, that is, losing exactly what you are going to need next time
UVM replaces the $display with four macros that bring two things for free: context —time, component, file— and a filter that is driven from outside
Notes: The question that orders the slide, and it is worth throwing it at the group before the answer: what is wrong with $display? The answer that always comes is “it is ugly”, and it is not that one. $display prints or does not exist: the decision of whether a message comes out is taken at the moment of writing it, by editing the code. What UVM adds is not format, it is that the decision moves to the moment of running, and it is taken from outside with a plusarg. That change of moment is the whole section: that is why the messages can be left in place, and that is why the log of a regression and the log of a debug can come out of the same binary. The piece of context, for whoever comes from VHDL or plain Verilog: none of this is simulator magic. `uvm_info is a macro that assembles a string and hands it to an object —the report server— that decides what to do. Everything that follows in the section is configuring that object.

## Slide 183: Reporting
The reporting macros
There are four and they differ by severity: `uvm_info, `uvm_warning, `uvm_error and `uvm_fatal. All four are counted in the Report Summary; what changes is the default action — `uvm_error comes with UVM_DISPLAY|UVM_COUNT and `uvm_fatal also kills the simulation
The ID is the first argument: a string that says who is talking. It is what you filter with afterwards, so it is worth making it the name of the component and always the same one
The message is the second, and it gets assembled with $sformatf when it carries data
The verbosity is the third, and only `uvm_info has it: it is the one that decides whether the message comes out or not
// ILLUSTRATION -- not compiled. The signature of each macro, not a call. `uvm_info (Message ID String, Message String, Verbosity) `uvm_warning(Message ID String, Message String) `uvm_error (Message ID String, Message String) `uvm_fatal (Message ID String, Message String)
Notes: The usual confusion: verbosity filters `uvm_info, and nothing else. The warnings, errors and fatals have no verbosity — they are controlled with actions, which is the last part of the section.

## Slide 184: Reporting
The reporting macros: what each one does
This is how it looks in the scoreboard: a `uvm_error when the comparison fails, with the message assembled with $sformatf
And this is how it comes out in the log. Look at what the line brings without anybody asking for it: the time, the file and the line, and the hierarchical path of the component that spoke
data_str = $sformatf( " %2h %0s %2h = %4h (%4h predicted)", cmd.A, cmd.op.name(), cmd.B, t, predicted_result ); if (predicted_result != t) `uvm_error("SCOREBOARD", {"FAIL: ", data_str}) else `uvm_info("SCOREBOARD", {"PASS: ", data_str}, UVM_HIGH)
UVM_ERROR tb_classes/scoreboard.svh(39) @ 290: uvm_test_top.env_h.scoreboard_h [SCOREBOARD] FAIL: 5b add_op ff = 015a (015b predicted)
Notes: Worth stopping on the log line and reading it out loud from left to right, field by field, because it is the one the student is going to look at a thousand times and nobody ever explains it: severity, time, file and line of the `uvm_error, and then uvm_test_top.env_h.scoreboard_h — the instance path. Only then comes the ID and the message. The pedagogical point is what is not in the code: the scoreboard did not print the time or its own name. The macro put them in. That is the whole argument in favour of never writing a $display in a testbench again. And the honest comparison with the $error of day 2: that scoreboard also made the test fail, but the context had to be written by hand — and there nobody writes the hierarchical path, because they do not know it.

## Slide 185: Reporting
The six levels, and why the message stays
The usual cycle: you fill the code with $display, you find the bug, you delete everything — and next week you write it again
With verbosity the messages stay in place and do not get in the way. It is two steps, and the second one does not touch the code:
  put a verbosity on each `uvm_info, according to how much noise it is
  set the ceiling of the run: global, or per branch of the tree
A message comes out if its verbosity is less than or equal to the ceiling. That is why UVM_NONE always comes out
// ILLUSTRATION -- not compiled. uvm_object_globals.svh:382-390, uvm-core 2020.3.1, // copied verbatim: code/.uvm/ is downloaded and gitignored, so the slide cannot // pull the enum straight out of the library. typedef enum { UVM_NONE = 0, UVM_LOW = 100, UVM_MEDIUM = 200, // the default: with nothing set, UVM_MEDIUM is what you get UVM_HIGH = 300, UVM_FULL = 400, UVM_DEBUG = 500 } uvm_verbosity; // Any message above the verbosity that was set does not get printed
Notes: The six levels, from least to most noisy: UVM_NONE, UVM_LOW, UVM_MEDIUM —the default one—, UVM_HIGH, UVM_FULL and UVM_DEBUG. UVM_FULL is the one nobody uses and the one that shows up in the enum on the slide, so it is worth naming. A message gets printed if its verbosity is less than or equal to the ceiling, so UVM_NONE always comes out. The rule of thumb worth handing down, because otherwise everybody invents their own: UVM_LOW for what you want to see in a regression —which test ran, how many transactions—; UVM_MEDIUM for the summary of a component; UVM_HIGH for every transaction that goes past. The monitors of the course are UVM_HIGH precisely for that: in a normal run they are not seen, and when something fails they get switched on with a plusarg. The formal detail that gets copied wrong: the verbosity is the third argument of the `uvm_info, and if you forget it, it does not compile. The ID —the first one— is a free string, but do not pick it at random: it is the key you are going to filter with afterwards. Make it the name of the component, in capitals, and always the same one.

## Slide 186: Reporting
The global ceiling: a plusarg, without recompiling
It gets set in two ways, and the first one is the one used every day: a plusarg on the command line
No code to touch and no recompiling. The same binary gives the log of the regression and the log of the debug
The problem shows up with the team: if there are ten people with their own debug messages, raising the global ceiling brings you everybody’s
That is why it has to be possible to ask for it per component, which is the next slide
./obj_dir/top/sim +UVM_TESTNAME=random_test +UVM_VERBOSITY=UVM_HIGH
Notes: Worth running it live, because it is the cheapest demonstration of the section: the same line above —./obj_dir/top/sim +UVM_TESTNAME=random_test— with and without +UVM_VERBOSITY=UVM_HIGH, and the log goes from 7 uvm_info to 22. With make they are 6 and 21, because run_sim adds +UVM_NO_RELNOTES and that takes the banner away. Without recompiling anything — it is the same binary. They look like few because this example sends ten operations on purpose, so the transcript fits on the screen; with the thousand of the other sections the difference is three orders of magnitude. The detail that has to be said so that it does not surprise anybody later: the plusarg sets the ceiling of the whole tree, from uvm_top down. There is no way of asking for “high, but only the monitor” from the command line with this flag; for that there is +uvm_set_verbosity, which is longer to type and almost nobody remembers. The honest way out, and the one the next slide teaches, is setting it from the code in the component you care about. And the underlying argument, in case the group underrates it: this is the mechanism that makes a regression log of a thousand tests readable. It is not classroom cosmetics.

## Slide 187: Reporting
uvm_cmdline_processor: the command line, whole
+UVM_VERBOSITY and +UVM_TESTNAME are not read by magic: they are read by a class, and it is available for your own plusargs
uvm_cmdline_processor clp = uvm_cmdline_processor::get_inst(); string valor; if (clp.get_arg_value("+COUNT=", valor)) count = valor.atoi();
It is a singleton: get_inst() from any class, without building anything and without passing it through the config_db
get_arg_value returns how many times the argument appeared, not the value: the value comes out through the ref. If it appeared twice you find out — $value$plusargs keeps quiet with the first one
And there are get_args(), get_plusargs() and get_uvm_args(), which return the whole command line in a queue: it is how you print under what conditions a regression from three months ago ran
Notes: The course uses $value$plusargs and $test$plusargs in the base_test because they are one line and they read themselves. Worth saying why in a production testbench this class always shows up: $value$plusargs is a system task, so it cannot be inherited, it cannot be substituted by the factory and it cannot be tested. The uvm_cmdline_processor is an object, and that is enough for the three things. The argument that pays off most is the last bullet and it is not the one you would expect: get_args() printing the whole line in the start_of_simulation_phase is what turns an old log into something reproducible. Without that, the log says what happened but not what it was run with, and a regression from three months ago cannot be repeated. The difference in the second bullet is worth an anecdote: two +COUNT= on the same line —because the script adds them and the user does too— is a real case, and $value$plusargs takes one without saying which. The uvm_cmdline_processor returns 2, so at least you can notice. It is the kind of thing you pay for once and remember.

## Slide 188: Reporting
The ceiling per branch: two methods and a tree
Every uvm_component comes with methods to set its own ceiling, in two flavours: only itself, or itself and everything hanging below (_hier)
Careful about which hierarchy it is: it is not the DUT’s module one. It is the tree that UVM assembles by calling build_phase() from the top down
It is the same tree the prefix of each message comes out of, and the same one the uvm_config_db uses as a scope
Instance hierarchy UVM builds in build_phase

## Slide 189
Notes: This diagram is worth more than it looks, because it explains where that very long prefix each message brings comes from: uvm_test_top.env_h.scoreboard_h. It is not decoration — it is the instance path of the component that spoke. And it is the same path the uvm_config_db uses for the scope. Worth saying it explicitly: when in the tests we said “the scope is a hierarchical path”, it was literally this path. A single tree serves both purposes. The clarification in the bullet is not a detail: this hierarchy is not the DUT’s. A scoreboard is not inside any module. It is the tree UVM assembles by calling build_phase from the top down, and it exists only in the testbench. Classroom trick: uvm_top.print_topology() prints this tree for real, written by the library. It is the best way of showing that it is not a drawing. +UVM_CONFIG_DB_TRACE is a different thing and it is better not to mix them: it does not draw the tree, it traces every set() and every get() of the config_db with the scope that was used — which is the knob for the other problem, the scope that does not match.

## Slide 190: Reporting
The ceiling per branch: where the call goes
The call goes after the hierarchy exists —otherwise the component is not there yet— and before the simulation starts
That window has a name and it is one of the nine phases: end_of_elaboration_phase
set_report_verbosity_level_hier() reaches the component and its children; set_report_verbosity_level(), only it
// To use the UVM hierarchy to control verbosity, the reporting methods have to // be called after the UVM hierarchy has been built, but BEFORE the simulation // starts. That is what end_of_elaboration_phase is for function void end_of_elaboration_phase(uvm_phase phase); //scoreboard_h.set_report_severity_action_hier(UVM_ERROR, UVM_NO_ACTION); scoreboard_h.set_report_verbosity_level_hier(UVM_HIGH); endfunction : end_of_elaboration_phase
Notes: The window is what has to be left burned in, because the mistake gets made in both directions. If the call goes in the build_phase, the component whose ceiling you want to raise does not exist yet —its parent builds it further down— and the call finds nobody. If it goes in the run_phase, the simulation has already started and you missed the messages of the earlier phases. end_of_elaboration_phase is exactly the gap between the two things: the whole tree, and the time still at zero. It is the first time in the course that it gets used for anything, and it is worth saying it that way — in the table of the nine phases of day 3 it was not decoration. The _hier suffix is the one that gets forgotten, and it fails silently: you set the ceiling of the env without _hier, the env prints nothing anyway, and the monitor you wanted to hear stays quiet. Rule of thumb: if you are aiming at a branch, _hier; if you are aiming at a class, without.

## Slide 191: Reporting
Switching off warnings, errors and fatal messages
A real situation: the DUT is fine, the scoreboard predicts the addition wrong, and the class is being fixed by somebody else. You need to carry on working in the meantime
Lowering the verbosity ceiling does not help: it only affects `uvm_info, and what has to be silenced is a `uvm_error
Another knob is needed
UVM_INFO @ 0: reporter [RNTST] Running test random_test... UVM_INFO tb_classes/scoreboard.svh(40) @ 150: uvm_test_top.env_h.scoreboard_h [SCOREBOARD] PASS: 43 and_op ff = 0043 (0043 predicted) UVM_ERROR tb_classes/scoreboard.svh(39) @ 290: uvm_test_top.env_h.scoreboard_h [SCOREBOARD] FAIL: 5b add_op ff = 015a (015b predicted) ... --- UVM Report Summary --- ** Report counts by severity UVM_INFO : 4 UVM_WARNING : 0 UVM_ERROR : 2 UVM_FATAL : 0 ** Report counts by id [RNTST] 1 [SCOREBOARD] 5 - $UVM_HOME/src/base/uvm_root.svh:633: Verilog $finish - S i m u l a t i o n R e p o r t: Verilator 5.052 2026-09-05 - Verilator: $finish at 820ps
Notes: The log on the slide is that of a scoreboard that adds wrong on purpose, and it is worth looking at the Report Summary at the end before the error: UVM_ERROR : 2, one for each add_op that came up in the ten operations of the example. That is the sum to do out loud: with the thousand operations of the other sections it is a hundred-odd errors, one per addition. That is the real problem the section comes to solve — not “the message is annoying”, but that the log stops being any use for looking for something else. The question to throw at the group, because the wrong answer is the intuitive one: “I lower the verbosity ceiling and that is it?”. No. A `uvm_error has no verbosity; the ceiling does not touch it. It is the same distinction as the first slide, and here it gets collected for the first time. And the honest clarification before teaching how to switch off errors, because otherwise it sounds odd: this is not so that the regression comes out green. It is to be able to work half an afternoon while somebody else fixes their class, and it comes out the same day.

## Slide 192: Reporting
Switching off messages: where it gets done
Warnings, errors and fatals are immune to the verbosity ceiling, and it is right that they should be: nobody wants to switch off an error by accident
The knob that does reach them is called actions, and it answers another question: not “does it get printed?” but “what gets done with this message?”
Printing is only one of the seven possible things
// ILLUSTRATION -- not compiled. uvm_object_globals.svh:354-364, uvm-core 2020.3.1, // copied verbatim: code/.uvm/ is downloaded and gitignored, so the slide cannot // pull the enum straight out of the library. typedef enum { UVM_NO_ACTION = 'b0000000, UVM_DISPLAY = 'b0000001, UVM_LOG = 'b0000010, UVM_COUNT = 'b0000100, UVM_EXIT = 'b0001000, UVM_CALL_HOOK = 'b0010000, UVM_STOP = 'b0100000, UVM_RM_RECORD = 'b1000000 } uvm_action_type;
Notes: The seven actions are a bitwise OR, not a list of mutually exclusive options: the same message can be printed and written to a file and counted towards the summary. That is why they combine with |. UVM_COUNT is the one most often explained wrong, and it is worth saying it in full: it is already switched on by default on every `uvm_error, and what it increments is a global counter for the run, not one per ID. On its own it kills nothing, because the default maximum is 0, which means “no limit”. The one that cuts is +UVM_MAX_QUIT_COUNT=N (uvm_root.svh:1187) —or set_report_max_quit_count(N), uvm_report_object.svh:578—, and that one really is the answer to the four-gigabyte log when a scoreboard fails on every transaction: you find out anyway, and in thirty seconds instead of in twenty minutes. UVM_NO_ACTION is the one the next slide uses to switch off the errors, and it has to be said out loud what it is not for: it is not so that the regression comes out green. It is to carry on working while somebody else fixes their class, and it comes out the same day. A UVM_NO_ACTION that survives a commit is a bug waiting to happen. And the pair worth naming: set_report_severity_action is by severity, set_report_id_action is by that ID string you picked when writing the message. That is where the discipline of having always used the same one gets paid back.

## Slide 193: Reporting
Switching off messages: the complete example, and the log you are left with
set_report_severity_action_hier(UVM_ERROR, UVM_NO_ACTION) on the scoreboard: when an error shows up in there, do nothing
It goes in the end_of_elaboration_phase of the env, for the same reason as the hierarchical verbosity
And the log below is the result: same DUT, same broken scoreboard, zero errors in the Report Summary
In code/u4/reporting the line is written and commented out: you uncomment it to reproduce this log, and comment it back. That it lives commented out in the repo is part of the lesson
// To use the UVM hierarchy to control verbosity, the reporting methods have to // be called after the UVM hierarchy has been built, but BEFORE the simulation // starts. That is what end_of_elaboration_phase is for function void end_of_elaboration_phase(uvm_phase phase); //scoreboard_h.set_report_severity_action_hier(UVM_ERROR, UVM_NO_ACTION); scoreboard_h.set_report_verbosity_level_hier(UVM_HIGH); endfunction : end_of_elaboration_phase
UVM_INFO @ 0: reporter [RNTST] Running test random_test... --- UVM Report Summary --- ** Report counts by severity UVM_INFO : 1 UVM_WARNING : 0 UVM_ERROR : 0 UVM_FATAL : 0 ** Report counts by id [RNTST] 1 - $UVM_HOME/src/base/uvm_root.svh:633: Verilog $finish - S i m u l a t i o n R e p o r t: Verilator 5.052 2026-09-05 - Verilator: $finish at 820ps
Notes: Say it out loud: switching off errors is for carrying on working while somebody else fixes their class, not so that the regression comes out green. And showing the Report Summary of the second log next to the first one is the best warning the section gives: the testbench says 0 UVM_ERROR and the DUT is still exactly as broken as it was when we broke it. That is the reason a UVM_NO_ACTION cannot survive a commit — it is a silent trap, and it is in the appendix. The scoreboard of this section adds too much ON PURPOSE, it is the bug we are showing. That is why code/u4/reporting/run.sh exports UVM_ERRORS_OK=1: by default a uvm_error makes the run fail, and here the error is the example.

## Slide 194: Reporting
uvm_report_catcher: demoting the error you were expecting
UVM_NO_ACTION switches off every error of a branch. When the test verifies the error path on purpose —a PSLVERR that has to arrive— what has to be silenced is one single one, and the rest has to carry on shouting
class demotar_pslverr extends uvm_report_catcher; virtual function action_e catch(); if (get_severity() == UVM_ERROR && get_id() == "PSLVERR") set_severity(UVM_INFO); // stops counting as an error return THROW; // and carries on, already downgraded endfunction endclass demotar_pslverr c = new(); uvm_report_cb::add(null, c); // null = the whole testbench; or a component
The catcher gets in before the report: it sees every message and can change its severity, its ID, its text or its action
THROW lets it carry on already modified; CAUGHT makes it disappear
And the difference that matters: the summary prints Number of demoted UVM_ERROR reports : 1. The blackout leaves a trace, which is what UVM_NO_ACTION does not do
Notes: It is the right answer to the previous slide, and the difference is one of honesty, not of syntax. UVM_NO_ACTION on the scoreboard switches off the error and the log ends up identical to that of a healthy testbench: nobody reading that log finds out. The catcher downgrades that message, lets all the others through, and on top of that counts it on a line of its own in the UVM Report catcher Summary. A reviewer who opens the log sees that there was an error and that somebody decided it was fine. When it really gets used: in the negative tests, which are half of a serious verification plan. Writing to a read-only register has to give PSLVERR; the test that proves it expects the error, and without a catcher that test can never come out green. It is exactly the case of the capstone. The implementation detail that surprises: a catcher is a uvm_callback, that is, the same piece as the callbacks of day 6. That is why it gets registered with uvm_report_cb::add and not with a set_ of the component. And the trap: if the catcher is too wide —by severity and nothing else— you have switched off every error of the testbench with more ceremony than UVM_NO_ACTION. The get_id() of the if is not optional.

## Slide 195: Reporting
Summary of the unit
Two knobs, and they do not cross: verbosity filters `uvm_info; actions decides what gets done with warnings, errors and fatals
Both can be set per component or per branch, in end_of_elaboration_phase
And there is a third one for the expected error: the uvm_report_catcher demotes it and leaves it counted in the summary, instead of switching it off without a trace
With that, debug messages get written once and stay in place for ever — which is the only thing that makes debug cheap
And it arrives here, at the end of day 3, on purpose: it is the tool the exercises of days 4 and 5 get debugged with — the day 5 one is solved by raising the verbosity, and there is no other way of finding it
Notes: Close the day by going back to the 47 %: of everything seen today —tests, components, phases, env— this is the section used every day, and the only one you notice when it is missing. A testbench without reporting works just the same; debugging it costs double. The control question, which is also number 6 of the review: “I lowered the verbosity ceiling and the `uvm_error still shows up, why?”. If the group answers it without hesitating, the section closed. And the warning for the day 5 exercise, worth giving now and not when they are stuck: the bug is not visible in the default log. It is printed, at UVM_HIGH. Whoever does not remember this section is going to read the code for half an hour before raising the verbosity.

## Slide 196
Review · Day 3
1 of 7 · uvm_test
What does +UVM_TESTNAME=add_test let you do that you could not do before?
☒ Pick the test on an already compiled testbench
☐ Run the simulation faster
☐ Change the DUT without recompiling: UVM re-elaborates on start-up
☐ Lower the verbosity of the messages
Pick the test without recompiling — UVM reads that plusarg and asks the factory for the test by name. It is the difference between 1000 tests × 5 minutes of compilation and a single compilation.

## Slide 197
Review · Day 3
2 of 7 · UVM Phases
In what order does UVM walk the hierarchy in build_phase and in connect_phase?
☐ Both from the top down
☐ Both from the bottom up
☒ build_phase top-down, connect_phase bottom-up
☐ In the order the components were declared, from the top down
Build top-down, connect bottom-up — and it makes sense: you cannot connect a component that does not exist yet, so first the whole hierarchy gets built and only then does it get connected.

## Slide 198
Review · Day 3
3 of 7 · Objections
What are raise_objection() / drop_objection() for in the run_phase?
☐ For reporting scoreboard errors
☒ For keeping the simulation alive while there is work
☐ For synchronizing two threads
☐ So that the run_phases of every component start at the same time
So that the phase does not end early — every run_phase runs in parallel, each one in its thread, and the phase ends when the last objection drops. Without raising it, the simulation ends on you at time 0.

## Slide 199
Review · Day 3
4 of 7 · The env
What does each one get: uvm_env and uvm_test?
☐ env generates the stimulus; test assembles the structure
☐ Both do the same thing, env is optional
☐ env runs the DUT; test runs the scoreboard
☒ env assembles the structure; test picks the stimulus
Structure vs. stimulus — each class does one single thing well. That is why the env almost always has only build_phase and connect_phase, and the test almost always has only a factory override.

## Slide 200
Review · Day 3
5 of 7 · Factory override
set_type_override() replaces base_tester with add_tester. When does it have to be called?
☒ Before the build_phase that creates the object runs
☐ At any moment: the factory applies it retroactively to what is already built
☐ After the connect_phase
☐ Inside the run_phase of the tester
Before the build_phase — the factory decides what to build at the moment of the create(). If the override arrives late, the env has already instantiated the base class and it does nothing.

## Slide 201
Review · Day 3
6 of 7 · Verbosity
The verbosity ceiling (+UVM_VERBOSITY=UVM_HIGH), which macros does it act on?
☐ On all four: info, warning, error and fatal
☒ Only on `uvm_info
☐ On error and fatal only
☐ On none: it only changes the format of the message
Only on `uvm_info — warnings, errors and fatals are immune to the verbosity ceiling, and it is right that they should be: nobody wants to switch off an error by accident. For those you need the actions mechanism.

## Slide 202
Review · Day 3
7 of 7 · Report actions
You want to silence the `uvm_error of a scoreboard somebody else is fixing. Where does the set_report_severity_action_hier() go?
☐ In the build_phase of the env
☐ In the run_phase of the test, before raising the objection
☐ In the constructor of the scoreboard
☒ In the end_of_elaboration_phase of the env
In end_of_elaboration_phase — it has to be after the hierarchy is built (otherwise the component does not exist yet) and before the simulation starts. That phase is exactly that window.

## Slide 203
Exercise · Day 3 · 1 of 2
A new test without touching the structure
cd code/ejercicios/d3 && bash run.sh
Write mult_tester and mult_test, with set_type_override
Without touching env.svh: the structure never finds out that the stimulus changed
The env brings a chequeo component that marks the exercise on its own
Notes: Before turning them loose on the exercise, go back to the slide “The map of day 3: what replaces what” of the object-based testbench and read the right-hand column straight through: the build_phase of the env, the config_db, the run_phase, the objections and the set_type_override and the $display that became uvm_info. The six rows are crossed out, and the day closes there. It is the day 2 exercise again, but with the factory. Worth having them compare the two: on day 2 the type was picked in the code of the testbench, here the factory picks it and the testbench does not change one line. And have them look at the coverage at the end: with nothing but multiplications it drops to 26 %. A focused test covers less, and that is the reason many are needed — and the reason adding one has to be cheap.

## Slide 204
Exercise · Day 3 · 2 of 2
The uvm_error that says nothing
cd code/ejercicios/d3b && bash run.sh
The scoreboard is right —it catches every mismatch— and when it fails it says FAILED and nothing else: even less than the line of the day-1 waves exercise
Make the uvm_error say which one failed: A, B, the operation, the DUT’s result and the one you predicted
And make the one that passes get printed too, at UVM_HIGH, so that it does not show up in the everyday log
The checker watches the same bus you do and knows which was the first that failed
Notes: It is the short exercise of day 3 and it closes the arc the day-1 waves exercise opened: there the student was the one reading the FAILED, here they are the one writing it. Ten minutes of typing, and the point is not the $sformatf. The point is the second request, which is the one that surprises: the PASS also gets written. The typical reaction is “what do I want a thousand PASS lines for?”, and the answer is that you do not want them today: you want them the day operation 700 fails and you need to know what happened in 699. That is why it gets written and hidden behind UVM_HIGH. That is the difference between severity and verbosity, told with your hands. The checker runs the same testbench three times, and it is worth telling because it is how a log gets tested: one with the DUT broken —+VTALU_BUG— so the error fires and can be read, one with the usual verbosity to demand that the PASS is not there, and one with +UVM_VERBOSITY=UVM_HIGH to demand that it is there once per comparison. A message that was not tested all three ways is a message that is going to lie in the nightly regression.

## Slide 205
Yesterday we left…
Where the testbench stands
UVM walked in: run_test(), the test, the phases, the env and the scoreboard, and the +UVM_TESTNAME that picks the class from the command line
The objection is what keeps the simulation alive, and the reporting already tells verbosity from action
And one bottleneck was left: the scoreboard is one and it is wired to the monitor. The day there are two listeners, the one that publishes has to be edited
Notes: The day 4 recap has to leave the observer problem served, because the whole unit is that: a producer that does not know its listeners. It is worth asking the question and waiting: “if tomorrow they want to measure coverage as well as compare, where do they touch?”. The natural answer —“I add a call in the monitor”— is exactly the one the unit comes to take apart.

## Slide 206
Agenda
Day 4 · ≈ 4 h · unit 5 · how the components talk
One producer, many listeners
A single place that watches the wire
When somebody has to wait
Who waits for whom
By the end of the day you can:
Hang a new subscriber off an analysis port without touching the one that publishes
Choose between an analysis port and a TLM FIFO, and say which of the two blocks
Remove the #500 at the end of a test and replace it with the objection that belongs there
Notes: The first one is row 11 of the closing self-assessment and it is what defines the unit: the observer exists so that adding a listener does not touch the one that publishes. The third one is the second exercise of the day and it stands as an objective on its own: the #500 is the patch everybody writes the first time, and taking it out forces you to understand what keeps the simulation alive.

## Slide 207
One producer, many listeners
Two ways of talking between objects
The structural paradigm asks which steps to follow. OOP asks what objects there are and how they talk to each other — and that is where the single-initial testbench ends
And talking, between objects, is exactly two things. The difference is whether the two run in the same thread or not
Same thread: one calls the other’s method and comes straight back. It is the write() of a uvm_analysis_port — the first two sections of the day
Different threads: the two run at the same time and they have to be coordinated, which means somebody is going to have to wait. It is put / get and the TLM FIFOs — the last two
The whole of day 4 is those two columns. We start with the left-hand one
Notes: This slide is the map of the day: the four sections that follow are the two columns below, in order. It is worth writing the two columns on the board and coming back to them every time a new port shows up, because the question to ask yourself in front of any UVM port is always the same: can this block? If it runs in my thread, no; if it runs in another one, yes, and then it has to be a task. That is also the criterion that orders the vocabulary of the day: write() is a function —it consumes no time—, put() and get() are task. The signature tells you which side of the divide you are on before you read a line of the implementation.

## Slide 208: One producer, many listeners
The one who publishes does not know who reads it
A piece of testbench data almost never has one addressee: every command the monitor sees is wanted by the scoreboard, the coverage and, tomorrow, the log
The obvious solution is for the producer to keep a handle to every consumer and call their method. It works, and adding a consumer forces you to touch the producer
It is the same problem the BFM solved in interfaces and BFM, one level up: there we hid the wire, here we want to hide the list of addressees
The answer is an old pattern: the producer publishes on a port and does not know —nor care— who is on the other side
The section builds it by hand with dice first, and only then replaces it with uvm_analysis_port. The example is deliberately foreign to hardware
Notes: The dice example is deliberate and it is worth defending if somebody asks why we do not start with the VTALU: you see the pattern without the noise of the protocol. When it shows up on the DUT in the analysis ports, the student is no longer learning two things at once. The question that orders the section: which is the only line that has to be written to add a fourth observer? A connect(). None in the producer. That is the criterion to look at every line of code from here on with. And it is worth anticipating the limit, because it is inter-thread communication: this is communication inside a single thread. write() is a function, it consumes no time, and it runs in the thread of the one publishing. To talk between threads something else is needed.

## Slide 209: One producer, many listeners
The problem: two dice, three things to count
Write a program that simulates rolling two dice (2d6) 20 times and reports the following
  The average of the values the dice gave
  A histogram with the frequency of values
  A coverage report that shows whether every possible value from 2 to 12 came up
Rolling 2d6: the sum goes from 2 to 12 and 7 is the most likely

## Slide 210
Notes: It is worth posing it as a programming problem before showing a single line: they are three consumers of the same piece of data, and each one does something different with it. Nobody thinks about hardware here, which is exactly the idea. The three reports have something in common that is worth pointing out now: none of them can be worked out from a single roll. The three accumulate and only report at the end, and that is why the three are going to need two methods, not one. And a quick question for the classroom, one that gets collected later: if tomorrow they ask for a fourth report —the most repeated roll, say—, which files have to be touched?

## Slide 211: One producer, many listeners
The three observers: the same shape, three bodies
class average extends uvm_component; `uvm_component_utils(average); protected real dice_total; protected real count; function new(string name, uvm_component parent = null); super.new(name, parent); dice_total = 0.0; count = 0.0; endfunction : new function void write(int t); dice_total = dice_total + t; count++; endfunction : write function void report_phase(uvm_phase phase); `uvm_info("AVERAGE", $sformatf("DICE AVERAGE: %2.1f", dice_total / count), UVM_NONE) endfunction : report_phase endclass : average
average is the simplest one: a write(int t) that accumulates, and a report_phase() that divides and reports at the end
That is the shape the three of them are going to have: they receive one roll at a time, and the result only exists once everything is over
Notes: It is worth showing the whole class only once —this one— and after that only the write()s, because what matters is that the shape repeats. Two details that get collected later: the report_phase runs after the run_phase —and after extract and check—, not inside it, and that is why the average comes out complete. And dice_total and count are protected: the one publishing cannot touch them, only call write(). When this is the VTALU, in the analysis ports, average is going to be the scoreboard and the report_phase the verdict of the run. Same shape.

## Slide 212: One producer, many listeners
The other two: the body changes, not the shape
function void write(int t); rolls[t]++; endfunction : write
function void write(int t); the_roll = t; dice_cg.sample(); endfunction : write
histogram keeps the rolls in an associative array and draws the bars in the report_phase
coverage copies the roll into the_roll and calls sample(): it is the covergroup of the conventional testbench, with the sampling tied to the data instead of to the clock
The three write()s are different on the inside and identical on the outside: same name, same argument. That is what is going to let us treat them the same
Notes: The point of the slide is the last bullet: three classes that look nothing alike expose the same door. When uvm_subscriber shows up, that door is going to be a contract of the language instead of a convention. The coverage here is the answer to a question left open in the conventional testbench: where do I sample? Here the sample() is not tied to a clock edge, it is tied to a piece of data having arrived. That is the right thing, and it is what the coverage of every testbench of the course does from here on. The whole file of each one is in code/u5/varios-objetos/01-sin-analysis-port/: what is not shown is the report_phase, which only formats.

## Slide 213: One producer, many listeners
The producer: it rolls the dice and returns a number
class dice_roller extends uvm_component; `uvm_component_utils(dice_roller); rand byte die1; rand byte die2; constraint d6 { die1 >= 1; die1 <= 6; die2 >= 1; die2 <= 6; } function new(string name, uvm_component parent); super.new(name, parent); endfunction : new function byte two_dice(); byte the_roll; void'(randomize()); the_roll = die1 + die2; return the_roll; endfunction : two_dice endclass : dice_roller
dice_roller randomizes two bytes with a constraint that keeps them between 1 and 6, and returns the sum
That is all it does, and it is right that it should be all: it produces the data and knows nothing about who uses it
Look at what it does not have: not a handle to coverage_h, nor to histogram_h, nor to average_h. That list lives somewhere else, and that is where the problem is
Notes: It is worth stopping on the absence: the producer is already well written. It does not need fixing, and in fact in the version with an analysis port it barely changes. The void'(randomize()) deserves a comment in passing: it throws away the return value on purpose. In the transactions we are going to see why that is a bad habit —a randomize() that fails and nobody finds out— and how it gets written properly. The question to leave hanging: if the producer does not have the list, who does? The slide that follows.

## Slide 214: One producer, many listeners
The one handing it out: the test, and it should not be
The dice_test extends uvm_test, instantiates the four components and starts
It works. But look at the run_phase, and in particular at what is inside the repeat (20)
task run_phase(uvm_phase phase); int the_roll; phase.raise_objection(this); // This part needs attention. // What belongs here is: // the Observer design pattern // a UVM analysis port // Otherwise none of the OOP magic is being used: // these are plain functions passing data along repeat (20) begin the_roll = dice_roller_h.two_dice(); coverage_h.write(the_roll); histogram_h.write(the_roll); average_h.write(the_roll); end phase.drop_objection(this); endtask : run_phase
Notes: This slide is the “before”, and it has to be allowed to look ugly. Look at the repeat (20): three write()s written out by hand, one per observer. Adding a fourth means touching this class; removing one, too. Worse still, and it is what is worth pointing at: the one left in charge of handing out the data is the test. Which means the dice_roller produces and the test distributes — two responsibilities that have no reason to be together, and the distributing one is the one that is going to change all the time. The question to throw out before moving on to the next one: if this were the VTALU, who would the dice_roller be and who the three write()s? The monitor, and the scoreboard plus the coverage. The analysis ports are literally this slide with other names.

## Slide 215: One producer, many listeners
Observer Design Pattern
Whoever publishes a tweet does not know who reads it or what they do with it, and yet it reaches everybody. That is the Observer
An object produces a piece of data and publishes it. The ones who need that data subscribe. The producer does not keep the list
Here the observed one is dice_roller_h; the observers —subscribers— are coverage_h, histogram_h and average_h
The property that buys everything: adding a fourth observer does not touch one line of the one producing
Observer: one sender publishes and N observers receive

## Slide 216
Notes: The analogy works better the other way round: the one who publishes does not know who reads them, and that is exactly the property you want in a monitor. Adding a new subscriber —another coverage, a log— does not touch one line of the one producing the data. The dice example is deliberately foreign to hardware: you see the pattern without the noise of the protocol.

## Slide 217: One producer, many listeners
The pattern, ready-made: the two ends of the wire
UVM brings the pattern ready-made, in two classes that are the two ends of the wire:
  uvm_analysis_port: Sends data to a set of subscribers (observers)
  uvm_subscriber: An extension of uvm_component that lets the component subscribe to a uvm_analysis_port
Notation: diamond = uvm_analysis_port, circle = analysis_export

## Slide 218
Notes: The names cost a minute and save half an hour later: port is the end of the one producing, export the end of the one consuming, and the connect() is always called on the port. uvm_analysis_port is a broadcast: it does not care whether it has zero, one or ten subscribers, and writing to an unconnected port is not an error — the data is lost in silence. It is one of the silent traps of the course, and the symptom is a scoreboard that never reports anything. uvm_subscriber is the other end and it is a parameterized class: #(int) here, #(command_transaction) in the analysis ports. The connection ends up typed by the compiler, not by a string.

## Slide 219: One producer, many listeners
uvm_analysis_port
We declare a variable of type uvm_analysis_port that states the type of data it is going to carry
We instantiate the analysis port in build_phase
We write data into the port through the .write() method
Once we write data into the port, it goes to all of its subscribers
We use the connect() method to connect the subscribers to the port. This method takes a single argument, and it is the subscriber’s export (analysis_export), not another port
// Same as version 01, but publishing: instead of returning the number it writes // it to an analysis port, and stops knowing who reads it. class dice_roller extends uvm_component; `uvm_component_utils(dice_roller); rand byte die1; rand byte die2; constraint d6 { die1 >= 1; die1 <= 6; die2 >= 1; die2 <= 6; } function new(string name, uvm_component parent); super.new(name, parent); endfunction : new // 1) declare the port, with the data type it will carry uvm_analysis_port #(int) roll_ap; // 2) instantiate it in build_phase, with new(): ports do not go through the factory function void build_phase(uvm_phase phase); roll_ap = new("roll_ap", this); endfunction : build_phase task run_phase(uvm_phase phase); int the_roll; phase.raise_objection(this); repeat (20) begin void'(randomize()); the_roll = die1 + die2; // 3) write: the port calls write() on every subscriber roll_ap.write(the_roll); end phase.drop_objection(this); endtask : run_phase endclass : dice_roller
Notes: Three steps and no more: declare the port, instantiate it in build_phase, write with write(). On the other side the subscriber implements write() and gets connected in connect_phase. The detail that surprises: ports are not created with the factory, they are instantiated with new().

## Slide 220: One producer, many listeners
uvm_subscriber
We extend the uvm_subscriber class parametrically, so that it knows what type of data it is going to read
The class gives us an object called analysis_export
The class requires us to write a method called write() that takes a single argument t, of the same type as the extension of the class
In our example, we have 3 subscribers (average, coverage and histogram)
// uvm_subscriber: // extends the uvm_component class and lets you hook onto an analysis port // It is a parameterizable class! // The class gives you something and asks for something in return // * It gives you an object called analysis_export // * It asks you to write a write() method that handles the data class coverage extends uvm_subscriber #(int); `uvm_component_utils(coverage); int the_roll; covergroup dice_cg; coverpoint the_roll {bins twod6[] = {2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12};} endgroup function new(string name, uvm_component parent = null); super.new(name, parent); dice_cg = new(); endfunction : new function void write(int t); the_roll = t; dice_cg.sample(); endfunction : write function void report_phase(uvm_phase phase); `uvm_info("COVERAGE", $sformatf("COVERAGE: %2.0f%%", dice_cg.get_inst_coverage()), UVM_NONE) endfunction : report_phase endclass : coverage
Notes: uvm_subscriber is a deal in two parts and it is worth stating it that way: I give you an analysis_export, you give me back a write(). Nothing else. The analysis_export is neither declared nor instantiated — it comes with the class. The #(int) of the extends is the parameterized classes getting collected again: it defines what type the t of the write() is, and the compiler takes care that a port of int cannot be connected to a subscriber of something else. The connection is typed, it is not a string. Comparing it with the previous version of this same class is worth it: the write() is identical. The only thing that changed is who it inherits from and who calls it. That is the entire point of the section — the observer never finds out that it is now an observer. And a detail that shows up in the output: here the coverage is read with get_inst_coverage(), not with get_coverage(). It is a Verilator limitation —the type-wide one always returns 0— and it is in docs/en/verilator.md.

## Slide 221: One producer, many listeners
The producer, publishing now
// 1) declare the port, with the data type it will carry uvm_analysis_port #(int) roll_ap; // 2) instantiate it in build_phase, with new(): ports do not go through the factory function void build_phase(uvm_phase phase); roll_ap = new("roll_ap", this); endfunction : build_phase task run_phase(uvm_phase phase); int the_roll; phase.raise_objection(this); repeat (20) begin void'(randomize()); the_roll = die1 + die2; // 3) write: the port calls write() on every subscriber roll_ap.write(the_roll); end phase.drop_objection(this); endtask : run_phase
The three numbered steps are everything that changed with respect to the previous version: declare the port, instantiate it in build_phase, write with write()
roll_ap = new(...): ports are not created with the factory. They are the wiring of the testbench, not interchangeable pieces
The two_dice() that returned a number is gone: now the roll gets published and the producer carries straight on
Notes: The comparison with the previous version is the whole slide: the dice_roller did not gain a handle to anybody. It gained one port. Why ports go with new() and not with type_id::create(): the factory is there to substitute types, and a port never gets substituted. It is a question that always comes up and that is the short answer. And the write() here is worth looking at with inter-thread communication in mind: it is a function, so it consumes no time and it runs in the producer’s thread. When the one consuming needs to make the one producing wait, this is not enough.

## Slide 222: One producer, many listeners
connect_phase(): where the wiring gets assembled
We need to link the producer with the consumer
UVM provides a phase method (connect_phase()) to connect the objects
UVM calls the build_phase method TOPDOWN, and once it is done with every object in the hierarchy, UVM calls the connect_phase method BottomUP
The connection process has 2 fundamental parts
  uvm_subscribers contain an object called analysis_export, which we must not instantiate since it comes along when we extend the uvm_subscriber class
  The uvm_analysis_port class provides a method called connect()
Notes: The order of the two phases is not an implementation detail, it is what makes this work: you cannot connect what does not exist yet. That is why build_phase is top-down and finishes entirely before the first connect_phase starts. That connect_phase is bottom-up matters less in practice, but it has its reason: a composite component connects its children to each other only once every child has connected its own. In the agents, when the agent connects driver and sequencer inside itself and the env connects the agent outwards, it will show. The analysis_export that shows up on its own is one of the few things in UVM that come free: it comes with the class, and forgetting to instantiate it is not a mistake because there is nothing to instantiate.

## Slide 223: One producer, many listeners
connect_phase(): where the wiring gets assembled
A single line of connect_phase() hooks the subscriber up to the analysis port: ap.connect(sub_h.analysis_export)
// build_phase: UVM calls it TOP-DOWN, the parent first. function void build_phase(uvm_phase phase); dice_roller_h = new("dice_roller_h", this); coverage_h = new("coverage_h", this); histogram_h = new("histogram_h", this); average_h = new("average_h", this); endfunction : build_phase // connect_phase: BOTTOM-UP, and always port.connect(export). function void connect_phase(uvm_phase phase); dice_roller_h.roll_ap.connect(coverage_h.analysis_export); dice_roller_h.roll_ap.connect(histogram_h.analysis_export); dice_roller_h.roll_ap.connect(average_h.analysis_export); endfunction : connect_phase
Notes: This is the “after”, and it has to be put next to the “before”, the version without the analysis port. The run_phase of the test is left without the three write()s: now it only raises the objection and starts the producer. The distribution moved to the connect_phase, which is where the structure goes. The line to read slowly is dice_roller_h.roll_ap.connect(coverage_h.analysis_export), and the direction matters: the port connects to the export, never the other way round. It is the mantra that comes back in threads, in put and get and in agents, and the compiler does not always catch you. Pocket rule to remember the direction, and it has to be said this way because the easy version breaks straight away: the one that calls connect() is the one that has the port, and it hands it the other one’s export. Here the one with the port is the producer; in put and get the uvm_get_port belongs to the consumer, and there it is the consumer that connects. “The producer connects” works on this slide and fails in the next section. And the acid test of the section: to add a fourth observer you have to write the class and one line here. Not one in dice_roller.

## Slide 224: One producer, many listeners
The solution, wired up
In the connection diagram we can see that the dice_roller class has a uvm_analysis_port object called roll_ap
Each subscriber has an analysis_export object
The connection between the two is made through the connect() method
Wiring of the dice example: roll_ap against the three analysis_export

## Slide 225
Notes: It is the first TLM diagram of the course and it is worth teaching how to read it now, because the ones from the rest of the day and the one from the agents use the same convention: diamond is analysis port, square is put/get port, circle is export. The arrow goes from the one producing to the one consuming. What has to be pointed out about the drawing is that three arrows come out of the roll_ap and a single line of code comes out of the dice_roller: the write(). The multiplicity is not in the producer, it is in the wiring. And the closing of the section, which links to the next one: all of this happened inside a single thread. write() is a function, it cannot have an @ or a #, and it came back before time moved. When the one producing and the one consuming have to wait for each other, this is not enough — and that is inter-thread communication.

## Slide 226: One producer, many listeners
Summary of the unit
Two objects talk to each other in exactly two ways, and the difference is whether they run in the same thread or not
Same thread: one calls the other’s method and comes straight back. It is a function, it cannot block. It is the write() of an analysis port
Different threads: they have to be coordinated and somebody is going to wait. It is a task, it can block. It is put/get, and they are the last two sections
The question in front of any UVM port is always the same: can this block? The signature tells you before you read the implementation
The analysis port solves the underlying problem: the one who publishes does not know who reads it, and adding a reader does not touch one line
It is the same old observer pattern, and it is the same move the BFM made in interfaces and BFM: one level up
Notes: The slide to open and close day 4 with, because it is the map. Write the two columns on the board and come back to them every time a new port shows up. And the criterion that orders the whole vocabulary: write() is a function —it consumes no time—, put() and get() are task. In SystemVerilog that is not a naming convention, it is the language telling you which side you are on.

## Slide 227
A single place that watches the wire
A single place that watches the wire
Today the scoreboard and the coverage each watch the signals on their own: both wait for done, both read op_set, both know the protocol
That is the same code written twice, and the day the protocol changes you have to remember both places
The missing piece has a name in the industry: the monitor. A single one watches the bus, assembles the transaction and publishes it
The scoreboard and the coverage become subscribers, like the dice of the previous unit: they never touch a wire again
In UVM jargon those two form the analysis layer, and that is where the name uvm_analysis_port comes from
Notes: It is the same pattern as the dice, now on the DUT — and that is the whole section. What has to be stressed is where the dividing line of the testbench runs, because it is the one that orders everything that comes after: on one side of the monitor you speak in signals, on the other in transactions. The BFM of interfaces and BFM did that for the stimulus; the monitor does it for the analysis. The practical consequence is worth saying out loud: from here on, any analysis component can be written without knowing anything about the protocol. A new subscriber does not need to know that a done exists. And the one that only shows up in the agents: if everything that knows how to speak the protocol is together —BFM, monitors, driver—, that box can be instantiated twice. That is the agent, and this section is the one that gathers the pieces.

## Slide 228: A single place that watches the wire
Which pieces show up
command_monitor — watches the start of every operation and publishes what was asked for
result_monitor — watches the done and publishes what the DUT answered
The BFM stops being only signals: it gains three always and a handle to each monitor
The scoreboard and the coverage stop waiting for edges and get a write() instead
The tester never finds out about any of it: it goes on sending stimulus just like yesterday
Notes: The slide is the inventory of the section and it is worth using it as a map: there are five pieces and only two are new. It is worth saying out loud which ones, because the student tends to believe that a new topic rewrites the whole testbench. That there are two monitors and not one is the decision that gets asked about the most, so better to get ahead of it: they watch different things and at different moments. The command_monitor watches when an operation starts; the result_monitor, when the DUT answers. Between those two instants there are cycles in the middle, so they cannot be the same always. And the last bullet is the one to underline, because it is the promise the section keeps: the tester does not get touched. All the work of this section happens on the analysis side, and the stimulus side never finds out. It is the first time the course separates the two halves of the testbench, and in the section that follows the other one gets done.

## Slide 229: A single place that watches the wire
Testbench diagram
VTALU testbench with analysis ports

## Slide 230: A single place that watches the wire
The handles the BFM keeps
Up to now the class read the interface. Here it flips around: the interface keeps a handle to the class and it is the interface that calls the method
interface vtalu_bfm; import vtalu_pkg::*; // These handles get assigned in the build_phases of the classes command_monitor command_monitor_h; result_monitor result_monitor_h; byte unsigned A; byte unsigned B; bit clk; bit reset_n; bit start; wire done; wire [15:0] result; wire ovf; operation_t op_set;
These handles are set by each monitor in its build_phase, right after pulling the BFM out of the config_db
function void build_phase(uvm_phase phase); virtual vtalu_bfm bfm; if (!uvm_config_db#(virtual vtalu_bfm)::get(this, "", "bfm", bfm)) `uvm_fatal("COMMAND MONITOR", "Failed to get BFM") bfm.command_monitor_h = this; ap = new("ap", this); endfunction : build_phase
Notes: This slide holds the inversion that costs the most in the section and it is worth saying it slowly: up to now the class read the interface. Here it is the other way round — the interface has a handle to the class (bfm.command_monitor_h = this) and it is the interface that calls the method. The reason is that an always of the interface can have a sensitivity list, and a class function cannot. We need the hardware to give notice; for that the hardware has to know who to give notice to. The line that does everything is bfm.command_monitor_h = this, and it goes in the build_phase. If you forget it, the monitor compiles, runs, and never publishes: the scoreboard is left without commands and the uvm_fatal shows up on the other side, in a class that is not to blame. It is one of those errors that get hunted in the wrong place. A detail that helps: the handle is to the class, not virtual. That is why the always can call write_to_monitor() directly without the Verilator hole that affects tasks — here the one declaring the task is the class, not the interface.

## Slide 231: A single place that watches the wire
Monitoring the VTALU commands
Three always in the BFM: the command one fires when an operation starts, the reset one on the falling edge of reset_n, and the result one when the DUT raises done
// Here is the first monitor (commands) // A very simple FSM. If start is up, check whether this is a new command // If it is, send it to the TB with commands_monitor.write_to_monitor() always @(posedge clk) begin : cmd_monitor bit new_command; if (!start) new_command = 1; else if (new_command) begin command_monitor_h.write_to_monitor(A, B, op_set); new_command = (op_set == 3'b000); // handle no_op end end : cmd_monitor always @(negedge reset_n) begin : rst_monitor if (command_monitor_h != null) //guard against VCS time 0 negedge command_monitor_h.write_to_monitor(A, B, rst_op); end : rst_monitor always @(posedge clk) begin : rslt_monitor if (done) result_monitor_h.write_to_monitor(result); end : rslt_monitor
And on the other side, the method they give notice to: it packs the command_s up and publishes it on the analysis port
function void write_to_monitor(byte A, byte B, bit [2:0] op); command_s cmd; cmd.A = A; cmd.B = B; cmd.op = op2enum(op); `uvm_info("COMMAND MONITOR", $sformatf("A:0x%2h B:0x%2h op: %s", A, B, cmd.op.name() ), UVM_HIGH) ap.write(cmd); endfunction : write_to_monitor
Notes: The three always are the seam between the hardware and the classes, and it is worth reading the condition of each one: the command one fires when start goes up and there was no command in flight; the reset one, on the falling edge of reset_n; the result one, when the DUT raises done. The guard if (command_monitor_h != null) is not paranoia: at time 0 the UVM tree does not exist yet and the negedge reset_n has already arrived. Without the guard it is a null pointer from the simulator. The write_to_monitor() is short on purpose: it assembles the command_s, logs it with UVM_HIGH —which means it is only visible with +UVM_VERBOSITY=UVM_HIGH— and calls ap.write(). Everything else happens on the other side of the port, and the monitor does not know who is over there. And the detail that gets collected in the transactions: what travels is still a struct. The day it is a transaction, this same line is going to be a create().

## Slide 232: A single place that watches the wire
The VTALU Coverage Class as a Subscriber
With the command_monitor there is a single place in the whole testbench that knows what a command looks like on the wire
Whoever needs to know which operation ran subscribes to its analysis port and implements write(). They never look at a signal again
// With the analysis port this is far simpler, // because nothing here has to know about the ALU signals: // what arrives is a command_s struct that wraps the command // function void write(command_s t); A = t.A; B = t.B; op_set = t.op; op_cov.sample(); zeros_or_ones_on_ops.sample(); endfunction : write
Notes: It is worth opening the coverage class of the object-based testbench alongside and comparing: over there was a forever waiting for edges; here there is a write() and nothing else. The coverage stopped having any notion of time. And that is not cosmetic, it is the answer to the question left open in the conventional testbench: where the sampling happens. Before, it sampled on the clock, which means cycles got counted; now it samples when the monitor sees a command, which means operations get counted. That is the right thing, and the coverage number changes meaning. The question for the group: if the DUT sat ten cycles doing nothing, how many samples did the old version take and how many does this one? Ten and zero. The old one was filling bins with nothing.

## Slide 233: A single place that watches the wire
Subscribing to multiple analysis ports
The basic UVM analysis port mechanism lets a uvm_subscriber grab a single analysis_port
However, in cases like a scoreboard, we need one and the same component to receive data from 2 analysis ports
The reason for the limit: uvm_subscriber gives you a single write(), and that is the method the port calls. Two ports have nowhere to come in
UVM solves it without splitting the component, with the uvm_tlm_analysis_fifo class, which is unbounded by construction: its constructor passes size = 0 (tlm1/uvm_tlm_fifos.svh:281, with the comment “analysis fifo must be unbounded”)
And write() is a function that does void'(this.try_put(t)): it throws the return value away. A bounded FIFO would drop without warning — which is why this one is built with no cap
It is parameterized and it has two faces: an analysis_export on one side —which gets connected like any subscriber— and a try_get() on the other
try_get() takes an element out and returns 0 if the FIFO is empty, without blocking
Which means: it turns “they tell me when it arrives” into “I go and get it when I need it”
Notes: The scoreboard needs two sources —the command and the result— and a uvm_subscriber can listen to only one. The FIFO turns “they tell me when it arrives” into “I go and get it when I want”, which is what it needs in order to compare in pairs.

## Slide 234: A single place that watches the wire
Subscribing to multiple analysis ports
Scoreboard class:
uvm_tlm_analysis_fifo #(command_s) cmd_f; function void build_phase(uvm_phase phase); cmd_f = new("cmd_f", this); endfunction : build_phase // Every time the DUT hands a result to the analysis port, this method // gets triggered function void write(shortint t); shortint predicted_result; command_s cmd; cmd.op = no_op; // Here is where the prediction happens: look in our FIFO for the command // that was sent, skipping the resets and the no_ops with the // do....while // since whenever there is a result there must be an operation, // a result with no operation behind it is an error do if (!cmd_f.try_get(cmd)) `uvm_fatal("SCOREBOARD", "No command in self checker") while ((cmd.op == no_op) || (cmd.op == rst_op)); case (cmd.op) add_op: predicted_result = cmd.A + cmd.B; sub_op: predicted_result = cmd.A - cmd.B; and_op: predicted_result = cmd.A & cmd.B; xor_op: predicted_result = cmd.A ^ cmd.B; mul_op: predicted_result = cmd.A * cmd.B; endcase // case (op_set) if (predicted_result != t) `uvm_error("SCOREBOARD", $sformatf( "FAILED: A: %2h B: %2h op: %s actual result: %4h expected: %4h", cmd.A, cmd.B, cmd.op.name(), t, predicted_result )) endfunction : write
Notes: The scoreboard is asymmetric and that is where the whole point is: the result reaches it through write() —it gets pushed— and the command it goes and fetches itself with try_get() from the FIFO. One is push, the other is pull. Why like this and not two write()s: a uvm_subscriber has a single write(), and besides the order matters. The scoreboard does not want to be told about the command when it arrives; it wants it at the moment the result appears, so that it can compare in pairs. The FIFO turns “they tell me” into “I go and get it when I want”. The do ... while that skips no_op and rst_op is the part that gets copied wrong: those two operations produce no result, so if they are not thrown away, the comparison shifts by one place and from there on everything fails. The symptom is a scoreboard that screams on every line, and it is exactly the day 5 exercise. And the uvm_fatal of the try_get() is not paranoia: if there is a result and there is no command, the broken one is the testbench, not the DUT. Better to die there than to report a thousand false errors.

## Slide 235: A single place that watches the wire
The other way: `uvm_analysis_imp_decl
`uvm_analysis_imp_decl(_cmd) // makes the class uvm_analysis_imp_cmd `uvm_analysis_imp_decl(_result) class scoreboard extends uvm_component; uvm_analysis_imp_cmd #(command_s, scoreboard) cmd_imp; uvm_analysis_imp_result #(shortint, scoreboard) result_imp; function void write_cmd(command_s t); ... endfunction // one write per port function void write_result(shortint t); ... endfunction endclass
The macro generates a class for each suffix, and each one calls a different write_: that way a component receives from two ports without a FIFO
It is what you are going to see in most production code, so you have to be able to read it
The course uses the FIFO anyway, for an underlying reason: write_cmd() runs when the command arrives, and the scoreboard needs it when the result arrives. The FIFO gives it that control; the macro forces it to keep the data by hand
Notes: Same treatment as the `uvm_field_* macros of the components and as `uvm_do of the sequences: they get named, they get explained, and it gets said why the course does not use them. The rule of the course, once again: read them all, write the explicit ones. What the macro hides and is worth saying: uvm_analysis_imp is a class that already exists in UVM; the only thing `uvm_analysis_imp_decl does is manufacture variants with a different name, because SystemVerilog does not let you have two write()s in the same class. Which means the macro adds no mechanism, it adds names. Where it goes: in the package, outside every class, and only once per suffix in the whole testbench. Declaring it twice with the same suffix is a compilation error that shows up far from the place where you wrote it. And the honest comparison: with the macro the scoreboard comes out shorter and more coupled —it has to carry the command by hand until the result arrives—; with the FIFO it comes out one line longer and it decides the order itself. For a scoreboard that matches things up in pairs, the FIFO wins. For a component that only counts things from two ports, the macro is better.

## Slide 236: A single place that watches the wire
Subscribing to the monitors
We connect the analysis ports to the monitors using the connect_phase() method in the env class:
class env extends uvm_env; `uvm_component_utils(env); random_tester random_tester_h; coverage coverage_h; scoreboard scoreboard_h; command_monitor command_monitor_h; result_monitor result_monitor_h; function new(string name, uvm_component parent); super.new(name, parent); endfunction : new function void build_phase(uvm_phase phase); random_tester_h = random_tester::type_id::create("random_tester_h", this); coverage_h = coverage::type_id::create("coverage_h", this); scoreboard_h = scoreboard::type_id::create("scoreboard_h", this); command_monitor_h = command_monitor::type_id::create("command_monitor_h", this); result_monitor_h = result_monitor::type_id::create("result_monitor_h", this); endfunction : build_phase function void connect_phase(uvm_phase phase); result_monitor_h.ap.connect(scoreboard_h.analysis_export); command_monitor_h.ap.connect(scoreboard_h.cmd_f.analysis_export); command_monitor_h.ap.connect(coverage_h.analysis_export); endfunction : connect_phase endclass
Notes: Three connect()s and there is the whole testbench. Worth reading them out loud as sentences: the result goes to the scoreboard, the command goes to the scoreboard’s FIFO, the command also goes to the coverage. The surprising one is the second: command_monitor_h.ap.connect(scoreboard_h.cmd_f.analysis_export). The export does not belong to the scoreboard, it belongs to the FIFO the scoreboard has inside it. A uvm_analysis_port can have several destinations —the ap of the command_monitor feeds two— and it costs it nothing: write() walks through all of them. And the detail that gets forgotten and gives no warning: cmd_f is instantiated with new(), not with the factory. The FIFO is registered —`uvm_component_param_utils in tlm1/uvm_tlm_fifos.svh:256— but the course builds it with new() because it passes the size through the constructor and create() cannot. What is not in the factory are the ports and the exports: they extend uvm_port_base with no utils macro. If you forget the new() the connect() blows up with a null, and that one at least is an honest error.

## Slide 237: A single place that watches the wire
When the DUT does not answer in order
The scoreboard of this section does a try_get() from a FIFO: the first command that went in is the one that matches the first result that came out. That holds because the VTALU answers in order, one operation at a time
A real bus does not. In AXI every transfer carries an ID and the responses can come back crossed over: the FIFO starts comparing the response of one with the request of another, and screams on every one
transaccion esperado [int]; // associative, indexed by whatever pairs them up function void write_cmd(transaccion c); esperado[c.id] = c; endfunction function void write_result(respuesta r); if (!esperado.exists(r.id)) `uvm_error("SB", "a response nobody asked for") else begin comparar(esperado[r.id], r); esperado.delete(r.id); end endfunction
The pattern is always the same: a table indexed by whatever pairs them up, a delete once it has been compared, and at the end of the run the table has to be left empty
That check at the end is half the value: what stayed inside are the requests the DUT never answered
Notes: The question that opens the slide is the one to ask of anybody else’s scoreboard before trusting it: “and what if the DUT answers out of order?”. The one in this section falls over, and it is fine that it falls over — the VTALU does not do that. What is not fine is not knowing it. The symptom when it happens is cruel and worth anticipating, because it sends you hunting in the wrong place: it is not one comparison that fails, it is every one after the first crossed-over one. The testbench says a thousand errors and the DUT has zero. It is the row “the scoreboard screams on every one” of the debug appendix, with another cause. The associative array is the canonical answer and there is no mystery to it; what always gets forgotten is the check_phase that verifies it was left empty. Without that, a DUT that stops answering passes green: there is never a bad comparison, there are simply comparisons that were not made. It is the same hole as the drain_time of the tests, seen from the other side. And the variant that shows up when there is no ID: pairing by content. You keep a queue of expected ones and look for the one that matches, instead of the first. It is more expensive and it has a trap of its own —two identical transactions—, and that is why the ID exists.

## Slide 238: A single place that watches the wire
On one side of the monitor you speak in signals, on the other in transactions
The monitor is the only class that knows a clk exists. Coverage and scoreboard receive data and have no idea where it came from
The Observer of talking to several objects, applied to the DUT: the monitor publishes and does not keep the list. Adding an observer is one line in the connect_phase
And the limit, which is the section that follows: all of this happens in a single thread. The always of the BFM calls write_to_monitor(), which calls ap.write(), which calls the write()s of the subscribers — a chain of functions, without time moving
Notes: The sentence in the title is the real summary of the section and it is worth leaving it written up: on one side of the monitor you speak in signals, on the other in transactions. That border is what makes it possible for the scoreboard of the transactions to exist without looking at a wire. The third bullet is the hinge towards inter-thread communication: since it is all a chain of functions, no link can wait. If the one consuming needs to make the one producing wait —or the other way round—, something else is needed, and that is the uvm_tlm_fifo. Worth asking the question before moving on: what would happen if the write() of a subscriber had an @(posedge clk) inside it? It does not compile. A function cannot consume time, and that is the whole limitation.

## Slide 239: A single place that watches the wire
Summary of the unit
Up to yesterday the scoreboard and the coverage each watched the signals on their own: the same protocol code written twice
The piece that was missing has a name in the industry: the monitor. A single one watches the wire and publishes what it saw
There are two: command_monitor publishes what was asked for, result_monitor publishes what the DUT answered
The scoreboard and the coverage become subscribers: they stop waiting for edges and only implement write()
That pair —monitors that publish, subscribers that analyse— is the analysis layer, and that is where the name of the port comes from
The tester never finds out about any of it. That is the proof the split came out right: changing the analysis does not touch the stimulus
And the scoreboard with a FIFO holds as long as the DUT answers in order. When it does not, the pattern is a table by ID that has to be left empty at the end
Notes: Closing of the unit where the testbench takes the shape it is going to have until the end. Worth saying it like this: from here on, every time something new has to be analysed —one more coverage, one more checker— the answer is always going to be the same, hang a subscriber off it, and never touch the monitor. It is literally the exercise of the day, and it is also what is going to be left outside the agent in the agents.

## Slide 240
When somebody has to wait
You were already doing this, with modules
The name is scary and you have been using the mechanism forever: two modules with ports, each one with its always, passing data to each other
// Sends the data through the shared variable and signals it by toggling get_it // Then the producer blocks on the put_it signal module producer ( output byte shared, input bit put_it, output bit get_it ); initial repeat (3) begin $display("Sent %0d", ++shared); get_it = ~get_it; @(put_it); end endmodule : producer // The consumer blocks on the get_it signal, waiting for data from the producer // when the producer toggles that signal, it processes the data and toggles put_it // when done, to unblock the producer module consumer ( input byte shared, output bit put_it, input bit get_it ); initial forever begin @(get_it); $display("Received: %0d", shared); put_it = ~put_it; end endmodule : consumer
That is communication between threads. The only thing missing is doing it between objects, which have no ports
Notes: The slide exists to defuse the fright before the word TLM shows up. It is worth pointing at the code and saying it that bluntly: here are two processes running at the same time and passing data to each other over a wire, and nobody called that “inter-thread communication” in twenty years of Verilog. It is the same thing. The only thing that changes in the rest of the section is where each process lives: instead of two always in two modules, two run_phase() in two objects. And since an object has no port list, the wire has to be replaced by something. The question to leave hanging, which is exactly the one on the next slide: what does the wire get replaced with? The answers that are going to come out —a shared variable, a semaphore, a mailbox— are all correct, and that is precisely the problem UVM comes to solve.

## Slide 241: When somebody has to wait
An object has no port list
What SystemVerilog does have is shared handles, semaphores and mailboxes
That is enough to solve it, and that is the problem: everybody solves it differently, and afterwards nobody can read the testbench of the person next to them
UVM standardizes a single way, in two pieces:
  Ports: they get instantiated in a uvm_component so that its run_phase() can talk to another thread. Put port to send, get port to receive
  TLM FIFO: the object that joins a put port to a get port. new() creates it with size 1 by default —new(name, parent, size = 1)—, and with 0 it would be unbounded. The one in the example uses the default
With size 1 the FIFO is not a buffer, it is a meeting point: the one putting waits for the other one to take out
Notes: What has to be taken away from the slide is that size 1 is not a limitation of the class: it is the default argument of the constructor. With new("f", this, 0) the FIFO is unbounded, and there the one putting never blocks. Size 1 is the one that synchronizes: it blocks the producer until the consumer takes out, and that replaces the semaphore and the flag everybody used to write by hand. It is the same start/done handshake of the BFM, but between objects.

## Slide 242: When somebody has to wait
The producer as an object
The producer declares a uvm_put_port and calls put(). That is all: no signal handshake, no shared flag, no semaphore
// UVM solution to interthread communication // It has 2 parts: // * Ports-Objects: instantiated in our uvm_components so that // run_phase can talk to other threads // * TLM Fifos (they hold only 1 element) class producer extends uvm_component; `uvm_component_utils(producer); int shared; // uvm_put_port is a parameterized class // this class takes care of the whole synchronization mess around // get_it and put_it uvm_put_port #(int) put_port_h; function void build_phase(uvm_phase phase); put_port_h = new("put_port_h", this); endfunction : build_phase function new(string name, uvm_component parent); super.new(name, parent); endfunction : new task run_phase(uvm_phase phase); phase.raise_objection(this); repeat (3) begin put_port_h.put(++shared); `uvm_info("PRODUCER", $sformatf("Sent %0d", shared), UVM_MEDIUM) end phase.drop_objection(this); endtask : run_phase endclass : producer
Notes: What has to be pointed out is what is not in this class: there is no @(posedge something), there is no wait, there is no variable saying “ready”. The producer puts and carries on; if the other one has not taken it out yet, the put() stops it on its own. The detail of form, which is the one that gets copied wrong: the port gets instantiated in the build_phase like any other component, with new("name", this). It is not a data field: it takes a parent, and that is why it shows up in print_topology(). But it is not a uvm_component either — uvm_put_port extends uvm_port_base #(IF), and what hangs off the tree is an internal uvm_port_component the port builds for itself (uvm_port_base.svh:137). The FIFO on the next slide really is a component. And the parameter: uvm_put_port #(T). That T has to be the same in the port, in the get port and in the FIFO. If they do not match it does not compile, which is the good news —it is one of the few UVM connection errors you see at compile time and not at three in the morning—.

## Slide 243: When somebody has to wait
The consumer as an object
On the other side, uvm_get_port and a get(). With the FIFO empty, get() blocks and the thread stays there
When the producer puts a piece of data in, the get() unblocks and carries on with the data already read. Nobody wrote the synchronization: the FIFO gives it
class consumer extends uvm_component; `uvm_component_utils(consumer); // uvm_get_port handles all the interthread coordination uvm_get_port #(int) get_port_h; int shared; function void build_phase(uvm_phase phase); get_port_h = new("get_port_h", this); endfunction : build_phase function new(string name, uvm_component parent); super.new(name, parent); endfunction : new task run_phase(uvm_phase phase); forever begin get_port_h.get(shared); `uvm_info("CONSUMER", $sformatf("Received: %0d", shared), UVM_MEDIUM) end endtask : run_phase endclass : consumer
Notes: get() is a task, and that word is the whole section. A function cannot have an @ or a #, so it cannot wait for anybody; a task can. If somebody wonders why the analysis ports of the previous section did not block, the answer is right there: write() is a function. The argument by reference is also worth naming: get(t) does not return the data, it writes it into the variable you hand it. It is the TLM convention and it surprises you the first time, because you expect a t = get(). And the practical warning: a get() on a FIFO that never fills up is a thread hung forever. There is no error and no warning — the simulation ends when the objection drops and that consumer simply never ran. It is a sibling of the forgotten item_done() of day 6.

## Slide 244: When somebody has to wait
Instantiating the three: two components and a FIFO
The uvm_tlm_fifo takes the same parameter as the two ports: if they do not match, it does not compile
The three get instantiated in the build_phase of the test, like any component. The FIFO is a uvm_component too
And the order is the usual one: UVM calls every build_phase from the top down, and only once it has finished does it start the connect_phase from the bottom up
class communication_test extends uvm_test; `uvm_component_utils(communication_test) producer producer_h; consumer consumer_h; uvm_tlm_fifo #(int) fifo_h; function new(string name, uvm_component parent); super.new(name, parent); endfunction : new function void build_phase(uvm_phase phase); producer_h = new("producer_h", this); consumer_h = new("consumer_h", this); fifo_h = new("fifo_h", this); endfunction : build_phase // Connect phase: the two ports and the fifo already exist -- build_phase // runs first, top-down -- so this is where they get wired together. function void connect_phase(uvm_phase phase); producer_h.put_port_h.connect(fifo_h.put_export); consumer_h.get_port_h.connect(fifo_h.get_export); endfunction : connect_phase endclass : communication_test
Notes: It is worth saying again why the order is that one, because here you see what it is for: the connect_phase connects a port to an export, and for that both objects have to exist. If connect were top-down, the test would try to connect children that had not been built yet. The classic error of this slide, which compiles and fails at run time: creating the FIFO in the connect_phase instead of the build_phase. UVM catches it with an ILLCRT fatal —“It is illegal to create a component (‘x’ under ‘y’) after the build phase has ended” (uvm_component.svh:1721)—, and at least it warns you with the name. Forgetting the connect() of a put/get port also warns, and well: resolve_bindings() reports a UVM_ERROR [Connection Error] connection count of 0 does not meet required minimum of 1 with the name of the port, in end_of_elaboration and before a single cycle runs (uvm_port_base.svh:886). The one that stays quiet is the analysis port, because its minimum is 0: a write() into an unconnected port is legal and prints nothing. It is the same asymmetry as the previous section, and it is the one to remember. And one worth pointing out in passing: here the producer and the consumer are children of the test, not of an env. It is on purpose, because the section is about the mechanism. In the real testbench this goes inside the agent, with the sequencer on one side and the driver on the other.

## Slide 245: When somebody has to wait
Connecting them: put_export and get_export
It is the same connect() as the analysis ports: on one side the port, on the other the export the FIFO provides
uvm_tlm_fifo exposes twelve handles; the two that get used are put_export for the one that puts and get_export for the one that takes out —which is an alias of get_peek_export, and that is the name you are going to see in print_topology()—
The rule that holds for all of TLM: the port connects to the export, never two ports to each other
// Connect phase: the two ports and the fifo already exist -- build_phase // runs first, top-down -- so this is where they get wired together. function void connect_phase(uvm_phase phase); producer_h.put_port_h.connect(fifo_h.put_export); consumer_h.get_port_h.connect(fifo_h.get_export); endfunction : connect_phase
UVM_INFO @ 0: reporter [RNTST] Running test communication_test... UVM_INFO producer.svh(28) @ 0: uvm_test_top.producer_h [PRODUCER] Sent 1 UVM_INFO consumer.svh(19) @ 0: uvm_test_top.consumer_h [CONSUMER] Received: 1 UVM_INFO producer.svh(28) @ 0: uvm_test_top.producer_h [PRODUCER] Sent 2 UVM_INFO consumer.svh(19) @ 0: uvm_test_top.consumer_h [CONSUMER] Received: 2 UVM_INFO producer.svh(28) @ 0: uvm_test_top.producer_h [PRODUCER] Sent 3 UVM_INFO consumer.svh(19) @ 0: uvm_test_top.consumer_h [CONSUMER] Received: 3 UVM_INFO $UVM_HOME/src/base/uvm_report_server.svh(1009) @ 0: reporter [UVM/REPORT/SERVER] --- UVM Report Summary --- ** Report counts by severity UVM_INFO : 7 UVM_WARNING : 0 UVM_ERROR : 0 UVM_FATAL : 0 ** Report counts by id [CONSUMER] 3 [PRODUCER] 3 [RNTST] 1 - $UVM_HOME/src/base/uvm_root.svh:633: Verilog $finish - S i m u l a t i o n R e p o r t: Verilator 5.052 2026-09-05 - Verilator: $finish at 0s
Notes: Two things about the output, which do not belong to this section but are seen here first. The messages come out with `uvm_info, not with $display: that is why every line brings the time, the hierarchical path of the component and the file along on its own. That is free, and it is reporting, which they already saw closing day 3. And the other one: every @ says 0. In this example there is not a single #delay —the blocking handshake suspends and resumes within the same instant—, so the synchronization of the two threads does not come from the clock: it comes from the one-element FIFO. In the example that follows the clocks show up and the numbers stop being 0.

## Slide 246: When somebody has to wait
NON-blocking communication
Blocking is fine as long as the one waiting has nothing better to do. With a clock in the middle, standing there waiting means losing an edge
That is what the non-blocking versions are for: try_put() and try_get()
They return 1 if they could and 0 if they could not, and carry on. That is why they are function and not task: they consume no time
class consumer extends uvm_component; `uvm_component_utils(consumer); uvm_get_port #(int) get_port_h; virtual clk_bfm clk_bfm_i; int shared; function void build_phase(uvm_phase phase); get_port_h = new("get_port_h", this); clk_bfm_i = example_pkg::clk_bfm_i; endfunction : build_phase // Consumer and producer run on different clocks // The consumer has its first positive edge at 7ns // and then checks the data every 14ns, because it uses bfm.clk (= 14ns) // The producer produces one datum every 17ns task run_phase(uvm_phase phase); forever begin @(posedge clk_bfm_i.clk); if (get_port_h.try_get(shared)) `uvm_info("CONSUMER", $sformatf("Received: %0d", shared), UVM_MEDIUM) end endtask : run_phase function new(string name, uvm_component parent); super.new(name, parent); endfunction : new endclass : consumer
UVM_INFO @ 0: reporter [RNTST] Running test communication_test... UVM_INFO producer.svh(18) @ 17: uvm_test_top.producer_h [PRODUCER] Sent 1 UVM_INFO consumer.svh(21) @ 21: uvm_test_top.consumer_h [CONSUMER] Received: 1 UVM_INFO producer.svh(18) @ 34: uvm_test_top.producer_h [PRODUCER] Sent 2 UVM_INFO consumer.svh(21) @ 35: uvm_test_top.consumer_h [CONSUMER] Received: 2 UVM_INFO producer.svh(18) @ 51: uvm_test_top.producer_h [PRODUCER] Sent 3 UVM_INFO consumer.svh(21) @ 63: uvm_test_top.consumer_h [CONSUMER] Received: 3 UVM_INFO $UVM_HOME/src/base/uvm_report_server.svh(1009) @ 68: reporter [UVM/REPORT/SERVER] --- UVM Report Summary --- ** Report counts by severity UVM_INFO : 7 UVM_WARNING : 0 UVM_ERROR : 0 UVM_FATAL : 0 ** Report counts by id [CONSUMER] 3 [PRODUCER] 3 [RNTST] 1 - $UVM_HOME/src/base/uvm_root.svh:633: Verilog $finish - S i m u l a t i o n R e p o r t: Verilator 5.052 2026-09-05 - Verilator: $finish at 68ns
Notes: try_get() returns 0 and carries on: it does not wait. It is the difference between a consumer that hangs until there is data and one that can do something else in the meantime. Careful, in results.txt the zeros are not visible —the consumer only prints when it gets data—: they are in the timeline of the slide that follows. The time on each line is not printed by the message: UVM puts it in the @, and that is why here you can read the race between the two clocks without having written a single line of formatting.

## Slide 247: When somebody has to wait
NON-blocking communication: the timeline
Timeline of the non-blocking example: at 7 ns and 49 ns the FIFO is empty and try_get() returns 0

## Slide 248
The producer puts a piece of data in every 17 ns and the consumer looks every 14 ns: the clocks run differently, and on two edges the FIFO is empty
There try_get() returns 0 and the consumer carries on. With get() it stayed waiting
Notes: The numbers are not from a drawing: they are the @ of the Sent and Received of results.txt, the previous slide. The edge to make them see is the one at 49 ns. Data 3 only gets put in at 51, so the consumer arrives a little early, leaves empty-handed and comes back 14 ns later. With get() that thread was left blocked right there, and in a testbench with a clock that is a lost edge.

## Slide 249: When somebody has to wait
How TLM diagrams are read
Interthread communication with put port, get port and uvm_tlm_fifo

## Slide 250
The convention holds for all the UVM material you are going to read afterwards:
  Square: put port / get port — the one that starts the call
  Circle: export — the one that receives it and implements it
  Diamond: analysis port — the one from the two previous sections
Notes: It is worth the student taking the convention home, because it is the same one in the UVM User Guide, in the Verification Academy and in any testbench diagram they get handed at work. It does not belong to this course. The rule that orders the three figures, and the one that makes a TLM diagram readable without a legend: the square end always points at the circle. The one with the square is the one that calls; the one with the circle is the one that has the method written. That is why a port connects to an export and never to another port. The diamond is the special case they have already seen: an analysis port can point at many circles at once, and that is why it is drawn differently. The other two are one to one.

## Slide 251: When somebody has to wait
fork: the three ways of starting in parallel
fork wait_done(); count_cycles(); join // goes on when BOTH have finished fork wait_done(); count_cycles(); join_any // goes on with THE FIRST; the other stays alive fork wait_done(); count_cycles(); join_none // goes on NOW; both stay running
Variant | The parent goes on… | What it is used for
join | when all of them finish | two checks that both have to close
join_any | when the first one finishes | response against a timeout
join_none | right away | launching threads that live for the whole test
The difference between the three is not how they start —all three start everything at once— but when the one that started them goes on
You have used join_none already: it is the fork of the day 2 testbench class, and it is what UVM does on its own with one run_phase() per component
The branch left alive after a join_any does not die on its own. It goes on until it finishes — or until somebody kills it, which is the next slide
Notes: It is the unit called threads and up to here the threads were put there by UVM. This slide and the next two are the three words of the language any production monitor or driver is written with, and the three fit in one table. The point worth repeating, because it is where everybody gets confused the first time: all three start the same. The fork processes are all launched at the same instant in the three variants. The only thing that changes is what the parent process does immediately afterwards, and that is why the middle column is the one to read. One example per variant is enough to make it stick. join: send the stimulus and count the cycles, and do not go on until both have finished. join_any: wait for the DUT’s response or for a timeout to expire, whichever happens first. join_none: the monitor’s run_phase, which starts and stays watching forever while the rest of the testbench goes on. And the hook back to day 2, worth making explicit: the hand-written testbench class used fork ... join_none to start the three objects. It was not a coincidence nor a trick — it is exactly what UVM does when it runs the run_phase of a hundred components at once.

## Slide 252: When somebody has to wait
disable fork and wait fork: turning off what stayed on
// The response-against-timeout idiom. The outer fork ISOLATES fork begin fork begin wait_done(); `uvm_info("BFM", "it arrived", UVM_LOW) end begin repeat (100) @(posedge clk); `uvm_error("BFM", "timeout") end join_any disable fork; // kills the sister that lost, and nobody else end join wait fork; // kills nobody: it waits for ALL the children of this thread
disable fork kills every child process of the thread that executes it. That is why the outer fork begin ... end join: without it, it also takes down whatever was already running
wait fork is the opposite: it kills nothing, it waits for the children to finish. It is what a test uses so as not to close with transactions in flight
The join_any + disable fork pair is the timeout of every production BFM. It gets written once and copied forever
Whichever finishes first wins: if done arrives before the 100 edges, the timeout uvm_error is not printed; if it does not, the uvm_info of "it arrived" is not printed. The disable fork kills the loser
Notes: The disable fork without the isolating fork ... join is the classic bug of this construct and is worth drawing: it kills every child of the current thread, not those of the fork next door. If the run_phase had already launched a monitor with join_none and then does a bare disable fork, the monitor dies and the testbench goes on running blind. There is no error, there is no warning: there is a log that stops having lines. The way to remember it is to think about the scope: disable fork does not say which fork. It says “the children of this process”. The outer fork begin ... end join creates a new process whose only children are the two of the join_any, and that is why the disable cannot reach any further. wait fork is the quiet partner and gets used far less than it should: it is what is needed at the end of a sequence or of a run_phase that launched things with join_none and does not want the phase to end with half the stimulus in the air. In UVM the same problem is solved with objections — but inside a task, wait fork is the answer.

## Slide 253: When somebody has to wait
⚠ The trap: the for index inside the fork
// A -- a single variable, shared by the three threads. A join_none runs // nothing: it schedules. By the time the three run, the for is over. for (i = 0; i < 3; i++) fork got = {got, $sformatf("%0d", i)}; join_none wait fork; check("int i outside the for, no copy", "333"); // B -- declared inside the for: one per pass, and nothing to copy. for (int j = 0; j < 3; j++) fork got = {got, $sformatf("%0d", j)}; join_none wait fork; check("int j declared in the for", "012"); // C -- the slide's one: the automatic as the first line of a begin/end. // Here the copy is NOT made when the fork is scheduled, so k reads the same // i that A does and gives the same answer as A. This is the finding. for (i = 0; i < 3; i++) fork begin automatic int k = i; got = {got, $sformatf("%0d", k)}; end join_none wait fork; check("fork begin automatic k = i; end (the slide's)", "333"); // D -- the LRM 9.3.2 one: the automatic declared in the fork, no begin/end. // Same workaround, written where the LRM puts it, and this one does copy. for (i = 0; i < 3; i++) fork automatic int k = i; got = {got, $sformatf("%0d", k)}; join_none wait fork; check("fork automatic k = i; no begin/end (LRM 9.3.2)", "012");
A join_none does not execute anything yet: it leaves the thread ready and goes on. By the time the thread runs, the for has already finished and the variable holds the last value
If the variable is declared inside the for, each pass has its own and there is no problem. It is what the LRM says and what Verilator does
If it comes from outside —an int of the run_phase, a field of the class— it has to be copied with an automatic, and where the copy is written changes the result: inside a fork begin ... end it does not copy; declared in the fork itself, with no begin/end —which is the LRM 1800-2017 §9.3.2 form— it does
Measured on Verilator 5.052, and the file ends in $fatal the day any of it changes (make repros): the four variants print 3 3 3, 0 1 2, 3 3 3 and 0 1 2
Notes: It is the most expensive threads bug and the hardest to see when reading the code, because the three versions look very much alike. It is worth asking the question before showing the answer: “what does the first one print?”. Almost everybody says 0 1 2. The explanation to leave behind is a single sentence: join_none does not run the thread, it schedules it. The for walks straight to the end, and only then does the scheduler give the three threads their turn — and they read the variable now, not when they were launched. With i outside there is a single variable, and now it holds 3. The version with for (int j …) works and it is worth saying why, so it does not look like magic: the LRM declares automatic the variable of a for that declares it, so each pass has its own copy. It is measured here, it is not theory. The case where the automatic is needed anyway is the one that shows up in real life: the index is not the for’s, it is a field of the class or an argument of the task. There is no copy per pass there and it has to be made by hand — and here is the part this slide used to get wrong: the automatic as the first line of a fork begin ... end does not copy. On Verilator 5.052 variant C prints 3 3 3, just like A. The one that copies is D, the LRM §9.3.2 one: the declaration inside the fork, with no begin/end. The two look so alike that it is easy to write the one that does not work. The practical rule to take home: if a thread launched with join_none reads a variable from outside, declare the copy in the fork, not inside a begin.

## Slide 254: When somebody has to wait
Summary of the unit
Inter-thread communication between objects is the equivalent of what ports do between modules: passing data from one thread to another
UVM provides it with uvm_put_port, uvm_get_port and uvm_tlm_fifo
Any object that wants to communicate with another thread has to instantiate a port and connect it to a FIFO
Careful with the pair of names: the analysis ports of the two previous sections are intra-thread —write() is a function and runs in the thread of the one publishing—; this is inter-thread, and that is why put() and get() are task
And underneath it all there is fork: join waits for all, join_any for the first, join_none for none. disable fork kills the children and wait fork waits for them
Now we have to use this to wire our TB: we are going to separate the stimulus generation from the driver of the DUT
Notes: Worth closing with the two-column table that one producer, many listeners opened with, because it is the one that orders the four units of the day: Intra-thread — uvm_analysis_port + uvm_subscriber, write() is a function, it consumes no time, a single thread, and it is for the analysis layer. Inter-thread — uvm_put_port / uvm_get_port + uvm_tlm_fifo, put() and get() are task, they block, two threads, and they are for handing stimulus to a driver. The short way of telling them apart, and it is question 3 of the review: if it is a function, it is intra-thread. A function cannot have an @ or a #, so it cannot wait for anybody. The word task is the one that gives away that there are two threads.

## Slide 255
Who waits for whom
What to send and how to send it
The analysis ports split the analysis: the monitor watches, the subscribers interpret. The same is still missing on the stimulus side
Today the base_tester does two things: it picks the operation and it applies it on the BFM cycle by cycle. They are two jobs that change for different reasons
The what changes with every test. The how changes only if the protocol of the DUT changes — which means, almost never
Separating them leaves the protocol written in a single place: the driver. Every new test writes what to send and never looks at an @(negedge clk) again
And since the two run in different threads, the joint is the one from inter-thread communication: uvm_put_port, uvm_get_port and a uvm_tlm_fifo in the middle
Notes: It is the third time the course does the same operation, and it is worth saying it that explicitly because it is what has to be taken home: in interfaces and BFM we took the protocol out of the test and put it in the BFM; in the analysis ports we took the observing out of the analysers and put it in the monitor; here we take the applying of the stimulus out of the generator and put it in the driver. The question that orders everything: does this change when the test changes, or when the design changes? If it changes with the test, it is stimulus. If it changes with the design, it is structure. They do not go in the same class. And the notice of where this is heading: in the agents this put/get pair is called a sequencer and comes already in place, and the tester is called a sequence. What we are assembling by hand here is exactly what UVM gives you ready-made — that is why it gets assembled by hand first.

## Slide 256: Who waits for whom
The tester does two jobs, and one of them is not its own
This is how the base_tester of the analysis ports was left, and it does two jobs:
  it picks which operation to send
  and it applies it on the BFM, cycle by cycle
The second one is the one that should not be there: it is protocol, and the protocol does not change when the test changes
The class that takes that job away is called a driver: it takes a piece of data from the testbench and turns it into signals
task run_phase(uvm_phase phase); byte unsigned iA; byte unsigned iB; operation_t op_set; phase.raise_objection(this); bfm.reset_alu(); repeat (1000) begin : random_loop op_set = get_op(); iA = get_data(); iB = get_data(); bfm.send_op(iA, iB, op_set); end : random_loop #500; phase.drop_objection(this); endtask : run_phase
Notes: It is worth reading the code pointing a finger at where one job ends and the other starts: get_op() and get_data() are the what; everything that follows —the bfm.send_op(), the wait, the cycle— is the how. They are glued together in the same task and that is why they cannot be changed separately. The proof that they are wrongly together is a question: if tomorrow the DUT adds a signal to the protocol, how many classes have to be touched? Every one that inherits from base_tester, even though none of them knows anything about protocol. That is coupling, and the classic symptom is exactly this one — a class that changes for two different reasons. The name driver is worth saying already, even though the class does not exist yet, so that the word does not show up for the first time on day 6. A driver is what turns a piece of data into signals. Nothing more than that, and that is why it is the only class of the testbench that has the right to write an @(negedge clk).

## Slide 257: Who waits for whom
How it ends up split
The result: one class decides what to send and another one knows how to send it, and between the two there is a FIFO instead of a method call
The VTALU tester and driver separated by a uvm_tlm_fifo

## Slide 258
Notes: The box in the middle is the one to point at, because it is the one that surprises: between the tester and the driver there is no arrow. There is a FIFO. The tester does not call the driver, and it does not even have a handle to it. It is worth making the comparison with the diagram of the analysis ports, which is two sections back: over there the monitor did not know its listeners either. It is the same idea applied on the other side of the testbench, and it is the reason why on day 6 every sequence can be changed without touching the driver. And the difference between the two diagrams that does matter, because it is question 3 of the review: that one was intra-thread —write() is a function and does not wait for anybody—, this one is inter-thread. Here the one putting can be left waiting, and that is precisely the synchronization that used to have to be written by hand.

## Slide 259: Who waits for whom
The env: seven objects and five connect()
Mantra: “Ports connect to exports”
function void build_phase(uvm_phase phase); command_f = new("command_f", this); random_tester_h = random_tester::type_id::create("random_tester_h", this); driver_h = driver::type_id::create("driver_h", this); coverage_h = coverage::type_id::create("coverage_h", this); scoreboard_h = scoreboard::type_id::create("scoreboard_h", this); command_monitor_h = command_monitor::type_id::create("command_monitor_h", this); result_monitor_h = result_monitor::type_id::create("result_monitor_h", this); endfunction : build_phase function void connect_phase(uvm_phase phase); // PORTS CONNECT TO EXPORTS! driver_h.command_port.connect(command_f.get_export); random_tester_h.command_port.connect(command_f.put_export); result_monitor_h.ap.connect(scoreboard_h.analysis_export); command_monitor_h.ap.connect(scoreboard_h.cmd_f.analysis_export); command_monitor_h.ap.connect(coverage_h.analysis_export); endfunction : connect_phase
Notes: Count the objects of this build_phase: there are seven, plus five connect(). That number is the one to remember, because in the agents this same testbench is going to have one agent and two subscribers. Worth writing it on the board so you can come back to it. The two new lines of the connect_phase are a pair and get read together: the tester puts into the put_export of the FIFO, the driver takes out of the get_export. Nobody connects the tester to the driver — they do not know each other, and that is the point. The mantra has a reason worth giving instead of repeating it like a parrot: the port is the one that asks for the service, the export is the one that offers it. The FIFO offers both ends, so it has two exports. If you write it the other way round it does not compile, and the compiler message is one of the worst in UVM. And the detail that gets forgotten: command_f = new(...), not create(). It is not that the FIFO is missing from the factory —it is registered, tlm1/uvm_tlm_fifos.svh:62—: it is that the size goes through the constructor and create() does not know how to pass it. The ones that really are not in the factory are the ports and the exports.

## Slide 260: Who waits for whom
The base_tester, without a single signal
Only one thing changes: where there was a handle to the BFM there is now a uvm_put_port #(command_s) called command_port
random_tester and add_tester do not get touched. They only define get_op() and get_data(), and neither of the two knew how the stimulus was applied
That is the return on having separated things properly in the env: the change stopped at the base class
virtual class base_tester extends uvm_component; `uvm_component_utils(base_tester) // the handle to the BFM is replaced by a uvm_put_port uvm_put_port #(command_s) command_port; function void build_phase(uvm_phase phase); command_port = new("command_port", this); endfunction : build_phase pure virtual function operation_t get_op(); pure virtual function byte get_data(); task run_phase(uvm_phase phase); byte unsigned iA; byte unsigned iB; operation_t op_set; command_s command; phase.raise_objection(this); command.op = rst_op; command_port.put(command); repeat (1000) begin : random_loop command.op = get_op(); command.A = get_data(); command.B = get_data(); command_port.put(command); end : random_loop #500; phase.drop_objection(this); endtask : run_phase
Notes: What matters about this class is what disappeared: there is not a single @(negedge clk), nor a bfm.start, nor the wait for the done. The tester was reduced to picking what to send and putting it on the port. And yet random_tester and add_tester were not touched: they only define get_op() and get_data(), and neither of the two knew how the stimulus was applied. That is what separating properly buys you — the change stopped at the base class. The put() is a task and it blocks: if the driver is still handling the previous operation, the tester waits there. The one-element FIFO of inter-thread communication is what synchronizes the two threads, without a single semaphore. And there is a #500 at the end, before the drop_objection, worth pointing out as what it is: a patch. It is there so that the objection does not drop while the last operation is still travelling. In the sequences it disappears, because finish_item() only comes back when the operation has really finished. An eyeballed #500 in a testbench is always an unanswered question.

## Slide 261: Who waits for whom
The driver: the only one that touches the wire
A forever with two lines: get() a command —which blocks until there is one— and apply it with send_op(). The whole protocol lives here
class driver extends uvm_component; `uvm_component_utils(driver) virtual vtalu_bfm bfm; uvm_get_port #(command_s) command_port; function void build_phase(uvm_phase phase); if (!uvm_config_db#(virtual vtalu_bfm)::get(this, "", "bfm", bfm)) `uvm_fatal("DRIVER", "Failed to get BFM") command_port = new("command_port", this); endfunction : build_phase task run_phase(uvm_phase phase); command_s command; forever begin : command_loop // Blocking: if there are no commands to send, it waits command_port.get(command); bfm.send_op(command.A, command.B, command.op); end : command_loop endtask : run_phase
Notes: This division is the one UVM formalizes in the agents: the tester decides WHAT to send, the driver knows HOW to send it. In a real agent the tester is going to be called a sequence and this put/get is going to be called get_next_item / item_done. Anticipating it here makes day 6 start downhill.

## Slide 262: Who waits for whom
Summary of the unit
The testbench ended up split into three layers that change for different reasons: the stimulus (tester), the protocol (driver and monitors) and the analysis (scoreboard and coverage)
None of them knows the insides of the others: between them only commands and results travel
What is still missing is for the testbench to know how to tell what is going on, which is the unit that follows
Notes: It is worth closing the day with the three layers written on the board, because it is the map that orders everything that comes: stimulus, protocol, analysis. The four sections of today were about building that separation, and tomorrow’s do not add layers — they put UVM names on the ones already there. The control question, which besides answers itself if the day closed properly: in which of the three layers does an @(negedge clk) live? In one only, the protocol. If it shows up in another one, something got separated wrong. And the notice about what is missing, worth giving now: between the tester and the driver travel command_s, which are structs. They work, but they do not randomize themselves, they do not compare themselves and they do not print themselves — and that is exactly what day 5 is going to fix by turning them into transactions.

## Slide 263
Review · Day 4
1 of 5 · Observer Pattern
In the Observer pattern, what does the observed object know about its observers?
☐ How many there are and of what type
☐ Only the first one that subscribed
☐ It knows them because they get handed to it in the constructor, one by one
☒ Nothing: not how many there are, not who they are
It knows nothing — and that ignorance is the whole point. Adding a fourth subscriber does not force you to touch one line of the one publishing.

## Slide 264
Review · Day 4
2 of 5 · Analysis Ports
A uvm_subscriber needs data from two different analysis ports. How does that get solved?
☐ By implementing the write() method twice
☒ With a uvm_tlm_analysis_fifo for the second port
☐ By registering the component twice in the factory, once per port
☐ By connecting both ports to the same analysis_export
With a uvm_tlm_analysis_fifo — a uvm_subscriber has a single write(), so it can only listen to one port. The FIFO gives an analysis_export on one side and a try_get() on the other. It is what the VTALU scoreboard does. The other way is `uvm_analysis_imp_decl, which manufactures one write_ per suffix: they are not two write() in the same class, which SystemVerilog does not allow.

## Slide 265
Review · Day 4
3 of 5 · Intra vs. inter thread
When the monitor publishes and the write()s of the subscribers run, how many threads are involved?
☐ One per subscriber
☐ Two: the publisher’s and the subscriber’s
☒ Only one: write() is a function call
☐ One per subscriber plus the monitor’s, and UVM syncs them at the end of the delta
Only one, and it is intra-thread communication — write() is a function, not a task: it consumes no time and runs in the thread of the one publishing. That is precisely why another mechanism (put/get + FIFO) is needed to talk between threads.

## Slide 266
Review · Day 4
4 of 5 · Put and get ports
The consumer calls get() and the uvm_tlm_fifo is empty. What happens?
☒ It blocks until the producer puts a piece of data in
☐ It returns 0 and carries on
☐ A UVM fatal error
☐ It returns the last piece of data read, which stays in the FIFO until overwritten
It blocks — get() is blocking, and that is why it is declared task and not function. That is the whole synchronization: no hand-written signal handshake is needed.

## Slide 267
Review · Day 4
5 of 5 · try_get()
And try_get() with the FIFO empty?
☐ It blocks just like get()
☐ It returns 1 with a garbage value
☐ It waits one clock cycle and tries again, up to the timeout of the phase
☒ It returns 0 immediately, without blocking
It returns 0 and carries on — it is the non-blocking version, and that is why it can be a function. Notice that the scoreboard uses it in a do ... while to skip over the no_ops and the rst_ops.

## Slide 268
Exercise · Day 4 · 1 of 2
One more observer, without touching the ones already watching
cd code/ejercicios/d4 && bash run.sh
A uvm_subscriber #(command_s) that counts the commands
Instantiate it and connect it in the env, without touching the connections that are already there
It is marked by cross-checking: your count has to come out the same as the command_monitor’s
Notes: The short exercise of the course: twenty minutes. What is being practised is not writing the class —it is ten lines— but the connect_phase: if they forget the connect, the class compiles, runs, and counts zero. That is why the marking is done by cross-checking against the lines the command_monitor prints: it is not enough for the number to exist, it has to match what another component saw.

## Slide 269
Exercise · Day 4 · 2 of 2
The #500 is a patch
cd code/ejercicios/d4b && bash run.sh
The put and get testbench with one line changed: the env’s FIFO comes unbounded
The tester empties its thousand commands at t = 0, waits the usual #500, drops the objection — and the simulation ends in green with 13 commands on the bus
It gets fixed in the driver: an objection while there is a command in flight
env.svh does not get touched: the unbounded FIFO is the DUT of this exercise
Notes: It is the exercise that puts hands on the two things the section claims and does not demonstrate: that put() blocks, and that the tester’s #500 is a patch. The number is measured and is worth saying: with the size-1 FIFO the testbench sends the thousand operations; with the unbounded FIFO, 13. Nobody touched the DUT, nobody touched the stimulus, and the difference is a constructor’s default argument. What the back-pressure was doing without anybody having designed it that way: keeping the tester in step with the bus. Take it away and the tester is left talking to itself. The fix has to be discussed, because the obvious answer —raise the #500— is the one to reject. The question that orders it: who knows when the bus is done? Not the tester, which knows when it is done putting. It is the driver, which is the one driving. That is why the objection goes there, and that is why it is the pattern of any real UVM driver. And the detail that decides whether the exercise works, which is also from the field: the raise/drop pair goes after the get(), not around it. Around it, the driver holds an objection waiting for work that is never coming, and the test never ends — which is the other failure mode of the debug appendix table.

## Slide 270
Yesterday we left…
Where the testbench stands
The monitor publishes and knows nobody: the scoreboard and the coverage hang off it, and adding a third does not touch the one that publishes
The TLM FIFOs settled who waits for whom, and fork/join who runs with whom
But the data is still three loose fields: A, B and op travel separately, they get copied by hand, and comparing them means writing the whole comparison
Notes: The day 5 recap has to install the discomfort of the loose data, because that is what justifies a whole unit about objects that do nothing but carry data. The third bullet is literal: in yesterday’s testbench, copying a command is three assignments, and comparing it is three ==. With two more fields it is five and five. Today that becomes copy() and compare(), written once.

## Slide 271
Agenda
Day 5 · ≈ 4 h 30 · unit 6 · the data
Copying an object that contains another
Transactions
Constrained random
By the end of the day you can:
Write a constraint that reaches a corner case, and measure whether the dist does what it says
Close a bin that was left open, with a directed case asked for through randomize() with {}
Explain the difference between copying the handle and copying the object, and what happens when the object contains another
Notes: The second one is the novelty of the day and the one that pays off the most at work: measuring is half of it, closing is the other half. The last two exercises of the afternoon are two thirds of that cycle —measure the dist, close the bin— and day 7 closes it by accumulating seeds. Row 12 of the self-assessment says measure, not write, and that is on purpose: a dist with the weights right can give a histogram that lies, and whoever never measured it has no way of knowing.

## Slide 272
Copying an object that contains another
The handle is not the object
From the transactions on, the testbench data stops being a struct and becomes objects that travel: the monitor creates them, the scoreboard compares them
And there a problem appears that a struct did not have. A struct gets copied when you assign it; an object does not: obj1_h = obj2_h copies the handle, not the data
Which means two parts of the testbench can be looking at the same object without knowing it. If one modifies it, the other sees the change halfway through
Copying it for real has to be written, and written at every level of the hierarchy, or the fields from above get lost in silence
This section is the OOP that is missing so that the transactions can be copied, compared and printed without lying
Notes: It is an OOP section in the middle of UVM, and it is worth saying why it is here and not on day 2: because only now is it needed. Up to reporting —the closing of day 3— the data was a struct and copied itself. The bug in the second bullet gets written by everybody once, and the symptom is horrible: you send a transaction to the scoreboard, you go on using the same handle for the next one, you modify it, and the scoreboard compares against data that changed after it received it. It does not fail every time, and when it does it looks like a DUT bug. The other half —the super at every level— has a different and more treacherous symptom: the day somebody puts a new class in the middle of the hierarchy, the convert2string() stops printing half the fields and nobody finds out, because it goes on printing something. The question to start with: if handle_a = handle_b, how many objects are there? One. It is the same question as in classes and extensions, now with consequences.

## Slide 273: Copying an object that contains another
Never duplicate code
“If we find ourselves copying code and making small modifications to it inside our program, we are doing things wrong. Code must never be duplicated.”
In OOP, instead of copying code…
we extend classes

## Slide 274: Copying an object that contains another
convert2string(): the problem
The four levels of the hierarchy

## Slide 275
The hierarchy goes from the general to the particular, and each class adds fields of its own
We want two things from it: to be able to copy a whole object and to print it whole, without anything from the levels above getting lost
This first version works. Count how many times the name of a field of the base class shows up
// ILLUSTRATION -- not compiled. The WRONG way to write convert2string! // The classes are drawn as comments: only the methods are on screen. //class trago; virtual function string convert2string(); return $sformatf("Hielos: %0d", hielos); endfunction : convert2string //class fernet extends trago; function string convert2string(); string coca_s; coca_s = (con_coca) ? "si" : "no"; return $sformatf("Hielos: %0d Coca: %s", hielos, coca_s); endfunction : convert2string //class fernet_doble extends fernet; function string convert2string(); return {$sformatf("hielos: %0d coca: %0b mesa: %s", hielos, con_coca, mesa) }; endfunction : convert2string
Notes: This version works, and that is the problem: it looks fine and it is wrong. Every convert2string() prints every field by hand, including the ones it inherited. Go to the $sformatf of the bottom-most class and count how many times the name of a field of the class above is repeated. Every one of those repetitions is a line you have to remember to touch the day a field gets added. The question that sets up the next slide: what happens if tomorrow somebody puts a new class in the middle of the hierarchy? The ones below go on printing what they knew, the one in the middle does not show up, and there is no error. The method still returns a string.

## Slide 276: Copying an object that contains another
convert2string(): the deep version
A new level in the hierarchy breaks convert2string(): graduacion does not appear in the string

## Slide 277
The day somebody puts a class in the middle, the ones below go on printing what they knew and the one in the middle does not show up. And there is no error: the method still returns a string
The rule that fixes it: each class prints only what is its own and asks super for the rest
Nobody knows what is further up, so inserting a level breaks nothing
// ILLUSTRATION -- not compiled. The same three methods written deep, with the // classes drawn as comments. The version that does compile is deep.sv. //virtual class trago; virtual function string convert2string(); return $sformatf("Hielos: %0d", hielos); endfunction : convert2string //class con_alcohol extends trago; function string convert2string(); return {super.convert2string(), $sformatf("\ngraduacion: %0d",graduacion)}; endfunction : convert2string //class fernet extends con_alcohol; function string convert2string(); string coca_s; coca_s = (con_coca) ? "si" : "no"; return {super.convert2string(), "\nCoca: ",coca_s}; endfunction : convert2string
Notes: The rule, short: every method of the hierarchy takes care only of its own fields and asks super for the rest. Nobody knows what is further up, and that is why inserting a class in the middle breaks nothing. The pattern repeats in the same way in the three methods of the section —convert2string(), do_copy(), do_compare()— and in the three of UVM too. If you get into the habit of writing the call to super first, before touching your own fields, you never forget it. It is worth pointing out the parallel with something they have already seen: it is exactly the same argument as the super.new() of classes and extensions. The top part of the object has to be built too — and it also has to be printed, copied and compared.

## Slide 278: Copying an object that contains another
The equals sign copies nothing
obj1_h = obj2_h copies nothing: it leaves two handles pointing at the same object
If you modify it through one, the other sees it. There is no notice, there is no warning
With a struct that did not happen: it gets copied when you assign it. It is the difference to keep in mind from here to the end of the course
Notes: It copies the handle, not the object. It is the bug everybody writes once: you modify the transaction you already sent to the scoreboard and the scoreboard sees the change halfway through. This is where the clone() of the transactions comes from.

## Slide 279: Copying an object that contains another
Copying for real is two steps
Copying for real is two steps, and they have to be written: instantiate a new object and hand it the data field by field
// ILLUSTRATION -- not compiled. The initial block of deep.sv:110-118, on its own. initial begin fernet_hielo1_h = new(.hielos(2), .con_coca(1), .graduacion(2), .mesa("mesa 4"), .medidas(2)); $display("\n--- Fernet 1 ---\n", fernet_hielo1_h.convert2string()); fernet_hielo2_h = new(); $display("\n--- Fernet 2 before the copy ---\n", fernet_hielo2_h.convert2string()); // do_copy is a method that copies member by member // it suffers from the same problem already seen with convert2string() // Each class can copy the variables defined in that class // super.do_copy() has to be used to copy the inherited ones fernet_hielo2_h.do_copy(fernet_hielo1_h); $display("\n--- Fernet 2 after the copy ---\n", fernet_hielo2_h.convert2string()); end
The new() is the first step and it is not optional: without a new object on the other side, there is nowhere to copy to
The second step is by hand, field by field. SystemVerilog has no built-in deep copy
And field by field means the fields of the classes above too, which is exactly what gets forgotten
Notes: It is worth making the comparison with the assignment of the previous slide out loud: a = b is one line and copies nothing; copying for real is two steps and both have to be remembered. That the language does not bring a deep copy is not an oversight by the committee: there is no general answer. If the class has a handle to another object, do you copy the handle or the object? It depends, and that is why you have to decide it yourself in every do_copy(). It is exactly the same dilemma the transactions are going to have if some day they carry an array of objects inside. In this course it does not happen, but it is worth leaving the question on the table.

## Slide 280: Copying an object that contains another
do_copy(): each class touches what is its own
do_copy(): Every class in the hierarchy has to call its parent class, and therefore every do_copy() method needs the same type of argument. But we have different classes… We use polymorphism
class fernet_con_hielo extends fernet_doble; byte medidas; function new(int hielos = 0, bit con_coca = 0, int graduacion = 0, string mesa = "", byte medidas = 0); super.new(hielos, graduacion, con_coca, mesa); this.medidas = medidas; endfunction : new function string convert2string(); return {super.convert2string(), "\n", $sformatf("medidas: %0d", medidas)}; endfunction : convert2string //do_copy passes the argument up to its parent class function void do_copy(trago copia); fernet_con_hielo copia_fernet_con_hielo; super.do_copy(copia); // Then the copy gets cast to a variable of its own class type $cast(copia_fernet_con_hielo, copia); this.medidas = copia_fernet_con_hielo.medidas; endfunction : do_copy endclass : fernet_con_hielo
Notes: Here is the detail that looks bureaucratic and is not: every do_copy() of the hierarchy takes an argument of the base class, not of its own. If each one took its own type, the call to super.do_copy(rhs) would not compile — the types would not match. The price is that inside every method you have to $cast in order to read your own fields. And as we saw in the factory, that $cast checks at run time: if somebody tries to copy a mojito onto a fernet, it returns 0 and it has to be caught. It is the first time a signature convention shows up that exists only so that polymorphism can work. In UVM it is going to be the same and with more rules: the argument has to be a uvm_object —and by convention it is called rhs—, do_compare() also takes a uvm_comparer, and so on. When those signatures show up in the transactions, the answer to “why like this?” is this slide.

## Slide 281: Copying an object that contains another
Summary: the terrible solution
function string convert2string(); return { $sformatf( "hielos: %0d coca: %0b mesa: %s medidas: %0d", hielos, con_coca, mesa, medidas ) }; endfunction : convert2string
It is the convert2string() of fernet_con_hielo, the bottom-most class: it prints all four fields by hand, including the three it inherited
It works, and that is why it is dangerous. The day fernet gains a field, this method goes on compiling and goes on printing — less than it should
The whole file is in code/u6/jerarquias/wrong.sv. The three do_copy()s in there do call super; the one with the vice is bad_copy(), at the very bottom
Notes: The rule to leave behind: a class only writes on its own fields. Everything else it asks super for. It is worth counting on screen: hielos shows up in four different convert2string() of this file and con_coca in three. Seven places to remember, and not one of them fails if you forget one. There is a bad_copy() a little further down the file worth opening if there is time to spare: it takes a fernet_con_hielo as an argument instead of a trago. It compiles and it works… until somebody calls it through a handle of the base class, and there no polymorphism can help.

## Slide 282: Copying an object that contains another
Summary: the deep solution
function string convert2string(); string coca_s; coca_s = (con_coca) ? "si" : "no"; return {super.convert2string(), "\nCoca: ", coca_s}; endfunction : convert2string function void do_copy(trago copia); fernet copia_fernet; super.do_copy(copia); $cast(copia_fernet, copia); this.con_coca = copia_fernet.con_coca; endfunction : do_copy
The same two methods, written the way they should be: each one calls super and then touches a single field, its own
convert2string() concatenates what the one above returned; do_copy() calls the one above first and then copies what is its own
With that shape, putting a new class in the middle of the hierarchy works on its own: the chain of super includes it without anybody editing anything
Notes: Closing of the section, and it is worth saying where all of this is going: the three methods they have just written by hand are exactly the three UVM asks for in a transaction. do_copy(), do_compare() and convert2string(), with the same rules about super and $cast. The difference is that in UVM they do not get called directly: you write do_copy() and the testbench calls copy(), which is the one that lives in uvm_object and takes care of the rest. Same idea as the phases — you write the bottom part, the library handles the protocol. And the question to walk out of the day with: if writing this properly costs three methods per class, why does nobody generate it? Somebody does: they are the `uvm_field_* macros. The course does not use them, and the reason is on the super.build_phase() slide of the components — they generate hundreds of lines nobody reads and that show up in the stack when something fails. Read them yes, write them no.

## Slide 283: Copying an object that contains another
Summary of the unit
obj1_h = obj2_h copies nothing: it leaves two handles pointing at the same object. If you touch it through one, the other sees it, and there is not even a warning
With a struct that did not happen —it gets copied when you assign it—, and that is the difference to keep in mind until the end of the course
Copying for real is two steps: instantiate a new object and hand it the data. That is where the clone() of the transactions comes from
In a hierarchy, each class has to touch a single field, its own, and call super. Writing the four fields by hand is the terrible solution
For that to work, the do_copy() / do_compare() all take the same type of argument, the base class. It is polymorphism, once again
The day somebody puts a class in the middle of the hierarchy, the deep version goes on working by itself. The other one you have to go out and fix
Notes: The handle bug is the one everybody writes once: you modify the transaction you already sent to the scoreboard, and the scoreboard sees the change halfway through. It does not fail at the time; it fails later, and somewhere else. The short way to close: the = copies the slip of paper with the address, not the house. And that is why UVM brings copy(), clone() and compare() ready-made — which is exactly the unit that follows.

## Slide 284
Transactions
The testbench is well divided up, and the data is not
The testbench is already well divided up, but the data is still a struct: command_s for the commands and a bare shortint for the results
A struct does nothing by itself. Printing a command is a $sformatf written by hand, and it is written three times: the two monitors and the scoreboard
The same with randomizing and with comparing: every component builds its own, and the day the struct gains a field you have to remember all three
And the result is not even a struct: it is a bare shortint, so the ovf of the VTALU —the second output— has nowhere to travel
A class, on the other hand, has methods: the data and what gets done with it live together, and the rest of the testbench shrinks
Notes: The honest question from the student is “and why not a struct?”. The answer: the struct does not randomize itself, does not compare itself and does not print itself. Everything the testbench used to do by hand with command_s becomes a method of the class, and the rest of the testbench shrinks. The fourth bullet is the most concrete argument and it is worth leaning on it: up to here the analysis port of the result carries a shortint, that is to say a number. The VTALU has two outputs —result and ovf— and that is why the scoreboard of the previous units checks half the DUT and lets the other half through. With a result_transaction with two fields, the check of the ovf shows up on its own. It is the first time in the course that the class is not tidiness: it is the only way.

## Slide 285: Transactions
A transaction is data with the methods that operate on that data
It is the word the industry uses, and there is no magic class behind it: a transaction is that and nothing more
The methods are four, and they are always the same:
  randomize() — it fills itself in, respecting its constraints
  convert2string() — it prints itself
  do_copy() — it copies itself
  do_compare() — it compares itself
What changes is not the data: it is who knows things about it. The tester used to know which values were legal; now it only says “randomize yourself”
And the rest of the testbench shrinks: the three hand-written $sformatf become one call to convert2string()
Notes: The sentence on the slide is the definition to leave written on the board: data with the methods that operate on that data. The third bullet is the shift in the division of responsibilities of the section: until today the tester knew which values were legal —it had a get_data() with the bias written by hand—. From today that lives in the transaction, in a constraint. The question to throw out: if tomorrow the DUT accepts 16-bit operands, how many classes have to be touched? One.

## Slide 286: Transactions
Defining a transaction: which class it extends
Transactions are defined by extending the uvm_sequence_item base class and writing the following methods:
  do_copy()
  do_compare()
  convert2string()
What follows is turning the old command_s structure into a class, command_transaction, method by method
// ILLUSTRATION -- not compiled. The struct as it is in code/u5/put-get/vtalu_pkg.sv, // the one this section turns into a class. typedef struct { byte unsigned A; byte unsigned B; operation_t op; } command_s;
Notes: Careful with the base class, because the old material says something else. The chain is uvm_sequence_item → uvm_transaction → uvm_object, and it is always the first one that gets extended. Two reasons. The small one: in IEEE 1800.2 uvm_transaction is a virtual class, it cannot be instantiated on its own. The big one: a uvm_sequence only knows how to send uvm_sequence_item. If the transaction extends plain uvm_transaction, everything from day 6 —start_item / finish_item— does not compile. Which means the base class we pick today is the one that lets us go on tomorrow.

## Slide 287: Transactions
The randomized fields: the “before”
Today the stimulus gets built with two hand-written functions, get_op() and get_data(), which draw the values with $random — the Verilog-95 one, with a global seed
The legal range of A and B and the bias to the edges are properties of the data, not of the test — and yet they live in the tester
SystemVerilog already brings this ready-made, and there is no need to write a single $urandom
// ILLUSTRATION -- not compiled. The two functions as they are in // code/u5/put-get/tb_classes/random_tester.svh, the section this one replaces. // // This function handles the fact that // the operation bus has 8 possible values, // but only 6 of them are valid operations virtual function operation_t get_op(); bit [2:0] op_choice; op_choice = $random; case (op_choice) 3'b000 : return no_op; 3'b001 : return add_op; 3'b010 : return sub_op; 3'b011 : return and_op; 3'b100 : return xor_op; 3'b101 : return mul_op; 3'b110 : return rst_op; 3'b111 : return rst_op; endcase // case (op_choice) endfunction : get_op // This function was meant to spread out // the probability of getting all zeros (prob = 1/3), // biasing the randomness a little so the prob is not 1/256, // since that would make our coverage goal hard to reach virtual function byte get_data(); bit [1:0] zero_ones; zero_ones = $random; if (zero_ones == 2'b00) return 8'h00; else if (zero_ones == 2'b11) return 8'hFF; else return $random; endfunction : get_data
Notes: It is worth reading this code as the “before” and asking the question before giving the answer: which part of this belongs to the test and which part belongs to the data? The legal range of A and B, and the bias to the edges, are properties of the data — they have nothing to do with what you want to test. The hand-written $random is the symptom: every component that wants a valid command has to repeat it. And if the DUT changes, all of them have to be remembered. A detail that gets charged for in the seeds slide: $random is the Verilog-95 one and has a global seed, so two threads calling it step on each other and the run is not reproducible. $urandom has a per-thread seed. The randomize() of the next slide uses the second one. The punchline for the next slide: SystemVerilog already brings this ready-made, and there is no need to write a single $urandom.

## Slide 288: Transactions
The randomized fields: the “after”
Every SystemVerilog class brings an implicit randomize(), which picks values for the fields marked rand
get_op() disappears: an enum randomizes itself over its legal values
get_data() too, and it gets replaced by a constraint with dist, which is where the bias to the edges gets declared
class command_transaction extends uvm_sequence_item; `uvm_object_utils(command_transaction) rand byte unsigned A; rand byte unsigned B; rand operation_t op; // :/ and NOT := --- this is the line that reproduces the bias towards the // corner cases that get_data() of the Functional coverage section did by hand (1/4 at 00, 1/4 at FF, // 1/2 in the middle). With ":=" the weight applies to EVERY value of the range, so the // middle takes 254 out of 256 and 00 comes up once every 256: the distribution // ends up almost uniform and the corner bins never fill. // The Constrained Random unit has the experiment with the numbers. constraint data { A dist { 8'h00 :/ 1, [8'h01 : 8'hFE] :/ 2, 8'hFF :/ 1 }; B dist { 8'h00 :/ 1, [8'h01 : 8'hFE] :/ 2, 8'hFF :/ 1 }; }
Notes: Three things about this code, in the order in which they get forgotten. rand in front of every field: without that the field does not enter the draw and randomize() leaves it as it was, without warning. It is the first place to look when a value always comes out the same. The dist with :/ and not :=: it reproduces the bias to the edges that the get_data() of the conventional testbench did by hand. The difference between the two operators is a whole unit of the course, and it is not a style detail — with := the 00 bin comes up 1 time in 256 and the corner cases never get filled. And the op with no constraint: an enum randomizes over its values, so no_op and rst_op are going to come out too. That is on purpose — the verification plan asks for operations after a reset.

## Slide 289: Transactions
The constructor: a uvm_object has no parent
uvm_sequence_item extends uvm_transaction, and that one uvm_object — which means a transaction is not a uvm_component. It therefore has a simpler constructor
A transaction does not live in the tree of the testbench: that tree is made of uvm_components, and it is the one UVM walks in build_phase. With no place in the tree there is no parent, and that is why the constructor only asks for a name
Objects get created and destroyed all the time while the simulation runs; components get built once, before it starts, and they stay
It is still worth giving them a name: it is the one that shows up in the UVM messages
// Constructor of a uvm_object: dead simple, it only takes a name. A // transaction has no parent because it does not live in the component tree. function new(string name = ""); super.new(name); endfunction : new
Notes: It is the distinction that has to be left clear: component is structure —it is in the tree, it has a parent, it has phases—; object is data —it gets created, it travels around the testbench and it gets thrown away—. Both are UVM classes, but only one of them builds the hierarchy. A trick to remember it: if you can draw it in the block diagram of the testbench, it is a component. If it travels along an arrow of the diagram, it is an object.

## Slide 290: Transactions
do_copy(): copy the object, not the handle
uvm_object brings two ready-made methods: copy(), which pours the data onto another object that already exists, and clone(), which also creates the new object
Both work only if the class implements do_copy(): the library knows how to copy, but it does not know which fields your transaction has
It is the same pattern as the rest of the section: copy() is the one that gets called, do_copy() is the one that gets written
The only difference is the argument: it has to be a uvm_object —hence the $cast—. UVM calls it rhs (right hand side) by convention, not by requirement
function void do_copy(uvm_object rhs); command_transaction copied_transaction_h; // Checks that make DEBUG easier if (rhs == null) `uvm_fatal("COMMAND TRANSACTION", "Tried to copy from a null pointer") if (!$cast(copied_transaction_h, rhs)) `uvm_fatal("COMMAND TRANSACTION", "Tried to copy wrong type.") super.do_copy(rhs); // copy all parent class data A = copied_transaction_h.A; B = copied_transaction_h.B; op = copied_transaction_h.op; endfunction : do_copy
Notes: The pattern is the one from the class hierarchies, with two UVM rules on top. The first one, the one that makes it compile: the argument has to be of type uvm_object —the base class of everything—, because what SystemVerilog demands for the virtual override to work is that the type and the direction match, not the name. rhs is the identifier used in the signature of uvm_object::do_copy and that is why everybody copies it, but you can call it whatever you like. The first thing to do is cast it. And since the $cast checks at run time, it goes with its uvm_fatal: if somebody tries to copy a result_transaction onto a command_transaction, you want to find out right there and not three components further on. The second one: the super.do_copy(rhs) goes before touching your own fields. It is the same discipline as in the class hierarchies and here it matters more, because uvm_transaction —two levels up— has fields of its own that you do not see: accept_time, begin_time, end_time and initiator. And the detail that confuses everybody: you write do_copy(), but you never call it. The testbench calls copy(), which lives in uvm_object, and that one takes care of invoking your do_copy(). It is the same division as the phases — you put in the bottom part, the library handles the protocol.

## Slide 291: Transactions
The MOOCOW rule: sharing yes, modifying no
Several components can see the same piece of data if they have handles to the same object. It is cheap and it works — as long as nobody modifies it
The rule that holds it up is called MOOCOW —Manual Obligatory Object Copy On Write—, and that is how The UVM Primer, by Ray Salemi, christens it
It says this: sharing a handle is fine as long as you do not touch the object. Whoever wants to modify, copies first
It is a discipline of the team, not something the language enforces. UVM only puts up the tool: clone(), which returns a uvm_object and has to be cast
Notes: The name is a joke from the UVM Primer, but the rule is the one that avoids the most expensive bug of the class hierarchies: you sent the transaction to the scoreboard, you still hold the handle, you modify it for the next one, and the scoreboard ends up comparing against data that changed after it received it. It does not fail every time — it fails under load, which is when it suits you worst. The practical version, without acronyms: whoever produces the data does not touch it again after publishing it. If you need to change it, clone. Look at how the tester of this section complies with it: it does not reuse the handle. Every turn of the repeat does a fresh create(). It is cheaper than cloning and it avoids the argument. And there is one documented exception they are going to see on day 6: the driver writes the result inside the item the sequence lent it. It is agreed between the two parties and it is the only place in the testbench where that gets done.

## Slide 292: Transactions
clone_me(): the $cast written a single time
Since clone() returns a uvm_object, every component that uses it ends up writing its own $cast — the same one, repeated
The UVM Primer convention is to add a clone_me() to the transaction that does both things and returns the right type already
UVM does not bring it: it is four lines written once in the data, so that none of the ones who use it have to remember the cast
function command_transaction clone_me(); command_transaction clone; uvm_object tmp; tmp = this.clone(); $cast(clone, tmp); return clone; endfunction : clone_me
Notes: It is a three-line method and it exists for one reason only: clone() returns a uvm_object, so everybody who uses it has to cast. Writing the $cast once inside the class is better than writing it fifty times outside. The name is not in the standard: clone_me() is a UVM Primer convention. In somebody else’s project it can be called something else or not exist at all — and there you are going to see the $cast repeated in every caller. And the trap that has to be named: clone() calls create() and then copy(), which ends up in your do_copy(). If do_copy() forgets a field, the clone comes out incomplete and nobody warns you. It is the same hole as in the class hierarchies, under another name.

## Slide 293: Transactions
do_compare(): comparing two objects without writing an if per field
compare() comes with uvm_object and returns 1 if the two objects are equal. It is the one that gets called; the one that gets written is do_compare()
It takes two arguments: the rhs —the other object— and a uvm_comparer, which is the comparison policy: how many differences to report and with what verbosity
Almost nobody touches the comparer, but it has to be declared because the signature asks for it
function bit do_compare(uvm_object rhs, uvm_comparer comparer); command_transaction compared_transaction_h; bit same; if (rhs == null) `uvm_fatal("RANDOM TRANSACTION", "Tried to do comparison to a null pointer"); // First check whether we are comparing the same type if (!$cast(compared_transaction_h, rhs)) same = 0; else // Deep comparison: what the parent compares, plus the three fields of // this class same = super.do_compare( rhs, comparer ) && (compared_transaction_h.A == A) && (compared_transaction_h.B == B) && (compared_transaction_h.op == op); return same; endfunction : do_compare
Notes: Two things that get copied wrong. The $cast here does not go with a uvm_fatal: if the type does not fit, the right answer is same = 0 —they are different, obviously, if they are not even of the same class—, not killing the simulation. It is the difference with do_copy(), where a wrong type really is a testbench bug. Worth showing them side by side. And the super.do_compare() goes chained with &&, not called and thrown away. The classic mistake is to write super.do_compare(rhs, comparer); on a line of its own and then same = (A == rhs.A) && ...: it compiles, it runs, and it silently stops comparing everything from the class above. The uvm_comparer of the second argument is the policy —how many differences to report, with what verbosity—. Almost nobody touches it, but it has to be declared because the signature asks for it.

## Slide 294: Transactions
convert2string(): the transaction prints itself
It is the method that returns the object as text. It gets written once, and it is used by the scoreboard, the monitor and anybody who has to report
$sformatf() builds the string with the same format specifiers as always
And the detail that makes a log readable: an enum has name(), which returns add_op instead of 3'b001. Without that the error says a number and nobody reads it
function string convert2string(); string s; // op.name() can be add_op, no_op ... s = $sformatf("A: %2h B: %2h op: %s", A, B, op.name()); return s; endfunction : convert2string
Notes: It is the most used of the three methods, and the one that gets the least attention: every message of the scoreboard and of the monitors of the rest of the course comes out of here. The .name() of the enum is the detail that changes the day: without it the log says op: 4 and you have to go looking for the typedef; with it, it says op: mul_op. The rule to take home: if a field is an enum, the log gets its name, never its value. Worth naming the relatives UVM brings and the course does not use: print() and sprint(), which print the transaction on their own if you registered the fields with the `uvm_field_* macros — or if you write do_print(), the manual equivalent of convert2string(), which does not show up in a single slide of the course. Careful with that: with no macros and no do_print(), a t.print() on the transactions here prints the header and nothing else. The format can be changed: the default is the uvm_table_printer —one row per field, with type and radix— and there is a uvm_line_printer that puts the whole object on one line. The reason to prefer convert2string() is simpler and should be said that way: written by hand it fits in one line that says what you care about, and in a file of a hundred thousand lines that matters.

## Slide 295: Transactions
The field macros: reading them even if you do not write them
class command_transaction extends uvm_sequence_item; `uvm_object_utils_begin(command_transaction) `uvm_field_int (A, UVM_DEFAULT | UVM_HEX) // an integral field `uvm_field_enum(operation_t, op, UVM_DEFAULT) `uvm_field_object(payload, UVM_DEFAULT | UVM_REFERENCE) // handle, not a copy `uvm_object_utils_end endclass
It is what you will find in every VIP you open. They generate do_copy, do_compare, do_print, do_pack and the automatic configuration, out of one declaration per field
The second argument is a mask: UVM_DEFAULT turns on every operation, and UVM_NOCOMPARE / UVM_NOPRINT turn one off. The radix (UVM_HEX, UVM_DEC) is only for printing
UVM_REFERENCE on a uvm_field_object copies the handle; without it, the copy is deep. It is the same decision as do_copy(), taken in a constant
The course writes them by hand for the reason already given: that gets debugged, this does not. But reading them you do have to know
Notes: This is the “and when you open the VIP at work” slide. The course’s decision —writing do_copy, do_compare and convert2string by hand— is taken and well taken, and it is not being reversed here: what gets added is the half that was missing, which is reading what somebody else wrote. The way to read it is always the same and is worth handing over as a recipe: the list of `uvm_field_* is the definition of what “equal” means and what “copy” means for that class. If a field is not on the list, compare() does not look at it — and that is the most expensive bug these macros produce: a scoreboard that goes green because the field that matters was left out of the declaration. The UVM_REFERENCE deserves its second, because it is the do_copy() trap again in another disguise: without it, copying the transaction also copies the object hanging off it, and a clone() in a monitor with heavy traffic gets expensive without anybody noticing. With it, the two transactions share the same payload — which is exactly what MOOCOW says must not be modified. The real cost, so the course’s decision does not look like taste: the macros expand into hundreds of lines per class, and when something goes wrong the error points inside the expansion. A hand-written four-line do_compare reads on the spot.

## Slide 296: Transactions
The seven steps, and why there are seven
What it costs to change the data type of a TB that already exists. We look at 2, 3, 6 and 7; 1, 4 and 5 are a direct port and are in the repo:
# | What | Where
1 | a result_transaction for the trip back | result_transaction.svh
2 | an add_transaction, additions only | add_transaction.svh
3 | the two testers merge into one | tester.svh
4 | the command_monitor publishes objects | command_monitor.svh
5 | the result_monitor, the same | result_monitor.svh
6 | the scoreboard uses compare() | scoreboard.svh
7 | add_test overrides the data | add_test.svh
Notes: The seven steps are the most boring part of the section and also the most honest, so it is worth framing them instead of rushing through them: this is what it costs to change the data type of a testbench that already exists. The real advice is to do it from the start. The one to keep an eye on is number 3, because it is the only one that deletes a class: add_tester disappears. That is where the result of the section is, and it is worth announcing it — moving the decision into the data made a whole structural class redundant. If the group is going fast, steps 4 and 5 get opened in the editor and compared with the ones from the analysis ports: the difference is that instead of filling a struct there is a create() and fields get filled. Nothing else.

## Slide 297: Transactions
Step 2 · an add_transaction that only adds
add_transaction extends command_transaction and adds a single constraint to it: op == add_op
That is enough to change the stimulus, and the tester_h never finds out: it uses the child class exactly as it used the mother
Constraints are inherited and they accumulate: the bias to the edges of A and B is still there, because the one in the base class does not go away
class add_transaction extends command_transaction; `uvm_object_utils(add_transaction) constraint add_only {op == add_op;} function new(string name = ""); super.new(name); endfunction endclass : add_transaction
Notes: Eight lines, and out of those only one does anything: constraint add_only {op == add_op;}. It is worth putting it next to the add_tester of the env, which did the same thing by redefining a method. Two ways of saying “additions only”, and today’s does not touch behaviour code — it only describes which values are legal. The conceptual point, which is the one that orders the day: constraints are inherited and they accumulate. add_transaction does not replace data, it adds to it. The solver has to satisfy both at once, so there is still bias to the edges in A and B — and that is exactly what we want. From there comes the warning: two inherited constraints that contradict each other do not give a compilation error, they give a randomize() that returns 0. It is case 1 of the Constrained random experiment.

## Slide 298: Transactions
Step 3 · two testers become one
task run_phase(uvm_phase phase); command_transaction command; phase.raise_objection(this); // ALL transactions come out of the factory, the directed ones too. // A new() here would compile and work just the same, but it would skip // add_test's set_type_override: the factory never hears about what you // build by hand. See the slide "the new() that eats the override". command = command_transaction::type_id::create("command"); command.op = rst_op; command_port.put(command); repeat (1000) begin : random_loop command = command_transaction::type_id::create("command"); // randomize() returns 0 if the constraints have no solution, and aborts // nothing. A bare assert() lets an unrandomized transaction through in // silence: the TB carries on, sending garbage. if (!command.randomize()) `uvm_fatal("TESTER", "randomize() failed") command_port.put(command); end : random_loop // Directed: the multiplier overflow case, which 1000 random operations // might never touch. It comes out of the factory like the others, but // since it is not randomized, add_transaction's constraint does not run: // the factory picks the TYPE, constraints only act inside randomize(). command = command_transaction::type_id::create("command"); command.op = mul_op; command.A = 8'hFF; command.B = 8'hFF; command_port.put(command); #500; phase.drop_objection(this); endtask : run_phase
The testbench of the env had base_tester and add_tester: two classes for two kinds of stimulus
Now there is only one. The repeat creates a transaction and tells it randomize(); what comes out of that is decided by the data, not by the tester
That is the line that deletes a class: the decision moved from the structure to the type of the transaction
Notes: It is the result of the section, measured in files: add_tester.svh stops existing. It is worth saying out loud, because the env had spent a while justifying that hierarchy and now half of it is redundant. And it is not that the env was wrong: it was the right answer while the data was a mute struct. When the data knows how to randomize itself, that step of the hierarchy runs out of work. It is a good example of abstractions being justified against the problem of the moment, not forever. The if (!command.randomize()) uvm_fatal is the line to copy properly: randomize() returns 0 if the constraints have no solution and it aborts nothing. There is a whole slide on that further on.

## Slide 299: Transactions
Step 6 · the scoreboard compares objects, not numbers
Both sides of the comparison are now result_transaction: the one that arrives from the result_monitor and the one the predictor builds
The write() takes the result t, looks for the command that corresponds to it in the command_monitor queue, and asks predict_result() for the prediction
The comparison comes down to one line —predicted.compare(t)— and the error message builds itself out of the convert2string() of the three transactions
function void write(result_transaction t); string data_str; command_transaction cmd; result_transaction predicted; do if (!cmd_f.try_get(cmd)) `uvm_fatal("SELF CHECKER", "Missing command in self checker") while ((cmd.op == no_op) || (cmd.op == rst_op)); predicted = predict_result(cmd); data_str = { cmd.convert2string(), " ==> Actual ", t.convert2string(), "/Predicted ", predicted.convert2string() }; if (!predicted.compare(t)) `uvm_error("SELF CHECKER", {"FAIL: ", data_str}) else `uvm_info("SELF CHECKER", {"PASS: ", data_str}, UVM_HIGH) endfunction : write
Notes: Comparing this write() with the one from the analysis ports is the best way to close the section: over there was a case with the prediction written inside it and a hand-written comparison; here there is a predict_result() that returns an object and a predicted.compare(t). What was gained is concrete: the error message is now built with convert2string() of the three transactions, so it says what was sent, what came out and what was expected, all with the enums by name. And the day the transaction gains a field, the log shows it on its own. A detail that has to be pointed out because it is the rule of the section applied: the predicted comes from type_id::create(), not from new(). It is a transaction that travels —even if it only travels as far as the compare() on the next line—, so it comes out of the factory like all the others. And the do ... while that skips no_op and rst_op is still the same as in the analysis ports: those operations produce no result, and if they are not thrown away the comparison shifts by one and everything fails.

## Slide 300: Transactions
Step 7 · the override, now on the data
class add_test extends random_test; `uvm_component_utils(add_test); function void build_phase(uvm_phase phase); command_transaction::type_id::set_type_override(add_transaction::get_type()); super.build_phase(phase); endfunction : build_phase function new(string name, uvm_component parent); super.new(name, parent); endfunction : new endclass
The whole test is two lines: the override and the super.build_phase()
And the override no longer changes a component —the tester— but a piece of data —the transaction—. The structure of the testbench stopped having an opinion about the test
super.build_phase(phase) goes after the override, and that order is not negotiable: the env gets built in there
Notes: It is worth putting this slide next to the add_test of the env and counting lines: the same idea, one level further down. Before, what generates was substituted; now, what is generated is. The order of the super is the trap of the slide, and it is a sibling of the one in the env: the factory decides what to build at the moment of the create(). If the override arrives afterwards, there is no error — the testbench runs with command_transaction and the “additions” test sends random operations. It does not break, it lies. And a question that always comes up: why does add_test call super.build_phase() here if the course says it is not needed? Because its base is random_test, a class of ours that has a build_phase with real work in it. The rule from the components was talking about uvm_component, which does not have one.

## Slide 301: Transactions
The new() that eats the override
command = new("command"); // NO command.op = rst_op; command = command_transaction::type_id::create("command"); // YES command.op = rst_op;
set_type_override() talks to the factory, and the factory only finds out about what goes through type_id::create()
A new() builds the type that line says and nothing else: the override does not reach it. It compiles, it runs, and it does not fail — that object simply got left out
It is the worst kind of bug: it does not break, it lies. With one test and one transaction it never shows; the day the override really mattered, it is already too late
The rule, short: every uvm_object that travels around the testbench comes out of type_id::create() — the transactions of the tester, and also the ones the monitors build and the predicted of the scoreboard
The ports and the exports are the exception: they are not in the factory and they get instantiated with new(), as we saw in one producer, many listeners. The TLM FIFO is registered, but the course builds it with new() anyway because the size goes through the constructor and create() cannot pass it
Notes: This slide comes out of a bug this very course had: the tester created the two directed operations —the reset and the FF x FF multiplication— with new(), so under add_test those two were NOT add_transaction. Nobody noticed because the testbench works just the same. The question to throw at the group, which is the one that orders everything: if the reset now comes out of the factory and under add_test it is an add_transaction, why does the constraint op == add_op not turn it into an addition? Because we do not randomize it. The factory picks the type; constraints only act on randomize().

## Slide 302: Transactions
And randomize() never goes on its own
assert (command.randomize()); // NO if (!command.randomize()) `uvm_fatal("TESTER", "randomize() failed") // YES
randomize() returns 0 when the constraints have no solution. It does not abort, it prints nothing on its own: it returns 0 and carries on
A bare assert() reports outside UVM: it does not go into the Report Summary —the same one we learned to read in reporting— and in many simulators execution carries on with the transaction unrandomized
And if the project compiles with assertions turned off, there are simulators that do not even evaluate the expression: randomize() simply never gets called
With `uvm_fatal the error brings component, time and file, and it stops the run right there
Notes: It is one extra line that pays for itself the first time somebody adds a contradictory constraint. Without the else, the symptom is a scoreboard failing on transactions with absurd values and half an afternoon spent looking for it in the DUT. The `uvm_fatal is not an exaggeration: an unrandomized transaction is not bad stimulus, it is stimulus you did not choose. Better for the run to die with a message than to tell somebody that last night’s regression meant nothing.

## Slide 303: Transactions
Summary of the unit
We saw how to use transactions to move data around the TB
That lets us simplify the components of the TB and even remove a class from our initial TB (add_tester)
The unit that follows groups the classes that talk to one and the same interface into a single reusable block: the uvm_agent
Notes: Closing of day 5, and it is worth saying what is missing: today the stimulus is generated by a tester you wrote yourself; in modern UVM that is a uvm_sequence running on a sequencer, and the set of driver + monitor + sequencer is packed into an agent. That is day 6.

## Slide 304
Constrained random
The other half of the pincer
The functional coverage of the conventional testbench tells you what is missing. It does not tell you how to get there: that is the stimulus
Writing a directed test per bin does not scale — there are 76 of them in the VTALU, and a real chip has thousands
The industry recipe is the other way round: random for the bulk, directed for the holes. And the random has to be legal, or the DUT complains about things that are never going to happen in silicon
Constrained random is writing the rules of the stimulus once, in the transaction, and letting the solver build the cases
Notes: It is the half of the pair that was missing: up to here the course measured coverage and built the transactions, but the stimulus still came out of a get_op() with a hand-written case. The sentence that orders the section: a constraint does not pick a value, it describes the set of legal values. The one that picks is the solver, and it picks differently from what you expect more often than you would like. The whole section is about measuring that instead of assuming it.

## Slide 305: Constrained random
rand and randomize(): what you have already seen
class command_transaction extends uvm_sequence_item; rand byte unsigned A; // rand -> it enters the draw rand byte unsigned B; rand operation_t op; // an enum randomizes over its values constraint data { ... } // the rules, in a block of their own endclass
randomize() comes from SystemVerilog, not from UVM: every class has it
It picks values for the rand fields that satisfy every active constraint at once
A constraint is not sequential code: it does not run from top to bottom, it has no order. It is a set of relations the solver satisfies together
That is why two constraints that contradict each other do not give a compilation error: they give a randomize() that returns 0
Notes: The bullet to say slowly is the third one, because it is the wrong mental model everybody brings along: a constraint does not run. It is not a long if, it does not go from top to bottom, and the order they are written in makes no difference. It is a system of equations, and randomize() hands it to a solver —in this course, z3— so that it returns a random solution out of all the ones that satisfy it. From there comes the consequence of the last bullet, and it is the most expensive trap of the section: two incompatible constraints compile perfectly. The error shows up at simulation time, randomize() returns 0, and if nobody checks the return value the class is left with the values it had. The testbench goes on running and sends garbage. The rule to take away from here, and one the course keeps everywhere in code/: a randomize() always goes inside an if that checks the return value. Never on its own.

## Slide 306: Constrained random
The other three words: randc and the two hooks
class command_transaction extends uvm_sequence_item; rand byte unsigned A; // it can repeat: 3 3 6 1 3 4 6 2 ... randc bit [2:0] indice; // it walks the 8 and only then repeats function void pre_randomize(); // runs BEFORE the draw if (!primera) A = A_anterior; // …with the values still old endfunction function void post_randomize(); // runs AFTER, with the new values checksum = A ^ B; // what is not drawn gets computed here endfunction endclass
randc is cyclic: it exhausts every value before repeating one. Measured on Verilator 5.052: 4 2 1 7 5 6 3 0 and only then does it start over
It is for walking a small space —an opcode, a register index— without waiting for chance to cover it. Only on small integral types: the LRM guarantees 8 bits and simulators usually stop at 16
pre_randomize() / post_randomize() are the two hooks randomize() calls on its own. The derived field —a checksum, a parity— gets computed in the second one, it does not get drawn
And a warning: whatever gets computed in post_randomize() does not take part in the solver. If it has to satisfy a constraint, it is a rand field
Notes: They are the three words of the language that are missing for the student to read any foreign transaction without stopping. None is hard; what is needed is knowing when each one is used. randc is the answer to “I want to go through every opcode”, and the argument is efficiency: with rand over eight values it takes some twenty-two draws to see all eight —the coupon collector’s problem—, and with randc eight are enough. And the width limit has a concrete reason: the solver has to carry the list of what has already come out, so a 32-bit randc would be a table of four billion entries. The two hooks are best explained by what they solve. post_randomize() is for the field that derives from the drawn ones: a CRC, a parity, the length of a payload that has already been drawn. Making it rand with a constraint tying it to the rest is asking the solver to solve a problem that is done with an XOR. pre_randomize() gets used less and has a trap worth naming: it runs before the draw, which means the fields still have the values of the previous transaction. That makes it useful for whatever depends on the past —keeping the previous address to ask for a contiguous access— and dangerous if you believe the new ones are already there. And the underlying warning, which is the same as the whole section’s: a field computed in post_randomize() is outside the system of equations. The solver does not see it, the constraints do not restrict it, and randomize() will never return 0 because of it.

## Slide 307: Constrained random
dist: := is not the same as :/
A dist {8'h00 := 1, [8'h01 : 8'hFE] := 1, 8'hFF := 1}; // the weight goes to EACH value A dist {8'h00 :/ 1, [8'h01 : 8'hFE] :/ 2, 8'hFF :/ 1}; // the weight gets SPLIT
dist sets weights: it does not change which values are legal, it changes how often they come up
With := the weight is applied to each value of the range: the middle range weighs 254 and the edges 1 each. A=00 comes up 1 time in 256
With :/ the weight belongs to the whole range: 1 – 2 – 1 gives 25 % on 00, 50 % in the middle, 25 % on FF. Which is exactly the bias the get_data() of the conventional testbench did by hand
Both lines compile, both run, and one of the two never fills the edge bins
Notes: The arithmetic has to be done on the board, because read out loud it does not sink in: with := the weights are 1, 1 and 1, but the middle one is applied to each one of its 254 values. A total of 256 equal parts, and A=00 comes up one time in 256. With :/ the parts are three —1, 2 and 1— and A=00 comes up one time in four. Sixty-four times more often, for two characters. And now the part that makes it dangerous: both versions work. Neither gives a warning, neither fails, the testbench runs the thousand transactions just the same. The only thing that changes is that with := the a_00 bin of the covergroup takes an eternity to fill, and whoever looks at the report concludes that a test is missing. It is exactly the kind of bug the course calls a silent trap, and that is why the next slide does not explain: it measures. The practical rule to hand down: if you write a dist, run a histogram before believing it.

## Slide 308: Constrained random
Do not assume it: measure it
// The weight goes to EVERY value of the range: the middle takes 254 of 256. class por_valor; rand byte unsigned A; constraint data {A dist {8'h00 := 1, [8'h01 : 8'hFE] := 1, 8'hFF := 1};} endclass // The weight is SPLIT inside the range: 1/4 at 00, 1/2 in the middle, 1/4 at FF. // It is the same bias get_data() of the Functional coverage section did by hand. class por_rango; rand byte unsigned A; constraint data {A dist {8'h00 :/ 1, [8'h01 : 8'hFE] :/ 2, 8'hFF :/ 1};} endclass
$ cd code/u6/transactions/constraints && bash run.sh 400 randomizations of each version := A=00 0.2% A=FF 0.2% the weight goes to each value :/ A=00 23.2% A=FF 27.0% the weight gets split
Measured histogram: with := the edge bins come out 0.2 %; with :/ they come out 23 % and 27 %

## Slide 309
Notes: This experiment came out of a bug in this very course: command_transaction had the dist written with :=, which means the bias to the corner cases the transactions claimed to have did not exist. The distribution was practically uniform and nobody found out, because the testbench passed just the same. That is the underlying point of the section, and it is worth saying it that bluntly: a badly written constraint does not fail, it lies. There is no warning, there is no compilation error, there is no test in red. The only thing that gives it away is the coverage that does not go up — and that is only noticed weeks later. A practical rule to take home: every time you write a dist, run a few thousand randomizations and print the histogram once. It costs ten minutes and it is the difference between believing and knowing.

## Slide 310: Constrained random
inside and randomize() with {}
class comando; rand byte unsigned A; rand byte unsigned B; rand operation_t op; constraint data { A dist {8'h00 :/ 1, [8'h01 : 8'hFE] :/ 2, 8'hFF :/ 1}; B dist {8'h00 :/ 1, [8'h01 : 8'hFE] :/ 2, 8'hFF :/ 1}; } // inside is a set of legal values. Without it the random also asks for // no_op and rst_op, which compute nothing. constraint utiles {op inside {add_op, and_op, xor_op, mul_op};} endclass
// The portable workaround meanwhile: turn off the split, which for a // directed case makes no sense anyway. c.data.constraint_mode(0); if (!c.randomize() with { op == mul_op; A == 8'hFF; B == 8'hFF; }) $fatal(1, "randomize() with failed even with the constraint turned off"); $display("with with: 1 try, A=%2h %s B=%2h", c.A, c.op.name(), c.B);
inside {a, b, c} is the set of legal values: without it, the random also asks for no_op and rst_op, which compute nothing. Here it also leaves out sub_op, so that the draw comes out uniform among four
randomize() with { ... } adds constraints for that call only: the directed case gets asked for at the point of use, without touching the class and without writing a new tester. It is the tool of coverage closure
Notes: The number that comes out of running 02_with.sv is the whole argument of the section: 400 random attempts fill mul_max a handful of times —6 with the default seed, between 2 and 8 depending on which one you use— because the dist biases towards the edges. The arithmetic is worth doing out loud: op comes out uniform among four and each leg lands on FF one time in four, that is 1/4 × 1/4 × 1/4 = 1 in 64, which over 400 attempts is six and a bit. With the badly written dist of the previous slide, the probability of both legs landing on FF is 1/65536 per operation: you never touch it. The mental sequence is always the same: I run random, I look at which bin was left empty, I write a three-line with {}, I run again. Never “I write 76 tests”. The Verilator limitation the section states is there on purpose, and it is worth stating it properly because it is not a matter of “it works or it does not”. Verilator resolves the dist by picking a concrete value first and only then checks the rest: if the one drawn does not satisfy the with, it returns 0 instead of looking for another. The success rate is therefore the probability of the bin. Measured: with {A == 8'hFF} resolves 25 % of the time —the weight of that bin—, with {A inside {[1:10]}} 2 %, and a field with no dist 100 %. Why it matters more than it looks: the symptom is an intermittent directed case, which works when you try it and fails in the overnight regression. The numbers are in code/verilator/repro-dist-with.sv, and the workaround —turning the constraint off— is the same constraint_mode() you see further on.

## Slide 311: Constrained random
soft: the default a with {} can override
class command_transaction extends uvm_sequence_item; rand byte unsigned A; constraint por_defecto { soft A == 8'h00; } // "zero, unless somebody asks otherwise" endclass t.randomize(); // A = 00 t.randomize() with { A inside {[1:10]}; }; // A between 1 and 10: the soft drops on its own
A soft constraint is a wish, not a rule: if it clashes with another, the solver drops it instead of returning 0
It is the modern way of writing a default value in the transaction without forcing anybody to call constraint_mode(0) to override it
The hard constraint wins, and between two clashing soft ones the one declared later wins — the order does matter here, and only here
Measured on Verilator 5.052: with the with {} it comes out between 1 and 10; without it, 00
Notes: This is the piece that makes the previous slide scale to a real testbench. The randomize() with {} is for asking for a directed case, but if the class already has a hard constraint saying otherwise, the with does not override it: it contradicts it, and randomize() returns 0. The old way out was constraint_mode(0) — which forces whoever writes the test to know the name of a constraint in a class they did not write. The design rule to leave behind, because it is the one used in every modern VIP: what is a rule of the protocol goes hard; what is a preference of the stimulus goes soft. An address aligned to 4 is hard, because the DUT does not accept anything else. That burst_len defaults to 1 is soft, because the test that wants long bursts has the right to ask for them without permission. The tie-break between two soft ones is worth saying and not using: the last one declared wins, and if that matters to you for anything, the constraint was badly written. They came in with IEEE 1800-2012, so any simulator of the last decade has them — and Verilator too, measured right up there.

## Slide 312: Constrained random
The order of resolution biases without warning
rand bit es_reset; rand byte unsigned A; constraint c {es_reset -> A == 8'h00;} // "if I ask for a reset, the operands at zero"
It looks harmless. It is not: the solver picks among the solutions, not among the values of each field
With es_reset = 1 there is one; with es_reset = 0, 256. You asked for a reset half the time and you will see it 1 time in 257
The “any operation after a reset” bin of the plan does not get filled, and the report does not tell you why
The answer from the language is solve es_reset before A: pick the control field first
One cell against a 16 by 16 block: the 257 solutions, and only one has the reset

## Slide 313
Notes: The sentence that dismantles the intuition is the one in the first bullet, and it is worth repeating it word for word: the solver picks uniformly among the solutions, not among the values of each field. Nobody wrote that es_reset was going to come out 1 half the time; that came from assuming each field gets drawn separately, and it does not. It is worth counting the 257 solutions out loud, because the number convinces more than the argument: es_reset=1 forces A=00, that is to say a single combination; es_reset=0 leaves A free, that is to say 256. The draw is over the 257, and the reset takes one of them. The connection with the verification plan is what makes this slide worth it: the row “any operation after a reset” does not get filled, the coverage stays pinned down, and the report does not say why. A student without this slide adds random tests for an afternoon. And the warning about the cure, so that it does not get overused: solve ... before does not change which solutions are legal, only the order in which the solver picks. It is a distribution knob, not a correctness one — and it costs solver time, so it goes where it is needed and not out of habit.

## Slide 314: Constrained random
Measured, with the workaround that Verilator does honour
class sesgada; rand bit es_reset; rand byte unsigned A; constraint c {es_reset -> A == 8'h00;} endclass // The language's answer is "solve es_reset before A": pick the control field // FIRST and then solve the rest. Verilator 5.052 accepts the syntax and does // NOT honour it -- it leaves es_reset stuck at 0, which is worse than // ignoring it. Repro in code/verilator/repro-solve-before.sv. // // The workaround that IS portable: ask explicitly for the split of the // control field. It says the same and does not rely on the solver ordering well. class pareja extends sesgada; constraint reparto {es_reset dist {1'b0 :/ 1, 1'b1 :/ 1};} endclass
2000 randomizations of each version as written es_reset=1 in 0.3% (1 in 257) with dist on es_reset es_reset=1 in 51.7%
Verilator 5.052 accepts solve ... before and does not honour it: it leaves the field pinned at 0, which is worse than ignoring it. Repro in code/verilator/repro-solve-before.sv
The portable workaround: ask for the spread of the control field with a dist. It says the same thing and it does not depend on the solver getting the order right
Notes: It is the second Verilator hole of the course, alongside the transition bins, and it gets treated the same way: it gets said head on, with a minimal repro and with a workaround that works. The concept belongs to the language, not to the simulator. What does have to be stressed is the asymmetry: the biased constraint gives 0.3 %, which is exactly what the theory predicts — which means the Verilator solver is fine; what is missing is the ordering directive. And the general moral, which holds for any tool: if the stimulus has a control field (a mode, a kind of operation, an “inject an error”), do not trust it to come out even. Measure it.

## Slide 315: Constrained random
When there is no solution
class comando; rand byte unsigned A; constraint chico {A < 8'h10;} constraint grande {A > 8'hF0;} // contradicts the previous one: no solution endclass initial begin comando c; c = new(); // 1. Both constraints active: there is no A that satisfies the two. if (!c.randomize()) $display("1. randomize() returned 0: the constraints do not close"); else $display("1. randomize() gave %2h (should not get here)", c.A); // 2. constraint_mode(0) turns a constraint off at run time. c.grande.constraint_mode(0); if (!c.randomize()) $display("2. randomize() returned 0 (should not get here)"); else $display("2. with 'grande' turned off: A=%2h, and it honours 'chico'", c.A); // 3. rand_mode(0) takes the field out of the draw: it keeps its current value. c.A.rand_mode(0); if (!c.randomize()) $display("3. randomize() returned 0 (should not get here)"); else $display("3. with A out of the draw: A=%2h, the same as before", c.A); $finish;
1. randomize() returned 0: the constraints do not close 2. with 'grande' turned off: A=06, and it honours 'chico' 3. with A out of the draw: A=06, the same as before
constraint_mode(0) turns one constraint off at run time; rand_mode(0) takes one field out of the draw and leaves it with the value it had — and if that value does not satisfy the constraints that name it, randomize() returns 0
They are for the test that needs to break a rule on purpose — injecting an illegal opcode, for instance — without touching the class everybody else uses
Notes: Here the circle closes with the assert(randomize()) slide: case 1 is precisely what happens when two constraints contradict each other, and without the else the testbench goes on sending the previous transaction. And the pairing with the soft slide, worth closing here: a soft constraint is the one the solver drops on its own when it gets in the way. constraint_mode(0) is the same thing asked for by hand and from the outside, and it is what is left when the constraint in the way is hard and the class is not yours.

## Slide 316: Constrained random
How a constraint that does not close gets debugged
// 1. Make the testbench say so. Without this there is no bug: there is silence if (!t.randomize()) `uvm_fatal("RAND", "the constraint did not close") // 2. Bisection: turn them off one at a time until it closes. The last one you turned off is it foreach (nombres[i]) begin t.chico.constraint_mode(0); if (t.randomize()) `uvm_info("RAND", "it closes without 'chico'", UVM_LOW) t.chico.constraint_mode(1); end // 3. Take the field out of the draw and see which value was blocking it t.A.rand_mode(0);
The symptom is never “it does not close”: it is a randomize() that returns 0 and a transaction with the previous one’s values. First it has to be made noisy
The method is bisection, just like with git bisect: constraint_mode(0) one at a time until it closes. The one you had not turned off yet is the culprit
The other cut is by field: rand_mode(0) leaves the value it had and shows whether the conflict was that one
The cause is almost always the same: a constraint of the base class that the test’s with {} contradicts. There the design answer is soft
Notes: It is the half hour everybody loses once, and there is a way of losing it only once. It is worth saying the order out loud because it is the one that works. Step zero, and the one people skip: make it noisy. A randomize() without an if does not produce a visible bug, it produces stale stimulus. The course asks for it in all of code/ and the traps appendix has it catalogued; here is where it gets collected. Step one: bisection. A commercial simulator prints the set of conflicting constraints —Questa says Constraint solver failed and lists the blocks—, but Verilator returns 0 and says nothing, so bisection by hand is the tool there is. It is boring and takes two minutes, which is exactly why it is worth having the reflex instead of staring at the code. Step two, when bisection is not enough: the conflict is not between two constraints but between a constraint and a field that already has a value. There rand_mode(0) on the suspect freezes it and the message changes. And the design moral, which is the one that avoids the problem instead of solving it: if a base class defines hard constraints that a reasonable test is going to want to override, those constraints should have been soft. A hard constraint is a rule of the DUT, not a preference of whoever wrote the class first.

## Slide 317: Constrained random
This is how coverage gets closed
The closure cycle: randomize, read the report, fill the missing bin, another seed

## Slide 318
No step asks for a new class: dist and inside in the transaction, three lines of with {}, and rand_mode(0) or constraint_mode(0) to break a rule
That is coverage closure, and it is what a verification engineer spends the day on
What it is not: writing one test per bin. Nor looking at the total percentage
The stimulus still comes out of a tester you wrote yourself. In modern UVM that is a uvm_sequence — and that is day 6
Notes: Close by going back to the conventional testbench: the 86.8 % of u2/convencional comes out of 1000 random operations with the bias to the edges put in by hand. Now the student knows how to write that same bias in a constraint, measure it, and add the with {} for the cases that are missing. And leave the day 6 question hanging: if the stimulus is constraints and not code, what does a tester class with a run_phase go on existing for? It does not go on existing. It is called a sequence.

## Slide 319: Constrained random
“Another seed, and again”: what it moves and what it does not
$ SEED=7 bash run.sh # u6/transactions/constraints, 400 randomizations seed: 7 :/ A=00 25.0% A=FF 22.0% # with SEED=8: 20.8% and 27.0% $ SEED=7 bash run.sh # u2/convencional, and again with SEED=8 covergroup : 86.8% (66/76) # both times. And the merge, the same
SEED=N passes +verilator+seed+N, and run_sim prints the one it used: a failure that comes up once every ten runs does not get debugged, it gets repeated
It does move the percentages of a dist measured with few samples: 400 randomizations give 25 % or 21 % depending on the draw. It is a sample, not the distribution
It does not move the 10 bins that are missing. With 1000 operations the random already got as far as it can, and another seed is tossing the coin expecting a different result
That is why “another seed” is the last step of the previous cycle and not the first: the with {} comes first
Notes: This slide exists to defuse a misunderstanding the previous cycle invites: “if I do not close, I run another seed”. It was measured, and no: code/u2/convencional gives 66 out of 76 with the default seed, with 7 and with 8, and the merge of the three gives 66. The 10 that are missing are not missing out of luck — they are missing because Verilator generates the enum’s automatic bins over the base type: 3'b110 does not exist in operation_t, so auto_5 stays at 0 forever, with its nine crosses. No seed is going to touch them. The seed is good for two other things, and both are matters of craft. First: reproducing. An intermittent bug does not get debugged, it gets repeated; and to repeat it you have to know which seed it came up with, which is exactly why run_sim prints it on every run. Second: accumulating, when the stimulus has not saturated yet. A real regression is the same test over a hundred seeds overnight, and the coverage gets merged — verilator_coverage --write does in Verilator what the ucdb merge does in Questa. Here it does not show because the example is small; on a chip it is half the work. And the +verilator+rand+reset+2 that shows up in the documentation is something else and it is worth not mixing them up: it does not touch randomize(), it decides what the uninitialized signals of the DUT start with. With 2 they start at random instead of at zero, which is the way to discover the register nobody reset and that in silicon does not start at zero.

## Slide 320: Constrained random
Summary of the unit
The coverage tells you what is missing; constrained random is how to get there. They are the two halves of the same pincer
Writing a directed test per bin does not scale: there are 76 bins in the VTALU. The recipe is the other way round — random for the bulk, directed for what is left
A constraint is not sequential code: it does not run from top to bottom. It is a system of equations the solver resolves all together
That is why two constraints that contradict each other do not give a compilation error: they give a randomize() that returns 0
dist sets weights, not legality. And := is not :/: the first weighs each value of the range, the second the whole range
randomize() returns 0 and carries on. That is why it always goes inside an if with `uvm_fatal — it is the most expensive silent trap of the course
Notes: The last bullet is the one to leave burned in and the one that connects with the appendix of the traps. An unchecked randomize() does not break: it leaves the fields with the previous value and the testbench goes on sending stimulus that is not the one you think. The coverage is going to tell you three days later. And the tool notice that is needed from today: without z3 installed, Verilator resolves randomize() by returning 0 in silence. It is in docs/en/verilator.md, and it is the reason day 5 asks for the solver.

## Slide 321
Review · Day 5
1 of 8 · Deep copy
obj1_h = obj2_h. What did I copy?
☒ Nothing: both handles point at the same object
☐ Every field of obj2_h into obj1_h
☐ Only the rand fields
☐ A shallow copy: the first level is copied and the handles inside get shared
Nothing — there is no copy, there is a second name for the same object. If you modify it through one handle, the other one sees it. Out of that comes the MOOCOW rule: if you are going to modify, copy first.

## Slide 322
Review · Day 5
2 of 8 · super.do_copy()
Why does every do_copy() in the hierarchy have to call super.do_copy()?
☐ Because UVM demands it in order to register the class
☐ So that the object ends up registered in the factory
☒ Because otherwise the fields of the classes above do not get copied
☐ Because do_copy() is pure virtual and the base class has no implementation
Otherwise the fields above get lost — it is the same problem as convert2string(): the day somebody puts a new level in the middle, the method stops seeing half the data and nobody warns you.

## Slide 323
Review · Day 5
3 of 8 · clone()
clone() returns a uvm_object. Why is it recommended to also write a clone_me()?
☒ To wrap the $cast in a single place
☐ Because clone() does not copy the data
☐ Because clone() is deprecated in IEEE 1800.2 and copy() replaces it
☐ To be able to clone components as well as transactions
So as not to repeat the $cast — without it, every place that clones ends up writing its own cast. It is the same idea as always: if you are going to repeat it, wrap it.

## Slide 324
Review · Day 5
4 of 8 · dist: := against :/
A dist {8'h00 := 1, [8'h01:8'hFE] := 1, 8'hFF := 1}; — how often does A = 8'h00 come out?
☐ A third of the time: they are three entries with the same weight
☐ Half: the edges share it between the two of them
☐ Never: := only takes single values, not ranges, and the range is dropped
☒ Once every 256: with := the weight goes to each value
1 in 256 — := gives weight 1 to each one of the 254 values in the middle, so the range weighs 254 against the 1 and 1 of the edges. To spread the weight inside the range you need :/. Both spellings compile and run: the difference only shows up in the coverage that does not go up.

## Slide 325
Review · Day 5
5 of 8 · randomize() with {}
cmd.randomize() with { A == 8'hFF; } — what happens to the constraints the class already had?
☐ They get replaced: for that call only what is inside the braces counts
☒ They add up: both have to be satisfied
☐ They stay switched off until the next randomize() without a with
☐ It depends on the declaration order: the one lower in the file wins
They add up — the with {} adds constraints for that call only, and erases nothing. That is why it is the tool for closing a bin without writing a new class: three lines at the point of use, and the rest of the stimulus stays what it always was. And that is also why it clashes with a dist that already biases the same field: both have to hold at once.

## Slide 326
Review · Day 5
6 of 8 · constraint_mode()
randomize() with { A == 8'hFF; } on a field the class spreads with a dist returns 0 three times out of four. What is the workaround?
☐ Retry in a do ... while until it returns 1
☒ constraint_mode(0) on the dist constraint, for that object
☐ Raise the weight of the 8'hFF bin in the dist of the class
☐ rand_mode(0) on the field: it takes the dist out and lets the with rule
Switch off the constraint that gets in the way — Verilator solves the dist by picking a value first and only then checking the rest, so the probability of success is the probability of the bin: measured, with {A == 8'hFF} solves 25 % of the time. constraint_mode(0) switches it off for that object alone and touches nobody else. It is exactly the line the d5c exercise asks for.

## Slide 327
Review · Day 5
7 of 8 · rand_mode()
What does cmd.A.rand_mode(0) do?
☐ It switches off every constraint that mentions that field
☐ It randomizes it once and freezes it afterwards
☐ It makes the solver resolve it last, after all the other fields
☒ It takes the field out of the draw and leaves it the value it had
It stops being rand — they are the two run-time knobs and they get mixed up often: rand_mode(0) takes a field out of the draw, constraint_mode(0) switches off a constraint. One picks what gets drawn, the other which rules hold. It is what you use to pin one operand by hand and go on randomizing the rest.

## Slide 328
Review · Day 5
8 of 8 · The order of resolution
rand bit es_reset; rand byte unsigned A; with constraint c { es_reset -> A == 8'h00; }. How often does es_reset = 1 come out?
☐ Half the time: it is a rand bit and nothing forbids it
☐ Never: the implication forces it to 0
☒ 1 in 257: the solver draws among the solutions
☐ It depends on the seed, and over enough runs it averages out to half
1 in 257 — the solver picks uniformly among the solutions, not among the values of each field: es_reset=1 leaves a single combination (A = 00) and es_reset=0 leaves 256. The “any operation after a reset” bin of the plan does not get filled, and the report does not say why. The answer in the language is solve es_reset before A; Verilator accepts it and does not honour it, so the portable workaround is to ask for the spread of the control field with a dist.

## Slide 329
Exercise · Day 5 · 1 of 3
The scoreboard screams and the DUT is healthy
cd code/ejercicios/d5 && bash run.sh
The TB of the transactions reports FAIL on almost every operation
The DUT is the same one that has been passing since the spec. The bug belongs to the TB
The messages that give it away are UVM_HIGH: turn the verbosity up
If you get stuck, the debug toolbox appendix has the row for this symptom; the silent traps one has the cause
Notes: It is the exercise that looks most like a day at work: the scoreboard screams and you have to decide who to believe. Let them start without the hint. Almost all of them are going to look at the RTL first — that is already half the lesson. When they get stuck, the hint is the verbosity: the uvm_info of the monitor are UVM_HIGH and they show what the monitor says it saw, which does not match what the scoreboard compares. The bug is a single line of command_monitor.svh: the monitor copies one of the two operands wrong.

## Slide 330
Exercise · Day 5 · 2 of 3
Measure your dist
cd code/ejercicios/d5b && bash run.sh
One class, one dist and a histogram. No UVM, no DUT, no testbench
The weights already say 10, 80 and 10. Run it first, and look at what comes out
What is asked is that the three buckets give 10 / 80 / 10, with ±2 points of tolerance
The difference between what is there and the solution is one character
Notes: It is the short exercise of the course and the one to leave for whoever ran out of time: it compiles and runs on its own, without UVM. The point is in the order: it gets run before touching anything. The file says 10, 80 and 10, the output says 0.1 % on the edges, and there the question of the section appears on its own — if the numbers are right, what is wrong? The operator is wrong, and there is no warning to say so. It is worth asking them to run it two or three times with different SEED= before calling it closed: with 4000 samples the 10 % bucket moves a good point between runs, between 9 and 11 — that is why the checker accepts ±2. A measured percentage is a sample, not the distribution — which is the other half of the rule of the section. An infrastructure detail worth mentioning if somebody asks why a program with no DUT takes twenty seconds: Verilator resolves every randomize() that has constraints by calling z3 from outside, so that is 4000 calls to an external process. And if they do not have it installed, randomize() returns 0 and every bucket gives zero — another one that does not break, it lies.

## Slide 331
Exercise · Day 5 · 3 of 3
Closing a bin
cd code/ejercicios/d5c && bash run.sh
The test sends a reset and 60 random operations, and the report shows the bin “both legs at FF, multiplying” empty
Write the directed case that closes it. But ask for it with randomize() with {}, not by assigning the fields, which is what this section’s tester does three lines above
It is graded by comparing the coverage before and after: it has to go up
It is row 3 of the verification plan of day 1: the only one of the twelve whose stimulus column says directed case
Notes: It is the exercise the course was missing, because coverage closure shows up twice as a noun and never as a verb. Here the student does the whole cycle: run, look at which bin was left empty, write three lines, run again. The trap is set on purpose and it is the one from constrained random: command_transaction has a dist on A and on B, and Verilator resolves the dist by choosing a value before looking at the with. With the distribution active, with {A == 8'hFF} resolves one out of every four times and the rest returns 0. Whoever does not read the hint is going to see an exercise that sometimes passes and sometimes does not — which is exactly the symptom the section describes. The workaround is constraint_mode(0), and it is worth defending it as a design decision and not as a patch for the simulator: a directed case does not want a distribution of probabilities, it wants a value. The seed of the run.sh is fixed. Without fixing it, some runs would fill the bin on their own with the 60 random ones — and that is the exercise day 7 starts with.

## Slide 332
Yesterday we left…
Where the testbench stands
The data is an object: command_transaction with do_copy, do_compare and convert2string, and the scoreboard compares objects, not fields
The stimulus is asked for instead of written: randomize(), constraint, dist, and the histogram that says whether the distribution does what it promises
And two things are left stuck together that do not belong together: the tester is structure and stimulus at once, and the env names the monitor and the driver one by one
Notes: The day 6 recap has to name the two separations the unit makes, because there are two and they get confused: the agent separates the structure and the sequence separates the stimulus. Both are the same operation —taking something out of the component tree— applied to different things. The third bullet is the one to leave said in the student’s own words: today, to test three stimuli and their combinations, six test classes are needed. That grows factorially, and it is the reason the unit exists.

## Slide 333
Agenda
Day 6 · ≈ 4 h 45 · unit 7 · the reusable testbench
Agents
Callbacks
Sequences
By the end of the day you can:
Say what an agent with is_active = UVM_PASSIVE builds and what it does not
Explain why a uvm_sequence does not show up in print_topology()
Remove the last hard-wired line of a test, with default_sequence through uvm_config_db
Notes: The first two are rows 13 and 14 of the closing self-assessment. The 14th is the question thrown on day 1, when the UVM class diagram showed up, and it gets answered today: uvm_object is the data and uvm_component is the structure. The third one is what closes the unit and the day: when that line goes, no line of the test names a component from inside the env, and only then is the testbench reusable for one agent. Coordinating two is day 7.

## Slide 334
Agents
The problem: a testbench that cannot be copied
The env we left in the transactions works, but it is a welded block: seven components and five connect() written by hand
Every one of those components exists for a single reason: it drives or watches the same interface, the vtalu_bfm
Ask what happens if the design brings two VTALU: you have to copy the seven objects, the five connections, and rename everything
Copying and pasting structure is exactly what we had been avoiding since the env
UVM puts a name on the solution: uvm_agent
The env of transactions against the env with an agent

## Slide 335
Notes: The question that orders the whole section: what is the natural unit of reuse in a testbench? It is not the component, and it is not the env. It is the interface. Everything that knows how to speak one protocol gets packed together, and that box gets instantiated once for every interface of the design. That is the agent, and it is nothing more. If the group comes from RTL, the analogy works on its own: the agent is to the testbench what a parameterizable module is to RTL. Nobody instantiates a FIFO by copying its registers one at a time.

## Slide 336: Agents
What is inside an agent
A uvm_agent is one more uvm_component: same tree, same phases, same factory
What changes is what it puts inside, always the same:
  a sequencer, which hands out stimulus
  a driver, which turns it into signals of the BFM
  the monitors, which watch the bus and publish transactions
And it exposes outwards two uvm_analysis_port: the one that publishes commands and the one that publishes results
The scoreboard and the coverage do not go inside: they are analysis, and they live in the env hanging off those two ports
From this section on every piece uses its base class: uvm_driver #(T), uvm_sequencer #(T) and uvm_monitor instead of a plain uvm_component
Internal structure of the agent

## Slide 337
Notes: There is a decision here that is worth saying out loud because the UVM Primer takes it the other way round: it puts the scoreboard and the coverage inside the agent. We do not. The reason is practical: the day you put a passive agent on an interface that somebody else drives, you do not want a second scoreboard thrown in for free. The agent is the protocol layer; the analysis belongs to the env, which is the one that knows what is being verified. The other reason is that if the scoreboard lives inside, the two analysis ports that the agent exposes have nobody to serve, and half the design ends up decorative. About the last bullet, because somebody is going to open code/u7/agents and see it: up to the transactions the monitors extended uvm_component; from here on they extend uvm_monitor. And uvm_monitor does not add a single line of behaviour — it is uvm_component under another name. What it adds is intent: anybody who opens the testbench knows what that class does without reading it, and print_topology() shows it as a monitor. It is the same economy as uvm_env: half the value of UVM is not in the code of the library, it is in everybody using the same names for the same things. uvm_driver and uvm_sequencer do bring things —the seq_item_port and the arbitration—; uvm_monitor, uvm_env and uvm_agent are almost pure vocabulary.

## Slide 338: Agents
The jump: from the tester to the sequence
In the put and get ports we split the stimulus in two: the tester chose what to send, the driver knew how
We joined them with uvm_put_port / uvm_get_port and a uvm_tlm_fifo in the middle: three components in the tree and two connect()
UVM already brings that done, and with a name: the uvm_sequencer
The driver stops being a generic uvm_component and becomes uvm_driver #(T), which already comes with a seq_item_port
And the tester disappears: a uvm_sequence replaces it, and that is not a component — it is an object, it is not in the tree and it does not get connected
From the put/get to the seq_item_port

## Slide 339
Notes: This is the hardest jump of the course, and the reason is that there are two changes on the same line. It is worth separating them. Change one, structural: the FIFO is called a sequencer and comes with the driver. Change two, conceptual: the stimulus generator stops being a component. A component is built once in build_phase and lives the whole simulation; a sequence is created, runs, finishes and gets thrown away — and you can run another one right after on the same sequencer. That is what lets a test combine stimuli without touching the structure, and that is what the sequences section is all about. The question to throw at the group: why does the driver of the passive agent not exist, but the monitor does? Because driving is optional, watching is not.

## Slide 340: Agents
The handshake: get_next_item() / item_done()
The driver no longer does get(): it does get_next_item(), which blocks until the sequence has something
When it has finished driving the signals, it calls item_done()
That second call is what the put/get pair did not have: it is the driver saying “that is it, send me the next one”
Without item_done() the sequence hangs forever in its finish_item(), and the simulation stops advancing without a single error message
The pair always goes complete, and in that order
task run_phase(uvm_phase phase); command_transaction command; forever begin : command_loop seq_item_port.get_next_item(command); bfm.send_op(command.A, command.B, command.op); seq_item_port.item_done(); end : command_loop endtask : run_phase
Notes: Forgetting item_done() is mistake number one of the first week, and the symptom is misleading: no error, no warning, the simulation simply stops advancing in time and the objection never gets dropped. Verilator has no timeout by default: it keeps spinning until you kill it. The trick to remember it: get_next_item / item_done is a loan, not a copy. The sequence lends you the item and waits for you to give it back. put/get was a delivery: the tester dropped the command and moved on. And out of that comes the other useful difference: since the sequence still holds the handle, the driver can write the result inside it and the sequence reads it when it comes back from finish_item(). The sequences section uses that.

## Slide 341: Agents
The driver, now a uvm_driver
uvm_driver #(command_transaction) brings the seq_item_port for free: it is not declared nor instantiated with new()
The build_phase no longer looks for the BFM straight in the config_db: it asks the agent config for it
The run_phase is three lines: ask for the item, bfm.send_op(...), say it is done. The driver does not touch a wire
The protocol stays where we left it in interfaces and BFM: inside the BFM. That is why the driver of an agent is so short, and why changing protocol does not touch it
class driver extends uvm_driver #(command_transaction); `uvm_component_utils(driver) virtual vtalu_bfm bfm; function new(string name, uvm_component parent); super.new(name, parent); endfunction : new function void build_phase(uvm_phase phase); vtalu_agent_config cfg; // The BFM is not asked for on its own: ask for the agent config, and it comes from there. if (!uvm_config_db#(vtalu_agent_config)::get(this, "", "config", cfg)) `uvm_fatal("DRIVER", "Failed to get agent config") bfm = cfg.bfm; endfunction : build_phase task run_phase(uvm_phase phase); command_transaction command; forever begin : command_loop seq_item_port.get_next_item(command); bfm.send_op(command.A, command.B, command.op); seq_item_port.item_done(); end : command_loop endtask : run_phase endclass : driver
Notes: It is worth opening the driver of the put and get ports alongside and counting lines: they are almost the same. The only thing that changed is where the item comes from —before a uvm_get_port, now the seq_item_port— and that there is an item_done() at the end. The question worth asking: why is the driver so short? Because the protocol is not here. It is in the BFM since interfaces and BFM, and this class only translates transaction into call. That is the division of labour that makes an AXI agent have the same twenty-line driver. And the corollary, which is the one from the bus appendix: when the protocol changes, the BFM and the monitor change. The driver, the agent, the env and the test never find out.

## Slide 342: Agents
The sequencer gets declared with a typedef
uvm_sequencer is a parameterized class: it is parameterized with the type of item it is going to hand out
There is no need to extend it for anything: it is used as is
A typedef in the package gives it a short name, and that name is the one used by the agent and the create()
typedef uvm_sequencer #(command_transaction) sequencer;
The command_transaction of the transactions already extends uvm_sequence_item, so it does not have to be touched: that is why we chose that base class and not uvm_transaction
The typedef goes after the `include of the transaction and before the driver and the agent
Notes: This is the moment when the decision from the transactions gets cashed in. If that day the transaction had extended uvm_transaction, today this typedef would not compile: uvm_sequencer #(T) requires that T derive from uvm_sequence_item. It is worth saying explicitly: it is the first time in the course that a decision from an earlier section enables —or breaks— the next one. That is exactly what “adaptable code” means and it is not a phrase out of a manual. And in case somebody tries it: extending uvm_sequencer to add things to it is almost always a sign that it belonged in the sequence. The sequencer is an arbiter, not a place to put logic.

## Slide 343: Agents
The minimal sequence
A uvm_sequence #(T) has a task body(): that is all there is to write
Every item goes between start_item() and finish_item()
start_item() blocks until the sequencer gives us the turn; finish_item() blocks until the driver called item_done()
The randomize() goes between the two: that way the constraints get resolved at the moment the item is about to be handed over, not before
This is the direct translation of the tester of the transactions, and nothing more than that — the sequences section is about what can be done in here
class command_sequence extends uvm_sequence #(command_transaction); `uvm_object_utils(command_sequence) function new(string name = "command_sequence"); super.new(name); endfunction : new task body(); command_transaction command; // All transactions come out of the factory, the directed ones too: // a new() would skip add_test's set_type_override. command = command_transaction::type_id::create("command"); start_item(command); command.op = rst_op; finish_item(command); repeat (1000) begin : random_loop command = command_transaction::type_id::create("command"); start_item(command); // The randomize() goes BETWEEN start_item and finish_item: that way the // constraints are solved when the item is about to be handed over, and // not before. Today it makes no difference; the day a constraint // depends on the DUT state, it will. if (!command.randomize()) `uvm_fatal("COMMAND SEQ", "randomize() failed") finish_item(command); end : random_loop // Directed: the multiplier overflow, which 1000 random operations might // never touch. It comes out of the factory like the others, but since it // is not randomized, add_transaction's constraint does not run. command = command_transaction::type_id::create("command"); start_item(command); command.op = mul_op; command.A = 8'hFF; command.B = 8'hFF; finish_item(command); endtask : body
Notes: Two things worth marking in the code, because they are the ones that get copied wrong. First: the transaction comes out of type_id::create(), the reset one and the directed multiplication one too. It is the same rule as the transactions —the factory only finds out about what goes through create()— and here it matters again because the add_test is still around. Second: randomize() between start_item and finish_item is not a whim of style. Randomizing before works just the same today, but it breaks the day a constraint depends on the state of the DUT or on the previous response: by then the value had already been chosen. Randomizing late is the correct habit and it costs nothing to adopt it from day one.

## Slide 344: Agents
is_active: active and passive
uvm_agent brings a field is_active of type uvm_active_passive_enum, with two values: UVM_ACTIVE and UVM_PASSIVE
Active: the sequencer and the driver get built. The agent drives the interface
Passive: they do not get built. The agent only watches an interface that somebody else drives
The monitors and the two analysis ports get built always: a passive agent keeps feeding scoreboard and coverage
It is read with get_is_active() and decided in the build_phase, with an if
Active against passive

## Slide 345
Notes: The honest question is “and what do I want an agent that drives nothing for?”. Three answers from the field, in order of frequency: One, output interfaces. A port the DUT drives and you only verify does not need a driver, and the passive agent gives you the monitor and the coverage for free. Two, integration. When the block you verified becomes part of a chip, the interface stops being yours: the block next door drives it. The same agent, with one different line in the config, still works. That is the real return on having built an agent. Three, the one from the example: living with stimulus that is not yours — a legacy module, a reference model, a generator from another team.

## Slide 346: Agents
And it can be seen
bash run.sh +TOPOLOGY prints the tree of components UVM built
clase_agent_h vtalu_agent command_ap uvm_analysis_port command_monitor_h command_monitor driver_h driver seq_item_port uvm_seq_item_pull_port result_ap uvm_analysis_port result_monitor_h result_monitor sequencer_h uvm_sequencer seq_item_export uvm_seq_item_pull_imp modulo_agent_h vtalu_agent command_ap uvm_analysis_port command_monitor_h command_monitor result_ap uvm_analysis_port result_monitor_h result_monitor
Same class, two instances, and one has four components fewer
There too are the seq_item_port and the seq_item_export that the driver and the sequencer bring already fitted, without anybody declaring them — against the put and get ports, where the uvm_put_port had to be declared and new()ed
print_topology() is besides the debug tool for when a connect() points at a component that does not exist
Notes: This tree is printed by the library, not by the course, and that is the whole point: up to here the hierarchy was a diagram on a slide, and now it is an output you can grep. It is worth running it live — it is the print_topology() of the reporting section, now with something worth looking at. The two things to make them see, side by side: clase_agent_h has driver_h and sequencer_h, and modulo_agent_h does not. That is is_active in practice — the same class type, instantiated twice, and one built two objects fewer. Both monitors are in both, because watching is never optional. And the one that is not there: there is no sequence in this tree. A sequence is a uvm_object, not a uvm_component, so it does not live in the topology. It is the question thrown out on day 1 with the class diagram, and here it can be answered pointing at the screen.

## Slide 347: Agents
The config object of the agent
The agent needs two pieces of data from outside: which BFM and whether it is active
Both travel together in a configuration object, which is the public interface of the agent
It is a bare class, not a uvm_object: that is why the constructor can demand both pieces of data, and whoever forgets one does not compile
A uvm_object is created with type_id::create(), which only takes a name: the guarantee of the constructor is lost
The field is_active goes protected with a getter: nobody changes it after the agent has been built
// The agent config is NOT a uvm_object: it is a plain class. That is why the // constructor can DEMAND both values, and whoever forgets one does not compile. // A uvm_object is built with type_id::create(), which only takes a name, and // that guarantee is lost. class vtalu_agent_config; virtual vtalu_bfm bfm; // protected + getter: nobody changes it after the agent was built. protected uvm_active_passive_enum is_active; function new(virtual vtalu_bfm bfm, uvm_active_passive_enum is_active); this.bfm = bfm; this.is_active = is_active; endfunction : new function uvm_active_passive_enum get_is_active(); return is_active; endfunction : get_is_active endclass : vtalu_agent_config
Notes: Here the course departs from the custom of the industry on purpose, and it is worth saying so: most projects do class agent_config extends uvm_object and register it in the factory, so it can be overridden. It is a legitimate decision and it has its reason. The downside is the one in the bullet: you lose the constructor that forces you. What is not negotiable is the underlying idea, and it is the one to leave behind: every level of hierarchy receives its configuration through an object. If a component needs five pieces of data, that is not five uvm_config_db::get() scattered around: it is a config. The day you add the sixth piece of data, you touch one class and not six. Notice that the driver and the two monitors also ask for the config, not the BFM: the agent does not hand out handles by hand.

## Slide 348: Agents
The agent class: build_phase
It asks the uvm_config_db for its config and copies the is_active by hand: without super.build_phase(), uvm_agent’s, the one that would read it, never runs
It builds sequencer and driver only if it is active; the monitors and the two analysis ports, always
The analysis ports are ports: they get instantiated with new(), not with the factory
class vtalu_agent extends uvm_agent; `uvm_component_utils(vtalu_agent) vtalu_agent_config cfg; sequencer sequencer_h; driver driver_h; command_monitor command_monitor_h; result_monitor result_monitor_h; uvm_analysis_port #(command_transaction) command_ap; uvm_analysis_port #(result_transaction) result_ap; function new(string name, uvm_component parent); super.new(name, parent); endfunction : new function void build_phase(uvm_phase phase); if (!uvm_config_db#(vtalu_agent_config)::get(this, "", "config", cfg)) `uvm_fatal("AGENT", "Failed to get agent config") is_active = cfg.get_is_active(); if (get_is_active() == UVM_ACTIVE) begin : estimulo sequencer_h = sequencer::type_id::create("sequencer_h", this); driver_h = driver::type_id::create("driver_h", this); end : estimulo command_monitor_h = command_monitor::type_id::create("command_monitor_h", this); result_monitor_h = result_monitor::type_id::create("result_monitor_h", this); command_ap = new("command_ap", this); result_ap = new("result_ap", this); endfunction : build_phase
Notes: A detail worth gold that nobody tells: the build_phase of uvm_agent that the library brings only reads is_active from the resource pool. It is in code/.uvm/src/comps/uvm_agent.svh, it can be opened in class. Which means that in a testbench that calls super.build_phase(), a uvm_config_db#(int)::set(this, "mi_agent", "is_active", UVM_PASSIVE) works on its own, without a config object. Since this vtalu_agent does not call it, that mechanism is switched off, and that is why we assign it by hand. And here is where day 3 gets paid: uvm_agent and uvm_sequencer are the two classes in the library that do real work in their build_phase —uvm_agent reads is_active, and uvm_sequencer_param_base hooks up the response fifo (seq/uvm_sequencer_param_base.svh:288)—. It is exactly the case the rule for out there covers: if you extend either of the two and you write a build_phase, the super is mandatory. You inherited from an intermediate class that does real work, and skipping the super switches it off without a word. We can skip it because we wrote the line that replaces it; whoever does not write that line, cannot. Both ways are valid. What is not valid is half of each one: putting is_active in the config_db, not calling super.build_phase(), and then wondering why the agent starts up active. It happens often.

## Slide 349: Agents
The agent class: connect_phase
Inside: the seq_item_port of the driver against the seq_item_export of the sequencer — a single line, and only if it is active
Outwards: the ap of each monitor gets connected to the analysis port of the agent
That second connect() is the one that makes the agent a closed box: the env never touches command_monitor_h, it talks to command_ap
The mantra ports connect to exports still holds, with one more twist: a port also connects to another port of the same type, outwards. That is command_monitor_h.ap.connect(command_ap), and it is called port forwarding
Notes: Port forwarding is what confuses, and it is worth saying why it exists before how it is written. The agent wants to offer outwards a piece of data produced by a child of its own. It could expose the child —the env looking at agent.command_monitor_h.ap— and that is where the encapsulation ends: the day the monitor changes name, the env breaks. The way out is for the agent to have its own analysis port and plug it into the monitor’s. From outside a single port is seen, command_ap, and inside there can be whatever. It is exactly what a module does when it connects a port of its own to that of a submodule — the same idea, with classes. The detail that looks like it breaks the mantra: here a port connects to another port, not to an export. It is not a capricious exception — the direction is still the same, from the one who calls to the one who implements; the only thing that happens is that the agent is in the middle and implements nothing, it only forwards.

## Slide 350: Agents
How the env ends up
Four lines of structure instead of seven objects and five connections
The env no longer knows there is a driver, or a sequencer, or a FIFO: it knows there is an agent and that it has two analysis ports
The scoreboard and the coverage stay just as in the analysis ports: they are subscribers, and they find out about nothing
class env extends uvm_env; `uvm_component_utils(env) vtalu_agent agent_h; vtalu_agent_config agent_cfg_h; scoreboard scoreboard_h; coverage coverage_h; function new(string name, uvm_component parent); super.new(name, parent); endfunction : new function void build_phase(uvm_phase phase); virtual vtalu_bfm bfm; if (!uvm_config_db#(virtual vtalu_bfm)::get(this, "", "bfm", bfm)) `uvm_fatal("ENV", "Failed to get BFM") agent_cfg_h = new(.bfm(bfm), .is_active(UVM_ACTIVE)); uvm_config_db#(vtalu_agent_config)::set(this, "agent_h*", "config", agent_cfg_h); agent_h = vtalu_agent::type_id::create("agent_h", this); scoreboard_h = scoreboard::type_id::create("scoreboard_h", this); coverage_h = coverage::type_id::create("coverage_h", this); endfunction : build_phase function void connect_phase(uvm_phase phase); agent_h.command_ap.connect(scoreboard_h.cmd_f.analysis_export); agent_h.command_ap.connect(coverage_h.analysis_export); agent_h.result_ap.connect(scoreboard_h.analysis_export); endfunction : connect_phase
That is the env of a single VTALU. With two, it changes less than it looks
Notes: This is the slide for making the comparison live: open the env.svh of transactions alongside. The difference is not that it is shorter —which it also is—, it is what disappeared: the env of transactions named command_f, which means it knew the internal mechanism of how the stimulus reached the driver. This one does not name it. That is encapsulation measured objectively: count the names that the class above has to know. If the group is doing well on time, the question is worth it: what would have to change in this env to go from a FIFO to a sequencer? Nothing. It is already inside the agent.

## Slide 351: Agents
Two agents, one single string
The two agents execute the same line: uvm_config_db#(vtalu_agent_config)::get(this, "", "config", cfg)
And yet they have to receive different objects
The second argument of the set() resolves it: the scope, which is the path of the component that is going to read
"clase_agent_h*" reaches that agent and everything hanging off it — that is why the driver and the monitors find the same config without anybody passing it to them
The this of the set() is the starting point of that path: the env
The hierarchical scope of the config_db

## Slide 352
Notes: Here is the classic trap of the section, and it is one of the ones that never fail. With a single agent, everybody writes "*" in the scope and it works. The day the second one shows up, the second set() overwrites the first and both agents get the same config: the same BFM and the same is_active. With the order in env.svh —the class first and the module after— the one left standing is the passive one, so both start up passive, with no driver and no sequencer, and the test’s seq.start() lands on a null handle. With the order reversed they would be two drivers, but driving the same interface. What is invariant, and what to take away: the last set() wins, and both agents end up identical. The error does not show up in build_phase. The asterisk matters: "clase_agent_h*" with an asterisk reaches the children; "clase_agent_h" without an asterisk, only the agent. If you write it without an asterisk, the agent finds its config and the driver does not — uvm_fatal in build_phase, which at least is an honest error. Short rule to take away: the scope of the set() is a path, not a label.

## Slide 353: Agents
When the config_db does not find: +UVM_CONFIG_DB_TRACE
$ bash run.sh +UVM_CONFIG_DB_TRACE UVM_INFO ... Configuration 'config' (type vtalu_agent_config) set by env_h UVM_INFO ... Configuration 'config' read by accessor=uvm_test_top.env_h.clase_agent_h.driver_h UVM_INFO ... Configuration 'config' read by accessor=uvm_test_top.env_h.modulo_agent_h.command_monitor_h
The config_db is a database by strings: when it fails, it fails in silence or with a uvm_fatal that does not say why
+UVM_CONFIG_DB_TRACE makes UVM print every set() and every get(), with the complete hierarchical path of the component that asked for it
It works for the two questions one asks: did the set() reach this component? and which components actually exist?
It is a plusarg, not code: nothing has to be touched or recompiled
Notes: This is the tool that tests was missing, when we said that get(null, "*", ...) “does not fail: it lies”. With the trace on, lying becomes difficult: you see who put what and who read it. The use almost nobody discovers on their own is the second one: since every get() prints the path of the component that called it, the output is a census of the tree written by the library. If a component does not show up, it was not built. The exercise of the day uses exactly that to grade itself, and that is why it cannot be cheated: the student does not write those lines. A close relative worth naming: +UVM_OBJECTION_TRACE, for the other classic hang —the simulation that does not finish because somebody did not drop their objection—.

## Slide 354: Agents
The example: two VTALU and the legacy module
The case that justifies all of this: two sources of stimulus have to be compared on the same design
The top instantiates two VTALU and two vtalu_bfm
The first one is driven by our agent, in UVM_ACTIVE
The second one is driven by vtalu_tester_module, an ordinary module without one line of UVM, and we hang an agent on it in UVM_PASSIVE to watch it
Two scoreboards and two coverages: that is what answers which of the two stimuli covers more
module top; import uvm_pkg::*; import vtalu_pkg::*; `include "vtalu_macros.svh" `include "uvm_macros.svh" // The VTALU driven by the class testbench vtalu_bfm clase_bfm (); vtalu clase_dut ( .A(clase_bfm.A), .B(clase_bfm.B), .op(clase_bfm.op_set), .clk(clase_bfm.clk), .reset_n(clase_bfm.reset_n), .start(clase_bfm.start), .done(clase_bfm.done), .ovf(clase_bfm.ovf), .result(clase_bfm.result) ); // The VTALU driven by the legacy module vtalu_bfm modulo_bfm (); vtalu modulo_dut ( .A(modulo_bfm.A), .B(modulo_bfm.B), .op(modulo_bfm.op_set), .clk(modulo_bfm.clk), .reset_n(modulo_bfm.reset_n), .start(modulo_bfm.start), .done(modulo_bfm.done), .ovf(modulo_bfm.ovf), .result(modulo_bfm.result) ); vtalu_tester_module stim_module (modulo_bfm); initial begin // The top knows nothing about agents: it leaves the two interfaces with a // name and walks away. Handing them out is the test's job. uvm_config_db#(virtual vtalu_bfm)::set(null, "*", "clase_bfm", clase_bfm); uvm_config_db#(virtual vtalu_bfm)::set(null, "*", "modulo_bfm", modulo_bfm); run_test(); end endmodule : top
The module calls the very same bfm.send_op() as the driver: it receives the interface through its port instead of through a virtual interface, but the protocol it executes is exactly the same code
That is what makes the comparison fair: both stimuli speak identically to the DUT. The only thing being compared is what each one sends, not how
Notes: This top.sv is the one that closes the argument of the section, and it is worth reading looking for what did not change: there are two VTALU, two interfaces, two different config_db, and the vtalu_tester_module is still the same old Verilog module as always. Nobody touched it so it could live with UVM. That is the real scenario the section comes to solve, and it is worth naming it like this: you arrive at a project where there is already a stimulus written in Verilog that works and nobody is going to rewrite. With a passive agent you can watch it —scoreboard, coverage, assertions— without asking anybody’s permission or touching a line of it. The technical detail that makes the comparison fair, and that has to be pointed at with a finger: the module calls the same bfm.send_op() as the driver. It receives the interface through a port instead of through a virtual interface, but the protocol is the same code. If each one drove the bus its own way, comparing coverages would not mean anything.

## Slide 355: Agents
The test, and what is still missing
The test takes the two BFM out of the config_db, builds the env_config and passes it down
Then it starts the sequence by hand, on the sequencer of the active agent:
seq = command_sequence::type_id::create("seq"); seq.start(env_h.clase_agent_h.sequencer_h);
It works, but look at what that line does: the test goes across the hierarchy to reach the sequencer, and with that it knows the inside of the env again
Everything we have just encapsulated leaks out in one line
The sequences section fixes it: the sequence is handed to the sequencer through the config_db, and the test stops knowing where it is
function void build_phase(uvm_phase phase); virtual vtalu_bfm clase_bfm, modulo_bfm; env_config env_config_h; // The top left the two interfaces loose; the test packs them up. if (!uvm_config_db#(virtual vtalu_bfm)::get(this, "", "clase_bfm", clase_bfm)) `uvm_fatal("DUAL TEST", "Failed to get clase_bfm") if (!uvm_config_db#(virtual vtalu_bfm)::get(this, "", "modulo_bfm", modulo_bfm)) `uvm_fatal("DUAL TEST", "Failed to get modulo_bfm") env_config_h = new(.clase_bfm(clase_bfm), .modulo_bfm(modulo_bfm)); uvm_config_db#(env_config)::set(this, "env_h*", "config", env_config_h); env_h = env::type_id::create("env_h", this); endfunction : build_phase // +TOPOLOGY prints the component tree. It is how to SEE that the passive // agent built neither a sequencer nor a driver. function void end_of_elaboration_phase(uvm_phase phase); if ($test$plusargs("TOPOLOGY")) uvm_root::get().print_topology(); endfunction : end_of_elaboration_phase task run_phase(uvm_phase phase); command_sequence seq; phase.raise_objection(this); // The only thing left wired by hand: the test reaches across the // hierarchy to get to the sequencer. The sequences section takes it out of here. seq = command_sequence::type_id::create("seq"); seq.start(env_h.clase_agent_h.sequencer_h); #500; phase.drop_objection(this); endtask : run_phase
Notes: This is the slide to close the day with if there is no time for the summary: it leaves an open question and a concrete promise. And it is honest: seq.start(env_h.clase_agent_h.sequencer_h) is real code that works and that is seen in many testbenches. It is not “wrong”. It is simply the last thing in the testbench that is still hard-wired, and it is the one the section that follows knocks over. If somebody asks why we do not do it right from the start: because to understand the default_sequence you first have to have suffered writing the start() by hand.

## Slide 356: Agents
What this section does differently
The book does not use a sequencer here. In The UVM Primer the agent of this section still has the tester and the uvm_tlm_fifo inside, and the sequencer only shows up with sequences — where besides the tester disappears
We build the agent complete in one go: it is the way it is written today, and it makes the sequences section be only about sequences
The scoreboard and the coverage stay outside the agent, against what the UVM Primer does. A passive agent should not drag a scoreboard along
The config of the agent is not a uvm_object: it is a bare class, so that the constructor forces you. The industry usually makes it a uvm_object
The protocol lives in the BFM, the same as in the UVM Primer. Up to Verilator 5.051 this could not be done: an interface task called through a virtual interface did not propagate. It was fixed in 5.052 — docs/en/verilator.md
Notes: That the material says where it departs from its sources is not a detail of tidiness: it is what lets the student read the UVM Primer afterwards without believing that one of the two is broken. And along the way it leaves the lesson most used at work: the structure of a UVM testbench is not fixed by the standard, it is fixed by custom. IEEE 1800.2 does not say anywhere that the scoreboard goes in the env. It says what a uvm_agent is and nothing else. Everything else is convention — good, but convention.

## Slide 357: Agents
Summary of the unit
An agent packs everything that knows how to speak one interface: sequencer, driver and monitors, wired inside a single time
It gets instantiated once per interface, and it is configured with a configuration object, not with loose handles
is_active decides whether, besides watching, it drives
The env went from seven components wired by hand to one agent and two subscribers
The uvm_config_db stops being a global mailbox: the scope is a path in the tree, and with more than one agent it is what makes each one receive its own
One single thing was left hard-wired: the test still looks for the sequencer by hand to start the sequence. That is the sequences section
Notes: Close of the section and of the biggest jump of the course. It is worth saying where they ended up standing: with today’s material, the student can read the testbench of any UVM project and recognise the structure. An agent per interface, a config per level, analysis in the env. It is literally 80 % of what they will see on their first day. What is missing —sequences— is what they will write on their first day. That is why they go together on the same day and in this order: first the house, then what happens inside.

## Slide 358
Callbacks
The third hook
On day 1 we promised three ways of writing a new test without touching the env: constraints, factory override and callbacks. Two are done
The three are the same idea at different heights: the constraint changes values, the override changes a whole class, the callback changes what a class does at one point
The case that separates them: you are handed a VIP agent —from another team, or bought— and you need the driver to send a broken piece of data once in a while
With an override you have to rewrite the whole driver to change one line. With a callback you hook that line and nothing else
And there is a difference that is not a matter of style: callbacks stack. The override picks one class; the callbacks all run, every one of them, in order
Notes: This half section exists because unit 1 promises three hooks, and without it the course delivers two. Fifteen minutes are enough: the mechanics are small and what has to be left behind is the criterion for when it gets used. The criterion, said in one line: override when the what changes, callback when the when changes. If the new class differs from the old one in several methods, it is an override. If it is the same class with an addition at one point, it is a callback — and above all if the original class is not yours and you cannot touch it. The key word in all of this is VIP. In a real project half of the agents come from outside, with their licence and their support, and editing them is not an option: the next version wipes your change. The callback is the extension point the one who wrote the VIP left on purpose. And that they stack is what makes it possible for two engineers to hook different things into the same driver without stepping on each other. With overrides, the second one wins.

## Slide 359: Callbacks
The hook: one class, one empty virtual method
class driver_callback extends uvm_callback; `uvm_object_utils(driver_callback) function new(string name = "driver_callback"); super.new(name); endfunction : new // A task, not a function: a callback that only edits the transaction could // be a function, but one that adds delay needs to consume time. Making the // hook a task costs nothing and leaves both open. virtual task pre_send(driver drv, command_transaction cmd); endtask : pre_send endclass : driver_callback
A uvm_callback is not a component: it is not in the tree, it has no phases and it does not show up in print_topology() — just like a sequence
The base method is empty on purpose: with nobody registered, the testbench runs exactly as before
It is a task and not a function because a delay callback has to be able to consume time. One that only edits the transaction could be a function
Notes: It is worth stopping on the fact that it is a normal class, extending uvm_callback, which extends uvm_object. There is no magic: the only thing uvm_callback does is give it a place in the pool UVM keeps per component instance. The typedef class driver; at the top of the file is the boring and necessary part: the callback receives the driver, and the driver registers the callback, so one of the two has to be forward-declared. In a real testbench this lives in its own file for that very reason. If somebody asks why the base method is empty instead of abstract: because uvm_do_callbacks walks the whole queue, and an empty queue has to be legal. The empty base class is what makes “no callbacks” the normal case and not an exception.

## Slide 360: Callbacks
Two lines in the driver, and not one more
class driver extends uvm_driver #(command_transaction); `uvm_component_utils(driver) // Declares "this component accepts callbacks of this type". Without it the // add() below still hooks up and the callback still runs, but with a CBUNREG // warning and without the type check: outside the contract, and nearly silent. `uvm_register_cb(driver, driver_callback) virtual vtalu_bfm bfm;
task run_phase(uvm_phase phase); command_transaction command; forever begin : command_loop seq_item_port.get_next_item(command); // Every callback registered on this driver, in the order they were // added. With none registered this is a loop over an empty queue. `uvm_do_callbacks(driver, driver_callback, pre_send(this, command)) bfm.send_op(command.A, command.B, command.op); seq_item_port.item_done(); end : command_loop endtask : run_phase
`uvm_register_cb declares the type/callback pair. Without it the add() hooks up all the same and the callback runs — with a UVM_WARNING CBUNREG lost in the log, and without the type check or add_by_name
`uvm_do_callbacks is the extension point: it walks the queue of that instance of driver, in order
Notes: The diff against the driver of the Agents section is exactly two lines, and it is worth showing it with a live diff: diff code/u7/agents/tb_classes/driver.svh code/u7/callbacks/tb_classes/driver.svh. Everything else —the get_next_item, the send_op, the item_done— is the same. The failure mode of the missing uvm_register_cb is not the one you expect, and it is worth telling it with the source in hand because half the tutorials get it backwards: uvm_callback.svh:745 reports a UVM_WARNING CBUNREG and carries on — the add() puts the callback into m_base_inst.m_pool all the same (:781-785), and `uvm_do_callbacks reads that pool without consulting the registry (:964-1006). Which means: without the macro the callback runs, and what you lose is the type check and add_by_name by derived type. That is worse than an error: it is a warning among a thousand lines, and the testbench ends up outside the contract without anyone noticing. That is why the run.sh of the example does not check the macro but the effect: it counts how many times the callback ran and fails if it is zero. An example that “passes” without having injected anything proves nothing, whatever the reason it came unhooked. Where to put the `uvm_do_callbacks is the real design decision, and it is the same one taken by whoever writes a VIP: every hook point is a promise of forward compatibility. That is why VIPs have three or four, not thirty.

## Slide 361: Callbacks
Putting them in: the test, and nothing but the test
// end_of_elaboration and not build: the driver is a grandchild of the env, // and build_phase runs top-down -- when this test's build_phase returns, the // driver does not exist yet. function void end_of_elaboration_phase(uvm_phase phase); super.end_of_elaboration_phase(phase); flip_h = flip_bit_cb::type_id::create("flip_h"); jitter_h = jitter_cb::type_id::create("jitter_h"); // Both on the same driver, and both run: the queue is per component // instance, in insertion order. The passive agent has no driver, so there // is nothing to hook there. uvm_callbacks #(driver, driver_callback)::add(env_h.clase_agent_h.driver_h, jitter_h); uvm_callbacks #(driver, driver_callback)::add(env_h.clase_agent_h.driver_h, flip_h); if ($test$plusargs("CALLBACK_TRACE")) uvm_callbacks #(driver, driver_callback)::display(env_h.clase_agent_h.driver_h); endfunction : end_of_elaboration_phase
The test does not touch the env, nor the agent, nor the driver, nor the sequence. Just like the override, one level further down
end_of_elaboration_phase and not build_phase: the driver is a grandchild of the env, and when the build_phase of the test finishes it does not exist yet
The two callbacks go on the same instance and both run, in the order in which they were added
bash run.sh +CALLBACK_TRACE prints the queue of the driver
Notes: The phase trap is the one that takes somebody’s whole afternoon: uvm_callbacks::add needs the handle of the component, and the tree is built top down. In the build_phase of the test, env_h exists —it has just created it— but env_h.clase_agent_h is null. end_of_elaboration_phase runs with the whole tree assembled, which is exactly what is needed. The alternative that is sometimes seen is add_by_name("*driver_h", cb, this), with a pattern instead of a handle. It is useful when you do not want to go across the hierarchy, and it has the same phase problem. And the passive agent does not show up in either of the two lines for a reason that is obvious once said: it has no driver. Callbacks hang off instances, not off types, so “the driver of the active agent” is a concrete address in the tree.

## Slide 362: Callbacks
The flipped bit the scoreboard does not see
cd code/u7/callbacks && bash run.sh
The flip_bit_cb flips a bit of A in one out of every eight transactions. The scoreboard says nothing, and both runs close at 0 UVM_ERROR
It is not a hole in the checker: it is the proof that the monitor watches the wire, not what the driver thought it was going to send
A monitor that rebuilt the transaction from the driver —or that copied it from the sequencer— would have given PASS on data the DUT never saw
What can be seen of the jitter_cb is the time: same stimulus, more cycles
The hook | Changes | How many at a time
Constraint | the values | as many as you like
Factory override | the whole class | one
Callback | what a class does at one point | as many as you like
Notes: This is the slide of the half section, and the exercise of thinking is worth more than the code: “if I inject an error and the scoreboard does not scream, is the scoreboard wrong?” Let the group argue about it for a minute before answering. The answer is no, and it is one of the most important things in the course: the scoreboard predicts from what the monitor saw on the bus. If the driver sends A^1, the DUT computes with A^1, the monitor sees A^1 and the prediction gives A^1. All consistent. The only testbench this callback would break is one with a monitor that does not watch the signals — and that testbench was wrong before the callback ever existed. Out of that comes the rule we already saw in Agents and that now has a demonstration: the monitor watches the wire, always. An injection callback is, besides a tool, the cheapest test there is for finding out whether your monitor does it. To inject an error the scoreboard does have to catch, you have to break the DUT, not the stimulus — which is exactly what the +BUG=1 of the capstone does.

## Slide 363
Sequences
The only thing left hard-wired
The agents left the testbench encapsulated: one agent per interface, the analysis in the env, and nobody naming somebody else’s components
Except for one line, the one in the run_phase of the test:
seq.start(env_h.clase_agent_h.sequencer_h);
The test goes across the hierarchy to reach the sequencer, and along the way it gets to know the inside of the env we have just closed
And there is something bigger behind it: that command_sequence is one class doing three things — resetting, sending a thousand random operations and one directed
This section is about what happens inside body(), and about how a sequence gets started without wiring it
Notes: The sentence that orders the whole section: stimulus is not structure. A component is built once, before the simulation starts, and it stays there until the end. Stimulus changes from test to test, and sometimes it changes inside the same test. Transactions, agents and sequences are the same operation repeated on three different things: separating the data (transaction), separating the structure (agent), separating the stimulus (sequence). The question to throw at the group before going on: with the command_sequence of the agents, how many classes are needed to try three stimuli and their combinations? Six, and it grows factorially. In the UVM Primer that is called explosion of tester classes.

## Slide 364: Sequences
An object, not a component
The sequence lives outside the component tree; the sequencer, inside

## Slide 365
The uvm_sequencer is a uvm_component: it is in the tree, it has a parent, it has phases, the build_phase of the agent builds it
The uvm_sequence is a uvm_object: it is not in the tree, it has no parent, it has no phases, and it gets created with a single argument — just like the transactions
Practical consequence: it gets created, runs, finishes and is thrown away. You can run another one right after, or two at once, without touching the structure
Notes: There is a detail here that confuses and is worth getting ahead of, because they are going to see it in the log: even though the sequence is not in the tree, UVM reports it hanging off the sequencer, with an @@ in the middle: uvm_test_top.env_h.clase_agent_h.sequencer_h@@full_seq.random_seq That does NOT mean it is a child of the sequencer. The @@ is precisely the mark that what follows is a sequence and not a component: to the left, the path of the sequencer it runs on; to the right, the path of nested sequences. If somebody looks for sequencer_h.full_seq with uvm_root::get().find() they are never going to find it. The other consequence, the one used every day: since it is not a component, a sequence can have configurable fields that get changed between the create() and the start(). That is what full_seq.count = 200 does at the end of the unit, and with a component it could not be done: by the time you want to change it, the build_phase has already gone by.

## Slide 366: Sequences
The smallest sequence there is
// The smallest sequence there is: a single item. // // It is a uvm_object, not a uvm_component: it is not in the tree, it has no // parent, it has no phases. It gets created, it runs, and it gets thrown away. class reset_sequence extends uvm_sequence #(command_transaction); // `uvm_object_utils, NOT `uvm_component_utils: the constructor takes a single // argument and there is no parent to pass. `uvm_object_utils(reset_sequence) function new(string name = "reset_sequence"); super.new(name); endfunction : new // body() is a TASK, not a function: it blocks inside. Nobody calls it by // hand; UVM calls it when somebody starts the sequence. task body(); command_transaction command; command = command_transaction::type_id::create("command"); start_item(command); // blocks until the sequencer gives us our turn command.op = rst_op; // only now do we decide what to send finish_item(command); // blocks until the driver calls item_done() endtask : body endclass : reset_sequence
It extends uvm_sequence #(T), parameterized with the item it is going to send
It gets registered with `uvm_object_utils — not with `uvm_component_utils
Constructor with a single argument: name, without parent
All the work lives in body(), which is a task: it can block
Nobody calls body() by hand: UVM calls it when somebody starts the sequence
Notes: The two typing mistakes everybody makes the first time, and which give messages that do not help: 1. `uvm_component_utils instead of `uvm_object_utils. The error talks about a constructor with two arguments and nobody relates it to the macro. 2. function body() instead of task body(). The declaration compiles, and then the start_item() inside does not, because a function cannot block. And a design one worth marking: the command is declared inside body(), not as a field of the class. In the UVM Primer it is a field. If it is a field, two runs of the same sequence share the handle, and the day somebody starts the same sequence twice in parallel you have two threads writing the same object. And a protocol one, which is what makes this sequence exist: the first item of every test is a reset. The VTALU starts up with reset_n at 0 and never raises done; the driver stays in its while (bfm.done == 0) and the sequence, in the first finish_item(). There is no error: the simulation stops advancing. It is the same symptom as the forgotten item_done(), with another cause, and it is worth showing it once in class by deleting the reset_sequence from full_sequence.

## Slide 367: Sequences
The handshake, now from the sequence side
Timeline of start_item, get_next_item, item_done and finish_item

## Slide 368
The same four calls as the agents, looking at the other lane: start_item() blocks the sequence until the sequencer gives it the turn, and finish_item() blocks it until the item_done() of the driver
Simulation time advances only in the amber bar: filling the item does not cost a clock edge
Two threads, four calls and no #delay in the middle
Notes: Confusion number one of the section: believing that finish_item() comes back when the item was delivered. No: it comes back when the driver called item_done(), that is when the operation finished in the DUT. It is the difference between “I sent it” and “it is done”, and it is what makes the Fibonacci sequence possible. Out of that comes as well why the #500 that the tester of the transactions had at the end disappeared: it was not stimulus, it was a patch so the objection would not drop before its time. With finish_item() the stimulus no longer gets cut in half. Careful, honesty: the last result can still end up uncompared, because the objection gets dropped as soon as start() comes back and the result_monitor publishes one edge later. It can be seen in the log of the add_test run with +UVM_VERBOSITY=UVM_HIGH: 1001 commands, 1000 comparisons. If somebody asks about the non-blocking cousin: there is try_next_item(), which comes back right away with null if the sequencer has nothing. It is the same get() / try_get() pair from the communication between threads and it is useful when the protocol forces you to drive the bus even when there is no stimulus — idle cycles, refresh of a DRAM. The VTALU does not need it: between one operation and the next the signals can stay still.

## Slide 369: Sequences
What happens between start_item() and finish_item()
task body(); command_transaction command; repeat (count) begin : random_loop // Through the factory, same as in the Transactions section: that is what lets // add_test change the TYPE without touching a line of this sequence. command = command_transaction::type_id::create("command"); start_item(command); // Late randomization: the values are picked AFTER getting the // sequencer's turn, not when the object was created. if (!command.randomize()) `uvm_fatal("RANDOM SEQUENCE", "randomize() failed") finish_item(command); end : random_loop endtask : body
When start_item() comes back, the sequence already has the turn of the sequencer: nobody else is going to beat it to the driver
Only then do the fields get filled, or the randomize happen. That is late randomization: the values get chosen at the last possible moment
It is useful because by then it is already known what state the DUT is in, and a constraint can depend on that
randomize() still goes with its else: it returns 0 and aborts nothing — it is the same thing they saw in the Constrained random unit
Notes: The honest question: “and what if I randomize before start_item()?”. It works. On a small testbench you do not notice the difference. You notice it when the sequence has a thousand items queued up and a constraint depends on something that changes during the run —an address that has already been written, a buffer that has filled up, the previous result—. If you randomized everything at the beginning, you decided with old information. The other reason, more practical: between start_item() and finish_item() is where UVM calls pre_do() and mid_do(), which are the hooks people use to inject errors without touching the original sequence. If you fill the item before, those hooks have nothing to do. And the hook back to day 5: this is where the randomize() with {} of the coverage closure goes. The directed case gets asked for at the point of use, without writing a new class. The slide that follows is exactly that, with the Verilator trap included.

## Slide 370: Sequences
Directed late randomization, and the Verilator hole
start_item(command); command.data.constraint_mode(0); // 1. I switch off the dist if (!command.randomize() with {A inside {[1:10]};}) // 2. I ask for the directed one `uvm_fatal("SEQ", "randomize() failed") finish_item(command);
Measured with Verilator 5.052, on a class with the constraints of command_transaction, 100 randomizations of each form:
with {op == mul_op} 100 of 100 op has no dist with {A inside {[1:10]}} 1 of 100 A does have one constraint_mode(0) + with {A inside ...} 100 of 100 the workaround
The rule, in one line: if the with {} touches a field that has a dist, switch that constraint off first
It is not the language, it is the tool: repro-dist-with.sv in code/verilator/
Notes: It is the same limitation they already saw in the Constrained random unit, but here it shows up in the place where they are really going to use it, so it is worth measuring it again against the real transaction. What the measurement adds on top of what docs/en/verilator.md says: the trigger is not “there is a dist in the class”. It is the with {} restricting a field that has a dist. Asking for op == mul_op works perfectly, even though A and B have dist in the same resolution. That is why the sequences of the section do not run into this: none of them uses with {}. And the workaround is not a concession: for a directed case, switching off the distribution constraint is the right thing anyway. The dist is there so the random hits the edges; if you already know which value you want, it has nothing to contribute. constraint_mode(0) is per object, not per class, and the object gets thrown away after finish_item(): there is no need to remember to switch it back on.

## Slide 371: Sequences
The item comes back with the result inside
task run_phase(uvm_phase phase); command_transaction command; shortint unsigned alu_result; forever begin : command_loop seq_item_port.get_next_item(command); // blocks until there is an item bfm.send_op(command.A, command.B, command.op, alu_result); command.result = alu_result; // the way back seq_item_port.item_done(); // unblocks the finish_item() end : command_loop endtask : run_phase
The driver writes command.result before calling item_done()
The sequence still holds the handle to that same object: when finish_item() comes back, the result is there
It is the way back, and that is why command_transaction gains a field result in this unit — the only change to the transaction since it was created
It breaks MOOCOW on purpose: the driver modifies an object it did not create. It is agreed between the two parties, and it is the only place in the testbench where it is done
Notes: This is the subtlest point of the section and it is worth saying it slowly: there is no return channel at all. There is no port, there is no FIFO. There is a shared handle, and the two parties agreed that the driver writes and the sequence reads, and that the safe moment to read is after finish_item(). If somebody asks “wasn’t the rule to clone?”: yes, that is the rule of the transactions, and this is the documented exception. UVM has besides a formal mechanism for this —the REQ/RSP pair of uvm_sequence #(REQ, RSP) with put_response() on the driver side and get_response() on the sequence side— that almost nobody uses, because writing the result into the request is enough in the vast majority of cases. It is worth naming so they recognise it if they see it. An implementation detail that does matter: the send_op reads bfm.result on the same edge on which it sees done high. One edge later the DUT has already started the next operation.

## Slide 372: Sequences
The formal way back: get_response()
// The sequence declares TWO types, and the response is no longer the request class fib_sequence extends uvm_sequence #(command_transaction, result_transaction); start_item(cmd); finish_item(cmd); get_response(rsp); // blocks until the driver answers // And the driver, on the other side: seq_item_port.get_next_item(req); rsp = result_transaction::type_id::create("rsp"); rsp.set_id_info(req); // without this the response does not find its sequence seq_item_port.item_done(rsp); // or item_done() now and put_response(rsp) later
The shared handle of the previous slide holds as long as the driver is blocking and serves one at a time. The course’s one is
A pipelined driver calls item_done() as soon as it pushes the command and the response arrives N cycles later: by then the sequence has already sent another item, and writing into req.result writes to the wrong item
set_id_info(req) copies the sequence and transaction id onto the response. It is what makes get_response() know who to answer
The other two cases where it is needed: a VIP that clones the item, and a protocol with more than one response per request
Notes: This is the half slide that avoids a poor answer in an interview. The question sounds like “how do you give the data back to the sequence?”, and answering “I write the result field into the item” is right for this driver and fails on any real bus. It is worth saying both halves together. The reasoning to leave behind: the shared handle trick is not a technique, it is a consequence of the driver being blocking. The condition is written in the get_next_item()/item_done() of the previous slide — as long as the item_done() is after having the response, there is a single item in flight and the handle is enough. The day somebody moves that item_done() up to gain throughput, the testbench keeps compiling and starts lying. The other failure mode, more treacherous: a VIP that clones the item between the sequence and the driver. There the driver writes into its copy, the sequence reads the original, and the result that arrives is always the previous one. There is no error, there is no warning: there is a scoreboard shifted by one. And the set_id_info() detail, which is the one that makes this fail silently the first time: if it is missing, the response is sent anyway and get_response() waits forever. A test that “hangs after the first transaction” and uses REQ/RSP is this bug until proven otherwise.

## Slide 373: Sequences
Fibonacci: when the stimulus depends on the result
task body(); byte unsigned n_menos_2 = 0; byte unsigned n_menos_1 = 1; command_transaction command; command = command_transaction::type_id::create("command"); start_item(command); command.op = rst_op; finish_item(command); `uvm_info("FIBONACCI", "Fib(01) = 000", UVM_MEDIUM) `uvm_info("FIBONACCI", "Fib(02) = 001", UVM_MEDIUM) // Up to 14 and no further: Fib(14) = 233 and Fib(15) = 377, which does not // fit in the 8 bits of A and B. for (int ff = 3; ff <= 14; ff++) begin : fib_loop command = command_transaction::type_id::create("command"); start_item(command); command.A = n_menos_2; command.B = n_menos_1; command.op = add_op; finish_item(command); // returns when the driver called item_done() n_menos_2 = n_menos_1; n_menos_1 = command.result; // the driver wrote it inside the item `uvm_info("FIBONACCI", $sformatf("Fib(%02d) = %03d", ff, n_menos_1), UVM_MEDIUM) end : fib_loop endtask : body
Every addition needs the result of the previous one: without a way back this cannot be written
finish_item() comes back after the ALU has finished, so command.result is already valid
It is the same env, the same agent, the same driver and the same BFM as the random test. Only the sequence changes
Notes: Fibonacci is not there to teach Fibonacci: it is there to force the case where the stimulus N+1 depends on the result N. A test like that with the tester of the transactions is impossible without giving the tester a handle to the monitor, that is without breaking the separation we had been building. Numbers for the blackboard: 0 1 1 2 3 5 8 13 21 34 55 89 144 233. It stops at 233 because the next one is 377 and A and B are 8 bits. Having the student see why the for goes up to 14 and not up to 20 is worth more than the whole sequence. And one that is seen in the real run: the whole test takes 500 units of time, against the 43,000 of the random test. Thirteen operations. A well-written directed test is cheap; what is expensive is the random, and that is why it runs at night.

## Slide 374: Sequences
Sequences that call sequences
full_sequence starting three sub-sequences on the same sequencer

## Slide 375
A sequence can start others: it is the way of composing stimulus without duplicating code
The command_sequence of the agents, split into three pieces that now get combined however you like
The sequencer arbitrates: whatever it receives, it hands the driver one item at a time
Notes: The idea of the slide is that a sequence is not a special layer: it is an object with a body(), and inside a body() another sequence can be started just the way the first one is started. There is no nesting limit nor a different class for “sequence that calls sequences”. The practical consequence, which is the one that counts: stimulus gets composed like functions. A small sequence —“write the four registers”, “send a maximum multiplication”— gets written once and afterwards goes into any scenario. It is exactly what in the conventional testbench was done by copying and pasting blocks of the tester. The last bullet is the one that avoids the most common misunderstanding: that three sequences are composed does not mean that their items get mixed on the bus. The sequencer hands over one at a time, and if two sequences compete on the same sequencer there is an arbitration policy deciding. With sequences nested on a single sequencer, the order is the one the body() says.

## Slide 376: Sequences
full_sequence: three pieces, one single sequencer
task body(); reset_sequence reset_seq; random_sequence random_seq; maxmult_sequence maxmult_seq; reset_seq = reset_sequence::type_id::create("reset_seq"); random_seq = random_sequence::type_id::create("random_seq"); maxmult_seq = maxmult_sequence::type_id::create("maxmult_seq"); random_seq.count = count; // get_sequencer() returns the sequencer start() handed us: the children run // on the same one. The second argument declares them CHILDREN -- without it // they compete with us in the arbitration instead of inheriting our turn. reset_seq.start(get_sequencer(), this); random_seq.start(get_sequencer(), this); maxmult_seq.start(get_sequencer(), this); endtask : body
get_sequencer() returns the sequencer that start() handed to this sequence: the daughters run on the same one
The second argument, this, declares them daughters. Without it they compete with the mother in the arbitration instead of inheriting her turn
random_seq.count = count is the advantage of the sequence being an object: it gets configured between the create() and the start()
To run two in parallel, fork / join around the start(), and the sequencer interleaves the items
Notes: get_sequencer() is the accessor of IEEE 1800.2; the field is called m_sequencer and the UVM Primer uses it directly. Both forms work — the get_ one is the one worth teaching, because m_ is the UVM convention for “this is internal”. And if somebody has already read production code they are going to ask about p_sequencer: it is a typed handle to the sequencer, which shows up when you use `uvm_declare_p_sequencer(mi_sequencer). It is only useful if you extended uvm_sequencer to put something of your own in it, because m_sequencer is of type uvm_sequencer_base and does not see those fields. Since in this course the sequencer is a bare typedef, p_sequencer contributes nothing. The second argument of the start() is the one almost nobody puts in and that almost always matters: without a parent, if mother and daughter ask for the turn at the same time the sequencer treats them as two independent sequences. With a parent, the daughter inherits priority and context. If they ask about the order with fork/join: the default arbitration is UVM_SEQ_ARB_FIFO, that is order of arrival. It gets changed with set_arbitration() of the sequencer, and there are six modes, one of them with weights.

## Slide 377: Sequences
Starting a sequence, form 1: start()
task run_phase(uvm_phase phase); full_sequence full_seq; full_seq = full_sequence::type_id::create("full_seq"); // THE TEST raises the objection, not the sequence: the sequence knows // nothing about phases, and has to be able to run inside another sequence. phase.raise_objection(this); full_seq.start(sequencer_h); // does not return until body() finished phase.drop_objection(this); endtask : run_phase
start(sequencer) hands the sequence the sequencer it is going to run on and does not come back until body() has finished
The test raises the objection before and drops it after: the run lasts exactly as long as the stimulus lasts
It is explicit and reads top to bottom. For a test that runs a single sequence, it is what suits
And it still has the problem of the first slide: sequencer_h came out of env_h.clase_agent_h.sequencer_h
Notes: start() does three things, in this order: it saves the sequencer (it is what get_sequencer() returns afterwards), it calls pre_body() / body() / post_body(), and it comes back. The detail to underline: the objection is raised by the test, not by the sequence. The sequence knows nothing about phases. That is on purpose — the same sequence has to be able to run inside another sequence, where raising an objection would make no sense, and in fact that is what full_sequence does with its three daughters. The sequencer_h is resolved by base_test in end_of_elaboration_phase, not in build_phase: during the build_phase of the test the agent has not built its sequencer yet. It is the same reason why the connections go in connect_phase.

## Slide 378: Sequences
Form 2: default_sequence through uvm_config_db
function void build_phase(uvm_phase phase); full_sequence full_seq; // super.build_phase() of base_test, which is a class of OURS: it builds the // env. What the course never calls is uvm_component's build_phase. super.build_phase(phase); full_seq = full_sequence::type_id::create("full_seq"); full_seq.count = 200; // WITHOUT this line main_phase ends at t=0: nobody raises the objection, // and a phase without an objection lasts zero. The test PASSES with no stimulus. full_seq.set_automatic_phase_objection(1); // The instance name carries the "_phase" suffix: that is the phase the // sequencer will start it in. Notice the test no longer names the sequencer // as a handle: it names it as a PATH, and that is a config, not code. uvm_config_db#(uvm_sequence_base)::set( this, "env_h.clase_agent_h.sequencer_h.main_phase", "default_sequence", full_seq); endfunction : build_phase
The test has no run_phase: the sequencer starts the sequence on its own, when the phase begins
The instance name carries the suffix _phase: "...sequencer_h.main_phase" means “in the main_phase of that sequencer”
It can be configured per instance (as here, with uvm_config_db #(uvm_sequence_base)) or per type (uvm_config_db #(uvm_object_wrapper) + get_type()). If both are there the one with the higher precedence wins, and at equal precedence the last set()
The sequencer stopped being a handle and became a path: that is already configuration, not code
Notes: The trap, and it is one of the ones that give no warning. Without the line set_automatic_phase_objection(1), nobody raises the objection of the main_phase. And a phase without an objection finishes as soon as it starts. What was tried with Verilator 5.052: the run finishes at t=0, prints the Report Summary with 0 UVM_ERROR / 0 UVM_FATAL, and exits with code 0. That is: the test PASSES without having sent a single piece of stimulus. It is in code/u7/sequences as no_objection_test, so it can be run in class alongside the good one. It is exactly the same kind of bug as the new() that eats the override of the transactions: it does not break, it lies. And in a regression of a thousand tests, a test that passes in zero seconds is one nobody looks at. Fine detail: main_phase is the one to use, not run_phase, but not because run_phase does not work — uvm_task_phase::traverse calls start_phase_sequence() on every task phase (base/uvm_task_phase.svh:121), so "…sequencer_h.run_phase" works just as well. The reason is one of coexistence: the run_phase runs in parallel with the schedule reset → configure → main → shutdown, and hooking onto main_phase puts the sequence inside that schedule instead of alongside it.

## Slide 379: Sequences
When to use which
 | seq.start(sqr) | default_sequence
Where it is written | run_phase of the test | build_phase of the test, or the top
Objection | the test handles it | set_automatic_phase_objection(1)
It reads | top to bottom | you have to go looking for it
Several sequences in order | trivial | one per phase
Changing it without recompiling | no | yes, it is a config
Knows the inside of the env | yes, through the handle | no, only the path
Reusable third-party agent | not always possible | it is the intended mechanism
For the tests of the course: start(), because it shows
For an agent you hand over to another team: default_sequence, because it lets them change the stimulus without touching your code
Notes: In the industry both live side by side and the choice is almost always political, not technical: start() when the one writing the test is the owner of the testbench, default_sequence when the testbench belongs to somebody else. A third way worth naming without developing: the same uvm_config_db from the top module, with null as the context. There the stimulus gets chosen from the command line and the testbench does not even get recompiled. That is how the big regressions work. And the row that matters for the arc of the section is the second to last: default_sequence is what finishes closing the env that the agents encapsulated.

## Slide 380: Sequences
The `uvm_do macro and why the course does not use it
`uvm_do(command) // one line command = command_transaction::type_id::create("command"); // four start_item(command); if (!command.randomize()) `uvm_fatal("SEQ", "randomize() failed") finish_item(command);
`uvm_do does exactly those four things: create, start_item, randomize, finish_item
What it hides: the randomize() without an else, so a constraint without a solution goes by in silence
What it prevents: filling fields by hand between the two calls — that is, everything on the previous slides
What it breaks: the error message points at the expanded macro, not at your code
There is a whole family (`uvm_do_with, `uvm_create, `uvm_send) and the same argument holds for all of them
Notes: It is the same discussion as the `uvm_field_* macros of the transactions, and the same conclusion: they save typing and charge you in debug. It is worth being fair: `uvm_do_with is genuinely convenient for a one-line inline constraint, and you are going to see it in every testbench in the world. You have to know how to read it. What the course does not do is teach it first: whoever learns with the macro does not know what happens between start_item() and finish_item(), and that is the whole section. A rule of thumb for work: read them all, write the explicit ones.

## Slide 381: Sequences
The override still works, and no sequence found out
// The same add_test as the Transactions section, word for word. No sequence finds // out: random_sequence still asks the factory for a command_transaction, // and the factory hands it back an add_transaction. class add_test extends full_test; `uvm_component_utils(add_test) function new(string name, uvm_component parent); super.new(name, parent); endfunction : new function void build_phase(uvm_phase phase); command_transaction::type_id::set_type_override(add_transaction::get_type()); super.build_phase(phase); endfunction : build_phase endclass : add_test
It is the same add_test as the transactions, word for word
random_sequence still creates command_transaction::type_id::create(); the factory hands it back an add_transaction
Measured result: 1000 operations, all add_op, 0 UVM_ERROR
maxmult_sequence still sends mul_op under add_test — because it does not randomize, and the constraint only acts on randomize()
Notes: It is the best proof that the separation worked: changing the data type did not require touching the stimulus, and changing the stimulus does not require touching the data type. Two independent axes, which in the transactions were stuck together and in the agents still shared a class. And the last bullet is the review of the trap of the transactions, now in a place where it can be seen running: the factory picks the TYPE, the constraints only act on randomize().

## Slide 382: Sequences
Two sequences on the same sequencer: the arbitration
Up to here every sequencer has had one sequence at a time. In a real testbench there are several in parallel on the same driver —background traffic, a directed test, an error injector— and somebody has to hand out the turns
fork fondo_seq.start(sqr); // priority 100, the default one urgente_seq.start(sqr, null, 500); // the third argument is the priority join
The mode, in sqr.set_arbitration(...) | How it hands out
UVM_SEQ_ARB_FIFO | order of arrival, and the priority is not looked at (default)
UVM_SEQ_ARB_STRICT_FIFO | the priority rules; at equal priority, order of arrival
UVM_SEQ_ARB_WEIGHTED | at random, with the priority as the weight
UVM_SEQ_ARB_RANDOM | at random, all equal
UVM_SEQ_ARB_STRICT_RANDOM | at random, but only among the highest priority ones
UVM_SEQ_ARB_USER | user_priority_arbitration(), you write it
The default ignores the priority: putting a 500 in and not changing the mode is the mistake of this slide, and nobody gives you a warning
Notes: The question that orders the slide is “who decides which item goes into the driver?”, and until today the answer was “there is nobody to decide about”. The sequencer arbitrates per item, not per sequence: two sequences in a fork do not take turns in blocks, they interleave item by item. It is worth saying because intuition says the opposite. The mistake to leave engraved is in the last bullet and it is out of a manual: the priority gets written, it gets run, and nothing happens — because UVM_SEQ_ARB_FIFO does not look at it. Priority without set_arbitration(UVM_SEQ_ARB_STRICT_FIFO) is an expensive comment. UVM_SEQ_ARB_STRICT_FIFO is the one used 90 % of the time, and the name confuses: strict is about the priority, not about the FIFO. It first orders by priority and only within each level does it respect the order of arrival. And the one almost nobody uses but is worth naming, because it explains what UVM_SEQ_ARB_USER exists for: there are protocols where the turn depends on the state of the DUT —do not send a write if the FIFO of the DUT is full—. That is not a priority, it is a function, and that is what the user mode is for. The cousin of that idea is is_relevant(), which keeps a sequence out of the arbitration until it says itself that it is ready.

## Slide 383: Sequences
lock() and grab(): when the arbitration is not enough
There are scenarios that cannot be interleaved: a configuration sequence, an atomic burst, a read-modify-write. If another sequence slips an item in the middle, the scenario stopped being the one you wrote
task body(); grab(); // cuts ahead of everyone and closes the door ... the items of the scenario, with nobody in between ... unlock(); // ungrab() is the same method, under another name endtask
lock() queues up: it waits its turn like anybody else and only then closes the door. grab() cuts in: it goes ahead of everyone, even of the higher priority ones
Both are released with unlock(). Without the unlock(), if the sequence is still alive the sequencer stays closed forever and without a single error; if its body() finishes, UVM takes it away and shouts SEQFINERR
The rule: grab() for reset and error recovery —what cannot wait—, lock() for everything else, and the unlock() in the same body()
Notes: The difference between the two is one single word and it is worth saying it like this: lock is polite, grab is rude. Both end up with the sequencer all to yourself; what changes is whether you wait your turn or take it. When it is really needed, because abusing this is a classic: only when the scenario loses its meaning if something gets interleaved. A read-modify-write on a register is the canonical example —if another transaction goes by between the read and the write, the value you write is old—. Sending ten items in a row does not need a lock: a sequence already guarantees that. The two endings of the missing unlock() have to be told together, because one warns you and the other does not. If the sequence holding the lock finishes its body(), uvm_sequencer_base::remove_sequence_from_queues (seq/uvm_sequencer_base.svh:1258-1267) takes the lock away from it and reports a UVM_ERROR SEQFINERR — “should not finish before locks … are removed”: annoying, but with a name on it. The silent case is the other one: the sequence is still alive and blocked on something else, and there the sequencer stays closed without anybody saying a word. That is the one that sends you looking on the wrong side: the simulation does not advance and the +UVM_OBJECTION_TRACE says nothing odd, because the objection is fine — the one that is stuck is the driver, waiting for an item that is never going to arrive. The tool that shows it is +UVM_TIMEOUT and then reading who has the lock. And the detail that saves an afternoon: grab() does not interrupt the item that is in flight. It cuts in at the next arbitration, not in the middle of a handshake — which is exactly what one wants.

## Slide 384: Sequences
The testbench, complete
The final testbench: sequences, agent, sequencer, driver, monitors and the analysis layer

## Slide 385
It is the diagram drawn today in any verification project, with the names used today
Everything inside the env is built once and does not change. What changes between one test and another is the cloud of sequences at the top
Notes: The diagram shows one agent, which is the unit of reuse; in code/u7/sequences there are two, the active one and the passive one of the agents, and the bottom one is identical except that it has neither sequencer nor driver. It is worth doing the count out loud: the conventional testbench was an initial of a hundred lines that drove signals. This one has test, env, agent, sequencer, driver, two monitors, coverage and scoreboard, and every piece can be replaced without touching the others. And the three layers at the top —sequences, agent, analysis— change for different reasons: the stimulus changes per test, the structure per design, the analysis per verification plan.

## Slide 386: Sequences
Summary of the unit · the sequence and the item
The stimulus came out of the component tree: it is a uvm_object, not a uvm_component, and that is why it gets created, configured, run and thrown away
Everything happens inside body(), between start_item() and finish_item(): that is where the item gets filled, that is where the randomize() goes, and that is where pre_do and mid_do hook on
The driver writes the result inside the item before item_done(): it is the way back, and it is what makes a stimulus that reacts possible
Two ways of starting: explicit start(sequencer), or default_sequence through uvm_config_db — which besides takes the last hard-wired line out of the testbench
Notes: The first half of the summary is the mechanism: what a sequence is, where the randomize() lives, and which way the result comes back. Anyone who got lost in the unit catches up here.

## Slide 387: Sequences
Summary of the unit · how they compose
Sequences compose: one calls others, in series or with fork/join
And when there is more than one sequencer, the one that composes is a virtual sequence, which comes just as day 7 starts ↪ day 7
With two sequences on the same sequencer the one who hands out is the sequencer: priority and set_arbitration(...), and lock()/grab() for the scenario that cannot be interleaved
With this the testbench of the course is complete —it is missing one single piece, tomorrow’s— and it is the way it is written today in the industry
Notes: Close of day 6. None of the pieces we did see is magic: we built them all by hand —the observer of talking to several objects, the FIFO of put and get, the tester of transactions— before UVM handed them to us done. That is the reason the course goes in this order and does not start with the uvm_agent. And the best place to go on reading is code/.uvm/src/: by this point uvm_sequence_base.svh can be opened and understood. What is left for tomorrow is the virtual sequence, and it is left out of today on purpose: it is only understood with this unit’s testbench closed, and the morning of day 7 is where the student looks at a new DUT and has to decide which structure it deserves.

## Slide 388
Review · Day 6
1 of 10 · is_active
An agent in UVM_PASSIVE, what does its build_phase build?
☒ The monitors and the analysis ports; the driver and the sequencer, no
☐ Nothing: a passive agent is an empty shell
☐ Everything the same as an active one, but without connecting the driver to the sequencer
☐ Only the sequencer, so it can receive sequences from another agent of the same env
The monitors, always; the sequencer and the driver are left at null — watching is never optional: a passive agent goes on feeding scoreboard and coverage. What gets skipped is what drives the interface, because there somebody else is already driving it.

## Slide 389
Review · Day 6
2 of 10 · The handshake of the driver
The driver calls get_next_item(), drives the signals and forgets the item_done(). What happens?
☐ Compilation error: UVM demands the complete pair
☐ The sequencer hands over the next item just the same, with a warning
☐ The item gets discarded and the scoreboard reports a mismatch on the next comparison
☒ The sequence stays waiting in finish_item() and does not advance any more
It hangs inside finish_item(), and without saying anything — it is the classic mistake of the first week, and the symptom misleads: there is no error and no warning, time stops advancing and the objection never gets dropped. get_next_item() is a loan; item_done() is giving it back.

## Slide 390
Review · Day 6
3 of 10 · Scope of the config_db
The env instantiates two agents and does both set() with the scope "*". What does each one receive?
☐ Both fail with uvm_fatal: the string "config" is duplicated
☐ Each one receives its own, in order of creation
☒ Both receive the same one: the second set() overwrites the first
☐ The first receives its config and the second is left with cfg == null
Both receive the same thing — the uvm_config_db does not match by order nor by type: it matches by path. With "*" both entries describe the same components, so the last one wins. The scope is a path in the tree, not a label.

## Slide 391
Review · Day 6
4 of 10 · The sequencer
typedef uvm_sequencer #(command_transaction) sequencer; compiles without touching the transaction of the transactions. Why?
☐ Because it is registered in the factory with `uvm_object_utils
☐ Because uvm_sequencer accepts any uvm_object
☐ Because the driver does the $cast internally
☒ Because command_transaction extends uvm_sequence_item
Because of the base class we chose in transactions — uvm_sequencer #(T) requires that T derive from uvm_sequence_item. If that day the transaction had extended a plain uvm_transaction, this typedef would not compile today. A decision of one section enabling the next.

## Slide 392
Review · Day 6
5 of 10 · super.build_phase()
Instead of the config object, you put is_active straight into the uvm_config_db. In this course the agent starts up active all the same. Why?
☐ Because is_active is protected and the config_db cannot write it
☐ Because the config_db does not accept enumerated types, only int and string
☐ Because is_active is fixed in the constructor and build_phase arrives late
☒ Because the one who reads it is uvm_agent::build_phase, and nobody calls super
That mechanism is switched off — uvm_agent::build_phase looks for is_active in the resource pool (it is in code/.uvm/src/comps/uvm_agent.svh, it can be opened). Without super.build_phase() that line never runs, and nobody warns you. Both ways are valid; what does not work is half of each one.

## Slide 393
Review · Day 6
6 of 10 · Object, not component
What is the practical difference of a uvm_sequence being a uvm_object and not a uvm_component?
☒ That it gets created, runs and is thrown away
☐ That it cannot be registered in the factory nor overridden
☐ That it cannot have rand fields nor constraints
☐ That UVM builds it in build_phase, like any other class of the tree
It gets created, runs and is thrown away — you can start several, one after the other, on the same sequencer. A component is built once in build_phase and lives to the end. That is why the stimulus cannot be a component: it changes from test to test, and sometimes within the same test. Out of that comes as well that it can be configured between the create() and the start(), the way full_seq.count = 200 does.

## Slide 394
Review · Day 6
7 of 10 · start_item()
start_item(command) has just come back. What is it that this guarantees?
☐ That the driver has already received the item and is driving the signals
☒ That the sequencer gave the turn to this sequence
☐ That the randomize() has already been resolved with the constraints of the class
☐ That the objection of the phase is already raised by the sequencer
You have the turn —nobody else is going to beat you to the driver— and you have not handed anything over yet — and that is why the randomize() goes after: it is the last possible moment to choose the values, when you already know what state the DUT is in. That is late randomization, and it is where pre_do() and mid_do() hook on.

## Slide 395
Review · Day 6
8 of 10 · The way back
At what moment does command.result have a value that can be read?
☒ When finish_item() came back, because the driver wrote it before calling item_done()
☐ As soon as start_item() came back
☐ When the result_monitor publishes it through its analysis port
☐ Never: to receive a response you have to use the REQ/RSP pair of uvm_sequence #(REQ, RSP)
After finish_item() — there is no return channel at all: there is a shared handle and an agreement between the two parties. The REQ/RSP pair exists and is the formal mechanism, but almost nobody uses it: writing the result into the request is enough. This is what makes Fibonacci possible.

## Slide 396
Review · Day 6
9 of 10 · default_sequence
You configure a default_sequence through uvm_config_db and forget the set_automatic_phase_objection(1). What happens?
☐ uvm_fatal in build_phase: the sequence does not find the sequencer
☐ It runs just the same: when there is a default_sequence, the sequencer raises the objection on its own
☒ The main_phase finishes at t=0 and the test passes with 0 errors
☐ The simulation hangs waiting for an objection nobody drops
It passes in zero seconds without sending a single piece of stimulus, and it lies — a phase without an objection finishes as soon as it starts. It is the same kind of bug as the new() that eats the override: it does not break, it deceives. And in a regression of a thousand tests, the one that passes in zero seconds is one nobody looks at.

## Slide 397
Review · Day 6
10 of 10 · Sub-sequences
full_sequence starts its daughters with reset_seq.start(get_sequencer(), this). What is the second argument for?
☐ To pass it the sequencer, because get_sequencer() only returns the type
☒ To declare the daughter a sub-sequence of the mother
☐ So the daughter runs in a separate thread, in parallel with the mother
☐ To register the daughter in the factory under the name of the mother, so it can be overridden
It declares the mother-daughter relationship — without it, the sequencer treats the two as independent sequences and they compete for the turn. With it, the daughter inherits the mother’s turn and her priority in the arbitration. And for the parallel that is not enough: a fork / join around the start() is needed.

## Slide 398
Exercise · Day 6 · 1 of 3
The agent that only watches
cd code/ejercicios/d6-agents && bash run.sh
The env has a single agent. Add the passive one on the second VTALU
And make is_active actually count: today the agent builds driver and sequencer always
It is graded with +UVM_CONFIG_DB_TRACE: the census of the tree is written by UVM, not by you
Notes: The exercise puts together the three things of the section that can be done wrong without the compiler saying anything: is_active, the hierarchical scope of the set(), and the connect_phase of the analysis ports. The trap almost everybody is going to find is the scope: with "*" in both set(), the second overwrites the first and both agents end up with the same config — same BFM and same is_active. The checker catches it by crossing the counts — the module sends 200 operations and the sequence more than a thousand, so if both agents see similar numbers it means they are watching the same interface. And the shortcut of putting both in UVM_PASSIVE so it “passes” does not work either: the checker demands that clase_agent_h still have a driver.

## Slide 399
Exercise · Day 6 · 2 of 3
A sequence that only multiplies
cd code/ejercicios/d6-sequences && bash run.sh
Write mult_sequence and the mult_test that starts it
The driver, the agent and the env are already there: adding stimulus does not touch the structure, which is precisely what the section came to demonstrate
It is graded crosswise against what the chequeo sees on the bus, not against your count
Notes: It is the same exercise as day 2 and day 3, for the third time and with the final tool: “I want it to only multiply”. On day 2 it was solved by adding virtual, on day 3 with a factory override, and today by writing twenty lines of body() without touching a single class of the testbench. It is worth having them compare the three: that is the whole story of the course in one exercise. The trap they are going to find is the first one of the section: if the sequence does not send a rst_op as the first item, the VTALU starts up with reset_n at 0, done never rises and the driver stays in the first finish_item(). The run.sh has a +UVM_TIMEOUT set so that finishes with a message instead of hanging.

## Slide 400
Exercise · Day 6 · 3 of 3
Three planted bugs, and none of them looks like the others
cd code/ejercicios/d6-debug && bash run.sh
 | File | How it shows up
1 | driver.svh | it hangs: it dies on [PH_TIMEOUT]
2 | default_seq_test.svh | it ends at t=0 and says PASS
3 | random_sequence.svh | it lies in green: add_test passes with the wrong stimulus
The checker says which of the three is still broken. Which line it is, is the exercise
Notes: It is the only exercise of the course where there is nothing to write: there is something to find. And it is the one that looks most like your first month on the job, where nobody hands you a file with a hole — they hand you a testbench that does not work. The idea that orders the three rows, and worth saying before letting them go: the failure modes of a UVM testbench do not look like each other. The one that hangs shows up at once and costs nothing. The other two pass in green, and those are the ones that cost weeks. All three are in the debug appendix table, and reading it is allowed: the list exists precisely so that the second time it takes them five minutes. The third one deserves its own comment because it breaks the reflex the course has been training: +TOPOLOGY is the right tool for “the tree is not the one you drew”… and here it is not enough, because what got built wrong is a uvm_object and the tree only shows uvm_component. The only way to see it is to look at what went out on the bus.

## Slide 401
Yesterday we left…
Where the testbench stands
The testbench was left reusable for one agent: agents with is_active, the analysis in the env, and the stimulus outside the tree, in sequences. The last piece —coordinating two— is this morning
No line of the test names a component from inside the env: the last one went with the default_sequence through uvm_config_db
And the other half of the verification plan is missing: the rows no scoreboard can close, because they are not about the result but about the protocol
Notes: The day 7 recap works as a hinge, and it is worth saying the two things it is made of: this morning UVM gets closed —the virtual sequence is the last piece, and with it the testbench of the course is whole— and this afternoon opens what UVM does not solve, which is the other half of the plan. The third bullet is the arc planted on day 1 with the verification plan and left open on purpose: the scoreboard checks what, the assertion checks how. Today it closes.

## Slide 402
Agenda
Day 7 · ≈ 5 h 15 · unit 8 · the other half
Warm-up: five seeds and a merge, with make regresion
Virtual sequences: the last piece of the reusable testbench
Assertions (SVA)
The capstone: an APB testbench, from scratch
From the VTALU to a real bus
The debug toolbox · The 21 silent traps
Glossary, references and wrap-up
Self-assessment: fifteen things you should be able to do by now
On Monday: what to do with this once the screen goes off
And afterwards, day 8: optional, and for whoever has already handed in the capstone
By the end of the day you can:
Write a property that sees a protocol violation, and say why --assert is not optional
Coordinate two interfaces from a single virtual sequence
Hand in a whole testbench for a DUT you have not seen before
Notes: The morning has three pieces and the order matters: the seed warm-up is ten minutes without SystemVerilog and it hooks into the make regresion the capstone is going to ask for; the virtual sequences close UVM; and SVA opens the other half of the plan. The afternoon is the capstone. The third objective is the one the course is worth, and it is honest to put it as an objective of the day even if the hand-in comes later: in a company format the capstone is handed in the next day, and in a term it goes to the exam period. What gets done this afternoon is starting it with the instructor next to you, which is when it pays off the most.

## Slide 403
Exercise · Day 7 · 1 of 2
The same sequence, another seed
cd code/ejercicios/d7-semillas && bash run.sh
The only exercise of the course without SystemVerilog: what gets written is the regression, six lines of shell
Run the same test with seeds 1 to 5 and merge the five coverages with verilator_coverage --write
It is graded by checking that the merge covers more than the best of the five on its own
Notes: It is the last row of the coverage closure table, done, and it is the warm-up of day 7: ten minutes, zero SystemVerilog, and it leaves in place the make regresion this afternoon’s capstone is going to ask for. It also closes the arc day 5 opened with the directed case: one fills the bin random cannot reach, the other accumulates what random does reach, and they do not replace each other. The detail to underline is why the test sends 25 operations and not a thousand: with a thousand this does not work. It is measured and it is on the slide “another seed, and again” — u2/convencional and u7/sequences give 66 out of 76 with any seed, and the merge too. With 25 the stimulus has not saturated yet and there each seed does cover a different piece: 41 to 47 bins each, 62 for the five merged. The rule they take away, in one line: another seed accumulates while the stimulus has not saturated, and reproduces an intermittent failure. It does not fill a bin the stimulus cannot reach. And the merge command is worth naming for what it is in the industry: verilator_coverage --write is here what the ucdb merge is in Questa. A real regression is a hundred seeds overnight and one single number in the morning.

## Slide 404
Virtual sequences
The problem: two interfaces and a single start()
A virtual sequence is a sequence that does not send items of its own: it only starts other sequences, on several sequencers
It shows up when the DUT has more than one interface —a configuration bus and a data stream, for example— and the test needs to coordinate them: configure first, then send traffic
It is called “virtual” because it is not tied to a type of item nor to a sequencer
The u7/agents already left us the scenario built: two VTALU. There the second agent was passive; with both active there are two sequencers, and something to coordinate
full_sequence is already half a virtual sequence: it sends no items of its own, it only starts others. The only thing it lacks is the second sequencer
Notes: First hour of day 7, and that is on purpose. It is the last piece of the reusable testbench, and it arrives on capstone day because it is the day the student looks at a new DUT and decides which structure it deserves. The capstone has two APB slaves, each with its own interface —one driven by the testbench, the other by a module— and that is the shape of the agents section: one active and one passive, a single sequencer, and no virtual sequence. This hour is what gives the student the criterion to decide that instead of guessing it, and what leaves them the answer written down for the day the second slave is theirs too. It is worth starting from the problem and not from the syntax, because the syntax is half a screen: what is hard to understand is why a new class is needed when full_sequence already composes sequences. The answer is the one in the last bullet, and it is geometric: a normal sequence knows one sequencer, the one start() handed it. Anything that wants to talk to two interfaces needs two handles, and those handles have to come from somewhere. The example runs and it is in code/u7/sequences/virtual/: it is the testbench of this section with two lines changed in the env, and everything else by reference. It is worth saying before showing the code, because it is half of the argument: a virtual sequence does not change the structure of the testbench.

## Slide 405: Virtual sequences
The virtual sequencer: handles, not items
class virtual_sequencer extends uvm_sequencer; `uvm_component_utils(virtual_sequencer) sequencer clase_sequencer_h; sequencer modulo_sequencer_h; function new(string name, uvm_component parent); super.new(name, parent); endfunction : new endclass : virtual_sequencer
// The handles are passed HERE and not looked up by string: in connect_phase // both agents already exist, and if somebody renames a component this does // not compile instead of returning null at simulation time. virtual_sequencer_h.clase_sequencer_h = clase_agent_h.sequencer_h; virtual_sequencer_h.modulo_sequencer_h = modulo_agent_h.sequencer_h;
It has no queue, it does not arbitrate, it does not talk to any driver. It is a uvm_component that exists in order to hold the handles and to live in the tree with a name
It extends uvm_sequencer without parameterizing it: the default item is uvm_sequence_item and none ever gets sent
The handles get assigned in the connect_phase, where the agents already exist
Notes: The question that comes up on its own: and why a component, if it is only two pointers? For two reasons. One, so the sequence reaches it with p_sequencer instead of looking it up by string. Two, because it has to be in the tree so the test can start a sequence on top of it: seq.start(env_h.virtual_sequencer_h). The book resolves the handles with uvm_top.find("*.env_h.sequencer_h"). It still works —uvm_top is there for compatibility, the current form is uvm_root::get()— but looking components up by string is fragile: the day somebody renames the env_h, the find() returns null and the fatal shows up far from the change. Assigning them in the connect_phase does not compile if the name changed, which is exactly what one wants.

## Slide 406: Virtual sequences
The virtual sequence: p_sequencer and two branches
// `uvm_declare_p_sequencer declares `p_sequencer` with the type above and casts // it on its own inside m_set_p_sequencer. Without it, get_sequencer() returns a // uvm_sequencer_base and every use would need a cast by hand. class coordinada_sequence extends uvm_sequence; `uvm_object_utils(coordinada_sequence) `uvm_declare_p_sequencer(virtual_sequencer)
// --- 1. Both ALUs get reset at the same time ----------------------------- // fork/join over TWO sequencers. Each branch blocks on its own driver, and // the join waits for both: that cannot be written inside a normal // sequence, which only knows the sequencer that started it. fork reset_a.start(p_sequencer.clase_sequencer_h); reset_b.start(p_sequencer.modulo_sequencer_h); join // --- 2. Parallel traffic, different on each interface ------------------- // A does the directed overflow case while B sends at random. fork maxmult.start(p_sequencer.clase_sequencer_h); random_b.start(p_sequencer.modulo_sequencer_h); join
`uvm_declare_p_sequencer declares p_sequencer with the type of the virtual sequencer and casts it on its own. Without it, get_sequencer() returns a uvm_sequencer_base and you have to cast by hand at every use
The fork/join is over two sequencers: each branch blocks on its driver and the join waits for both
That cannot be written inside a normal sequence, which knows a single sequencer
Notes: The uvm_declare_p_sequencer is sugar, and it is worth saying so: the only thing it does is declare the variable and redefine m_set_p_sequencer() with the $cast. If the sequencer it gets started on is not of that type, the fatal fires there and not twenty lines later. The detail that gets overlooked: the two branches of the fork start different sequences on different sequencers. If they were two sequences on the same sequencer, they would compete for the arbitration and the items would come out interleaved — which is a legitimate scenario, but it is another one. And a warning from the field: a virtual sequence with a single sequencer is a normal sequence with more ceremony. The class is justified when there are two.

## Slide 407: Virtual sequences
What no sequence on its own can do
// --- 3. What no single sequence can do ---------------------------------- // The result of VTALU A is the operand of B. It is a dependency BETWEEN // interfaces: the second one cannot even start being built until the // first one answered. primera.A = 8'h0F; primera.B = 8'h07; primera.op = mul_op; primera.start(p_sequencer.clase_sequencer_h); `uvm_info("COORDINADA", $sformatf( "A returned %0d: it goes as an operand into B", primera.result), UVM_LOW) segunda.A = primera.result[7:0]; segunda.B = 8'h01; segunda.op = add_op; segunda.start(p_sequencer.modulo_sequencer_h);
The result of VTALU A goes in as an operand of B: a dependency between interfaces, and in series. The second one cannot even be assembled until the first has answered
The result comes back inside the item, which is the way back of this unit
0F × 07 = 105, and B answers 106. Run it: code/u7/sequences/virtual/run.sh
Notes: This is the slide that justifies the class. The two fork of the previous slide could be imitated with two tests running in parallel; this one cannot, because there is a piece of data that crosses from one interface to the other in the middle of the scenario. It is exactly the shape of the real case the bus appendix promises: configure over APB, read the status, and only then send traffic over AXI with what the configuration returned. The protocol changes, not the structure. And the criterion for the afternoon: in the capstone the second slave is driven by a module, so there is one sequencer and this is not needed. The virtual sequence comes in the day both interfaces belong to the testbench and one depends on the other — and then it is written just like here. And the honest close: the example runs on two VTALU because it is the DUT we have. With two different interfaces —two transactions, two drivers— the virtual sequence is written the same: the handles would be of two types of sequencer, and nothing more.

## Slide 408: Virtual sequences
And if branch B has to wait for A?
// uvm_event: a notice, from one to many. It comes from the global pool, nobody builds it uvm_event listo = uvm_event_pool::get_global("dut_configurado"); listo.trigger(); // the branch that configured gives notice listo.wait_trigger(); // the one waiting blocks here listo.wait_ptrigger(); // the same, but if it already happened, it walks on // uvm_barrier: a meeting point between N branches uvm_barrier arranque = uvm_barrier_pool::get_global("arranque"); arranque.set_threshold(2); arranque.wait_for(); // neither of the two goes on until both have arrived
The join synchronizes at the end. When branch B has to wait for A in the middle, a synchronization object is needed
uvm_event is one to many: one gives notice, those waiting move on. And trigger(data) can carry a uvm_object attached
uvm_barrier is symmetric: nobody goes on until everybody has arrived. It is the “start together” of two agents that have to begin on the same cycle
A shared bit with wait(flag) is not enough: it loses the pulse if the one waiting arrived late, and it carries no data
Notes: This is the question that shows up on its own as soon as the fork of the previous slide is drawn, and it is worth answering right there: “and if branch B cannot start until A configured the DUT?”. The distinction to make clear is one to many versus symmetric. The uvm_event has a side that gives notice and another that waits, and the roles do not change: it is for “the reset finished”, “the DUT is configured”, “the interrupt arrived”. The uvm_barrier has no sides: the N branches execute the same line and none goes on until all are there. It is for “start together” and for “everybody wait until the configuration phase ends”. The wait_ptrigger() deserves its own second, because it is the classic race: if branch A triggers before B reaches the wait_trigger(), B waits forever. The p is for persistent: it asks whether the event already happened at some point. The practical rule: if you cannot guarantee the order, wait_ptrigger(). And why not a shared bit, which is the first thing anybody tries: a bit does not keep history, does not carry attached data, and cannot be reset between phases without somebody swallowing a pulse. The two UVM objects exist precisely because that homemade version fails once every hundred runs. Its own failure mode: a barrier with the threshold set wrong does not give an error — it hangs. The symptom is a test that ends on +UVM_TIMEOUT without a single UVM_ERROR, and +UVM_OBJECTION_TRACE shows the objection up and nobody moving on.

## Slide 409
Assertions (SVA)
The hole the scoreboard left
The scoreboard of this course checks the result: A op B against what the DUT gave back. A thousand operations, a thousand comparisons, zero errors
Nobody checks the protocol. A DUT that gives back the right result but drops done one cycle early, or raises it on a no_op, passes every test of the course
The rule of the protocol is written in three places: in prose in the spec, inside the BFM, and in the head of whoever wrote it. In none of the three is it checked
An assertion is that same sentence, in executable form, running on its own the whole simulation
Notes: It is worth opening the section with the question and leaving it hanging for half a minute: which part of the testbench would notice if the DUT raised done two cycles early? The honest answer is none, and it comes as a surprise, because by this point the testbench already has a scoreboard, coverage, two agents and sequences. The reason is structural, not an oversight: the scoreboard receives transactions, which is precisely what is left after erasing the protocol. The monitor erases it in the analysis ports and it does well: that is what makes the scoreboard not know that a clk exists. The price is that the layer that sees the wires —the interface— is the only one that can check them, and until today it only moved them. This is also the answer to “why is SVA the other half of verification?”: it is not another technique for doing the same thing, it is the half this testbench does not cover.

## Slide 410: Assertions (SVA)
Immediate and concurrent: the one you know and the new one
// IMMEDIATE: it is a STATEMENT. It runs when the thread goes past it, // once, and that is all. The one from the transactions is of this family. assert (cmd.op inside {add_op, sub_op, and_op, xor_op, mul_op}) else `uvm_error("SEQ", "invalid operation"); // CONCURRENT -- the new thing. It is a DECLARATION with a clock: it gets // plugged in when the simulation starts and evaluated on every edge, forever. a_done : assert property (@(posedge clk) start |=> ##[0:4] done);
The immediate one lives inside a begin/end, it is procedural, and it only exists while the thread is standing there
The concurrent one lives in no thread: it is a declaration, like an always. It gets written once and checks every edge of the whole simulation
That is why a concurrent one can describe something that lasts several cycles, and an immediate one cannot
Notes: The distinction is hard at first and it is worth anchoring it with the RTL analogy: an immediate one is to an if what a concurrent one is to an always_ff. The first executes; the second gets instantiated. The practical consequence is the one that matters: the immediate one can only look at the present —the value of a variable at that instant—, while the concurrent one has a time axis of its own and can say “if this happens, three cycles later that has to happen”. No amount of if writes that sentence without inventing state machines by hand. And the hook back to the transactions: assert(x.randomize()) is an immediate one, and there is the silent trap of that section —assert is a simulation directive, and with asserts switched off the argument does not get executed. Here you see why: they are the same keyword for two different things.

## Slide 411: Assertions (SVA)
Anatomy of a property
a_done_llega : // <- the label: NOT optional assert property ( @(posedge clk) // <- the clock: when it gets sampled disable iff (!reset_n) // <- when NOT to check start && (op_set != no_op) // <- the antecedent |-> // <- the implication ##[1:5] done // <- the consequent ) else `uvm_error("SVA", "..."); // <- what to do if it fails
It reads like a sentence: “on every edge of clk, as long as there is no reset, if start is up with a real operation, then done arrives within five cycles”
The label comes out in the error message and in the coverage report. A property without a label is an anonymous error at three in the morning
The seven parts are always the same. The rest of the section is learning what can go in each one
Notes: It is worth writing this slide on the blackboard as a template and going back to it every time a new property comes up: the student who gets lost in SVA almost always gets lost because they do not tell the antecedent from the consequent. The label deserves a paragraph of its own. Without it, the simulator invents one (__unnamed$$_0), and that name is the one that is going to show up in the log of the nightly regression and in the assertion coverage report. It is exactly the same argument as the begin : name the course has been using since interfaces and BFM. The disable iff is looked at in detail further on, but it is worth getting ahead of why it is so high up in the template: it is the part that gets forgotten most and the one that generates the most false positives.

## Slide 412: Assertions (SVA)
|-> against |=>, mistake number one
// |-> overlapping: the consequent starts on THE SAME edge a : assert property (@(posedge clk) start |-> !done); // |=> non-overlapping: the consequent starts on the NEXT edge b : assert property (@(posedge clk) start |=> !done);
a |=> b is exactly a |-> ##1 b. There is no more mystery than that
Which one goes in? It depends on whether the response is combinational (the same edge) or registered (the next one). In the VTALU, done comes out of an always_ff: it is always the next one
Getting it wrong does not have a single symptom: start |-> done with a registered done fails on every transaction —it sees the old done—, and a property whose antecedent never occurs passes vacuously. That is why it always goes with its cover
Notes: This is the first question of every SVA interview and it is worth practising it with the DUT in hand: done_1c <= start && (op != 3'b000) is an NBA, so what gets written on edge n is only read on n+1. With |-> the property would compare start against the old done. The operational rule, which is more useful than the theory: |=> is |-> ##1, so the question is not which of the two operators goes in but how many edges later the spec promises it. An assign answers on the same edge and a <= on the next one, but that is the easy case: the star property of this very section —start && op_set != no_op |-> ##[1:5] done— uses |-> for a done that comes out of an always_ff, because the spec promises a window of one to five edges and not a single one. And the trap to name out loud, without overstating it: getting this wrong sometimes shouts —|-> against a registered signal fails on every transaction— and sometimes stays quiet, when the antecedent you wrote never occurs and the property is vacuously satisfied. That second case is the one the final report takes as good, and it is the reason why the cover property slide is not an extra: it is the only check of the check.

## Slide 413: Assertions (SVA)
Looking at the past: $rose, $fell, $stable, $past
$rose(start) // 0 -> 1 between the previous edge and this one $fell(done) // 1 -> 0 $stable(A) // the value is the same as on the previous edge $past(result, 3) // the value it had 3 edges ago
The four of them compare against the previous sample, not against the previous instant. In SVA time is counted in edges of the property’s clock, not in nanoseconds
$stable is the one that writes “it was not touched”, which is half a library of protocol rules
$past(x, n) is a free delay line: it is good for checking a fixed latency without writing a state machine
Notes: Careful with $rose on a signal that moves on the same edge the property samples: it is not going to see it go up on that edge, it is going to see it go up on the next one. That is exactly the topic of the slide that follows, and it is worth planting it here. $past with the second argument is the one that gets underestimated the most: checking “the result of now corresponds to the operands of four edges ago” is one line, and by hand it is a shift register and three bugs. It is worth saying as well where they can be used, because there is a half-truth going around: they can be called from procedural code —an always @(posedge clk) if ($rose(req)) … is legal (1800-2017 §16.9.3) and Verilator 5.052 accepts it—, because that is where they infer the clock from. What they always need is a clock: in an initial with no clock event they mean nothing. And the practical limit of this flow: $past with the explicit clock argument is not supported by Verilator (Unsupported: $past expr2 and/or clock arguments).

## Slide 414: Assertions (SVA)
The property that is worth the section
// --- The stimulus --- // The rule from slide 1 of day 1, executable at last: while start is up, the // operands and the operation are not touched. property p_operandos_estables; @(negedge clk) start |=> $stable(A) && $stable(B) && $stable(op_set); endproperty : p_operandos_estables a_operandos_estables : assert property (p_operandos_estables) else `uvm_error("SVA", $sformatf( "%m: operand changed with start up: A=%0d B=%0d op=%s", A, B, op2enum().name()))
It is the rule of The VTALU spec, day 1: while start is up, the operands are not touched. It sat written in prose for six days
Eleven lines, and they check every transaction of every test, on both agents, without anybody connecting them to anything
The scoreboard cannot write this rule: by the time the transaction reaches it, the protocol has already been erased
Notes: This is the moment to go back to the spec slide and read it word for word. The distance between “start has to stay at 1 and the operands stable until the operation finishes” and the line of SVA on screen is almost zero — and that is the whole argument for why assertions get written early and not at the end: the specification is already written, it only has to be translated. The $stable(op_set) at the end is the one that tends to be missing and it is the one that catches the ugliest bug: changing the operation halfway through a transaction is legal for the compiler, illegal for the DUT and transparent for the scoreboard. It is worth showing the @(negedge clk) and not explaining it yet: leave it as a curiosity that gets cleared up on the next slide. Somebody is going to ask first.

## Slide 415: Assertions (SVA)
⚠ Two clocks: an assertion is worth what its sampling is worth
// TWO CLOCKS, and it is not an implementation detail: the BFM drives on // negedge and the DUT registers on posedge. An assertion samples in the // preponed region of the edge it is given, so a signal written ON the negedge // is not seen on that negedge: it is seen on the next one. With everything on // posedge, two consecutive no_op -- start goes down at t=111 and back up at // t=120, between two posedges -- read as ONE transaction with the operands // changing: 145 false positives every 1000 operations. With everything on // negedge, the false positives move to the done properties. // // stimulus (start, A, B, op_set) -> negedge, where the BFM writes // response (done, result) -> posedge, where the DUT registers default disable iff (!reset_n);
With a single clock | Over 1000 operations
everything on posedge | 145 false positives on the stability of operands
everything on negedge | false positives on the done properties
stimulus on negedge, response on posedge | 0 errors ✅
The BFM drives on negedge and the DUT registers on posedge. There is no single edge that makes all four properties correct
SVA sampling is the preponed region: a signal written on the edge is not seen on that edge, it is seen on the next one
Notes: This is the most valuable lesson of the section and it is not in the tutorials, so it is worth telling it with the trace in hand: on two consecutive no_op, start goes down at t=111 and comes back up at t=120 — between two posedge. The sampling does not see it go down. The two transactions read as a single one, with the operands changing in the middle, and the property screams 145 times about something that never happened. The short way of saying it: an assertion does not check what happened, it checks what it saw. And what it sees depends on a single character in the @(). It is another silent trap, and one of the worst: it compiles, it runs, and it throws 145 errors at you that do not exist. The beginner’s reflex is to loosen the property until it shuts up —and there they are left without a check. The correct reflex is to look at which edge the one driving the stimulus writes on. The underlying industrial way out is the clocking block, which declares the sampling once for the whole interface instead of repeating it property by property. It is in day 1 —030-interfaces-bfm.md and docs/clocking-blocks.md (in Spanish)— and it is worth naming again here, because only now is the full problem it solves in view.

## Slide 416: Assertions (SVA)
The pulse the sampling does not see
Two no_op in a row: start goes down at 111 and up at 120, between two posedge

## Slide 417
Between two posedge a whole start pulse fits that the sampling never sees
All on posedge: the two no_op read as one, and out come 145 screams
Stimulus on negedge: at t=120 it is already low, the antecedent does not start
Notes: This is the figure to pause on and walk through with a finger, because the whole argument is in two edges. It is worth asking before showing it: how many transactions does an assertion sampled on posedge see? The answer read off the drawing is one, and there are two. The amber band is what the section has been saying in words: between t=111 and t=120 the signal changes twice and no posedge sampling lands in there. It is not a bug of the simulator nor of the property — it is that sampling happens in preponed, and at t=130 what it sees is start high, same as at t=110. And the second row is the cure: the same drawing with the other edge. At t=120 the negedge sampling sees start low, the antecedent is false, and the property does not even start. One character. The detail almost nobody looks at: the values of A, B and op_set change exactly at t=120, that is, inside the transaction the posedge sampling believes it is watching. That is why the 145 errors talk about operand stability and not about something else.

## Slide 418: Assertions (SVA)
Variable latency, in one line
// The variable latency from the VTALU spec section, in one line: one cycle for the // one-cycle ops, four edges for the multiplication. property p_done_llega; @(posedge clk) start && (op_set != no_op) |-> ##[1:5] done; endproperty : p_done_llega a_done_llega : assert property (p_done_llega) else `uvm_error("SVA", $sformatf("%m: start con op=%s y done no llego en 5 ciclos", op2enum().name())) // The fine print: no_op is the only operation that does not answer. property p_no_op_sin_done; @(posedge clk) start && (op_set == no_op) |=> !done; endproperty : p_no_op_sin_done a_no_op_sin_done : assert property (p_no_op_sin_done) else `uvm_error("SVA", $sformatf("%m: done subio para una no_op"))
##[1:5] done says “between one and five edges later”. The VTALU takes one on add/sub/and/xor and four on the multiplication: one property covers both
##n is an exact delay, ##[a:b] a window, ##[1:$] “at some point” — which is almost never what you want: a property without an upper bound can never fail by timeout
The antecedent excludes no_op on purpose: it is the only operation that does not answer, and putting it inside would turn the property into a generator of false positives
Notes: The upper bound is what separates a useful assertion from a decorative one. ##[1:$] done is also true for a DUT that answers next Tuesday: it compiles, it passes, and it checks nothing. The number that goes there comes out of the specification, not out of what the DUT does today — and if it is not in the specification, that is the finding of the section. The 5 in this example has a deliberate margin over the 4 real edges of the multiplication. It is worth asking the group whether they would prefer ##[1:4], and why. The honest answer is that it depends on whether the specification says “four” or says “up to five”: an assertion is a contract, and tightening it more than the contract turns it into a source of false positives when somebody changes the pipeline. The p_no_op_sin_done below is the complement and it uses |=> precisely because of what the previous slide said: done comes out of an always_ff.

## Slide 419: Assertions (SVA)
disable iff and the reset
default disable iff (!reset_n); // once, for the whole interface property p; @(posedge clk) disable iff (!reset_n) // or property by property start |=> done; endproperty
During a reset everything is wrong on purpose: done drops, start drops, the transactions halfway through get abandoned. Without disable iff, every reset is a batch of false positives
disable iff aborts the evaluations in flight, it does not make them fail. The property forgets what it was waiting for and starts from zero
The default disable iff at the top of the interface applies it to all of them: it is one line against twenty repetitions
Notes: The second classic mistake, after the |->/|=>. And the symptom misleads: the regression fills up with errors at the beginning of every test, which is precisely when one looks least, because “it is still initialising”. It is worth naming the inverse mistake, which is more dangerous: a disable iff with the condition the wrong way round —disable iff (reset_n)— switches the property off during normal operation and leaves it active only during the reset. It always passes, it never checks, and there is no way of realising it from the log. It is the second silent trap of the section and it is also headed off with cover property. The difference between aborting and failing matters when the reset arrives halfway through a long transaction. In this DUT it is one cycle; on a real bus, with transactions of dozens, it is the difference between a usable property and one that has to be switched off.

## Slide 420: Assertions (SVA)
Where they live: inside the interface
They go with the signals, in the interface, not in the class testbench. There they see clk, start, A, B and done without anybody passing them along
They do not have to be connected, nor instantiated, nor built in a build_phase. They exist because the interface exists
The top of the agents instantiates two BFM: the same properties check both VTALU, including the one driven by the legacy module nobody wrote
A passive agent gets them thrown in for free: watching an interface is now also checking it
Notes: This is the slide that connects the section with the whole architecture of the course. The interface had been the place where the testbench moves wires; from here on it is also where it watches over them, and both for the same reason: it is the only layer that sees them. The reuse argument is the one that convinces a team: the properties travel with the interface. Whoever instantiates this BFM in another project gets the protocol check already fitted, without reading a line of UVM. It is exactly what does not happen with a scoreboard, which has to be built, connected and configured. And the twist from the agents is worth saying slowly: the legacy module —the “boss’s tester”, without one line of UVM— is also being checked. Nobody asked its permission. That is the exercise of the day.

## Slide 421: Assertions (SVA)
bind: when the interface is not yours
// The checker lives outside. The RTL is not touched -- often it cannot be. module apb_checks (input bit PCLK, PSEL, PENABLE, PREADY); a_setup : assert property (@(posedge PCLK) PSEL && !PENABLE |=> PENABLE); c_setup : cover property (@(posedge PCLK) PSEL && !PENABLE); endmodule // And in the top, one line per module you want to watch over: bind apb_regs apb_checks chk (.*);
The previous slide holds when the interface is yours. Somebody else’s RTL, the bought IP and the legacy module do not get edited
bind puts an instance inside another module from the outside: the checker sees the DUT’s internal signals as if it had been written there
The .* connects by name. One bind covers every instance of that module — or bind top.dut ... for a single one
You can also bind to an interface, and Verilator supports both forms
Notes: This is the interview question that follows the previous slide, and it is worth putting it like this: “very nice to put the properties in the interface — and when the interface is not yours?”. The answer is bind, and it is the way assertions are used in the industry: one checker file per block, all bound from the top, and the RTL without a line of verification inside. The underlying reason is not aesthetic: in a synthesis flow the RTL that is handed over is the one that gets synthesized, and putting assert property inside it forces everybody to carry the verification along. With bind, whoever synthesizes does not compile the checker file and that is that. The concrete advantage, and the one that makes it worth it: the bound checker sees the DUT’s internal signals — the FSM state, the wait state counter —, which is exactly what the interface does not see. That is where assertions stop checking the protocol and start checking the implementation. And the warning: a badly written bind does not fail, connects nothing and the property is left not running. As always, the antidote is the cover property — if the cover is at zero, the bind did not arrive.

## Slide 422: Assertions (SVA)
The integration with UVM: the else that makes it count
// The default: $error, and in Verilator also $stop — it cuts off on the first failure a : assert property (p); // What you want in UVM: the failure counts and the simulation goes on a : assert property (p) else `uvm_error("SVA", $sformatf("%m: operand changed"));
Without an else, the default action of an assertion that fails is $error —and in several simulators, $stop. The simulation gets cut off and the Report Summary does not get printed
With an else that calls `uvm_error, the failure comes in through the same channel as everything else: it counts in the summary, it respects +UVM_MAX_QUIT_COUNT, and the run.sh detects it without changing a line
The %m of the message prints which instance of the interface failed: top.clase_bfm or top.modulo_bfm
Notes: It is the bridge between the two halves of the course and it has to be made explicit: the assertion is not a world apart with its own report. It is one more uvm_error, and that is why uvm_summary_ok of common.sh detects it without anything having had to be touched. The reason the default is no good is practical: a nightly regression that gets cut off at the first failure reports one failure. The same run with uvm_error reports all 154, and that is the difference between “something is wrong” and “it is wrong on every multiplication”. The %m looks like a detail and it is not: with two instances of the same interface, a message without %m does not say which of the two ALUs broke. It is the same problem get_full_name() solved in reporting, with the tool of the language instead of the one of the library.

## Slide 423: Assertions (SVA)
Every assertion goes with its cover property
// And the cover that goes with it: without this, a regression where the random // never subtracted too much leaves the assertion green having checked nothing. c_ovf : cover property (@(posedge clk) done && ovf); c_sub_sin_borrow : cover property (@(posedge clk) done && (op_set == sub_op) && !ovf); c_mult_3ciclos : cover property (@(posedge clk) $rose(start) && (op_set == mul_op) ##3 done); c_mult_4ciclos : cover property (@(posedge clk) $rose(start) && (op_set == mul_op) ##4 done); c_un_ciclo : cover property (@(posedge clk) $rose(start) && (op_set inside {add_op, sub_op, and_op, xor_op}) ##1 done);
covergroup : 86.8% (66/76) user : 80.0% ( 4/ 5)
A property whose antecedent never occurs passes. Without assertion coverage, a switched-off check looks exactly like a green check
c_mult_3ciclos stays at zero forever: the chain of the multiplier is done3 → done2 → done1 → done_mult, that is four edges, not three. The cover at 0 gives away that the mental model of the latency was wrong
In Verilator the cover property land in the same coverage.dat as the covergroups of the conventional testbench: code, functional and assertion coverage, one single report
Notes: This slide closes the circle the conventional testbench opened and it is worth saying so: the question “how do I know I measured?” had three answers in the course, and this is the third one. Functional coverage says what stimulus was generated; assertion coverage says which checks actually got evaluated. The case of c_mult_3ciclos is a pedagogical gift and it came out of writing the section, not out of inventing it: the intuitive count was three —the module is called vtalu_mult— and the hardware takes four, because the done travels through a pipeline of its own. The property with ##3 would have passed just the same if it had been a badly written assert, and the cover at zero is the only thing that gives it away. The rule to take away: for every assert property you write, write the cover property of the antecedent. It is two lines and it is the difference between a testbench that checks and one that says it checks.

## Slide 424: Assertions (SVA)
Assertion or scoreboard: the same rule, two places
 | Assertion | Scoreboard
What it checks | the protocol: who moves, and when | the transformation: A op B
Where it lives | in the interface, with the wires | in the testbench, with the transactions
When it screams | on the exact edge on which it breaks | when the result arrives
What it needs | nothing: it plugs itself in | monitor, analysis port, connect_phase
Short rule: protocol → assertion. Data → scoreboard. Writing a protocol check in the scoreboard is rebuilding the time the monitor has just taken care of erasing
And the other way round: writing the reference model of a multiplier in SVA is possible and it is a bad idea
Notes: The question that always comes up: why not check everything in a single place? The answer is that the two layers see different things and neither can see the other’s without undoing the monitor’s work. The advantage of the “it screams on the exact edge” is the one that saves the most time in real life, and it is worth putting in numbers: a scoreboard mismatch gives you a wrong result and you have to track backwards until you find the cycle where it started. An assertion gives you the cycle. On a bus with overlapping transactions, that is the difference between half an hour and two days. The other half of the rule matters too: SVA does not replace the scoreboard. Nobody wants to read a reference model written in properties, and whoever tried it tells it as an anecdote.

## Slide 425: Assertions (SVA)
The example of the section: the bug the scoreboard does not see
// +BUG=1: changes B halfway through the multiplication. The // multiplier already latched A and B on the first edge, so the // RESULT DOES NOT CHANGE: the scoreboard stays green. The only // thing that sees it is the assertion. That is the whole section. if (bug_operandos && iop == mul_op) begin @(negedge clk); @(negedge clk); B = ~iB; end do @(negedge clk); while (done == 0); oresult = result; start = 1'b0;
** Report counts by severity UVM_INFO : 2 UVM_WARNING : 0 UVM_ERROR : 154 UVM_FATAL : 0 ** Report counts by id [MAXMULT] 1 [RNTST] 1 [SVA] 154
+BUG=1 changes B halfway through the multiplication. The multiplier has already latched the operands on the first edge: the result comes out right all the same
The scoreboard compares 1000 operations and does not find a single difference: in the summary there is not one [SELF CHECKER]. It is doing its job properly — this bug is not a data bug
The assertion catches it 154 times, on the exact edge. It is the same example as reporting, turned inside out: over there the scoreboard was broken to teach reporting; here the protocol gets broken to show who sees it
Notes: Run both runs live if there is time: bash code/u8/assertions/run.sh does the clean one and the buggy one, one after the other, and the comparison of the two Report Summary is the slide. It is worth pointing out why the bug is invisible, because it is not obvious: the pipeline does a_int <= A on the first edge and mult1 <= a_int * b_int on the second. Everything that happens to A and B after the first edge gets discarded. A designer would say the DUT is robust; a verification engineer would say the testbench is lying — the stimulus violated the contract and nobody found out. And the punchline: this bug is not hypothetical. It is exactly what the legacy module of the exercise does, and it is exactly the kind of thing that survives for years in a block that “works”.

## Slide 426: Assertions (SVA)
The traps of this section
The symptom | The cause | How to head it off
The property always passes | the antecedent never occurs | one cover property per assertion
False positives on every transaction | you sample it with the edge it is written on | stimulus and response go on different edges
False positives at the start of every test | the disable iff (!reset) is missing | default disable iff once, at the top
The log says PASS and the properties did not run | --assert is missing at compile time | the cover at 0 is the one that warns you
The four share the shape of the appendix: they compile, they run, and they lie
The fourth is the cheapest to commit and the most expensive: without --assert, Verilator compiles the properties and does not evaluate them. All green, zero checking
Notes: The fourth row deserves a minute because it is specific to the flow of this course and comes as a surprise: --assert is not a “more warnings” flag, it is the switch that turns a declaration into a check. Without it, the whole block of the interface is expensive documentation. And the antidote is the same for all four, which is the elegant part: the cover property. If the cover is at zero, either the property does not run, or its antecedent does not occur. In both cases you have to go and look, and in both cases the assert on its own would have said that everything is fine. These four are added to the appendix of the silent traps, which from this section on are twenty-one.

## Slide 427: Assertions (SVA)
Summary of the unit
A concurrent assertion is a declaration with a clock: it gets written once and checks every edge of the simulation, on its own
The anatomy never changes: label : assert property (@(clock) disable iff (reset) antecedent |-> consequent) else action;
|-> is the same edge and |=> is |-> ##1. The question is not which of the two, it is how many edges later the spec promises it
The properties live in the interface, with the signals. They do not get connected, they do not get built, and they travel with it
In UVM the action is `uvm_error, so the failure counts in the Report Summary instead of killing the simulation
Every assertion goes with its cover property: it is the only check of the check
And the one that takes the section: an assertion is worth what its sampling is worth. The stimulus gets sampled where the stimulus gets written
Notes: If the group takes away a single sentence, let it be the last one. Everything else in this section is syntax and can be looked up; the sampling is judgement, and it is what separates a property that checks from one that makes noise or from one that stays quiet. The second one to take away is the one about the cover property, for a cultural reason: it is the only defence against the testbench that feels safe. A team with three hundred assertions and no assertion coverage does not know how many it is running. And it is worth closing with the location on the map: this is the half that was missing. The scoreboard checks what the DUT computes; the assertions, how you talk to it. A serious verification plan has both columns.

## Slide 428: Assertions (SVA)
What this section does differently
The UVM Primer has no SVA. It teaches the class testbench end to end and leaves the assertions out: they belong to the other half of SystemVerilog
This section exists because the question comes anyway —in the interview, and in the first real block one gets to verify
The two clocks, the table of the 145 false positives and the cover property that never gets covered did not come out of a tutorial: they came out of writing this section on the VTALU of the course and looking at why it did not add up
Everything here runs on Verilator, without licences, with the same run.sh as the other thirty-seven examples
Notes: It is worth being explicit with the group about where each thing comes from, because it is part of what the course teaches: the difference between reading about SVA and writing SVA is exactly the two-clocks slide. No tutorial has it because the tutorials use a DUT where stimulus and response share an edge. It is also the answer to “why one more UVM course?”. This one runs. And when something does not add up, the section tells why it did not add up instead of changing the example. What is left out and is worth naming so nobody discovers it late: formal assertions, expect, and the prefabricated bus properties that come with commercial VIP. With what is in this section they can be read without help.

## Slide 429
Exercise · Day 7 · 2 of 2
The legacy module violates the protocol and nobody knew
cd code/ejercicios/d7-sva && bash run.sh
The “boss’s tester” of the agents drives its VTALU by hand for the multiplication, and it goes about getting the operand of the next one ready while it waits for done. It has been in production for years
The scoreboard compares a thousand operations and does not find a single difference: the multiplier latched A and B on the first edge. The bug is not a data bug
Write the property that does see it. The two done ones are already there, as a template
The checker asks for three things: that it fire on modulo_bfm, that it not fire even once on clase_bfm, and that the scoreboard stay green
Notes: The exercise gets solved with a three-line property, but the second condition of the checker is the one that teaches: whoever samples it on posedge is going to see false positives on the interface that does respect the protocol, and the message is going to send them to look at the edge. It is the two-clocks slide, cashed in. It is worth insisting on the cover property hint for whoever gets no firings: the natural reflex is to loosen the property until it does something, and it is the wrong reflex. The cover at 0 tells “the property is badly written” apart from “the antecedent does not occur”, and they are two different problems. And the moral that goes beyond the exercise: nobody wrote the property thinking about the boss’s module. It lives in the interface, and that is why it checks everybody who uses it — including code that was written five years before this testbench existed.

## Slide 430
Review · Day 7
1 of 5 · Immediate and concurrent
What is the underlying difference between assert(x.randomize()) and assert property (@(posedge clk) …)?
☒ One is a statement; the other, a declaration with a clock
☐ None: the second is syntactic sugar for the first
☐ The first can be switched off from the command line and the second cannot
☐ The first is only valid inside a class and the second only inside a module, because of the scheduler
Statement against declaration — the immediate one runs when the thread goes past it; the concurrent one gets evaluated on its own, on every edge of its clock. It is to an if what the concurrent one is to an always_ff: one executes, the other gets instantiated. That is why only the concurrent one can describe something that lasts several cycles.

## Slide 431
Review · Day 7
2 of 5 · |-> against |=>
The done of the VTALU comes out of an always_ff. Which implication goes in start |?? done?
☐ |->, because the antecedent and the consequent belong to the same transaction
☒ |=>, because what gets written with <= is read one edge later
☐ Either of the two: the difference is a matter of style
☐ Neither: for registered signals you have to use $past() on the antecedent
|=> when the consequent comes out of a <= — because |=> is |-> ##1, and the question to ask is how many edges later the spec promises it. With |-> against a registered signal the property does not pass vacuously: it fails on every transaction, because it compares against the old done. The one that passes quietly is the one whose antecedent never occurs — which is why it always goes with its cover property.

## Slide 432
Review · Day 7
3 of 5 · The sampling edge
All the properties of the VTALU sampled on @(posedge clk) give 145 errors over 1000 operations, and the DUT is healthy. Why?
☐ The disable iff (!reset_n) is missing
☐ The posedge is too fast: the clock has to be divided
☐ Covergroups and assertions cannot share the clock without a clocking block
☒ The stimulus is written on the negedge and the sampling does not see it
An assertion is worth what its sampling is worth — the BFM writes the stimulus on the negedge, and on two consecutive no_op start goes down and comes back up between two posedge: the sampling does not see it go down. The stimulus gets sampled where the stimulus gets written. Stimulus on negedge, response of the DUT on posedge: zero errors. With a single clock there is no way.

## Slide 433
Review · Day 7
4 of 5 · The assertion that checks nothing
An assert property reports 0 failures during the whole regression. What do you know?
☒ Nothing yet: it may never have been evaluated at all
☐ That the rule it describes holds
☐ That the DUT is free of protocol bugs
☐ That the property has a badly written disable iff and stayed off the whole time
Zero failures and zero evaluations look the same — its antecedent may never have occurred, or --assert may be missing and it is not even being evaluated. That is why every assertion goes with its cover property: it is the only check of the check. In the section, c_mult_3ciclos stays at 0 and gives away that the real latency is four edges, not three.

## Slide 434
Review · Day 7
5 of 5 · Assertion or scoreboard
The DUT gives back the right result but drops done one cycle earlier than the specification says. Who catches it?
☐ The scoreboard, when it compares the result
☐ The functional coverage, because the done bin is left empty
☒ An assertion in the interface: it is a protocol bug
☐ The uvm_fatal of the command_monitor, which would stop seeing commands on the bus
Protocol → assertion. Data → scoreboard — and it is not a preference: by the time the transaction reaches the scoreboard, the protocol is no longer there. Writing the check there would be rebuilding by hand the time the monitor has just erased.

## Slide 435
Capstone · Day 7
The whole testbench, from a blank sheet
cd code/ejercicios/d7-final && cat spec.en.md
The previous exercises gave you a file with a hole in it. This one gives a DUT, a spec and nothing else
The DUT is not the VTALU: it is an APB3 slave with four registers. It has addresses, two phases per transfer, a wait state and an error response
Everything gets written: the interface with the protocol, the transaction, the driver, the monitor, the agent, the scoreboard, the covergroup, the sequences and the tests
The checker goes in stages, and each one prints its STAGE N OK. It can be finished one at a time — and that is the way to do it
Notes: It is the afternoon of day 7 and it is the exercise that justifies the whole course. It is worth saying it that bluntly: up to here the student has completed somebody else’s structure, which is exactly what they are going to be asked for on the first day of a real project — but they have never built one. The difference between “I did the course” and “I know how to do it” is this afternoon. If the group is short of time, stage 1 —the monitor— on its own already leaves something: it is the deliverable the bus appendix recommends as the first one, and it gets done in half an hour. The other use, for whoever is studying alone: it is the exercise that can be shown in an interview. A UVM testbench on an APB, written from scratch, with its coverage plan, is exactly the example they ask for.

## Slide 436: Capstone · Day 7
The DUT: four registers and the small print
Addr | Name | Access | Contents
0x00 | CTRL | RW | bit 0 = EN · bit 1 = CLR, autoclear
0x04 | SCRATCH | RW | 32 bits, and adds to ACC if EN
0x08 | ACC | RO | the accumulator
0x0C | STATUS | RO | bit 0 = EN · bit 1 = OVF, sticky
// The handshake: the write does not wait, the read inserts ONE wait state. // rd_wait re-arms as soon as PENABLE drops, that is between one transfer and // the next, with no need to count cycles. logic rd_wait; always_ff @(posedge PCLK or negedge PRESETn) begin if (!PRESETn) rd_wait <= 1'b1; else if (!PENABLE) rd_wait <= 1'b1; else if (access && !PWRITE) rd_wait <= 1'b0; end assign PREADY = !PSEL ? 1'b1 : (PWRITE ? 1'b1 : !rd_wait); assign PSLVERR = access && !mapped;
The read puts in one wait state: the driver waits for the handshake, it does not count cycles
From 0x10 upwards, PSLVERR. Writing an RO, on the other hand, is not an error
Notes: The four traps of the spec are put there on purpose and all four are about a spec badly read, not about UVM: the wait state of the read, the CLR that never gets read at 1, the read-only register that gets written without giving an error, and the accumulator that only runs with EN=1. They are the four that hang the first testbench, and they are together in a section of spec.en.md called The small print — in a real spec they are not going to be together nor in a section with that name. The assign of the PREADY is the whole slide if one has to be picked: it says that the write does not wait and the read does, and out of that comes the do @(posedge PCLK); while (!PREADY); of the driver. A driver that takes for granted that ACCESS lasts one cycle reads PRDATA one cycle too early — and it does not fail every time, which is the worst that can happen.

## Slide 437: Capstone · Day 7
The order: monitor, driver, scoreboard, coverage
1 · The monitor. The top.sv brings two slaves: one for your testbench and another driven by an ordinary module, without UVM. A passive agent on that one, and let us see the eight transfers. Without a driver
2 · The driver. The protocol inside the interface, and a directed sequence that writes and reads the four registers
3 · The scoreboard. The DUT modelled in software. The checker runs it twice: against the healthy DUT it has to keep quiet, and with +BUG=1 it has to scream
4 · The coverage. The covergroup with the nine rows of the verification plan of the spec: at least 20 points, 90 % covered. And two rows come empty
5 · The properties. The APB protocol inside apb_if.sv, with --assert. With +BUG=2 there is a bug the scoreboard cannot see
Notes: The order is not a whim of the checker: it is the field advice of the appendix From the VTALU to a real bus. The first thing that gets written is the monitor, because whoever starts with the driver writes stimulus nobody is watching and discovers a week later that their monitor does not reconstruct. That is why the top.sv comes with the second slave: so the monitor has something to watch before the driver exists. Stage 3 is the one that gets discussed the most and the one that pays off the most: a scoreboard that has never seen an error is not tested. +BUG=1 takes the CTRL.EN gate off the DUT, so the accumulator always adds. A model that has not modelled EN passes both runs and the checker catches it — which is exactly what a regression with a mutation test would do. And a hint about shape for stage 3, which saves a rewrite: the APB answers in order and one at a time, so a queue is enough and the scoreboard can compare on the spot. It is worth writing that assumption down in the plan like any other, because it is the first one that falls over when the DUT stops being a simple slave: there the pattern is the table indexed by ID of the analysis ports. And stage 4 closes the circle of day 6: the covergroup does not get invented, it gets copied from the table of the verification plan. If a bin is left at zero, there is a row of the plan that was not verified — no matter how green the scoreboard is.

## Slide 438: Capstone · Day 7
Stage 5: the bug the scoreboard cannot see
// In apb_if.sv, with the signals. The payload does not move until it ends property p_payload_estable; @(posedge PCLK) PSEL && !(PENABLE && PREADY) |=> $stable({PADDR, PWRITE, PWDATA}); endproperty a_payload_estable : assert property (p_payload_estable) else `uvm_error("SVA", $sformatf("%m: the payload moved before PREADY"))
+BUG=2 does to the usual module what d7-sva did to the legacy tester: it moves PADDR in the middle of ACCESS
The DUT answers at the new address, the monitor reconstructs eight spotless transfers, and the scoreboard has nothing to compare wrongly
Measured: 8 UVM_ERROR [SVA] and the same 8 transfers in the monitor’s log. The only one that notices is the assertion
And rows 8 and 9 of the plan come empty: back to back and unaligned address. The bins are called back_to_back and unaligned
Notes: This is the stage that makes the capstone integrate the whole day and not half of it. The argument “the scoreboard checks what, the assertion checks how” came all the way from day 1 and got demonstrated on the VTALU; here it gets demonstrated on a bus with addresses, two phases and a wait state, which is where the student is going to need it. It is worth doing the arithmetic out loud, because it is what convinces: with +BUG=2 the module changes the address after SETUP. The DUT is combinational in its decoding, so it serves the new address. The monitor samples on the handshake edge, so it reconstructs the transfer with the new address. Monitor and DUT agree — there is nothing the scoreboard can compare wrongly. The only one that knows the address moved is the one that was watching the wire on every edge. The two empty rows are the other half of the exercise and they are deliberately uncomfortable: the two things they measure are promised in the spec, each on a loose line, and none of the seven rows above measures them. Row 9 also trips up the scoreboard that decodes with the whole address — PADDR[1:0] is ignored, so 0x06 is the SCRATCH. And a trap worth telling because the course itself fell for it: the obvious reading of “PSLVERR is valid together with PREADY” is PSLVERR |-> PREADY, and it is false on this DUT. PSLVERR is combinational, so on an unmapped read it is already high during the wait state. Written as an assertion it fires on the healthy DUT. That rule is a cover, not an assert.

## Slide 439
Appendix · From the VTALU to a real bus
What does not change
The DUT of the course has a three-signal handshake. On Monday you are going to run into AXI, APB or AHB, and the honest question is how much of this is any use
The tree, all of it: test → env → agent → sequencer, driver and monitors, with the analysis hanging off the analysis ports. It is the same diagram
The agent is still one per interface. A DUT with a configuration APB and a data AXI is two agents, not one bigger agent
The configuration still comes down through one object per level, and the scope of the config_db is still a path
The sequence is still an object that gets created, runs and is thrown away
Notes: This appendix exists because everybody asks the question when they finish, and the short answer is good news: the architecture does not change at all. What changes is a single class, the driver, and one more single class, the monitor. It is worth saying it with numbers so it does not sound like consolation: of the nine classes of code/u7/sequences, in an APB agent two get rewritten —driver and monitor—, the transaction gains fields, and the rest —test, env, agent, config, scoreboard, coverage, sequences— gets copied and adapted. And the underlying reason is the one the course has been repeating since the env: what knows about the protocol is shut away in one place. Changing protocol touches that place and nothing else. If the student had to rewrite the env, it would be a sign that the agent was badly built.

## Slide 440: Appendix · From the VTALU to a real bus
What does change
The driver stops being a linear task. An operation of the VTALU is raising start and waiting for done. A bus has phases —address, data, response— and in AXI the five channels run independently: the driver goes from a send_op() to several threads with fork
The monitor has to reconstruct. Watching one edge is no longer enough: the address of one channel has to be paired with the data of another, by ID. It is the hardest class of the agent, and the one most underestimated
The transaction grows: address, burst type, length, strobes, response. And the constraints stop being decorative — in AXI a burst cannot cross a 4 KB boundary, and that is a constraint, not a comment
Virtual sequences stop being a luxury: configure over APB, then send traffic over AXI with what the configuration gave back. The shape is the one from sequences —virtual_sequencer, p_sequencer, one fork per interface—; the only thing that changes is that the two sequencers are of different types
RAL shows up. If the DUT has registers —and it does—, uvm_reg gives you the model and the register tests already done
Notes: The first bullet is the one to underline, because it is where the intuition the course built breaks. In the VTALU, “an operation” and “an exchange on the bus” are the same thing. In AXI they are not: a write transaction is three channels that can go in any order, and item_done() gets called when the response arrived, not when the address was put out. A practical consequence worth getting ahead of: the moment the driver has several transactions in flight, the get_next_item / item_done pair stops being enough and a uvm_tlm_fifo shows up inside the driver, or the pipelined mode. It is not a new topic: they are the same pieces as threads and as put and get. And about the second bullet, to bring the anxiety down: the monitor of a known protocol almost never gets written. It gets bought or downloaded.

## Slide 441: Appendix · From the VTALU to a real bus
Vertical reuse: the block env inside the system env
class soc_env extends uvm_env; apb_env apb_env_h; // the block env, without touching a line of it axi_env axi_env_h; soc_scoreboard sb_h; // the system one watches both ends, not the transfers function void build_phase(uvm_phase phase); // What changes is not the env's code: it is its CONFIGURATION apb_cfg.is_active = UVM_PASSIVE; // here the APB is driven by the SoC's CPU uvm_config_db #(apb_env_config)::set(this, "apb_env_h*", "cfg", apb_cfg); apb_env_h = apb_env::type_id::create("apb_env_h", this); endfunction endclass
The reuse of the agents section is horizontal: two instances of the same agent in the same env. This one is vertical, and it is the one that pays off in a SoC
The block env does not get edited. What changes is its config: the agent becomes passive because at system level the bus is driven by the DUT, not the testbench
That is why is_active and the config object are not ceremony: they are the hinge that makes the same code work at both levels
What does not move up is the block scoreboard: the system one compares the SoC’s input against its output, and the block one goes on measuring its bus
Notes: This is the answer to “and what are all those classes for, if my DUT has a bus?”, and the answer is that the block testbench is not written for the block: it is written so that in six months it goes whole inside the chip’s testbench. The concrete rule that decides whether an env is reusable, worth handing over as a three-point checklist: it does not create its own interface —it receives it through config_db—, it does not read from the config_db with absolute paths —no uvm_test_top.env_h.*, because at system level that path does not exist—, and it does not raise objections of its own unless it is the one in charge. An env that breaks any of the three compiles just the same and cannot be instantiated twice. The change from active to passive is the typical case and is worth explaining slowly: at block level the testbench drives the APB because there is nobody else. At SoC level that bus is driven by the real processor, so the same agent has to watch without driving — and that is already solved, it is the is_active of the agents section. Not one new line. And the fact that closes the capstone: the env they wrote in d7-final already is reusable, because its config comes from outside and so does its interface. It was not a coincidence; it was the apb_env_config.

## Slide 442: Appendix · From the VTALU to a real bus
Where to start
Look for a VIP before writing an agent. Almost nobody writes an AXI agent from scratch: the vendors sell them and there are free ones. Writing your own is a project of months and it is not the one you were asked for
The protocol before the methodology. 90 % of the bugs of a new agent are about a badly read protocol, not about UVM. The spec of the bus first
The first thing that gets written is the monitor, not the driver. If you cannot see the bus you cannot verify anything — not even somebody else’s stimulus
And there the passive agent is your first real deliverable: watch before driving
SVA in parallel. A bus has rules that get checked where they happen, not in the scoreboard, and on a bus with overlapping transactions that is the difference between half an hour and two days. You already have the tool: the assertions, with the advantage that the properties travel inside the interface of the VIP
Notes: The order of this slide is field advice and it is worth defending: whoever starts with the driver writes stimulus nobody is watching, and discovers a week later that their monitor does not reconstruct. Whoever starts with the monitor can plug it in passively on somebody else’s stimulus —or on a test from the designer— and is already contributing on the first day. If somebody asks where the learning path goes on after this course, the short list, in order: TLM2 —uvm_tlm_generic_payload and the sockets, which is how bus VIPs get connected to each other—, the RAL backdoor —docs/en/verilator.md explains why it is not here—, the uvm_sequence_library for the stress test you do not write, and reading the dv/ of a real open project: the agents of OpenTitan and the AXI VIP of pulp-platform/axi are production code and they read for free. And one that is not UVM and is worth the career: formal with SymbiYosys, which proves the same properties they wrote today without any stimulus. What is not on that list is what they have already seen: RAL is day 8, the regression with seeds is the day 7 warm-up and make regresion, and the clocking block is half a section of unit 2. And a last one, which is not technical: in a real project the testbench almost always already exists. What gets asked for on the first day is not building one, it is adding a test to it — which is exactly what they practised in the exercises of days 3 and 6.

## Slide 443
Appendix · The debug toolbox
The tools we saw, all together
Tool | What for | Where it came up
VLT_TRACE=1 + GTKWave | see the real signals | The VTALU spec
+UVM_VERBOSITY=UVM_HIGH | see the monitors’ messages | Reporting
+UVM_CONFIG_DB_TRACE | who put what in the config_db, and who read it | Agents
+TOPOLOGY → print_topology() | the tree UVM actually built | Agents
+UVM_OBJECTION_TRACE | who raised and who dropped the objection | Tests
+UVM_TIMEOUT=N,NO | a ceiling for the hang, instead of waiting | Tests
+UVM_MAX_QUIT_COUNT=N | kill the run at the Nth error | Reporting
The bottom six are plusargs: no code gets touched and nothing gets recompiled. On a testbench with UVM that is minutes of difference per attempt
Notes: This appendix exists because the tools are spread over four sections and they are all needed together, at the worst moment: when something does not work and the clock is running. It is the slide worth printing — and in fact it is already printed: docs/en/uvm-cheatsheet.pdf is this table, the class hierarchy, the nine phases and the handshake of the driver on a single A4 side. The source is res/en/machete.html, it opens with a double click and it prints with Ctrl+P. The point to say out loud is the one about the plusargs. A $display added by hand costs a recompilation of UVM —minutes— and on top of that you have to remember to take it out. Six of these seven are already fitted in the binary you compiled: they get switched on from the command line and they leave no trace. The seventh, VLT_TRACE, also needs the $dumpfile/$dumpvars block in the top — today u2/convencional and ejercicios/d1b have it. And one detail of +UVM_TIMEOUT that bites, because it does not error out: the value is an integer in time units, not an expression with a unit. UVM reads it with $sscanf(…, "%d,%s") (uvm_root.svh:916), so +UVM_TIMEOUT=5ms does not complain: it takes the 5 and cuts the simulation off at 5 ns. You write +UVM_TIMEOUT=5000000,NO, and the NO is so that a set_timeout() written in the testbench does not overwrite what you asked for on the command line. +TOPOLOGY is not from UVM: it is from the base_test of the course, which reads the plusarg and calls uvm_root::get().print_topology(). It is worth clarifying so nobody looks for it in the LRM. The same for VLT_TRACE=1, which is from the run.sh. And one that is not in the table because it is not a tool but a habit: running with SEED=N. A bug that shows up once every ten runs does not get debugged until you can repeat it at will.

## Slide 444: Appendix · The debug toolbox
Which one to use, according to the symptom
The symptom | The first suspect | What to look at it with
It ends at t=0 and says PASS | nobody raised the objection | +UVM_OBJECTION_TRACE
It never ends | an item_done() that was not called, or an objection that does not get dropped | +UVM_TIMEOUT=5000000,NO and then the trace
The scoreboard screams on every one | the monitor samples badly — the DUT hardly ever is the problem | +UVM_VERBOSITY=UVM_HIGH
The config_db does not find | the scope of the set(), not the get() | +UVM_CONFIG_DB_TRACE
The coverage gives 0 % | the new() or the sample() of the covergroup is missing | read the .dat with verilator_coverage
The tree is not the one you drew | a create() without the factory, or a late override | +TOPOLOGY
The golden rule is in the second column: suspect number one is never the DUT. It is the testbench watching it
Notes: This slide is the index of the previous one, and the order of the rows is not accidental: they are the six things that actually happen, ordered by how many times you are going to see them. The first and the second are two sides of the same coin: the objection. If nobody raises it, the sim ends at zero; if nobody drops it, it never ends. That is why the objection trace is the first tool to switch on when the simulation time makes no sense. The third is the one from the day 5 exercise, and the lesson it leaves is a matter of craft, not of syntax: a monitor that samples on the wrong edge invents failures that do not exist and makes you lose days. Before opening the RTL, look at what the monitor says it saw. The fourth has a trap inside the trap: get(null, "*", ...) does not fail —it gives back the first thing it finds— so the symptom is not “it does not find”, it is “it found somebody else’s”. The trace shows it; the get does not. And to close: the last column is all there is. If the symptom is not here, the next step is the waveforms, which is the tool that does 47 % of the work.

## Slide 445
Appendix · The 21 silent traps
It compiles, it runs, and it lies
The symptom | The cause | How to head it off | Section
The coverage gives 0 % | the new() or the sample() of the covergroup is missing | one sample() per transaction, in the subscriber | Functional coverage
The daughter runs the method of the mother | without virtual, SV resolves by the type of the variable, at compile time | virtual on every method somebody is going to extend | Polymorphism
The component reads somebody else’s config | get(null, "*", …) gives back the first thing that matches | get(this, "", …), and +UVM_CONFIG_DB_TRACE | Tests
The test passes with the wrong stimulus | the set_type_override() arrived after the create() of the env | the override first, always. +TOPOLOGY gives it away | The env
The register model goes green and the field was never tested | the access starts with WO: bit_bash skips it and do_check drops it from the mask | if the field is readable, WC or W1C. WO* only if it really is not | RAL · d8
None of these five gives a warning. None leaves the regression in red. All of them get discovered weeks later, or do not get discovered
Notes: This appendix is the one to print out and stick next to the monitor. They are spread over seven sections because each one shows up when the concept shows up, but they are needed together — and they are needed at the worst moment. The thesis of the appendix is in the subtitle, and it is worth stating it as a general rule of the craft: in verification, the expensive mistake is not the one that breaks, it is the one that lies. A compilation error costs two minutes. A testbench that passes measuring the wrong thing costs a tape-out. The fourth row is the one that hurts the most in a big team, because whoever commits it is not the one who suffers it: somebody adds an override in their test, somebody else moves the create(), and the stimulus changes without anybody touching the stimulus file. That is why the +TOPOLOGY of the agents is so cheap: it is ten seconds of reading the tree UVM actually built, against the one you drew in your head.

## Slide 446: Appendix · The 21 silent traps
The one publishing and the one listening
The symptom | The cause | How to head it off | Section
The subscriber counts 0 and the monitor prints 1000 | the connect() in the connect_phase is missing | cross-check it: against what the one that already worked says | Analysis ports · d4
The monitor never publishes, and the scoreboard screams | bfm.command_monitor_h = this is missing in the build_phase | the uvm_fatal shows up in the class that is not to blame | Analysis ports
The copy loses the fields of the mother | a do_copy() that does not call super.do_copy(rhs) | every do_copy() calls the one above first | Hierarchies
Two different transactions compare equal | super.do_compare() called on a loose line and thrown away | chained with &&, never loose | Transactions
The four have the same shape: the one that fails is not the one that got it wrong. That is why the first reflex —opening the file that screamed— is the wrong reflex
Notes: The bfm.command_monitor_h = this row is the one that teaches the pattern best, and it is worth telling it as a story: whoever forgets that line sees a uvm_fatal from the scoreboard, opens the scoreboard, and the scoreboard is perfect. The monitor —which is the one that got it wrong— says absolutely nothing, because its always in the interface never called it. The rule that comes out of there, and that holds for all four: when something screams, go up a layer. The one that reports a mismatch is the last of the chain; the bug is almost always in the one feeding it. The last two are the ones from the deep operations of the class hierarchies and it is worth pointing out the asymmetry: do_copy() without super loses data in silence; do_compare() without && compares too few of them, and gives back equal for two objects that are not. The second is worse, because it switches off the whole scoreboard without switching it off.

## Slide 447: Appendix · The 21 silent traps
Stimulus, scope and objections
The symptom | The cause | How to head it off | Section
The edge bins never get filled | dist with :=: the weight goes to each value of the range | measure the histogram once, with :/ | Constrained random
The randomize() does not run with the asserts switched off | assert(x.randomize()) — assert is a simulation directive | if (!x.randomize()) uvm_fatal(…) | Constrained random
Under the override, some transactions are of the old type | a new() where a type_id::create() belonged | what goes through the factory is what gets created with create() | Transactions
Both agents start up the same | two set() with scope "*": the second overwrites the first | the scope is the path of the one that reads, with * at the end | Agents · d6
The agent starts up active even though you set is_active in the config_db | the missing super.build_phase(): the one that reads it is uvm_agent | either a config object, or super — never half of each | Agents
The simulation never ends | an item_done() that was not called | +UVM_TIMEOUT=5000000,NO first, the trace after | Agents
It ends at t=0 and says PASS | nobody raised the objection around the sequence | +UVM_OBJECTION_TRACE | Sequences
Notes: The last two are the only ones on the list that do make noise — one hangs and the other ends oddly — and they are here because the noise they make does not point at the culprit. A hang does not say what was left waiting; a t=0 says PASS, which is worse than an error. The one about assert(randomize()) deserves being told in full because it is the one most badly copied from the internet: assert is not a function, it is a directive, and a simulator with asserts disabled does not execute the argument. Which means the randomize simply does not happen, the transaction gets sent with the previous values, and the testbench carries on as if nothing had happened. The one about the new() that eats the override is the subtlest of day 5, and it is worth showing the number: in add_test, two of the transactions of the testbench were built with new() and therefore were not add_transaction. Nobody found out, because the scoreboard compared fine all the same. And a closing recommendation for whoever is studying alone: read this appendix now and again on the day something does not work. The first time you understand none of them; the second you understand exactly the one that is happening to you.

## Slide 448: Appendix · The 21 silent traps
The four from the assertions
The symptom | The cause | How to head it off | Section
The log says PASS and the properties did not run | --assert is missing at compile time | the cover property at 0 is the only one that warns you | Assertions
The property always passes | the antecedent never occurs, or the implication is the one that is wrong | one cover property per assert property | Assertions
145 false positives and the DUT is healthy | you sample it with the edge it is written on | stimulus on negedge, response of the DUT on posedge | Assertions · d7
False positives at the start of every test | the disable iff (!reset_n) is missing | default disable iff, once, at the very top | Assertions
The four are of the same family as the ones above, with one aggravating factor: a broken assertion looks exactly the same as one that works. There is no output to look at
Notes: These four reached the appendix with the assertions and they are the only ones on the list where the check itself is what fails — the rest are bugs of the testbench; these are bugs of the one checking the testbench. That is why the antidote is always the same and that is why it is worth repeating it until you are sick of it: one cover property per assert property. The first row is the cheapest to commit in this flow and it is worth showing it live: taking --assert out of the run.sh of code/u8/assertions leaves the run with +BUG=1 at 0 UVM_ERROR. The 154 failures disappear without anything warning you. The third is the lesson of the section and the only one on the list that is not in any tutorial. The wrong reflex, when the false positives show up, is to loosen the property until it shuts up: there you are left without a check and with the feeling of having fixed it. The right reflex is to ask on which edge the one driving the stimulus writes.

## Slide 449: Appendix · The 21 silent traps
And the one the clocking block brings
The symptom | The cause | How to head it off | Section
The scoreboard fails once every twenty and the waveform looks fine | half the signals get read through cb.sig and the other half through sig | if it went into the clocking block, the whole protocol reads it through there | Interfaces and BFM
It is the only one on the list that a tool adds: without a clocking block it does not exist. Badly used it is worse than not using it
Two names for the same wire, and they differ by one cycle: code/u2/clocking/mezcla.sv prints 3 and 4 at the same instant
The variant of the same mistake: waiting for @(posedge clk) and then reading cb.sig. If you adopt the clocking block, you adopt its event too
Notes: This trap closes the appendix and it is the one that best sums up its thesis, because the symptom is the worst of all the ones on the list: intermittent. The rest fail always or never fail; this one fails when the data changes, which is one run in however many and precisely the one you are not watching. And it has a twist worth marking out loud: it is the only one on the list that shows up because you used the tool that avoids another problem. The clocking block takes the sampling race out and puts the possibility of this mixture in. It is not an argument for not using it — it is the argument for using it whole, or not using it. The rule in one line, which is Dave Rich’s: if a signal belongs to the timing contract of a clocking block, it is always accessed through that contract. The long material is in docs/clocking-blocks.md (in Spanish).

## Slide 450
Glossary · the words of the trade
What it is called on the job, and not in the textbook
What a textbook says | What gets said at work
coverage of the functionality / of the code | functional / code coverage
the test plan | verification plan, coverage plan
reaching full coverage | coverage closure
edge cases | corner cases
hand-written / random stimulus | directed / constrained-random stimulus
signal plots | waveforms
the random number seed | seed
the nightly test run | regression
the first chips back · redoing the masks | first silicon · respin
a check written for the simulator | assertion — and assert property never gets translated
reading a signal at a given moment | sampling — and the edge it happens on, the sampling edge
test bed, test harness | testbench, always — nobody says anything else
The concepts are the ones in the course; these are the exact words that the LRM, the User Guide and every answer you are going to find use. This table is the bridge
Notes: This slide exists because between knowing a concept and being able to look it up there is a vocabulary, and it is the one nobody teaches: the student has just learned the concepts and from tomorrow every search, every question on a forum and every interview goes through these exact words. The last row is not a joke. “Test bed” and “test harness” turn up in translated books and in software, and nobody says them here: in an interview or in a mail to the team you say testbench. The same with coverage, seed and tape-out. A rule of thumb for work: the technical nouns are fixed and do not get paraphrased. “Randomize the transaction”, “run the regression”, “this does not close coverage”. It sounds like jargon and it is how the trade talks.

## Slide 451: Glossary · The pieces
One line each, to have them together
Word | What it is
handle | the name of an object — it is not the object
factory | the dictionary of types: you ask for the base class and you get the derived one
override | changing the type the factory hands out, without touching whoever asks for it
transaction | a piece of data that travels through the testbench: a uvm_sequence_item
agent | everything that knows how to speak one interface, in a box
sequence / sequencer | the stimulus (object) and the arbiter that hands it out (component)
virtual sequence | the one that sends no items of its own: it coordinates several sequencers
driver | turns a transaction into signals
monitor | watches the bus and publishes transactions
scoreboard | compares what came out against what should have come out
subscriber | anybody listening to an analysis port
objection | the “I still have work to do” that keeps the phase alive
assertion | a rule of the protocol written so the simulator checks it
property | the rule itself: clock, antecedent, implication, consequent
antecedent / consequent | the “if” and the “then” of a property
cover property | counts how many times a property actually held. The check of the check
Notes: It is the slide to keep open while reading somebody else’s code, and also the one that serves as a quick review before an interview. The two rows that get confused the most are sequence and sequencer, and the way not to get them wrong is the one from day 6: the one ending in -er is the component —it is in the tree, it has phases—; the other is the object that gets created, runs and is thrown away. The same holds for driver and monitor. The rule is about the pieces of the tree and not about the suffix: the UVM policies —uvm_printer, uvm_comparer, uvm_packer, uvm_recorder— and the uvm_report_catcher end the same way and are objects. And the first row is the hardest one and the one that costs the most: handle. If the student takes a single word away from this glossary, let it be that a handle is not an object. The virtual sequence row brings two more words along that are going to show up in any production testbench: the virtual sequencer, which is a component without a queue whose only contents are the handles to the real sequencers, and p_sequencer, the handle already cast to that type that `uvm_declare_p_sequencer declares for you. A warning about sequence, which now shows up twice in the course with two meanings: the UVM one is an object that generates stimulus; the SVA one (sequence ... endsequence, the assertions) is a temporal expression —“this, and three edges later that”— and has nothing to do with it. The context always tells them apart, but the first time it confuses.

## Slide 452: Glossary · Three words that mislead
virtual — in SystemVerilog it is three unrelated things: a virtual method (resolved by the object), a virtual class (abstract, it does not get instantiated) and a virtual interface (a handle to an interface). That they share the word is an accident of the language
assert — in SystemVerilog it is two things: the immediate one, a statement that runs where the thread goes past, and the concurrent one (assert property), a declaration with a clock that gets evaluated on its own the whole simulation — the assertions. The assert(randomize()) that is seen everywhere is the first one, and it is a poor way of checking a return value: that is why the course uses `uvm_fatal
coverage — without a surname it means nothing. If somebody tells you “we are at 90 %”, the question is always code or functional?
And one of scale: a test in UVM is a class, not a file nor a run. The run is a run; the set of runs, a regression
Notes: The three are here because each one has already caused a confusion in the course, and it is worth closing by naming them. virtual was flagged in polymorphism and it comes back in the testbench in objects with the virtual interface. The question that sorts it out: virtual what? If it is a method, it looks at the object. If it is a class, it does not get instantiated. If it is an interface, it is a handle. The assert is the trap of the transactions and it is worth repeating why: it reports outside UVM, it does not go into the Report Summary, and with the assertions switched off there are simulators that do not even evaluate the expression — which means randomize() does not get called. And the last row looks obvious until the first project meeting, where “how many tests do you have” and “how many tests did you run last night” are two different questions with two very different numbers.

## Slide 453
References
IEEE 1800-2017 — SystemVerilog Language Reference Manual. The final arbiter of every discussion about syntax.
IEEE 1800.2 / Accellera UVM — the methodology, and the UVM User Guide. You have the code of uvm-core on disk: make uvm.
Verification Academy — Siemens EDA · verificationacademy.com
Salemi, Ray. The UVM Primer — Boston Light Press, 2013. The book I learned UVM with, and where several of the examples in code/ came from.
2024 Siemens EDA / Wilson Research Group Functional Verification Study. Source of the data of Trends. The charts are our own: they are generated with make figs from res/trends/data.json.
On RAL: the Using the Register Layer Classes chapter of the UVM 1.2 User’s Guide from Accellera is the long explanation, and the table of the twenty-five field accesses —RW, WOC, W1C…— is in the IEEE 1800.2, under uvm_reg_field. What the unit does not use lives in the same place: add_hdl_path for the backdoor, and IP-XACT (IEEE 1685) or SystemRDL (Accellera) to generate the model instead of writing it.
On clocking blocks, which is the liveliest discussion of the course: the threads by Dave Rich on Verification Academy (2014, 2022 and 2024), his paper The Missing Link: The Testbench to DUT Connection, and the DV Coding Style Guide from lowRISC/OpenTitan, which prescribes them as a rule. The summary, with the links and the quotes, in docs/clocking-blocks.md (in Spanish).
Notes: The list is ordered by when you are going to need it, and it is worth saying so. The LRM and the User Guide are for consulting: nobody reads them straight through, you go and look things up when there is a discussion about syntax or semantics. The Verification Academy is the place where almost everything this course left out lives, and it is free with registration. About Salemi’s book it is worth repeating what docs/en-que-se-diferencia.md (in Spanish) says: this course does not replace it and does not follow it. If somebody wants a second pass over the same concepts written by another person, it is the best one there is to start with. And the point about the charts, because it is the part a student may want to verify: the percentages of unit 1 are from the Wilson Research Group study; the charts are our own and get regenerated with make figs from a JSON that is in the repo. Nothing in unit 1 is an image downloaded from the internet.

## Slide 454
If you want to keep reading
The book I learned with The UVM Primer Ray Salemi · Boston Light Press, 2013 · ISBN 978-0974164939
This course is not that book: it has another structure, another DUT, another simulator and four units of material the book does not cover. What it does share is credited in NOTICE, and the complete list of differences is in docs/en-que-se-diferencia.md (in Spanish).
Notes: It is worth saying out loud when you get here: the book is short, it is well written and it is still the best way to start in English. If the course was of any use to somebody, let them buy it.

## Slide 455: Credits
Part of the examples in code/ derives from those of the UVM Primer, published by its author under Apache-2.0. Here they stay under Apache-2.0, with the NOTICE the licence asks for and the list of changes.
The course —slides/ and docs/— is CC BY 4.0. The tools in tools/, MIT.
The trend charts are our own, made from the published percentages of the Wilson Research Group / Siemens EDA study.
reveal.js and forkit.js by Hakim El Hattab (MIT); the typefaces Chakra Petch and IBM Plex under SIL OFL 1.1.
Notes: This slide is not legal formalism, and it is worth saying why it is here: the course asks to be cited, so it has to cite first. What was borrowed is named, with its licence and with the list of changes in the NOTICE. The practical part for whoever wants to reuse the material: CC BY 4.0 the slides and the docs, Apache-2.0 the code, MIT the tools. It can be taught, adapted, translated and charged for. The only condition is citing the source, and there is no hidden “non-commercial” clause. If somebody asks why three licences instead of one: because they are three different things. The code derives from Apache-2.0 code and has to go on being that; the slides are original work and CC BY is the one an academic setting understands; the tools are software and MIT is what anybody copying them expects.

## Slide 456
This is as far as we got
What you take with you
You know why verification exists as a discipline, and what the numbers of the industry say
You wrote a conventional testbench, you measure it with functional coverage, and you know how to read the number that comes out
You can read and write OOP in SystemVerilog: classes, inheritance, polymorphism, parameterized classes, the factory
You built a complete UVM testbench —test, env, components, monitors, driver, scoreboard, transactions, agents and sequences— piece by piece, understanding what replaces what
You wrote assertions: the other half of the plan, the one no scoreboard can close because it is not about the result but about the protocol
And you handed it in: the capstone is a DUT you had not seen before, its spec, and the whole testbench from a blank sheet — which is literally what gets asked for at work
And all of that runs on your machine, with free tools, without asking anybody for a licence
Notes: It is worth reading the list out loud and slowly, because after seven days nobody has a sense of how much they saw. It is seven bullets and each one was a whole course a week ago. The one to underline is the last, and not out of activism: all of this runs on the student’s machine. There is no part of the course left in demo mode because a licence is missing, and that means that the day they want to repeat an example, try out an idea or show something to somebody, they can. Most of the UVM material they are going to find from here on does not have that property. And the honest clarification before the slide about what was left out, so nobody leaves with the wrong idea: this is an introductory course, and what follows is a list of what was not covered. Finishing it is not knowing UVM — it is being able to read somebody else’s testbench, write one of your own, and understand the next thing you learn without it sounding like gibberish.

## Slide 457: What was left out
and where to go on
Topic | Why you are going to run into it
uvm_event, uvm_barrier | The synchronization that is left when the objection is not enough
uvm_heartbeat | The one that warns you a component stopped showing signs of life in a regression of hours
uvm_sequence_library | A bag of sequences the sequencer picks from at random: the stress test without writing it
uvm_pool, uvm_queue | The collections of UVM. An associative array is enough until it has to be shared
TLM2, phase jumps | The limit of the course, and it is explicit
UPF, gate-level, PSS | Three worlds apart: low power, the netlist with delays, and generating the tests from a model
The three places to go on: the LRM IEEE 1800-2017, the UVM User Guide from Accellera, and Verification Academy
And one almost nobody uses: the code of uvm-core. It is on your disk, in code/.uvm/src/, and by this point you can read it
And if you get stuck: Discussions, with one category per day. An example that does not run or an explanation that does not get understood are issues of the course, not problems of yours
And if you want to go on right here: day 8 is optional and starts after the self-assessment and On Monday — RAL, the reference model in C, and a second capstone
Notes: RAL came out of this table and is now unit 9, optional, with the example that runs in code/u9/ral/ and the exercise d8-ral. It is on day 8, after this slide and not in the middle, because it is only understood once the student has already written the scoreboard RAL replaces — and because as far as we know it is the first course that shows it running on a free simulator. What was left out of RAL, and is said in the unit: the backdoor and generating the model from IP-XACT. The clocking block also came out of this table: it is half a section of unit 2, with its example that runs in code/u2/clocking/. The callbacks came out for the same reason: they are half a section of unit 7, with the code/u7/callbacks/ that injects the error in the driver — the third hook unit 1 promises. And regression and seeds as well: the exercise d7-semillas is the whole cycle, and make regresion left it as a tool, with a report of the bins that were left open. SVA came out of this table and is now a whole unit, and it is one of the most original things the course has: no introductory UVM book brings it. The virtual sequences came out too: they are the first hour of today, with an example that runs in code/u7/sequences/virtual/. The last three rows are worth reading out loud with this sentence in front: an introductory course that lists what it does not cover is worth more than one that pretends to cover everything. uvm_heartbeat, the sequence library and the collections get understood in an afternoon when they are needed; UPF, gate-level and PSS are another career. The last line is not a joke. After this course the student can open uvm_component.svh and understand what build_phase does, because they saw every piece the library hands them built by hand. If there is time, open it live and look together for the m_set_full_name() that makes the config_db find things. It is the best way to close the course: the library stops being magic.

## Slide 458
Self-assessment
Fifteen things you should be able to do by now · 1 of 3
Can I…? | Where it is
1 · Explain why 47 % of a verification engineer’s time goes on debug, and what this course does about it | Trends
2 · Write a five-column verification plan for a DUT I have not seen before | The verification plan
3 · Say why 100 % code coverage does not mean the DUT is verified | Functional coverage
4 · Say what to look at first when a covergroup reports 0 % | Functional coverage
5 · Explain which race a clocking block avoids — and why they are optional anyway | Interfaces and BFM
Notes: This rubric is for the student, not for the instructor, and it is worth saying so: nobody grades it. It is good for two different moments —before the exam, as a study guide; and right now, as a diagnosis— and the instruction is the same in both: read the statement and ask yourself “can I explain it to somebody?”, not “does it ring a bell?”. The difference between the two answers is the whole course. Every row links to the section of the book, which is the version to read straight through, with the instructor note inside the text. A “no” is not bad news: it is a link. If it is being taught in class, project the three slides and ask for hands per row. The three that get the most hands are the ones to review, and that measurement is worth more than the complete review.

## Slide 459: Self-assessment
Fifteen things you should be able to do by now · 2 of 3
Can I…? | Where it is
6 · Extend a class and change its behaviour without copying it, and say what super does | Classes and extensions
7 · Change the class a testbench uses without touching the env, with a set_type_override | The factory pattern
8 · Explain why a UVM simulation ends at t=0 if nobody raises an objection | Tests
9 · Say why build_phase runs top down and connect_phase the other way round | Components and phases
10 · Make a scoreboard that fails say something more than “it failed” | Reporting
Notes: The 8 and the 9 are the two most often answered with a “it rings a bell”: they are mechanics of the library and they are understood by looking, until the day you have to debug a testbench that finishes without having sent any stimulus. If the student hesitates on either of the two, the Tests section is half an hour and closes them. The 10 is the one that pays off most in the long run and the one most underestimated. The whole course points at the 47 % of row 1: a uvm_error that prints “FAIL” leaves whoever is debugging exactly where they were, and one that prints the transaction, the prediction and the time saves them half a morning. It is the difference between a testbench that works and one you can work with.

## Slide 460: Self-assessment
Fifteen things you should be able to do by now · 3 of 3
Can I…? | Where it is
11 · Hang a new subscriber off an analysis port without touching the one publishing | A single place that watches the wire
12 · Write a constraint that reaches a corner case, and measure whether the dist does what it says | Constrained random
13 · Say what an agent with is_active = UVM_PASSIVE builds and what it does not | Agents
14 · Explain why a uvm_sequence does not show up in print_topology() | Sequences
15 · Write a property that sees a protocol violation, and say why --assert is not optional | Assertions (SVA)
All fifteen? Then what is left is the capstone: an APB slave, its spec, and the whole testbench from a blank sheet
Notes: The 14 is the question thrown out on day 1, when the UVM class diagram shows up, and it gets answered on day 6. If the student can answer it, they understood the division that explains half the library: uvm_object is the data and uvm_component is the structure. An object gets created and thrown away; a component gets built once and lasts the whole simulation. The 12 says measure, not write, and it is on purpose: the exercise d5b exists because a dist with the weights properly set can give a histogram that lies, and whoever never measured it has no way of knowing. And the last line is the only honest thing that can be said about the fifteen: they are a necessary condition, not a sufficient one. What proves somebody knows how to do this is a testbench of their own working, and that is the capstone. A student who ticks all fifteen and does not finish it did not finish the course.

## Slide 461
On Monday
What to do with this once the screen goes off
First thing: a testbench of your own, running. The capstone is the minimum. If it is already handed in, the next one is a DUT of yours — the one at work, the one from your thesis, whichever. A finished course proves nothing; a testbench does
Keep two pages and throw away the rest: the one-page cheat sheet and The 21 silent traps. They are the two you open with the simulator running
If you get stuck, ask here: Discussions has one category per day. An example that does not run is a course issue
And if something confused you, fix it. It is CC BY 4.0 and the whole repo is there: the slides, the examples, the graders and the linters. A PR that clears up a slide is worth as much as one that adds a section
Thanks for getting this far.
Notes: The last slide of the course, and it is worth it being short and in the imperative: after seven days nobody takes away one more new idea, but they do take away one instruction. The instruction is the first line, and it is worth saying it looking at the camera or at the group: the only thing that proves somebody can do this is a testbench of their own, running. Not the capstone marked, not the fifteen rows of the self-assessment in green: one of their own, on a DUT nobody prepared to be easy. The second bullet is the most practical advice on the slide and the one most thanked six months later. Of everything that got printed this week, what gets opened again is two pages: the cheat sheet —docs/en/uvm-cheatsheet.pdf, one page, A4— and the silent-traps table, which is written to be searched by symptom and not to be read. And the invitation in the fourth is not courtesy. The course improves where somebody trips: half the presenter notes exist because somebody asked the same thing twice. If it is taught in class, close by explicitly asking for the three things that were not understood — and writing them down before the group leaves.

## Slide 462
Yesterday we left…
Where the testbench stands
The capstone handed in: an APB slave, its spec, and a whole testbench written from a blank sheet — monitor, driver, scoreboard, coverage and properties
The scoreboard of that testbench predicts by hand the value of every register, and the coverage of the bus was written row by row
And that is done the same way at work… until the DUT has sixty registers. That is when both things get modelled, and that is the whole of day 8
Notes: This day is optional and it goes after the wrap-up, and both things are on purpose. The course ends on day 7: whoever got that far wrote a complete UVM testbench from a blank sheet and lacks nothing to go to work. What is here is what gets added once that has happened. The recap has a concrete job on day 8: the three pieces of today are only understood as a replacement for something the student has just written by hand. RAL replaces the register-by-register prediction, the golden model in C replaces the whole prediction, and the second capstone shows where the pattern of the first stops working. Without the capstone done, all three are abstractions without a problem.

## Slide 463
Agenda
Day 8 · ≈ 4 h · optional · what comes after the capstone
RAL, unit 9 — the register model over the same APB
The reference model in C, through DPI
The second capstone: a FIFO with backpressure
By the end of the day you can:
Read and write a register by name, without writing a single PADDR, and say what the adapter and the predictor do
Plug in a reference model written in C, and prove it with a mutation
Write a scoreboard for a DUT where a table is not enough
Notes: For whoever teaches it: in a company this is another half day, and it usually gets taught when the group has real registers in the project. In a term it is the optional unit, or the final assignment for those who want a high mark. The three objectives are deliberately concrete and not “understand RAL”: day 8 has no row in the 175b self-assessment, so the rubric the student takes away is these three verbs and the eight-question review. The third is the one that pays off the most of the three and the least expected — a FIFO has order and occupancy, and that does not fit in a four-row table.

## Slide 464
RAL
Unit 9 · optional · the register stops being an address
Every chip has configuration registers, and a small SoC has two hundred
Without RAL, the testbench writes them like this: addr = 8'h04, wdata = ..., and the scoreboard keeps a logic [31:0] for each one
The day the architect moves SCRATCH from 0x04 to 0x24, you have to look for 8'h04 all over the testbench — and 0x04 was also the value of something else
RAL —Register Abstraction Layer— is the layer that puts a name on that: model.SCRATCH.write(status, 'h1000_0000)
It is optional and it goes at the end on purpose: it is only understood once you have written the testbench it replaces
Notes: This unit is short and it is the last one, and both things are deliberate. RAL is the piece of UVM most often taught without context —there are courses that give it on day 2— and that way it is not understood: it looks like one more API. With the capstone just done, on the other hand, the student has the comparison inside their head. They wrote the scoreboard that predicts CTRL; now I show them the library that does it on its own, and also where it does not. The number of 200 registers is not rhetorical. A PHY block or a memory controller has that many, and the register spec arrives as a spreadsheet. The next step, which this course does not take, is generating the model from that spreadsheet with IP-XACT or SystemRDL: nobody writes 200 registers by hand. It is worth saying, because otherwise the student walks away with the idea that RAL is a lot of typing. And the argument about moving 0x04 to 0x24 is the one that convinces a sceptic: it is not elegance, it is that the map gets written only once.

## Slide 465: RAL
Three pieces, and only one knows what bus is underneath
Piece | What it is | How many times it gets written
uvm_reg_block | the map: registers, fields, addresses | one per DUT
uvm_reg_adapter | translates access ↔ bus transaction | one per protocol
uvm_reg_predictor | what the monitor saw, said in registers | none: it comes done
The model does not know there is an APB underneath. You change the adapter and the same model drives AHB
The adapter is the file that comes with a VIP you bought. It is twenty lines
And underneath everything, without a single change: the driver, the monitor and the agent of the capstone
Notes: The table is the slide. That the third column says one per DUT, one per protocol and none is the whole economic argument for RAL, and it is the one that holds the decision up in a project meeting. It is worth pointing at the last line with a finger: nothing the student wrote yesterday gets replaced here. code/u9/ral/ compiles the interface, the transaction, the driver, the monitor and the agent of d7-final/solucion/ exactly as they are, through +incdir. RAL is a layer, not a different testbench — and it is the reason why this unit fits into three files. If somebody asks about the backdoor: it exists, it gets declared with add_hdl_path and it reads the signal of the RTL without going through the bus. It does not go into the course because it depends on the hierarchy support of the simulator, which is precisely what changes between tools. The frontdoor —the one that uses the real bus— is the one you have to know.

## Slide 466: RAL
The model: the table of the spec, in code
// 0x00 -- CTRL. EN is an ordinary bit. CLR is not: writing a 1 clears ACC and // OVF, and the bit always reads back 0. class ctrl_reg extends uvm_reg; `uvm_object_utils(ctrl_reg) rand uvm_reg_field EN; rand uvm_reg_field CLR; function new(string name = "ctrl_reg"); super.new(name, 32, UVM_NO_COVERAGE); endfunction : new // configure(parent, size, lsb_pos, access, volatile, reset, has_reset, // is_rand, individually_accessible) virtual function void build(); EN = uvm_reg_field::type_id::create("EN"); EN.configure(this, 1, 0, "RW", 0, 'h0, 1, 1, 0); // "WC" is the name UVM has for exactly this: the write clears the field, // the mirror drops to zero, and the read returns that zero. Modelling it as // "RW" is the classic mistake, and it is what +MAL does. "WOC" also passes, // for the wrong reason: any WO* access takes the field out of bit_bash and // out of do_check, so nobody looks at it. See the RAL unit slides. CLR = uvm_reg_field::type_id::create("CLR"); CLR.configure(this, 1, 1, $test$plusargs("MAL") ? "RW" : "WC", 0, 'h0, 1, 1, 0); endfunction : build endclass : ctrl_reg
A field gets declared with configure(), and the argument that matters is the access string: "RW", "RO", "WC"…
That string is the specification. It is not documentation: it is what UVM uses to predict, and to generate the tests of The tests you did not write
Notes: configure(parent, size, lsb_pos, access, volatile, reset, has_reset, is_rand, individually_accessible) — nine positional arguments, and it is the ugliest signature in UVM. It is worth writing it on the blackboard once; afterwards the student copies it from the example, which is what everybody does. CLR is the field that justifies the slide. The spec of the capstone says “writing a 1 puts ACC and OVF at zero, and the bit always reads 0”, and that is trap 2 of the small print — the one that makes the hand-written scoreboard fail. The access that says exactly that is WC: the write clears the field, the mirror goes down to zero, and the read returns that zero. W1C works just as well here. And here is RAL’s silent trap, which is worth more than the slide. WOC —the name you write first, because it sounds like “write-only, clears”— also gives zero errors, but it gives them for the wrong reason: uvm_reg_bit_bash_seq.svh:129-133 skips every field whose access starts with WO (Accellera’s own comment says “Ignore Write-only fields because you are not supposed to read them”), and do_check takes it out of the comparison mask (uvm_reg.svh:2782-2788), so the mirror(UVM_CHECK) does not look at it either. With WOC bit 1 of CTRL is never tested and nobody prints anything; the only trace is in the timing, because the bashing of CTRL takes four transfers less. Green is not checked, and a WO* access is the cheapest way there is to switch off a check without noticing. The complete list of accesses is in the LRM 1800.2, and there are twenty-five. You do not have to know them by heart: you have to know that the list exists, and look there before inventing a set_compare or a callback. Half of the bad register models you come across are an RW field with patches on top.

## Slide 467: RAL
The adapter: the only thing that knows there is an APB
// Downstream: the model asks for a register access, this builds the bus item // the sequencer will hand to the driver. virtual function uvm_sequence_item reg2bus(const ref uvm_reg_bus_op rw); apb_transaction t = apb_transaction::type_id::create("t"); t.write = (rw.kind == UVM_WRITE); t.addr = rw.addr[7:0]; t.wdata = rw.data[31:0]; return t; endfunction : reg2bus // Upstream: a bus item comes back -- from the driver's response, or from the // monitor when prediction is explicit -- and this fills the generic operation // the model understands. // // PSLVERR is what makes status meaningful: an access to an unmapped address // comes back UVM_NOT_OK, and the write()/read() call reports it. virtual function void bus2reg(uvm_sequence_item bus_item, ref uvm_reg_bus_op rw); apb_transaction t; if (!$cast(t, bus_item)) `uvm_fatal("REG ADAPTER", "Not an apb_transaction") rw.kind = t.write ? UVM_WRITE : UVM_READ; rw.addr = t.addr; rw.data = t.write ? t.wdata : t.rdata; rw.status = t.slverr ? UVM_NOT_OK : UVM_IS_OK; endfunction : bus2reg
reg2bus goes down: the model asks for a generic access, this builds the transaction of the bus
bus2reg goes up: the transaction comes back —from the driver, or from the monitor— and this counts it in terms of an access
PSLVERR turns into UVM_NOT_OK, and there the status of every write() stops being decorative
Notes: Twenty-two lines, and that is the whole file. It is worth saying the number out loud, because RAL has a reputation for being heavy and the project-specific part is this one. The reg2bus / bus2reg symmetry is the one to fix: one function per direction, and neither of the two has state. The uvm_reg_bus_op is the common currency —kind, addr, data, status— and it is deliberately as flat as possible: any register bus fits in there. The const ref of the reg2bus comes from the signature of the base class and has to be copied exactly. It works on Verilator 5.052, which was not obvious. And a warning from the field: bus2reg is called by the predictor too, with the item the monitor saw. An adapter that reads something from the driver —or that depends on having built the transaction itself— works with automatic prediction and breaks the day you switch to explicit. That is why both functions are pure.

## Slide 468: RAL
Hooking it up: three lines and a connect_phase
function void connect_phase(uvm_phase phase); // The three lines that turn a model into a testbench component: which // sequencer carries the accesses, which adapter translates them, and where // the truth about the DUT comes from. model.default_map.set_sequencer(agent_h.sequencer_h, adapter); model.default_map.set_auto_predict(0); predictor.map = model.default_map; predictor.adapter = adapter; agent_h.ap.connect(predictor.bus_in); endfunction : connect_phase
set_sequencer is what makes model.CTRL.write() end up in the driver: the model sends items through the sequencer of the agent that already existed
set_auto_predict(0) switches off the automatic prediction, and the uvm_reg_predictor replaces it by listening to the analysis port of the monitor
And the model.build() of the build_phase: a uvm_reg_block is a uvm_object, not a component. Nobody calls it for you
Notes: The phase trap that takes everybody’s first afternoon is the last line of the slide. apb_reg_block::type_id::create("model") gives back an object with zero registers, because build() here is an ordinary method that gets called by hand —not the build_phase of a component, which UVM walks on its own—. The symptom is a uvm_fatal from uvm_reg_map that talks about a null register and does not mention the word build. The second thing to point out is where the sequencer comes from: it is agent_h.sequencer_h, the same one from the capstone, the same one the normal sequences run on. RAL does not bring a sequencer of its own. That means a register sequence and a traffic one compete for the same driver, and there the priorities show up — which is a topic for another course, but it is worth them knowing it exists.

## Slide 469: RAL
Prediction: who tells the model what happened
 | Who predicts | What happens if the DUT does something else
automatic | the write() call itself | the model does not find out: it believes what it meant to send
explicit | the uvm_reg_predictor, from the monitor | the model believes what happened on the wire
The automatic one is one line fewer and it is the one that comes up in the tutorials
The explicit one is the one to use, and for the same reason the scoreboard of the capstone looks at the monitor and not at the driver
And it is free: the monitor and its analysis port were already there
Notes: This is the judgement slide of the unit and it is worth not rushing it. With set_auto_predict(1), model.CTRL.write(status, 'h1) updates the mirror at the moment it gets called, before the bus has done anything. If the driver sends the transfer wrong, or the DUT ignores it, the model goes on being convinced that EN=1. It is exactly the design mistake the course has been attacking since day 1: the one who checks cannot believe the one who drives. With explicit prediction the path is the long and correct one: the driver drives, the monitor sees the wire, the analysis port publishes it, the predictor calls bus2reg and only then does the mirror change. It is the same drawing as the scoreboard, with a piece of the library instead of a hand-written class. The bonus, which can be seen in the example: since the predictor listens to the bus and not to the calls, the model also finds out about the transfers somebody else made — another sequence, another master, an ordinary module. Automatic prediction cannot do that even in principle.

## Slide 470: RAL
The whole path, from the call to the mirror
The RAL data path: from the write to the bus, and from the monitor to the mirror

## Slide 471
The way down is written; the way up —monitor, analysis port and bus2reg— was there
The uvm_reg_predictor is not written: instantiate it and plug in the map
The dashed one is set_auto_predict(1): the shortcut not to take
Notes: This is the figure worth having on screen while reading the connect_phase: every one of the three lines of that function is an arrow of the drawing. set_sequencer splices the way down, predictor.map/predictor.adapter give the predictor the two things it needs, and agent_h.ap.connect(...) is the arrow that goes up from the monitor. The symmetry is the point: the adapter shows up twice, once per direction, and it is the only piece of the drawing that knows there is an APB underneath. Swapping it for an AHB one moves those two boxes and no other. And the right half is not RAL: the monitor, the analysis port and the agent are the ones from the capstone, without a change. Worth saying it with a finger on the drawing, because it is what explains that the unit fits in three files. The dashed shortcut is the trap of the unit. With set_auto_predict(1) that arrow is enough for the mirror to change, so the bottom half of the drawing turns decorative: the model believes what the test meant to send, not what happened.

## Slide 472: RAL
The stimulus, without a single PADDR
// --- the frontdoor ----------------------------------------------------- // write() puts the value on the wire through the sequencer. There is no // second argument for the address: the address is in the map. model.CTRL.write(status, 'h1); // EN = 1 model.CTRL.read(status, data); `uvm_info("RAL", $sformatf("CTRL read back 0x%08h (status %s)", data, status.name()), UVM_MEDIUM) // --- prediction -------------------------------------------------------- // Nothing above updated the mirror by hand. The monitor saw the two // transfers, the predictor turned them into predictions, and the model // knows -- with set_auto_predict(0), which is the honest setting: what the // model believes comes from the BUS, not from what the test meant to send. if (model.CTRL.EN.get_mirrored_value() != 1) `uvm_error("RAL", "the predictor did not update CTRL.EN") `uvm_info("RAL", $sformatf("mirrored CTRL.EN = %0d, and nobody assigned it", model.CTRL.EN.get_mirrored_value()), UVM_MEDIUM)
There is no address in any call: the address is in the map
Nobody assigned the mirror. get_mirrored_value() gives back 1 because the monitor saw the transfer and the predictor counted it
Underneath, the driver of the capstone is doing SETUP, ACCESS and the wait state of the read, the same as yesterday
bash run.sh · code/u9/ral/
Notes: It is worth running it live and looking at the log with grep MONITOR: for every line of stimulus there is a complete APB transfer, with its address and its handshake, done by the driver they wrote. It is the demonstration that RAL does not replace the testbench, it drives it. The line most worth discussing is model.CTRL.read(status, data) against model.CTRL.mirror(status, UVM_CHECK). Both read from the DUT. The difference is that mirror compares against what the model believed before the read, and if it does not match it reports a uvm_error without anybody writing a check. It is a register scoreboard in one word. And the third form, which is not on the slide and is worth naming: set() + update(). set() changes the desired value in the model, without touching the bus, and update() writes only the registers whose desired value differs from the mirror. It is how a whole block gets configured at the start of a test, and it is where RAL stops being convenient and starts genuinely saving simulation time.

## Slide 473: RAL
The tests you did not write
rst_seq = uvm_reg_hw_reset_seq::type_id::create("rst_seq"); rst_seq.model = model; rst_seq.start(null); bash_seq = uvm_reg_bit_bash_seq::type_id::create("bash_seq"); bash_seq.model = model; bash_seq.start(null);
Both come from uvm-core. They know nothing about this DUT: they read the model and generate the stimulus and the check out of it
uvm_reg_hw_reset_seq reads everything after the reset and compares it with the reset value declared
uvm_reg_bit_bash_seq writes and reads every writable bit of every register, one by one, in both directions
Notes: This pair of sequences is the RAL argument that wins discussions, because it does not appeal to taste: they are two real tests, free, that on a block of 200 registers cover 80 % of the bugs of address decoding and of fields wired the wrong way round. There are more in the library and it is worth naming them: uvm_reg_access_seq (writes through the frontdoor and reads through the backdoor, and the other way round), uvm_reg_shared_access_seq for registers in more than one map, and uvm_mem_walk_seq for memories. The ones that need a backdoor stay out of the course for what was said before. The implementation detail worth telling, because it explains why the model has to be right: bit_bash does not skip the read-only fields — it writes the bit and demands that they read back as they were —, and it does the same with the reserved bits, which it treats as RO (uvm_reg_bit_bash_seq.svh:137-139, 149-152). What it really skips is the WO* family, NOACCESS and the fields with set_compare(UVM_NO_CHECK); individually_accessible it does not even look at. And it uses the access string to know what to expect back. Which means the quality of the test they give you is exactly the quality of the model you wrote.

## Slide 474: RAL
And that is why the model is the spec
CTRL.CLR as "WC" 0 UVM_ERROR, and bit_bash did write bit 1 CTRL.CLR as "RW" 2 UVM_ERROR, from uvm_reg_bit_bash_seq > Writing a 1 in bit #1 of register "model.CTRL" ... yielded 'h0000000000000000 instead of 'h0000000000000002
One word changed in a string, and a sequence nobody wrote catches it with the number of the bit
It is trap 2 of the small print of the capstone —CLR never reads as 1— and there a whole scoreboard was needed to see it
The register model is the only document of a project that is the spec and the code at the same time
bash run.sh runs both versions and compares them
Notes: This is the slide that justifies the unit, and the run.sh of the example produces it on its own: it runs builtin_test with the model right and with +MAL, which declares CLR as RW, and shows the two numbers side by side. The punchline to say out loud: in the capstone, that same trap cost writing a scoreboard, modelling the autoclear by hand and discovering the bug with a message of your own. Here it costs picking one word well, and the error message is written by Accellera, with the number of the bit inside. The honest downside, which has to be said so it does not sound like a brochure: if you get it wrong the other way round —you declare RW a field the DUT implemented as RW when the spec said something else— the model and the DUT agree on the mistake and no sequence says anything. The register model verifies the DUT against the spec written in the model, not against the real spec. That is why the review of the model against the document is still human work, and that is why stage 1 of the exercise prints the map so it can be compared by hand.

## Slide 475: RAL
What RAL does not do, and it has to be said
// The honest line of the whole unit. ACC and STATUS have an address, but // they are not registers: their value is produced by writes to OTHER // addresses. A register model predicts "what I wrote is what I will read", // and for these two that sentence is false, so mirror(UVM_CHECK) is turned // off on them. Reads still update the mirror -- a read is a prediction -- // and the accumulator itself stays where it was in the capstone: in the // scoreboard, which is the thing that does know how to add. ACC.VALUE.set_compare(UVM_NO_CHECK); STATUS.EN.set_compare(UVM_NO_CHECK); STATUS.OVF.set_compare(UVM_NO_CHECK);
ACC and STATUS have an address, but they are not registers: their value gets produced by a write to another address
A model predicts “what I wrote is what I am going to read”, and for these two that sentence is false. set_compare(UVM_NO_CHECK) says so in the model
The accumulator goes on being checked where it already was: in the scoreboard, which is the one that knows how to add
The read updates the mirror all the same — a read is a prediction
Notes: If they take a single idea away from this unit, let it be this one: an address is not a register. RAL models addressable storage, and it does it very well. It does not model behaviour. The accumulator of the capstone —which adds only with EN=1, which overflows, which gets cleared with CLR— is behaviour, and that lives in the scoreboard, as it lived yesterday. The failure mode of not saying it is the worst of all and it is an everyday one: the team puts RAL in, switches on mirror(UVM_CHECK) over the whole map, and the regression fills up with errors on the status registers. Since they are false positives, somebody switches the check off entirely — and from then on the model verifies nothing and nobody finds out. The difference between switching off three named fields and switching off the global check is the whole difference. The two UVM_WARNING the example prints —GET_MIRRORED_VAL/VOL— are the library saying the same thing on its own account: the mirror of a volatile field is not evidence. They are in the output on purpose.

## Slide 476: RAL
Summary of the unit
The model is the map of the spec in code, and the access string of each field is the part that verifies
The adapter is the only thing that knows about the bus: twenty lines, once per protocol
The prediction goes through the monitor, not through the call — the same rule as the scoreboard
It gives you hw_reset_seq and bit_bash_seq for free, and it charges you knowing what is not a register
And all of this runs on Verilator 5.052, which until today nobody had shown
Notes: The close of the unit and of the technical course. The last line is not marketing: when writing this unit it was first tested whether uvm_reg_adapter and the frontdoor worked on Verilator, before writing a single slide, and the result is measured in docs/en/verilator.md. Everything the unit uses works: the model, the adapter, the uvm_reg_predictor, mirror(UVM_CHECK) and the two sequences of the library. For whoever goes on alone, the order of what is missing: uvm_reg_access_seq with a backdoor, generating the model from IP-XACT or SystemRDL —which is how it is really done—, and uvm_mem for memories. All three are extensions of what they saw here, not new topics. And the bridge to the exercise: the first thing they are going to be asked for in a project with registers is exactly this, with the spreadsheet of the spec on the left-hand side of the screen.

## Slide 477
Exercise · Day 8 · 1 of 2
Modelling the register map
cd code/ejercicios/d8-ral && cat README.md
It is literally the first thing you get asked for in a project with registers: they give you the table of the spec and you give back the model
The DUT and the testbench are the ones from the capstone. The adapter, the predictor and the tests come from the unit. The only thing you write is apb_reg_block.svh
Four registers, six fields, forty lines
The checker goes in stages: the map —printed and compared with the table, without simulating anything—, the accesses —the two sequences of the library— and what the model cannot predict
Notes: It is the shortest exercise of the fifteen and the one most like a real task from the first weeks of a project. Forty lines, and half of them are copying and pasting the pattern of CTRL. The stage that teaches is stage 1, and for a reason of method: the model gets printed —+UVM_TESTNAME=mapa_test— and gets compared line by line against the register table of the exercise README, before simulating anything. It is what has to be done with a real register model, where the typical mistake is not about UVM but an offset copied wrong from a 200-row spreadsheet. Stage 2 is where CLR falls: whoever declared it RW passes stage 1 without a problem and finds out here, with the number of the bit, thanks to a test they did not write. It is worth letting them fall there — it is the moment when the RAL argument stops being an opinion. And stage 3 is the one that separates: it asks you to switch off a check, which is the opposite of what the course has been asking for the last seven days. The justification has to come from them: STATUS.EN changed because of a write to another address, the model cannot know it, and a false positive that gets let through ends up with somebody switching the whole check off.

## Slide 478
The reference model in C
The scoreboard that rewrites the spec
The scoreboard of the course predicts in SystemVerilog: a case with the arithmetic of the VTALU. For five eight-bit operations it is perfect
For a DSP, a codec or a crypto engine, that arithmetic already exists, and in C: the algorithm team wrote it, and it is against that model that the spec was signed off
Rewriting it in SystemVerilog is maintaining two models and spending the project debugging the difference between them. That is not verifying: it is having two specs
The way out is not to rewrite it. Verilator compiles to C++, so the model gets linked inside the simulation: no socket, no separate process, no IPC
Notes: This is the technique that separates a course testbench from a production one, and the argument is not about convenience: it is about authority. In a project with serious arithmetic, the spec is not a PDF — it is a program in C that somebody ran against a thousand vectors before the RTL existed. A scoreboard that reimplements that program in SystemVerilog does not verify the DUT against the spec: it verifies the DUT against the reading the verification engineer made of the spec, which is another thing. The question worth throwing at the group before showing the code: “if the C model and the scoreboard differ, who is right?”. The uncomfortable answer is that you do not know, and finding out costs days. With DPI the question does not exist because there is only one model. And the reason why this section is so cheap in this course: DPI is part of the LRM and the commercial simulators ship it as a base feature —what leaves it out are the free student editions—; what costs you in a commercial flow is the toolchain: -sv_lib, compiling the .c separately, and remembering the library on every run. Here the simulator compiles to C++ by design, so the bridge is one more file on the command line and there is nothing to configure.

## Slide 479: The reference model in C
import "DPI-C": one declaration on each side
// The reference model lives in vtalu_golden.c and is called from here. This // is all that is needed on the SystemVerilog side: one declaration per // function, with the LRM types that cross the boundary. // // input int -> int output int -> int * // function -> returns task -> may consume time (not here) // // The name after "DPI-C" is the symbol the linker looks for, so it has to // match the one in the .c letter by letter. import "DPI-C" function int vtalu_golden(input int op, input int a, input int b, output int ovf); import "DPI-C" function void vtalu_golden_bug(input int on);
/* op, a and b arrive as SystemVerilog `int` (32-bit signed). The result goes * back as the return value and the borrow through a pointer, which is how an * `output int` argument crosses the boundary. */ int vtalu_golden(int op, int a, int b, int *ovf) { int r; a &= 0xff; b &= 0xff; *ovf = 0; switch (op) { case ADD_OP: r = a + b; break; /* 8-bit operands into a 16-bit result: a - b wraps, and the borrow is * the second half of the answer the scoreboard has to check. */ case SUB_OP: r = a - b; *ovf = (a < b); break; case AND_OP: r = a & b; break; case XOR_OP: r = a ^ b; break; case MUL_OP: r = mutar ? (a * b) & 0xff : a * b; break; default: r = 0; break; /* no_op and rst_op do not answer */ } return r & 0xffff; }
The name after "DPI-C" is the symbol the linker looks for: it has to match letter by letter with the one in the .c
An input int travels as an int; an output int arrives as an int *. A function cannot consume time; a DPI task can, but only declared context and calling back into an export "DPI-C" task
The .c goes on the verilator line as one more source. There is no DPI flag
Notes: It is worth reading the two declarations side by side, because the symmetry is the whole mechanism: the one above is the promise and the one below is who keeps it, and the compiler does not cross-check them — the one who joins them is the linker, at the end. Out of that comes the number one failure mode of DPI, which is worth naming before it shows up: an undefined reference to a function that is written, right there, in plain sight. Almost always it is one of two things — the name does not match, or the file got compiled as C++ and the symbol came out with a mangled name. That last one is literally what happens here: Verilator hands the user’s sources to the C++ compiler, so the .c needs the extern "C" that is in the file. Without that guard, the example does not link and the error does not say why. The type table of the LRM is longer —there is svBitVecVal for wide vectors, svOpenArrayHandle for arrays— and it is not needed here. The rule of thumb: if the data fits in an int, the signature writes itself; if not, you look up annex H of the 1800 and copy it.

## Slide 480: The reference model in C
The scoreboard: the prediction gets asked for, not written
// The ONLY difference with the sequences scoreboard, and it is the whole // section: there is no case with the arithmetic of the spec here. The // prediction is asked of the C reference model, the one that signed it. // // What does not change: the monitor, the analysis port, the FIFO, the // do_compare and the uvm_error. The golden model replaces SIX LINES -- the // ones that predict -- and no other piece of the testbench finds out. function result_transaction predict_result(command_transaction cmd); result_transaction predicted; int ovf; predicted = result_transaction::type_id::create("predicted"); predicted.result = vtalu_golden(int'(cmd.op), int'(cmd.A), int'(cmd.B), ovf); predicted.ovf = (ovf != 0); return predicted; endfunction : predict_result
It is the only difference from the scoreboard of the sequences. The monitor, the analysis port, the FIFO, the do_compare and the uvm_error do not change
The golden model replaces the six lines of predicting, and no other piece of the testbench finds out there is C on the other side
And the traffic goes both ways: the result comes back from C, and vtalu_golden_bug(1) goes from SystemVerilog to change the state of the model
Notes: The count is worth doing out loud because it is the design argument of the whole unit: one six-line function changed and nothing else did. That happens because the scoreboard was already well divided up —predicting and comparing are two jobs, and they were in two methods—, and it is the late reward for having separated predict_result from write three days ago. The int'(...) line is the one to point at: the UVM types do not cross the border. On the other side there is no command_transaction, there are three integers. When the data is an object —an image, a packet, a matrix— what gets passed is a pointer or an open array, and the one who decides the format is the C model, not the testbench. And the vtalu_golden_bug is not an ornament: a scoreboard that has never seen an error is not tested. run.sh runs the same test against a mutated model —the multiplication truncated to eight bits— and demands that the scoreboard scream. If it does not scream, the testbench is comparing against itself and nobody was going to find out. It is the same mutation test the checker of the capstone does with +BUG=1, from the other side of the wire.

## Slide 481: The reference model in C
What you gain, what you pay
You gain | You pay
One single model, the one that signed off the spec | the opcodes get synchronized by hand: one enum on each side
The model gets tested with the tools of C | an undefined reference does not say which of the two declarations is wrong
Arithmetic that in SystemVerilog is painful —floating point, matrices, crypto— | the C model runs in zero time: it cannot wait for an edge
Performance: it is a function call, not an IPC | a segfault in the model takes the whole simulation down with it
The rule for deciding: if the prediction already exists in C, DPI. If you write it yourself from scratch and it is five lines, a case in SystemVerilog and that is it
It runs: make u8/dpi — two tests against the healthy model, and one against the mutated one
Notes: The table is what has to be left written down, and the row that gives the most discussion is the first one on the right: the duplicated enum. It is real and it has no elegant solution —the LRM does not share types between the two sides—, and it is the first thing to look at when all the comparisons fail at once. If one in every six fails, it is the DUT; if all of them fail, it is the mapping. The third row on the right is the one that surprises and is worth getting ahead of: a DPI function runs in zero time, so the C model cannot synchronize with the clock. That is what import "DPI-C" task is for — with one clarification almost every tutorial skips: C cannot block by itself. A DPI task consumes time only if it is declared context and the C calls back into an export "DPI-C" task of SystemVerilog, which is the one that waits for the edge. And there it is no longer a golden model, it is a bus model, which is another topic. The rule of the second-to-last bullet is the one to take away, because the risk of this section is that somebody comes out wanting to do everything through DPI. The VTALU does not justify DPI: five eight-bit operations get written in a case and read better. The example exists so the technique has been seen when the DUT that does justify it comes along, and that DUT arrives sooner than you think.

## Slide 482
Review · Day 8
1 of 8 · The access string
CLR clears itself when you write a 1 to it. You declare it "WOC", and bit_bash and mirror(UVM_CHECK) give zero errors. What happened?
☐ Nothing: WOC is the access that describes a field that clears on a write
☐ WOC is not in the LRM, so UVM treats it as a plain RW
☒ Both skip WO* accesses: that bit never got tested
☐ The predictor leaves the mirror at x, and a comparison against x always passes
Green is not checked — uvm_reg_bit_bash_seq.svh:129-133 skips every field whose access starts with WO (“you are not supposed to read them”), and do_check takes it out of the comparison mask (uvm_reg.svh:2782-2788). The only trace is in the timing: bashing CTRL takes four transfers less. The right access is WC (or W1C), and with it the bit does get bashed. A WO* access is the cheapest way there is of switching a check off without noticing.

## Slide 483
Review · Day 8
2 of 8 · Automatic or explicit prediction
What changes between set_auto_predict(1) and hooking a uvm_reg_predictor to the monitor?
☒ With auto-predict the model believes what it meant to send, not what happened
☐ Nothing: the predictor is the internal implementation of auto-predict
☐ The predictor is faster: it does not build the bus transaction
☐ Auto-predict only works frontdoor, and the predictor works backdoor too
The one who checks cannot believe the one who drives — with set_auto_predict(1), model.CTRL.write() updates the mirror at the moment of the call, before the bus has done anything: if the driver sends the transfer wrong, the model stays convinced. With the predictor, the mirror only changes once the monitor has seen the wire. It is the same drawing as the capstone scoreboard, with a library piece instead of a hand-written class. And it is free: the monitor and its analysis port were already there.

## Slide 484
Review · Day 8
3 of 8 · volatile
STATUS changes on its own, without anybody writing it. What are you saying when you declare it volatile in configure()?
☒ That the mirror is not evidence: the value can change without going through the bus
☐ That UVM is going to re-read it from the DUT before every comparison, to be safe
☐ That the field drops out of the map and stops having an address
☐ That it has to be read backdoor, because the frontdoor does not get there in time
The mirror stops being evidence — a model predicts “what I wrote is what I am going to read”, and for a volatile field that sentence is false. The two UVM_WARNING GET_MIRRORED_VAL/VOL of the example are the library saying exactly that, and they are in the output on purpose. What does have to be checked gets checked where it is known: in the scoreboard, and in the model goes set_compare(UVM_NO_CHECK) on that field so that RAL does not invent an error.

## Slide 485
Review · Day 8
4 of 8 · mirror() against read()
model.CTRL.read(status, data) and model.CTRL.mirror(status, UVM_CHECK). How do they differ?
☐ read goes over the bus and mirror stays in the mirror, with no transfer at all
☐ mirror writes the mirror into the DUT, to leave the two of them equal
☐ read updates the mirror and mirror does not touch it, so as not to hide an error
☒ Both read from the DUT; mirror also compares against what the model believed
mirror is a register scoreboard in one word — both read from the DUT; the difference is that mirror compares against what the model believed before the read, and if it does not match it reports a uvm_error without anybody writing a check. And a read is a prediction: both update the mirror afterwards.

## Slide 486
Review · Day 8
5 of 8 · Who knows about the bus
What does the uvm_reg_block know about the APB?
☐ The base address and the width of PADDR, which reach it through the uvm_reg_map
☒ Nothing: the only one that knows about the bus is the adapter
☐ Everything: that is why there is one register model per protocol
☐ The SETUP and ACCESS timing, to predict the wait state of the read
The model does not know there is an APB underneath — swap the adapter and the same model drives an AHB. The adapter is twenty lines, once per protocol, and it is the file that comes with a VIP you bought. Watch out for one thing: bus2reg is called by the predictor too, with the item the monitor saw, so an adapter that depends on something the driver put there works in one direction and fails in the other.

## Slide 487
Review · Day 8
6 of 8 · DPI and time
Can an import "DPI-C" function of the golden model wait for a clock edge?
☐ Yes, by putting a #1 inside the .c
☒ No: a function runs in zero time
☐ Yes, as long as the .c is compiled with Verilator’s timing support
☐ Yes: the simulator suspends the C thread for the duration of the call
Zero time, like any function — to consume time you need import "DPI-C" task, and with a clarification almost every tutorial skips: C cannot block by itself. A DPI task consumes time only if it is declared context and from the C it calls back into an export "DPI-C" task of SystemVerilog, which is the one that waits for the edge. And at that point it is no longer a golden model, it is a bus model.

## Slide 488
Review · Day 8
7 of 8 · undefined reference
The .c is written and it compiles, and the link fails with undefined reference to the golden model function. What do you look at first?
☐ Whether the DPI flag is missing from the verilator command line
☐ Whether the .c is in its own -f and not mixed in with the .sv
☒ The name, and the extern "C": the symbol may have come out mangled
☐ Whether the SystemVerilog function is declared virtual so the symbol gets exported
The compiler does not cross the two declarations: the one that joins them is the linker — hence an error about something that is written, right there, in plain sight. It is almost always one of two things: the name does not match letter for letter, or the file got compiled as C++ and the symbol came out mangled. That last one is literally the case here: Verilator hands the user’s sources to the C++ compiler, so the .c needs its extern "C". And there is no DPI flag: the .c goes on the verilator command line like any other source.

## Slide 489
Review · Day 8
8 of 8 · The scoreboard that never shouted
The scoreboard with the golden model in C runs a thousand operations and reports not one. Is that enough?
☐ Yes: a thousand comparisons without a single difference is the definition of verified
☐ Yes, as long as the functional coverage closed at 100 % on top of that
☐ No, because both sides share the opcode enum and cancel each other out
☒ No: a scoreboard that has never seen an error is not tested
The model has to be broken on purpose — vtalu_golden_bug(1) mutates the multiplication and run.sh demands that the scoreboard shout. If it does not shout, the testbench is comparing against itself and nobody was going to find out: it is the same mutation test the capstone grader does with +BUG=1, from the other side of the wire. And the duplicated enum is real but it is a different symptom: if every comparison fails at once, it is the mapping; if one in six fails, it is the DUT.

## Slide 490
Exercise · Day 8 · 2 of 2
The reference model in C, and the two mutations that prove it
cd code/ejercicios/d8-dpi && bash run.sh
The only file of the exercise is vtalu_golden.c. Not one line of the testbench gets touched
Two operations are missing: the subtraction with its borrow —which goes out through a pointer— and the product with the mutation hook
The checker runs three times: healthy DUT against your model, mutated DUT (VTALU_BUG=1), and your mutated model (+GOLDEN_BUG)
Notes: Stage 2 is what makes the exercise worth it, and it is worth explaining first: against the healthy DUT, a model returning some fixed thing could pass by accident if the stimulus were poor. With the DUT lying on bit 0, there is no way of passing without having computed — it is the same mutation test as the capstone, pointed at the model instead of at the scoreboard. The subtraction is the one that trips people, and not because of the arithmetic: a - b is one line. What gets forgotten is the second half of the answer, the borrow, and it gets forgotten because it crosses the boundary in another way —through a pointer, which is how a SystemVerilog output int travels—. The scoreboard compares it, so without it every subtraction fails and no other operation does: that pattern of failures is the one to learn to read. And the trap you cannot see, which is solved in the skeleton on purpose so they do not lose the hour there: without extern "C", Verilator hands the file to the C++ compiler, the symbol comes out mangled, and the link fails with an undefined reference to a function written two lines above. It is DPI’s number one failure mode with Verilator.

## Slide 491
Capstone 2 · Day 8
The second final: a FIFO with backpressure
cd code/ejercicios/d8-fifo && cat spec.en.md
For whoever has already handed in the APB. The protocol is simpler —there are no addresses, no wait states, no error response— and even so it is harder
The APB one is a slave with no useful memory: an address and a value, and the scoreboard can be a table of four rows. A FIFO has order and occupancy, and both have to be carried
The bug of +BUG=1 is not a data bug: almost_full goes up one place late. The data still comes out right and in order, so a scoreboard that only compares rd_data passes green
The small print: the flags describe the state before the edge, rd_data arrives one cycle late, writing with the FIFO full is not an error, and a simultaneous read makes room for the write
Notes: This is the exercise that separates whoever understood from whoever copied the pattern, and the mechanism by which it separates is in the third bullet: the bug is in a control output, not in the data path. A scoreboard that compares what comes out of rd_data closes six of the seven rows of the plan and passes green with the DUT broken. To see it the flags have to be predicted, and to predict the flags the occupancy has to be modelled — that is, writing a reference model with state, which is what the first capstone could not ask for. It is worth saying why it goes second and not first: the APB is the DUT you run into in the first year, and the table-address-value pattern is the right one there. This one teaches when that pattern stops being any use, and that lesson is not understood without having used the pattern before. The trap that catches the most people is the order of updating the model: first look at whether the read takes something out —that frees a place— and only then whether the write goes in. The other way round, the simultaneous write with the FIFO full shows up as a lost piece of data that the DUT never lost, and the student spends an hour looking for the bug in the RTL. And the second one: the check_phase that claims data that never came out. Almost always the test ended one cycle too early, and it is the drain_time of day 3 showing up where nobody expected it.